## Slide 1: Department of Computer Applications
COMPUTER NETWORKS
Subject Code : BBCA304
BY
POOJITHA S
Assistant Professor

## Slide 2: Department of Computer Applications
🌐 Module 1: Outcomes (Data Communication & Basics of Networking)
By the end of this module, you will be able to:
Understand the basics of data communication
  You’ll learn what happens when two devices talk to each other — sender, receiver, medium, and protocols. 👉 Example: How a WhatsApp message travels from your phone to your friend’s phone.
Identify different types of networks
  LAN (local), MAN (city-wide), WAN (worldwide). 👉 Example: Wi-Fi at home (LAN) vs Internet (WAN).
Differentiate between OSI & TCP/IP models
  You’ll understand how communication is divided into layers, and why each layer is important. 👉 Example: Like dividing work in a company — reception, HR, accounts, delivery.
Explain transmission media (guided & unguided)
  You’ll be able to compare wired (cables, fiber optics) vs wireless (radio, satellite, Wi-Fi). 👉 Example: Using LAN cable in labs vs using Wi-Fi in college campus.
Connect theory to real-world applications
  You’ll realize how networks make possible the Internet, cloud, online banking, e-commerce, and more.

## Slide 3: Introduction on Computer Networks
What is Computer Networks ?
A Computer network is a number of computer (also known as node) connected by some communication link.
Two computers connected to the network can communicate with each other though nodes if they are not directly connected.
Some of the nodes in the network may not be computers at all but they are network devices like switches , routers etc to facilitate communication.
Computers are said to be interconnected if they are able to exchange information.
Example : Home Wi-Fi , Bank ATM Network , Online Gaming Network.

## Slide 4: Example 1
Wired Connection (LAN cable)
Internet → Router → Switch → Computers
The router brings the internet from your ISP (ex: Jio, Airtel).
The switch is used to distribute this internet connection to
many computers inside the building.
Each computer is connected with a LAN cable (Ethernet).
Example: In a computer lab, each desktop is connected with a LAN wire.

## Slide 5
Wireless Connection (Wi-Fi / Mobile)
Internet → Router → Phone (direct, no switch needed)
The router itself has Wi-Fi capability.
Phones, laptops, tablets can directly connect to the router’s Wi-Fi without cables.
No switch is needed because Wi-Fi is wireless distribution.
Example: At home, your phone connects directly to the Wi-Fi router (no wire).

## Slide 6
Routers :
Connects Different Networks.
What it does: Connects your local network (LAN) to other networks like the Internet.
How it works: Uses IP addresses (logical address) to decide the best path for data to travel.
IP = house address → fixed while you live there, but if you move, it changes.
Real-life example:
Think of the college main gate.
Inside the campus, everyone knows each other by face/roll number (MAC address).
But when a student wants to go outside the campus (to another city or college), they must go through the main gate (router) which checks their address (IP) and decides where to send them.
Nodes : Devices (nodes) like computers, smartphone, and printer communicate with each other or use the internet.
Ex : Smartphone → Students connect their mobiles to the Wi-Fi to access notes or submit assignments.

## Slide 7
Switches
Switches distributes the connection to multiple devices.
Works only Inside the Same Network (LAN)
What it does: Connects devices (PC, printer, laptop) inside a local area network and lets them share data.
How it works: Uses MAC addresses (hardware ID) it means the switch looks at the MAC address of devices to forward data the right device.
MAC = fingerprint → fixed forever, can’t change.
Real-life example:
Think of a college classroom.
The teacher (switch) knows every student (device) by their roll number (MAC address).
If one student passes a note to another, the teacher makes sure it goes only to that student, not everyone.

## Slide 8
Hubs
A Hub is a simple device that connects multiple devices in a network.
But it has no intelligence: it cannot identify who should receive the data
When one device sends data, the hub forwards it to ALL devices, not just the correct one.
Only the intended device will accept it, but everyone else also "hears" it unnecessarily.
Real Time Example:
Imagine in a classroom, one student makes a mistake.
The teacher (hub) doesn’t know which student did it.
So, the teacher scolds the entire class.
This wastes everyone’s time, even though only one student was responsible.
👉 That’s how a Hub works — it sends the message to everyone, even if it was meant for just one device.
A Hub is a simple device that connects multiple devices in a network.

## Slide 11
Applications in Daily Life
Social Media (Instagram, WhatsApp, YouTube)
Online Education (Zoom, Google Meet, NPTEL)
Banking & Payments (UPI, ATM, Net Banking)
Shopping & Entertainment (Amazon, Netflix)
Cloud Storage (Google Drive, OneDrive)
Real-Life Examples for Computer Networks
WhatsApp / Instagram 📱
Email (Gmail, Outlook) 📧
Phone Call / Video Call ☎️🎥
Google Search 🔎
College Wi-Fi 💻

## Slide 12: Data Communication
Data communication is the process of exchanging data (like text, images, audio, video) between two or more devices using a medium.
Components of Data Communications Networks

## Slide 13
Components:
Sender → the device that sends data (computer, phone).
Message → the information being sent.
Medium → the path (cable, Wi-Fi, satellite).
Receiver → the device that receives the message.
Protocol → the rules for communication (e.g., TCP/IP).
Example: Sending a WhatsApp message or email.

## Slide 14
Letter System as Data Communication
Imagine you want to Share a Message or Note to your best friend During Exam who lives in another city. Long ago, people used letters. You wrote the letter, gave it to the post office, it traveled through many hands, and finally reached your friend after days. That was slow communication.
When you send a letter:
Sender → You write the letter (like computer sending data).
Message → The content of the letter (data/information).
Medium → Postman, postal service, or road transport (like cable/wireless).
Receiver → The person who receives the letter (destination device).
Protocol (Rules) → Writing correct address, stamp, using envelope →
otherwise the letter won’t be delivered (similar to network protocols like IP address, TCP rules).

## Slide 15: Whatsapp System as Data Communication
What is Message?
A Message is a Unit of Communication that Convey Information From a Sender to Receiver.
Ex : Whatsapp , Email , Call
Sender (Phone A) → Data (“Hi”) → Medium (Internet) → Receiver (Phone B)

## Slide 16
1. Sender (Your Phone)
You type “Hi” on WhatsApp. Your phone becomes the source device that generates the data.
2. Message (The Data)
The text “Hi” is converted into digital data (0s and 1s). This data is what needs to travel.
3.Medium (The Internet / Network)
The data leaves your phone → passes through Wi-Fi or Mobile Network → travels across the Internet.
4. Receiver (Your Friend’s Phone)
The data finally arrives at your friend’s phone. WhatsApp app converts the digital signals back into text → displays “Hi” on their screen.
5.Protocol(Address)
Set of Rule That Govern How Data is Formatted and Processed for Communication Between Devices.
Example : Home Address

## Slide 17
Characteristics of Effective Communication
Delivery : Definition: Delivery means that the data sent by the sender must arrive at the correct destination (the right device or user).
Example: If you send an email to your friend, it must reach your friend’s email inbox and not someone else’s.
Accuracy : Definition: The data received should be the same as the data sent, without any changes, loss, or corruption.
Example: If you send a text message saying “Meet at 5 PM”, the receiver should get exactly that, not “Meet at 8 PM”.
Timeliness : Definition: Data must be delivered at the right time. Late data is often useless, especially in real-time communication.
Example: In online gaming or stock trading, if the data arrives late, it can affect the game result or financial decision.
Jitter (variation in packet delay, important in video/audio calls) : Definition: Jitter is the variation in the delay of received packets.
Example: In a video call, jitter causes the audio/video to break, lag, or go out of sync.

## Slide 18
Data Flow
Data Flow Communication between two devices can be simplex, half-duplex, or full-duplex as shown in Figure.
Simplex
Half-Duplex
Full-Duplex
1.Simplex
Meaning: Communication goes in only one direction. The sender can send, but the receiver cannot reply back.
Example: A keyboard sends data to the computer, but the computer cannot send data back to the keyboard. Another example is television – the TV station sends signals, and you only receive them.

## Slide 19
2. Half Duplex
Meaning: Communication goes in both directions, but only one side at a time can send data. When one device is sending, the other must wait.
Example: A walkie-talkie – when one person talks, the other has to wait and listen. They cannot both talk at the same time.
3. Full-Duplex
Meaning: Communication goes in both directions at the same time. Both sender and receiver can send and receive data simultaneously.
Example: A telephone call – both people can speak and listen at the same time without waiting.
Summary in one line:
Simplex → One way only.
Half-Duplex → Both ways, but one at a time.
Full-Duplex → Both ways at the same time.

## Slide 20: Networks
A network is a set of devices (often referred to as nodes) connected by communication links.
A node can be a computer, printer, or any other device capable of sending and/or receiving data generated by other nodes on the network.
“Computer network’’ to mean a collection of autonomous computers(An autonomous computer is an independent computer that can perform its tasks without depending on others) interconnected by a single technology. Two computers are said to be interconnected if they are able to exchange information.
Example :
Home Network (LAN – Local Area Network)
College Computer Lab (LAN)
Bank Network (MAN – Metropolitan Area Network)

## Slide 22
✅ Advantages of Computer Networks:
Resource Sharing – Computers can share printers, files, and internet easily.
Communication – Enables quick communication through emails, chats, and video calls.
Data Sharing – Files and data can be accessed by multiple users.
Cost-Effective – Reduces the need for separate devices (e.g., one printer for many).
Centralized Data – Data can be stored in one place (server) and accessed by all.
❌ Disadvantages of Computer Networks:
Security Issues – Risk of hacking, data theft, or viruses spreading.
Cost of Setup – Requires routers, switches, cables, or Wi-Fi setup.
Maintenance Needed – Needs regular monitoring and skilled people to manage.
If Network Fails – Communication and resource sharing stop.
Unauthorized Access – Without proper control, anyone may misuse resources.

## Slide 23
Goals of Networking
Resource sharing (printers, files).
Communication (email, messaging).
Reliability (backup).
Scalability (expansion with more devices).
APPLICATION OF COMPUTER NETWORKS

## Slide 24: Networks
Network Devices:
Router: A router connects multiple networks and routes traffic between them.
Switch: A switch connects multiple devices within a network and forwards data packets.
Hub: A hub connects multiple devices within a network, but it doesn't perform any routing or switching.
Modem: A modem connects
Network Protocols:
TCP/IP (Transmission Control Protocol/Internet Protocol): TCP/IP is a suite of protocols that governs data communication over the internet.
HTTP (Hypertext Transfer Protocol): HTTP is a protocol for transferring data over the web.
FTP (File Transfer Protocol): FTP is a protocol for transferring files over a network.
Network Security:
1. Firewall: A firewall is a security system that controls incoming and outgoing network traffic.
2. Encryption: Encryption is the process of converting data into a secure, unreadable format.
3. Authentication: Authentication is the process of verifying the identity of users or devices.
Network Applications:
Email: Email is a network application for sending and receiving electronic messages.
File Sharing: File sharing is a network application for sharing files between devices.
Video Conferencing: Video conferencing is a network application for real-time video communication.

## Slide 25: Networks Topology
Topology refers to the physical or logical arrangement of devices in a network. It describes how devices are connected to each other and how data is transmitted between them.
Topology can be viewed in two ways they are:
Physical Topology
Logical Topology
1. Physical Topology: Refers to the physical arrangement of devices
in a network, such as the layout of cables and devices. (Placement of various nodes)
2. Logical Topology: Refers to the way data is transmitted between
devices in a network, such as the path that data takes. (Deals with the data flow in the network)

## Slide 26: Networks Topology
Types of Network Topologies
Bus Topology: A bus topology is a network where all devices are connected to a single cable.
Star Topology: A star topology is a network where all devices are connected to a central device, such as a hub or switch.
Ring Topology: A ring topology is a network where devices are connected in a circular configuration, and data travels in one direction.

## Slide 27: Networks Topology
4. Mesh Topology: A mesh topology is a network where each device is connected to every other device, providing multiple paths for data transmission.
5. Tree Topology: A tree topology is a network where devices are connected in a hierarchical structure, with multiple levels of devices.
6. Point to Point Topology: Point-to-point topology is a type of topology that works on the functionality of the sender and receiver. It is the simplest communication between two nodes, in which one is the sender and the other one is the receiver. Point-to-Point provides high bandwidth.
Bandwidth – maximum amount of data that can be transferred over a network connection in a give time period.
7. Hybrid Topology : A Hybrid Topology is a network topology that combines two or more different types of topologies such as Star, Bus, Ring, Mesh etc., to form a single network.

## Slide 28: Networks Topology

## Slide 29: Networks Topology
Star Topology – Central device (hub/switch) connects all nodes; easy to manage but costly. Example : Computers in a school lab connected to a central switch.
Bus Topology – Single backbone cable; simple, cheap, but failure in backbone stops network.
Example : Early LANs with a single coaxial cable backbone.
3. Ring Topology – Devices connected in a loop; data travels in one direction; failure of one node affects all.
Example : All computers in the office are connected in a circular path (a ring).
4. Mesh Topology – Every node connects to every other; very reliable, but expensive.
Example: Airline reservation systems → Multiple servers connected to ensure no downtime.

## Slide 30: Networks Topology
5. Tree Topology – Combination of star & bus; scalable, but backbone failure affects whole network.
Example: Corporate offices with branches connected to headquarters.
6. Point - to – point : Direct connection between two devices.
Example : Telephone line between two people.
7. Hybrid Topology : Each department (Computer Science, Mechanical, Electronics) uses Star Topology to connect its computers to a departmental switch.
All the departmental switches are connected together using a Bus Topology or Ring Topology for inter-department communication.
The central server is connected using a Star topology for easy management.
This combination of Star + Bus (or Ring) forms a Hybrid Topology.

## Slide 31: Networks Topology
Why is Network Topology Important?
Network Topology is important because it defines how devices are connected and how they communicate in the network. Here are some points that defines why network topology is important.
Network Performance: It helps in running the network easily and hence increases network performance.
Network Reliability: Some topologies like Star, Mesh are reliable as if one connection fails, they provide an alternative for that connection, hence it works as a backup.

## Slide 32: Types of Networks
The types of network are classified based upon the size, the area it covers and its physical architecture. The four primary network categories are PAN,LAN, WAN and MAN. Each network differs in their characteristics such as distance, transmission speed, cables and cost.
The Different Types of Networks are :
PAN (Personal Area Network)
LAN (Local Area Network)
MAN (Metropolitan Area Network)
WAN (Wide Area Network)
Other types are:
WLAN (Wireless LAN)
SAN (Storage Area Network)

## Slide 33: Types of Networks
1. PAN (Personal Area Network)
Network organized by the individual user for its personal use.
Very small range (a few meters).
Connects personal devices like mobile phone, laptop, Bluetooth, smartwatch.
Example: Using Bluetooth headphones with your phone.

## Slide 34: Types of Networks
2. LAN (Local Area Network)
Group of interconnected computers within a small area. (room, building, campus).
Two or more pc's can from a LAN to share files, folders, printers, applications and other devices.
A LAN provides a data transfer rate of 10 to 100 Mbps. It is a high-speed network and is usually privately owned.
Example: A computer lab in a school , office network, home Wi-Fi.

## Slide 35: Types of Networks
Advantage of LAN
Easy to share devices such as printers, scanners etc.
Easy to share data such as printers.
Cost of LAN setup is low.
Disadvantages of LAN
Power-a good LAN is Required to be all the time.
Area covered is limited.

## Slide 36: Types of Networks
3. MAN (Metropolitan Area Network)
Design to extend over a large area.
Connecting number of LAN's to form larger network, so that resources can be shared.
Networks can be up to 5 to 50 km. Owned by organization or individual.
Data transfer rate is low compare to LAN.
Examples:
Cable TV network in a city.
Multiple college campuses connected within a city.
City-wide Wi-Fi projects.

## Slide 37: Types of Networks
Advantages
Efficiency and shared access.
All the computer-owing residents of the area have equal ability to go online.
MAN can cover a wider area than a LAN.
Disadvantages
It can be costly.
Security problem.
As the network consists of many computers over the span of a city, the connection can lag or become quit slow.
Example: Cable TV

## Slide 38: Types of Networks
4.WAN (Wide Area Network)
A WAN is a country-wide or worldwide network that contains multiple LANs and MANs.
Data transfer rate depends upon the ISP provider and varies over the location. Best example is the internet.
Examples:
The Internet (largest WAN).
Banking networks connecting branches worldwide.
Indian Railways reservation system.
Types of WAN:
Enterprise private network (EPN)
Virtual private network (VPN)

## Slide 39: Types of Networks
Advantages
Increased efficiency
Easy of communication
Lowered costs.
Disadvantages
Security problems.
Training costs.
Maintenance problems.
Example: Internet

## Slide 40: Network Model
A network model is like a blueprint that explains how data travels from one device to another across a network.
It organizes communication into layers, where each layer has a specific role and works with the layers above and below it.
Protocol Layering
Protocol Layering means dividing the whole process of communication into smaller manageable layers, Each layer has a defined function.
Advantages of Protocol Layering
Simplicity – Divides complex networking into smaller parts.
Flexibility – Each layer can be updated without changing others.
Troubleshooting – Easier to find where errors occur.

## Slide 41: Network Model
First Scenario

## Slide 42: Network Model
Second Scenario

## Slide 43: TCP/IP SUIT
What is TCP/IP?
TCP/IP(Transmission Control Protocol / Internet Protocol) is the family of protocols that runs the Internet.
It defines how devices address, route, transport, and present data so any two hosts can talk reliably (or quickly, when reliability isn’t needed).
It’s organized in layers. Each layer serves the one above it and uses the one below it.
The TCP/IP layers (4-layer view)
Link (Network Access) Layer
Internet Layer
Transport Layer
Application Layer

## Slide 44: TCP/IP SUIT

## Slide 45: TCP/IP SUIT
1.Link (Network Access) Layer or Subnetwork layer Moves frames or information on the local Area Network on Hardware & media details. Examples: Ethernet (802.3), Wi-Fi (802.11), radio, pair of copper wire
2. Internet Layer Delivers packets across networks (routing).
The name Inter-net implies IP moves Information between networks . IP is simple and fast. Core protocols:
IP (IPv4/IPv6) – addressing & routing
ICMP/ICMPv6 – diagnostics, errors (e.g., ping, TTL exceeded)
ARP (IPv4) / ND (Neighbour Discovery in IPv6) – map IP↔MAC on a LAN
(Routing protocols used by routers: OSPF, BGP, RIP, etc.)

## Slide 46: TCP/IP SUIT
3.Transport Layer
End-to-end host communication (ports, multiplexing, reliability, flow control).
TCP – reliable, connection-oriented (web, email, files)
UDP – simple, connectionless (DNS, streaming, VoIP, games)
4.Application Layer
User-facing protocols and formats. Examples: HTTP/HTTPS, DNS, SMTP/IMAP/POP3, FTP/SFTP, SSH, TLS, DHCP, NTP, SNMP, MQTT, GRPC, WebSocket's, etc.

## Slide 47: TCP/IP SUIT
Physical Layer → transmits frames as bits.
Data Link Layer → converts packet into frames.
Network Layer → takes the segment, adds an IP header, and calls it a packet.
Transport Layer → breaks the message into segments and adds a TCP or UDP header (with source/destination port, sequence number, etc.).
Application Layer → message (data generated by apps like WhatsApp, email, browser).

## Slide 48: TCP/IP SUIT
Real-Time Example: Visiting Google.com
Application Layer: Browser uses HTTP/HTTPS to request the Google homepage
Transport Layer: TCP ensures the request packets and response packets are delivered in order.
Internet Layer: IP addresses (your device → Google server) are used for routing.
Network Access Layer: Wi-Fi/Ethernet transmits data physically as signals.

## Slide 49: OSI MODEL

## Slide 50: OSI MODEL

## Slide 51: OSI MODEL
Developed by ISO (International Organization for Standardization).
A conceptual framework that describes how data is transmitted across a network.
Ensures interoperability between different devices and vendor(routers, switches).
The 7 Layers of the OSI Model (Top → Bottom)
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 52: OSI MODEL
1. Physical Layer
Deals with raw bits (0s and 1s) on the medium.
Defines cables, connectors, radio signals, voltages.
Examples: Ethernet cables, fibre optics, Wi-Fi signals, hubs, repeaters.
👉 Role: Transmission and reception of raw data
2. Data Link Layer
Packets are framed with MAC addresses for local delivery (device ↔ router).
Example: Wi-Fi (802.11) or Ethernet.
👉 Real time: Your laptop’s Wi-Fi card uses its MAC address to talk to your home router.

## Slide 53: OSI MODEL
3. Network Layer
Each segment is placed into packets with logical IP addresses.
Source IP = Your device’s IP
Destination IP = Gmail/Yahoo mail server IP.
Routers forward packets to the correct destination.
👉 Real time: Your email packet travels across the Internet backbone to Yahoo’s server.
4. Transport Layer
The message is broken into segments.
Uses TCP (Transmission Control Protocol) for reliable delivery.
Port numbers identify services (e.g., SMTP uses port 25 or 587).
👉 Real time: TCP ensures your email arrives completely, not half the message.

## Slide 54: OSI MODEL
5. Session Layer
A session (communication link) is established between your Gmail client and Google’s mail server.
Authentication (login credentials) is managed here.
👉 Real time: Gmail logs you in and keeps your session active while sending.
6. Presentation Layer
The email text (e.g., "Hello") is converted into a standard format (ASCII/Unicode).
If you attach an image, it’s compressed (JPEG).
Data is encrypted if HTTPS/TLS is enabled.
👉 Real time: Gmail encrypts your email so only Yahoo’s server can read it.

## Slide 55: OSI MODEL
7. Application Layer
Gmail app (or browser) prepares the email using SMTP protocol.
Your friend later reads it using IMAP/POP3.
👉 Real time: You click Send on Gmail.
Real-Time Example (WhatsApp message / Web browsing)
Application – You type “Hi” in WhatsApp.
Presentation – Message is encrypted (TLS).
Session – Chat session maintained with server.
Transport – TCP ensures message reliability.
Network – IP addresses route the packet.
Data Link – Wi-Fi/Ethernet frames deliver locally.
Physical – Sent as radio waves or electrical signals.
The OSI Model is a 7-layer framework that explains how data travels from one device to another, making networks organized, interoperable, and easier to troubleshoot.

## Slide 56: Differences Between TCP/IP and OSI model

## Slide 57: Transmission Media
Transmission medium can be broadly defined as anything that can carry information from a source to a destination.
Transmission media are the physical pathways or channels through which data, information, or signals are transmitted from one device (sender) to another (receiver) in a network.
The Transmission media is usually free space(Air ,Vacuum and water), metallic metal or fiber –optic cable.
These signals are transmitted from one device to another in the form of electromagnetic energy.
Electromagnetic energy is a combine of electric and magnetic fields vibrating in relation to each other includes power, radio wases , infrared light , visible light , ultraviolet light and X, gamma and cosmic rays. Each of these constitutes a portion of the Electromagnetic Spectrum

## Slide 58: Transmission Media
Example: Telephone lines, FM Radio.
Micro Waves
Infrared
Radio Waves

## Slide 59: Transmission Media
Guided Media
Guided media, which are those that provide a medium or channel from one device to another, include twisted-pair cable, coaxial cable, and fiber-optic cable.
A signal traveling along any these media is directed and contained by the physical limits of the medium.
Twisted pair and coaxial cable use metallic (copper) conductor that accept and transport signals in the form of electric current.
Optical Fiber is a cable conductor that accept and transport signals in the form of light.
Types of Guided Media:
1.Twisted Pair Cable
2. Coaxial Cable
3. Fiber – optic Cable

## Slide 60: Transmission Media
Twisted Pair Cable
1.Twisted Pair Cable
Consists of pairs of insulated copper wires twisted together which one wires is used to carry signals to the receiver and another is used only as a ground reference.
Twisting reduces interference (noise).
If both parallel the effect of these unwanted signal is not the same in both wires because they are different locations relative to the noise.
TPC is measure in length or inch.
Types:
Unshielded Twisted Pair (UTP)
The most common twisted-pair cable used in communications is referred to as unshielded twisted-pair (UTP).
Used in LAN, telephone lines.

## Slide 61: Transmission Media
Shielded Twisted Pair (STP)
IBM has Also produced a version of twisted pair cable for its use, called STP.
STP cable has a metal foil or braided mesh covering that encases each pair of insulated conductors.
Metal casing improves the quality of cable by preventing the penetration of noise or crosstalk,(how far and though what medium sound waves travel) it is bulkier and more expensive.
The most common UTP connector is RJ45 (RJ stands for registered jack) STP
RJ45 is a keyed Connector(can inserted in only one way).
Example: Ethernet cables (Cat5, Cat6).

## Slide 62: Transmission Media
Applications
Twisted-pair cables are used in telephone lines to provide voice and data channels.
Local-area networks, such as l0Base-T and l00Base-T, also use twisted-pair cables.
Category
Category | Specifications | Data Rate (Mbps) | Use
1 | UTP used in Telephone | <0.1 | Telephone
2 | Improved CAT 2 used in LAN | 10 | LAN
3 | Improved CAT 3 used in LAN | 20 | LAN
RJ45 female and RJ45 Male

## Slide 63: Transmission Media

## Slide 64: Transmission Media
2. Coaxial Cable
Coaxial cable (or coax) carries signals of higher frequency ranges than those in twisted pair cable (becz of two media)
coax has a central core conductor of solid or stranded wire (usually copper) enclosed in an insulating sheath, which is, in turn, encased in an outer conductor of metal foil, braid, or a combination of the two.
The outer metallic wrapping serves both as a shield against noise and as the second conductor, which completes the circuit.
The whole cable is protected by a plastic cover.
Provides better protection from interference than twisted pair.
Example: Cable TV connections, CCTV networks.

## Slide 65: Transmission Media
Coaxial Cable Standards
CC are Categorized by their RG (Radio Government)
RG stands for "Radio Guide" or historically "Radio Government".
It is a standardized numbering system used to identify different types of coaxial cables.
Each RG type has a specific diameter, impedance, and usage.

## Slide 66: Transmission Media
The most common type of connector used today is the Bayone-Neill-Concelman (BNC), connector.
Applications
Coaxial cable was widely used in analog telephone networks. (Carry 10,000 Voice Signals)
Digital telephone networks where signal cc could carry digital data up 600 Mbps.
Cable TV networks also use coaxial cables.
Another common application of coaxial cable is in traditional Ethernet LANs.

## Slide 67: Transmission Media
3.Fiber Optic Cable
A fiber-optic cable is made of glass or plastic and transmits signals in the form of light.
Light travels in a straight line as long as it is moving through a single uniform substance.
If a ray of light traveling through one substance suddenly enters another substance(of a different density), the ray changes direction. Bending of light ray
Example: Broadband internet (JioFiber, Airtel Fiber), undersea communication cables.

## Slide 68: Transmission Media
The modes of propagation are classical waveforms of light that travel via different paths within an optical fibre.
1. Multimode
A beam of light moves through the core in the different path it moves within the cable depends on the structure core.
Types
1. Multimode step index fiber : In multimode step-index fiber, the density of the core remains constant from the center to the edges.
2. Multimode Graded index :Decreases this Bending of the signal through the cable. The word index here refers to the index of refraction

## Slide 69: Transmission Media
2. Single Mode
Single-mode uses step-index fiber and a highly focused source of light that limits beams to a small range of angles, all close to the horizontal.

## Slide 70: Transmission Media
The subscriber channel (SC) connector, The straight-tip (ST) connector, MT-RJ(mechanical transfer registered jack) is a connector .
Applications
Fiber-optic cable is often found in backbone networks because its wide bandwidth is cost-effective..
Some cable TV companies use a combination of optical fiber and coaxial cable, thus creating a hybrid network.
Local-area networks such as 100Base-FX network (Fast Ethernet) and 1000Base-X also use fiber-optic cable.

## Slide 71: Transmission Media
Advantage
Higher bandwidth
Less signal attenuation
Immunity to electromagnetic interference
Light weight.
Disadvantages
Installation and maintenance
Unidirectional light propagation.
Cost

## Slide 72: Transmission Media
2. Unguided Media (Wireless Communication)
Unguided media transmits signals without physical cables, using the air, vacuum, or water as the medium. Data is carried through electromagnetic waves.
Types of Unguided Media:
Radio Wave
  Frequency range: 3 kHz – 1 GHz.
  Can travel long distances and penetrate buildings.
  Used for AM/FM radio, Wi-Fi, cordless phones.
2. Microwaves
  Frequency range: 1 GHz – 300 GHz.
  Requires line-of-sight (cannot pass through obstacles easily).
  Used in mobile phone communication, satellite links, WiMAX.

## Slide 73: Transmission Media
3.Infrared (IR)
  Short range, point-to-point communication.
  Cannot pass through walls.
  Used in TV remotes, short-range data transfer (IR blasters, printers).
4.Satellite Communication
  Uses satellites in Earth’s orbit to relay signals.
  Covers very large areas (global communication).
  Used in GPS, weather forecasting, satellite TV (DTH), international calls.

## Slide 74: Transmission Media

## Slide 75: Transmission Media
Aspect | Guided Media | Unguided Media
Definition | Transmission of data through physical path (cables/wires). | Transmission of data through air, water, or vacuum (wireless).
Medium | Twisted pair cable, Coaxial cable, Fiber optic cable. | Radio waves, Microwaves, Infrared, Satellite communication.
Direction | Signals are guided/constrained by the physical medium. | Signals are broadcast freely in space.
Installation Cost | Generally low to medium (depending on cable). | Can be expensive (satellite, towers) but no physical cables required.
Bandwidth & Speed | High (especially in fiber optics). | Comparatively lower; affected by interference.
Security | More secure, as signals are confined to the medium. | Less secure, as signals can be intercepted easily.
Reliability | Less affected by environment (except cable damage). | Affected by weather, obstacles, interference.
Mobility | Not portable (fixed connections). | Supports mobility (Wi-Fi, Mobile networks).
Examples | LAN in colleges, Internet via fiber optics, Telephone lines. | Wi-Fi, Mobile networks (4G/5G), Bluetooth, Satellite TV.

## Slide 76: THANK YOU