## Slide 1
COMPUTER NETWORKS
Subject Code : BBCA304
BY
POOJITHA S
Assistant Professor

## Slide 2: Outcomes of this Module (Data Link Layer)
Error Detection & Correction
Understand why errors happen during transmission (noise, interference).
Learn how errors are detected using techniques like:
  Block Coding (parity, Hamming codes).
  Cyclic Redundancy Check (CRC)
Know how some methods can even correct errors (not just detect).
Data Link Control (DLC) Services
Framing → How raw data is divided into frames for transmission.
Flow Control → How sender & receiver manage data speed to avoid overload.
Error Control → Ensures reliable delivery by detecting & correcting errors
Connectionless service → Send frames independently (like SMS).
Connection-oriented service → Establish connection before communication (like a phone call).
Protocols → Study common DLC protocols like HDLC (High-Level Data Link Control).

## Slide 3: Outcomes of this Module (Data Link Layer)
Media Access Control (MAC)
Learn how multiple devices share the same communication medium.
Random Access → Devices send data when they want (e.g., ALOHA, CSMA).
Controlled Access → Devices take turns in an organized way (polling, token passing).

## Slide 4: ERROR
What is an Error?
Error is a condition when the receiver's information does not match the senders.
Digital signals suffer from noise during transmission that can introduce errors in the binary bits traveling from sender to receiver.
That means a 0 bit may change to 1 or a 1 bit may change to 0.
Data (Implemented either at the Data link layer or Transport Layer of the OSI Model) may get Jumped by noise or get corrupted whenever a message is transmitted.
To prevent such errors, error-detection codes are added as extra data to digital messages. This helps in detecting any errors that may have occurred during message transmission.

## Slide 5: Types of Errors
Types of Errors are:
Single-Bit Error
Multiple-Bit Error
Burst Error
1. Single-Bit Error
A single-bit error refers to a type of data transmission error that occurs when one bit (i.e., a single binary digit) of a transmitted data unit is altered during transmission, resulting in an incorrect or corrupted data unit.
✅ Example:
Sent: 1011
Received: 1111 (only the 2nd bit changed).

## Slide 6: Types of Errors
2. Multiple-Bit Error
A multiple-bit error is an error type that arises when more than one bit in a data transmission is affected.
Although multiple-bit errors are relatively rare when compared to single-bit errors, they can still occur, particularly in high-noise or high-interference digital environments.
Sent data: 1011001
Received data: 1111011
Changes:
2nd bit: 0 → 1
5th bit: 0 → 1
7th bit: 1 → 0
👉 Here, 3 bits are wrong → multiple error.

## Slide 7: Types of Errors
3. Burst Error
When several consecutive bits are flipped mistakenly in digital transmission, it creates a burst error. This error causes a sequence of consecutive incorrect values.
Two or more bits in the data are changed due to noise or interference.
Errors occur in a sequence.
Example:
Sent: 1011001
Received: 1001111 (multiple bits changed in a row).

## Slide 8: Error Detection & Correction
What is it?
When data is sent from sender → receiver, errors may occur (due to noise, interference, etc.). 👉 Error Detection is the process of checking whether the received data has errors. (It does not correct the error, only detects it.)
Techniques of Error Detection and Correction
Parity Bit (Simple Method)
Checksum
Block Coding (like Hamming Code)
Cyclic Redundancy Check (CRC)

## Slide 9: Data Link Control (DLC) Services
The Data Link Layer (Layer 2 in the OSI model) is responsible for node-to-node delivery of data (from one computer to another directly connected in a network).
It ensures that data frames are delivered error-free, in the correct sequence, and without duplication.
The main services of DLC are:
Framing
Flow Control
Error Control
Connectionless and Connection-Oriented Services
Data Link Layer Protocols
High-Level Data Link Control (HDLC)

## Slide 10: Data Link Control (DLC) Services
Framing
The process of dividing the stream of bits received from the network layer into manageable units called frames.
Frames make it possible to detect and correct errors.
Methods of Framing:
  Character Count (field indicates number of characters in frame)
  Character Stuffing (special characters used to mark beginning & end of frame)
  Bit Stuffing (special bit pattern e.g. 01111110 used in HDLC)
📌 Example: Like putting data in an envelope before sending a letter.

## Slide 11: Data Link Control (DLC) Services
2. Flow Control
Ensures that the sender does not overwhelm the receiver with too much data at once.
Prevents buffer overflow at the receiver.
Techniques:
  Stop-and-Wait (send one frame, wait for acknowledgment before sending next)
  Sliding Window (multiple frames sent before acknowledgment, more efficient)
📌 Example: Talking to a friend slowly so they can take notes before you continue.

## Slide 12: Data Link Control (DLC) Services
3. Error Control
The physical layer of a network may not always be reliable, so data packets can get corrupted.
To prevent corrupted packets from reaching the network layer, error control is implemented at the data-link layer.
This is usually done using two main methods, both involving a CRC (Cyclic Redundancy Check) added to the frame header.
Method 1 : If a frame is corrupted, it is simply discarded. If it is correct, it is delivered to the network layer. This method is commonly used in wired LANs like Ethernet.

## Slide 13: Data Link Control (DLC) Services
Method 2 : If a frame is corrupted, it is discarded, but acknowledgments are also used to manage both flow control and error control between sender and receiver.
Combination of Flow and Error Control
Flow control and error control can work together in a network.
The acknowledgment (ACK) sent for flow control can also indicate that a packet was received without errors.
If the sender does not receive an acknowledgment, it means there was a problem with the sent frame.
Frames carrying such acknowledgments are called ACK frames to distinguish them from regular data frames.
This concept is applied in many simple network protocols.

## Slide 14: Data Link Control (DLC) Services
4. Connectionless and Connection-Oriented Services
DLC protocols can be Connectionless or Connection-Oriented.
More details are covered in Network and Transport Layers.
1. Connectionless Protocol
Frames are sent independently, with no relationship between them.
“Connectionless” ≠ no physical connection the transmission medium still exists.
Common in LAN data-link protocols.
Example : Ethernet (IEEE 802.3)
Frames are sent independently, no numbering, no guaranteed order.
Common in wired LANs.
Frames are not numbered; no ordering is maintained.

## Slide 15: Data Link Control (DLC) Services
2. Connection-Oriented Protocol
Logical connection is established before data transfer (Setup Phase).
Related frames are transmitted in order (Transfer Phase).
Connection is terminated after transfer (Teardown Phase).
Frames are numbered; receiver ensures correct order before delivering to network layer.
Rare in wired LANs; found in some point-to-point protocols, wireless LANs, and WANs.
Establishes a logical connection before sending frames.
Used in some Wireless WANs.
.

## Slide 16: Data Link Control (DLC) Services
5. Data Link Layer Protocols
The four protocols have been defined for the data-Link Layer to deal with Flow and Error Control.
Four traditional protocols: Simple, Stop-and-Wait, Go-Back-N, Selective-Repeat.
Simple and Stop-and-Wait are still used at the data-link layer.
Go-Back-N and Selective-Repeat are mostly used at the transport layer.
Finite State Machine (FSM) Concept:
FSM models the behavior of a data-link-layer protocol.
States: The machine has a finite number of states( limited or countable; )always in one state at a time.
(The system can move between these states based on events, but it cannot have unlimited states.)
Events: Defining the list of action to performed and determine the next state.
Actions: Tasks performed when an event occurs.
Initial State: The state where the machine starts when turned on.

## Slide 17: Data Link Control (DLC) Services
State: A state represents the current condition or situation of the system.
It defines what the system is doing or waiting for at a specific time.
The system stays in a state until an event occurs that causes it to change.
Example:
“Waiting for frame to send”
“Waiting for acknowledgment”
Initial State: The initial state is the starting point of the FSM when the system is first turned on or begins operation.
It is the default state before any event occurs.
From this state, the machine reacts to the first event and may transition to another state.
Example:
When the system starts, it is in the “Idle” or “Waiting to send” state.

## Slide 18: Data Link Control (DLC) Services
State = Current situation of the system.
Initial State = The first state where the system begins.
Event:
An event is something that happens or occurs that causes a change in the system’s state.
It acts as a trigger for the machine to perform an action or move to another state.
Example: A frame is received, timer expires, or acknowledgment arrives. (through the IP address)
Action:
An action is the response or task performed by the machine when an event occurs.
It defines what the system does as a result of the event.
Example: Send a frame, start a timer, or discard a frame.
Event = What happens
Action = What the system does in response
Trigger = A trigger is something that causes or starts an action or event. It’s the reason why a system changes from one state to another.

## Slide 19: Data Link Control (DLC) Services
Example (FSM with 3 States):
Starts at State I.
Event 1: Perform actions 1 & 2 → move to State II.
State II:
  Event 1 → perform action 3 → stay in State II.
  Event 3 → no action → move back to State I.
  The figure shows a machine with three states.
  There are only three possible events and three possible actions.
  The machine starts in state I. If event 1 occurs, the machine performs actions 1 and 2 and moves to state II.
  When the machine is in state II, two events may occur. If event 1 occurs, the machine performs action 3 and remains in the same state, state II.
  If event 3 occurs, the machine performs no action, but move to state I.

## Slide 20: Data Link Control (DLC) Services

## Slide 21: Data Link Control (DLC) Services
Representation of FSM (Finite State Machine)
Rounded-corner rectangles → represent states.
Coloured text → indicates events.
Black text → shows actions performed.
Horizontal line or slash ( / ) → separates event and action.
Arrows → show movement (transition) from one state to another.

## Slide 22: Data Link Control (DLC) Services
1. Simple Protocol
The first data-link layer protocol has no flow control and no error control.
Assumes the receiver can handle all incoming frames immediately.
The receiver is never Overloaded by data.
Frames are sent continuously without waiting for acknowledgment.

## Slide 23: Data Link Control (DLC) Services
The data-link layer at the sender gets a packet from its network layer, makes a frame out of it, and sends the frame.
The data-link layer at the receiver receives a frame from the link, extracts the packet from the frame, and delivers the packet to its network layer.
The data-link layers of the sender and receiver provide transmission services for their network layers.
Simple Protocol

## Slide 24: Data Link Control (DLC) Services
FSMs for the Simple Protocol

## Slide 25: Data Link Control (DLC) Services
Finite State Machines (FSMs) for Simple Protocol
The sender site should not send a frame until its network layer has a message to send.
The receiver site cannot deliver a message to its network layer until a frame arrives.
Each FSM has only one state, the ready state.
The sending machine remains in the ready state until a request comes from the process in the network layer.
When this event occurs, the sending machine encapsulates the message in a frame and sends it to the receiving machine.
The receiving machine remains in the ready state until a frame arrives from the sending machine.
When this event occurs, the receiving machine decapsulates the message out of the frame and delivers it to the process at the network layer.

## Slide 26: Data Link Control (DLC) Services
Finite State Machines (FSMs) for Simple Protocol
Each FSM has only one state — the Ready State.
Sender FSM:
Waits until the network layer has a message to send.
When it gets one → encapsulates it into a frame and sends it.
Receiver FSM:
Waits until a frame arrives from the sender.
When it arrives → decapsulates the message and delivers it to the network layer.

## Slide 27: Data Link Control (DLC) Services
Flow Diagram

## Slide 28: Data Link Control (DLC) Services
Flow of Data (Left to Right)
Network → Data-Link (Sender side):
The Network layer at the sender gives a packet to the Data-Link layer.
The Data-Link layer encapsulates the packet into a frame.
Data-Link (Sender) → Data-Link (Receiver):
The frame is transmitted across the physical link to the receiver’s Data-Link layer
Data-Link → Network (Receiver side):
The Data-Link layer at the receiver receives the frame.
It extracts (decapsulates) the packet from the frame.
Then it delivers the packet to its Network layer.

## Slide 29: Data Link Control (DLC) Services
Key Points
There is no flow control or error control in this simple protocol.
The receiver can always handle incoming frames immediately.
Each frame carries one packet from sender to receiver.
This diagram shows the basic service provided by the Data-Link layer — transferring packets between two directly connected nodes.

## Slide 30: Data Link Control (DLC) Services
2. Stop – and – Wait Protocol
Stop-and-Wait protocol provides both flow control and error control.
The sender sends one frame at a time and waits for an acknowledgment before sending the next frame.
Each data frame includes a CRC for error detection.
If the CRC is incorrect, the frame is considered corrupted and is silently discarded by the receiver.
The receiver’s silence indicates that a frame was either lost or corrupted.
The sender starts a timer after sending a frame.
If an acknowledgment is received before the timer expires, the timer is stopped, and the next frame is sent.

## Slide 31: Data Link Control (DLC) Services
If the timer expires before receiving an acknowledgment, the sender resends the previous frame.
The sender keeps a copy of the frame until its acknowledgment arrives.
Once the acknowledgment is received, the sender discards the frame copy and sends the next one.
Only one frame and one acknowledgment can be in the channel at any time.
Stop and Wait Protocol

## Slide 32: Data Link Control (DLC) Services
FSM Primitive Stop and Wait Protocol

## Slide 33: Data Link Control (DLC) Services
Sender States
The sender is initially in the ready state, but it can move between the ready and blocking state.
Ready States
When the sender is in this state, it is only waiting for a packet from the network layer.
If a packet comes from the network layer, the sender creates a frame, saves a copy of the frame, starts the only timer and sends the frame. The sender then moves to the blocking state.
Blocking State
When the sender is in this state, three events can occur.
If a time-out occurs, the sender resends the saved copy of the frame and restarts the timer.
b. If a corrupted ACK arrives, it is discarded.
c. If an error-free ACK arrives, the sender stops the timer and discards the saved copy of the frame. It then moves to the ready state.

## Slide 34: Data Link Control (DLC) Services
Receiver
The receiver is always in the ready state. Two events may occur:
a. If an error-free frame arrives, the message in the frame is delivered to the network layer and an ACK is sent
.b. If a corrupted frame arrives, the frame is discarded.

## Slide 35: Data Link Control (DLC) Services
Flow Diagram for Stop and Wait

## Slide 36: Data Link Control (DLC) Services
The first frame is sent successfully and acknowledged by the receiver.
The second frame is sent but gets lost during transmission.
After a time-out, the sender resends the second frame.
The third frame is sent and acknowledged successfully, but the acknowledgment is lost.
Due to the lost acknowledgment, the sender resends the third frame.
The receiver receives the same third frame twice, resulting in duplicate data being delivered to the network layer.
This duplication is an error in the Stop-and-Wait scheme.
To fix this issue, sequence numbers and acknowledgment numbers are introduced in the next section.

## Slide 37: Data Link Control (DLC) Services
Sequence and Acknowledgment Numbers
Duplicate packets can cause serious problems, such as repeating actions (e.g., ordering the same item twice).
To prevent duplicates, sequence numbers are added to data frames and acknowledgment numbers to ACK frames.
Sequence numbers help the receiver identify new frames and detect duplicates.
In the Stop-and-Wait protocol, numbering is simple and alternates between 0 and 1 (i.e., 0, 1, 0, 1, …).
Acknowledgment numbers also alternate as 1, 0, 1, 0, … corresponding to the next expected frame.
The acknowledgment number indicates the sequence number of the next frame the receiver expects.
Automatic Repeat Request mechanism ensures reliable and duplicate-free data transmission between sender and receiver.

## Slide 38: Data Link Control (DLC) Services
3. Go-Back-N (GBN) Protocol
Introduction
Go-Back-N (GBN) is a sliding window protocol used in the data-link layer for reliable data transmission.
It allows the sender to transmit multiple frames before needing an acknowledgment from the receiver.
The receiver, however, is simpler: it only needs to acknowledge the last correctly received frame in order.
Key Features
Sliding Window at Sender
  The sender can send N frames without waiting for an acknowledgment.
  N = window size, a fixed number of frames.
Receiver Behaviour
  The receiver accepts frames only in order.
  If a frame is missing, all subsequent frames are discarded (even if received correctly).

## Slide 39: Data Link Control (DLC) Services
Acknowledgment (ACK)
  Receiver sends an ACK for the last correctly received frame in sequence.
  The sender goes back and retransmits all frames starting from the missing/erroneous frame.
Error Handling
  Errors can be lost frames, corrupted frames, or lost acknowledgments.
  GBN handles this by retransmitting all frames from the lost frame onward.

## Slide 40: Data Link Control (DLC) Services
Working Principle
Sender can send frames 0, 1, 2, …, N-1 within the window.
Receiver checks the sequence number of incoming frames:
  If the frame is in order, it is accepted, and an ACK is sent.
  If the frame is out of order, it is discarded, and no ACK is sent for that frame.
If the sender times out (doesn’t receive ACK), it retransmits all frames from the last acknowledged frame.

## Slide 41: Data Link Control (DLC) Services
Example
Sender: [0] [1] [2] [3] [4]
↓ ↓ ↓
Receiver: [0] [1] X [3] [4]
Frame 2 lost → Receiver discards 3, 4
→ ACK (1) sent last
→ Sender retransmits from frame 2 onward

## Slide 42: Data Link Control (DLC) Services
4. Selective Repeat Protocol
Introduction
Selective Repeat (SR) is a sliding window protocol used in the data-link layer for reliable data transmission.
Unlike Go-Back-N (GBN), SR retransmits only the specific frames that are lost or erroneous, not all subsequent frames.
This makes SR more efficient, especially in high-error networks.

## Slide 43: Data Link Control (DLC) Services
Sliding Window at Sender and Receiver
Both sender and receiver maintain a window of size N (number of frames that can be sent or received without waiting for acknowledgment).
Receiver Behaviour
The receiver accepts frames that arrive out of order.
It buffers out-of-order frames until missing frames are received.
Only when the missing frames arrive, it delivers frames to the upper layer in order.
Acknowledgment (ACK)
Receiver sends an individual ACK for each correctly received frame.
ACK contains the sequence number of the frame being acknowledged.
Error Handling
If a frame is lost or corrupted, only that frame is retransmitted.
No need to retransmit subsequent frames, unlike GBN.

## Slide 44: Data Link Control (DLC) Services
Working Principle
Sender can transmit frames 0, 1, 2, …, N-1 within its window.
Receiver accepts frames in or out of order:
  If a frame is in order, deliver it to the upper layer and send ACK.
  If a frame is out of order, buffer it and send ACK.
Retransmission occurs only for frames that are not acknowledged within a timeout period.

## Slide 45: Data Link Control (DLC) Services
Example :
Sender: [0] [1] [2] [3] [4]
↓ ↓ ↓ ↓
Receiver: [0] [1] X [3] [4]
(stores 3,4)
→ Sender retransmits only frame 2
→ Receiver now has 2,3,4 and delivers in order.

## Slide 46: Data Link Control (DLC) Services
Piggybacking
A technique called piggybacking is used to improve the efficiency of the bidirectional protocols.
When a frame is carrying data from A to B, it can also carry control information about arrived (or lost) frames from B.
when a frame is carrying data from B to A, it can also carry control information about the arrived (or lost) frames from A.

## Slide 47: Data Link Control (DLC) Services
5. High-Level Data Link Control (HDLC)
High-level Data Link Control (HDLC) is a bit-oriented protocol (one in which control information (like frame boundaries, acknowledgments, etc.) for communication over point to-point and multipoint links.
It implements the Stop-and-Wait protocol.
Configurations and Transfer Modes
HDLC provides two common transfer modes that can be used in different configurations:
Normal Response Mode (NRM)
Asynchronous Balanced Mode (ABM)

## Slide 48: Data Link Control (DLC) Services
Normal Response Mode
Normal response mode (NRM), the station configuration is unbalanced.
We have one primary station and multiple secondary stations.
A primary station can send commands , a secondary station can only respond.
The NRM is used for both point-to-point and multiple-point links, as shown in Figure.

## Slide 49: Data Link Control (DLC) Services
2. Asynchronous Balanced Mode
Asynchronous balanced mode (ABM), the configuration is balanced.
The link is point-to-point, and each station can function as a primary and a secondary (acting as peers), as shown in Figure.
This is the common mode today.
NRM: Teacher (primary) asks → Student (secondary) answers.
ABM: Two friends having a conversation — both can talk or listen anytime.

## Slide 50: Data Link Control (DLC) Services
Framing
To provide the flexibility necessary to support all the options possible in the modes and configurations just described, HDLC defines three types of frames:
I-frames (Information frames) are used to data-link user data and control information relating to user data (piggybacking).
S-frames (Supervisory frames) are used only to transport control information.
U frames (Unnumbered frames) Information carried by U-frames is intended for managing the link itself.

## Slide 51: Data Link Control (DLC) Services

## Slide 52: Data Link Control (DLC) Services
Flag field -The flag field of an HDLC frame is an 8-bit sequence with the bit pattern 01111110 that identifies both the beginning and the end of a frame and serves as a synchronization pattern for the receiver.
Address field- The field of an HDLC frame contains the address of the secondary station. If a primary station created the frame, it contains a to address. If a secondary creates the frame, it contains a from address. An address field can be 1 byte or several bytes long, depending on the needs of the network.
Control field -The control field is a 1- or 2-byte segment of the frame used for flow and error control. The interpretation of bits in this field depends on the frame type.
Information field -The information field contains the user's data from the network layer or management information. Its length can vary from one network to another.
FCS field -The frame check sequence (FCS) is the HDLC error detection field. It can contain either a 2- or 4-byte CRC.
Control Field : The control field determines the type of frame and defines its functionality.

## Slide 53: Data Link Control (DLC) Services
Control Field for I-Frames
I-frames are designed to carry user data from the network layer. In addition, they can include flow and error control information (piggybacking). The subfields in the control field are used to define these functions.
The first bit defines the type. If the first bit of the control field is 0, this means the frame is an I-frame.
The next 3 bits, called N(S), define the sequence number of the frame.
The last 3 bits, called N(R), correspond to the acknowledgment number when piggybacking is used.
The single bit between N(S) and N(R) is called as P/F.
The P/F field is a single bit with a dual purpose(router and switch). It has meaning only when it is set (bit = 1) and can mean poll or final. It means poll when the frame is sent by a primary station to a secondary. (when the address field contains the address of the receiver)
It means final when the frame is sent by a secondary to a primary. (when the address field contains the address of the sender).

## Slide 54: Data Link Control (DLC) Services
Control Field for S-Frames
Supervisory frames are used for flow and error control whenever piggybacking is either impossible. S-frames do not have information fields.
If the first 2 bits of the control field is 10, this means the frame is an S-frame.
The last 3 bits, called N(R), corresponds to the acknowledgment number(ACK) or negative acknowledgment number (NAK) depending on the type of S-frame.
The 2 bits called code is used to define the type of S-frame itself. With 2 bits, we can have four types of S-frames, as described below:
1. Receive ready (RR)
2. Receive not ready(RNR)
3. Reject (REJ)
4. Selective reject (SREJ)

## Slide 55: Data Link Control (DLC) Services
Receive ready (RR): If the value of the code subfield is 00, it is an RR S-frame.
Receive Not Ready(RNR):Receive Not Ready (RNR) – S-frame with code subfield = 10, Similar to RR (Receive Ready) but adds “not ready” status. Informs sender that the receiver is busy and cannot accept more frames
3. Reject (REJ): If the value of the code subfield is 01, it is a REJ S-frame. The value of NCK is the negative acknowledgment number used in Go-Back-N ARQ
4. Selective reject (SREJ): If the value of the code subfield is 11, it is an SREJ S-frame. This is a NAK frame used in Selective Repeat ARQ. The value of N(R) is the negative acknowledgment number.

## Slide 56: Data Link Control (DLC) Services
Control Field for U-Frames
Unnumbered frames are used to exchange session management and control information between connected devices. U-frame codes are divided into two sections: a 2-bit prefix before the P/F bit and a 3-bit suffix after the P/F bit.
Together, these two segments (5 bits) can be used to create up to 32 different types of U-frames. Figure shows how U-frames can be used for connection establishment and connection release.
Node A asks for a connection with a set asynchronous balanced mode (SABM) frame, node B gives a positive response with an unnumbered acknowledgment (UA) frame.
After these two exchanges, data can be transferred between the two nodes (not shown in the figure). After data transfer, node A sends a DISC (disconnect) frame to release the connection it is confirmed by node B responding with a UA (unnumbered acknowledgment).

## Slide 57: Data Link Control (DLC) Services

## Slide 58: Media Access Control
MEDIA ACCESS CONTROL When nodes or stations are connected and use a common link, called a multipoint link, we need a multiple-access protocol to coordinate access to the link .Many protocols have been devised to handle access to a shared link. All of these protocols belong to a sublayer in the data-link layer called media access control (MAC). We categorize them into three groups.
There are two main categories of access methods:

## Slide 59: Media Access Control
Random Access (Contention-based)
In random access or contention methods, no station is superior to another station. A station that has data to send uses a procedure defined by the protocol to make a decision on whether or not to send.
Two features give this method its name.
1. There is no scheduled time for a station to transmit. Transmission is random and hence called random access.
2. No rules specify which station should send next. Station compete with one another to access the medium and hence called contention methods. If more than one station tries to send, there is an access collision-and the frames will be either destroyed or modified.

## Slide 60: Media Access Control
ALOHA
ALOHA, the earliest random-access method was developed at the University of Hawaii in early 1970. The medium is shared between the stations and hence has potential arrangements.
a. Pure ALOHA
➔ The original ALOHA protocol is called pure ALOHA. The idea is that each station sends a frame whenever it has a frame to send.
➔ Since there is only one channel to share, there is the possibility of collision between frames from different stations.
➔ There are four stations (unrealistic assumption) that contend with one another for access to the shared channel. Only two frames survive: frame 1.1 from station 1 and frame 3.2 from station 3.

## Slide 61: Media Access Control

## Slide 62: Media Access Control
The pure ALOHA protocol relies on acknowledgments from the receiver. If the acknowledgment does not arrive after a time-out period, the station resends the frame.
➔ If all these stations try to resend their frames after the time-out, the frames will collide again. Each station waits for a random time before resending, called the back-off time TB.
➔ In the second method after a maximum number of retransmission attempts Kmax' a station must give up and try later.

## Slide 63: Media Access Control
Vulnerable time-
Station A sends a frame at time t.
Now imagine station B has already sent a frame between t – T fr and t.
This leads to a collision between the frames from station A and station B. The end of B's frame collides with the beginning of A's frame. On the other hand, suppose that station C sends a frame between t and t + Tfr .Here, there is a collision between frames from station A and station C. The beginning of C's frame collides with the end of A's frame.
Pure ALOHA vulnerable time = 2 x Tfr

## Slide 64: Media Access Control
Vulnerable Period
For Pure ALOHA, the vulnerable period = 2 × (frame transmission time). Because:
A collision can occur if another frame starts anytime during the frame transmission or within one frame time before it starts.
Throughput Formula
Throughput is the product of the number of attempts () and the probability of success

## Slide 65: Media Access Control
= Average number of frames generated (including new + retransmitted ones) during one frame transmission time.
This means on average, there are attempts per frame time.
S = Average number of successful transmissions per frame time.
Now, in Pure ALOHA, for a frame to be successful, no other frame should be transmitted during its vulnerable period.

## Slide 66: Media Access Control
Throughput Let us call G the average number of frames generated by the system during one frame transmission time. Then it can be proved that the average number of successful transmissions for pure ALOHA is S=G x e-2G. The maximum throughput S maxis 0.184, for G =0.

## Slide 67: Media Access Control
. Slotted ALOHA
In slotted ALOHA we divide the time into slots of Tfrs and force the station to send only at the beginning of the time slot. This reduces Collision compared to pure aloha.
The vulnerable time for slotted ALOHA is one-half that of pure ALOHA. Slotted ALOHA vulnerable time = Tfr Throughput It can be proved that the average number of successful transmissions for ALOHA is S = G x e-G. The maximum throughput Smaxis 0.368, when G = 1.

## Slide 68: Media Access Control
2. Carrier Sense Multiple Access (CSMA)
➔ Carrier sense multiple access (CSMA) requires that each station first listen to the medium before sending. The principle "sense before transmit" or "listen before talk."
➔ CSMA can reduce the possibility of collision, but it cannot eliminate it. Stations are connected to a shared channel.
➔ The possibility of collision still exists because of propagation delay; when a station sends a frame, it still takes time for the first bit to reach every station and for every station to sense it.

## Slide 69: Media Access Control
Persistence Methods This method tells, What should a station do if the channel is busy? What should a station do if the channel is idle? Three methods have been devised
1. I-persistent - In this method ,after the station finds the line idle, it sends its frame immediately.
2. Nonpersistent- In this method, a station that has a frame to send senses the line. If the line is idle, it sends immediately. If the line is not idle, it waits a random amount of time and then senses the line again.
3. p-Persistent -This method is used if the channel has time slots with a slot duration equal to or greater than the maximum propagation time. In this method, after the station finds the line idle it follows these steps:
With probability p, the station sends its frame.
With probability q = 1 - p, the station waits for the beginning of the next time slot and checks the line again. a. If the line is idle, it goes to step 1. b. If the line is busy, it acts as though a collision has occurred and uses the backoff procedure.

## Slide 70: Media Access Control

## Slide 71: Media Access Control
3.Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
In this method, a station monitors the medium after it sends a frame to see if the transmission was successful. If so, the station is finished. If, however, there is a collision, the frame is sent again
. 1. At time t1, station A has executed its persistence procedure and starts sending the bits of its frame.
2. At time t2, station C has not yet sensed the first bit sent by A. Station C executes its persistence procedure and starts sending the bits in its frame, which propagate both to the left and to the right.
3. The collision occurs sometime after time t2' Station C detects a collision at time t3 when it receives the first bit of A's frame.
4. Station C immediately transmission.
5. Station A detects collision at time t4 when it receives the first bit of C's frame; it also immediately aborts transmission.
6. CSMA / CD used in half duplex (communication in both direction but not at same time)..

## Slide 72: Media Access Control
Minimum Frame Size
➔ For CSMA/CD to work, a restriction on the frame size is required.
➔ Before sending the last bit of the frame, the sending station must detect a collision, if any, because it does not keep a copy of the frame.
➔ Therefore, the frame transmission time Tfr must be at least two times the maximum propagation time Tp.

## Slide 73: Media Access Control
Procedure
It is similar to the one for the ALOHA protocol, but there are differences.
1. Addition of the persistence process.
2. In ALOHA, we first transmit the entire frame and then wait for an acknowledgment. In CSMA/CD, transmission and collision detection is a continuous process.
3. A short jamming signal that enforces the collision in case other stations have not yet sensed the collision.

## Slide 74: Media Access Control
Energy Level
The level of energy in a channel can have three values: zero, normal, and abnormal.
➔ At the zero level, the channel is idle.
➔ At the normal level, a station has successfully captured the channel and is sending its frame.
➔ At the abnormal level, there is a collision and the level of the energy is twice the normal level.
A station that has a frame to send or is sending a frame needs to monitor the energy level to determine if the channel is idle, busy, or in collision mode.

## Slide 75: Media Access Control
Throughput
The throughput of CSMA/CD is greater than that of pure or slotted ALOHA. The maximum throughput occurs at a different value of G and is based on the persistence method and the value of p in the p-persistent approach.
1. For I-persistent method the maximum throughput is around 50 percent when G =1.
2. For nonpersistent method, the maximum throughput can go up to 90 percent when G is between 3 and 8

## Slide 76: Media Access Control
4. Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA)
The basic idea behind CSMA/CD is that a station needs to be able to receive while transmitting to detect a collision.
➔ When there is no collision, the station receives one signal its own signal. When there is a collision, the station receives two signals: its own signal and the signal transmitted by a second station.
➔ To distinguish between these two cases, the received signals in these two cases must be significantly different.
➔ In a wired network, the received signal has almost the same energy. In case of collision, the detected energy almost doubles.
➔ In a wireless network, much of the sent energy is lost in transmission. The received signal has very little energy. Collision may add very little additional energy. This is not useful for effective collision detection.

## Slide 77: Media Access Control
Collision must be avoided on wireless network, using the following strategies
1. Interframe Space (IFS) Collisions are avoided by transmission even if the channel is found idle. When an idle channel is found, the station does not send immediately. It waits for a period of time called the interframe space or IFS.
2. Contention Window The contention window is an amount of time divided into slots. A station that is ready to send chooses a random number of slots as its wait time. The number of slots in the window changes according to the binary exponential back-off strategy(set to one slot the first time and then doubles each time the station cannot detect an idle channel after the IFS time).
3. Acknowledgment With all these precautions, there still may be a collision resulting in destroyed data. In addition, the data may be corrupted during the transmission. The positive acknowledgment and the time-out timer can help guarantee that the receiver has received the frame.

## Slide 78: Media Access Control

## Slide 79: Media Access Control
Procedure
➔ The channel needs to be sensed before and after the IFS. The channel also needs to be sensed during the contention time.
➔ For each time slot of the contention window, the channel is sensed.
➔ If it is found idle, the timer continues; if the channel is found busy, the timer is stopped and continues after the timer becomes idle again.

## Slide 80: Media Access Control

## Slide 81: Media Access Control
1. Before sending a frame, the source station senses the medium by checking the energy level at the carrier frequency.
The channel uses a persistence strategy with backoff until the channel is idle.
After the station is found to be idle, the station waits for a period of time called the Distributed interframe space (DIFS); then the station sends a control frame called the request to send (RTS).
2. After receiving the RTS and waiting a period of time called the short interframe space (SIFS), the destination station sends a control frame, called the clear to send (CTS), to the source station. This control frame indicates that the destination station is ready to receive data.
3. The source station sends data after waiting an amount of time equal to SIFS.
4. . The destination station, after waiting an amount of time equal to SIFS, sends an acknowledgment to show that the frame has been received.

## Slide 82: Media Access Control
Network Allocation Vector
Collision avoidance aspect of this protocol is accomplished by a feature called NAV.
➔ When a station sends an RTS frame, it includes the duration of time that it needs to occupy the channel.
➔ The stations that are affected by this transmission create a timer called a network allocation vector (NAV) that shows how much time must pass before these stations are allowed to check the channel for idleness.
➔ Each station, before sensing the physical medium to see if it is idle, first checks its NAV to see if it has expired.
Collision During Handshaking
Two or more stations may try to send RTS frames at the same time. These control frames may collide. However, because there is no mechanism for collision detection, the sender assumes there has been a collision if it has not received a CTS frame from the receiver. The back off strategy is employed, and the sender tries again.

## Slide 83: Media Access Control
Frame Exchange Time Line
Figure shows the exchange of data and control frames in time.

## Slide 84: Media Access Control
2. Controlled Access
In this method, stations cannot transmit whenever they want.
Access to the channel is controlled in an orderly manner.
Collisions are avoided because only one device can send at a time.
Techniques of Controlled Access:
Reservation
Polling
Token Passing

## Slide 85: Media Access Control
Reservation
➔ In the reservation method, a station needs to make a reservation before sending data.
➔ Time is divided into intervals.
➔ In each interval, a reservation frame precedes the data frames sent in that interval.
Figure shows a situation with five stations and a five-mini slot reservation frame. In the first interval, only stations 1, 3, and 4 have made reservations. In the second interval, only station 1 has made a reservation.

## Slide 86: Media Access Control
2. Polling
➔ Polling works with topologies in which one device is designated as a primary station and the other devices are secondary stations.
➔ The primary device controls the link; the secondary devices follow its instructions.
➔ The primary device, therefore, is always the initiator of a session
➔ If the primary wants to receive data, it asks the secondary’s if they have anything to send; this is called Poll function. Secondary responds with DATA if any ,else negative ack (NAK) if it has nothing to send.
➔ If the primary wants to send data, it tells the secondary to get ready to receive; this is called Select function. It transmits SEL and waits for acknowledgement from secondary before sending data.

## Slide 87: Media Access Control
Polling

## Slide 88: Media Access Control
3. Token Passing
➔ In the token-passing method, the stations in a network are organized in a logical ring.
➔ A special packet called a token circulates through the ring.
➔ The token gives the station the right to access the channel and send its data.
➔ When a station has some data to send, it holds the token and sends its data and releases the token once data is sent.
➔ When a station receives the token and has no data to send, it just passes the data to the next station.
➔ Stations must be limited in the time they can have possession of the token.
➔ The token must be monitored to ensure it has not been lost or destroyed.
➔ Stations do not have to be physically connected in a ring; the ring can be a logical one.

## Slide 89: Media Access Control
➔ The problem with this topology is that if one of the links-the medium between two adjacent stations fails, the whole system fails.
➔ The dual ring topology uses a second ring which operates in the reverse direction compared with the main ring.

## Slide 90: Media Access Control
Real Time Example:
“Controlled access is like in a classroom:
Reservation = students book time to speak.
Polling = teacher asks each student one by one.
Token passing = only the student holding the mic can speak.”