## Slide 1: ACADEMIC YEAR -2023-24( ODD SEM) Subject: DIGITAL DESIGN AND COMPUTER ORGANIZATION Subject Code: BCS302
Prepared By,
Prof. Yogesh N
Assistant Professor
Dept. of Computer Science & Design
ATMECE, Mysuru

## Slide 2
MODULE-1 8 Hr
Introduction to Digital Design: Binary Logic, Basic Theorems And Properties Of Boolean Algebra, Boolean Functions, Digital Logic Gates, Introduction, The Map Method, Four-Variable Map, Don’t-Care Conditions, NAND and NOR Implementation, Other Hardware Description Language – Verilog Model of a simple circuit.
MODULE-2 8 Hr
Combinational Logic: Introduction, Combinational Circuits, Design Procedure, Binary Adder- Subtractor, Decoders, Encoders, Multiplexers. HDL Models of Combinational Circuits – Adder, Multiplexer, Encoder. Sequential Logic: Introduction, Sequential Circuits, Storage Elements: Latches, Flip-Flops.
MODULE-3 8 Hr
Basic Structure of Computers: Functional Units, Basic Operational Concepts, Bus structure, Performance –Processor Clock, Basic Performance Equation, Clock Rate, Performance Measurement. Machine Instructions and Programs: Memory Location and Addresses, Memory Operations, Instruction and Instruction sequencing, Addressing Modes.

## Slide 3
MODULE-4 8 Hr
Input/output Organization: Accessing I/O Devices, Interrupts – Interrupt Hardware, Enabling and Disabling Interrupts, Handling Multiple Devices, Direct Memory Access: Bus Arbitration, Speed, size and Cost of memory systems. Cache Memories – Mapping Functions.
MODULE-5 8 Hr
Basic Processing Unit: Some Fundamental Concepts: Register Transfers, Performing ALU operations, fetching a word from Memory, Storing a word in memory. Execution of a Complete Instruction. Pipelining: Basic concepts, Role of Cache memory, Pipeline Performance.

## Slide 4
Course Outcome
The student will be able to:
CO1: Apply the K–Map techniques to simplify various Boolean expressions.
CO2: Design different types of combinational and sequential circuits along with Verilog programs.
CO3: Describe the fundamentals of machine instructions, addressing modes and Processor performance.
CO4: Explain the approaches involved in achieving communication between processor and I/O devices.
CO5:Analyze internal Organization of Memory and Impact of cache/Pipelining on Processor Performance.

## Slide 5
Text Books:
1. M. Morris Mano & Michael D. Ciletti, Digital Design With an Introduction to Verilog Design, 5e,Pearson Education.
2. Carl Hamacher, ZvonkoVranesic, SafwatZaky, Computer Organization, 5th Edition, Tata McGraw Hill.

## Slide 6
Assessment Details (both CIE and SEE)
The weightage of Continuous Internal Evaluation (CIE) is 50% and for Semester End Exam (SEE) is 50%.
The minimum passing mark for the CIE is 40% of the maximum marks (20 marks out of 50) and for the SEE minimum passing mark is 35% of the maximum marks (18 out of 50 marks). A student shall be deemed to have satisfied the academic requirements and earned the credits allotted to each subject/course if the student secures a minimum of 40% (40 marks out of 100) in the sum total of the CIE(Continuous Internal Evaluation) and SEE (Semester End Examination) taken together.

## Slide 7: 1. CIE for the theory component of the IPCC (maximum marks 50) IPCC means practical portion integrated with the theory of the course. CIE marks for the theory component are 25 marks and that for the practical component is 25marks. 2. 25 marks for the theory component are split into 15 marks for two Internal Assessment Tests (Two Tests, each of 15 Marks with 01-hour duration, are to be conducted) and 10 marks for other assessment methods mentioned in 22OB4.2. The first test at the end of 40-50% coverage of the syllabus and the second test after covering 85-90% of the syllabus. 3. Scaled-down marks of the sum of two tests and other assessment methods will be CIE marks for the theory component of IPCC (that is for 25 marks). The student has to secure 40% of 25 marks to qualify in the CIE of the theory component of IPCC.

## Slide 8
15 marks for the conduction of the experiment and preparation of laboratory record, and 10 marks for the test to be conducted after the completion of all the laboratory sessions.
On completion of every experiment/program in the laboratory, the students shall be evaluated including viva-voce and marks shall be awarded on the same day.
The CIE marks awarded in the case of the Practical component shall be based on the continuous evaluation of the laboratory report. Each experiment report can be evaluated for 10 marks. Marks of all experiments’ write-ups are added and scaled down to 15 marks.
The laboratory test (duration 02/03 hours) after completion of all the experiments shall be conducted for 50 marks and scaled down to 10 marks.
Scaled-down marks of write-up evaluations and tests added will be CIE marks for the laboratory component of IPCC for 25 marks.
The student has to secure 40% of 25 marks to qualify in the CIE of the practical component of the IPCC.

## Slide 9
SEE for IPCC: Theory SEE will be conducted by University as per the scheduled timetable, with common question papers for the course (duration 03 hours)
1. The question paper will have ten questions. Each question is set for 20 marks.
2. There will be 2 questions from each module. Each of the two questions under a module (with a maximum of 3 sub-questions), should have a mix of topics under that module.
3. The students have to answer 5 full questions, selecting one full question from each module.
4. Marks scored by the student shall be proportionally scaled down to 50 Marks
The theory portion of the IPCC shall be for both CIE and SEE, whereas the practical portion will have a CIE component only. Questions mentioned in the SEE paper may include questions from the practical component.

## Slide 10
Module-1 Introduction to Digital Design
Binary Logic, Basic Theorems And Properties Of Boolean Algebra,
Boolean Functions, Digital Logic Gates, Introduction,
The Map Method, Four-Variable Map, Don’t-Care Conditions,
NAND and NOR Implementation,
Other Hardware Description Language – Verilog Model of a simple circuit.

## Slide 11
Objectives
● To demonstrate the functionalities of binary logic system

## Slide 12
Introduction
Analog signal is a signal whose amplitude can take any value between given limits. An analog circuits operates on continuous signals.
Digital signal is a signal whose amplitude can have only given discrete values between defined limits. A digital circuits operates on discrete signals.
Clock is a periodic, rectangular waveform used as a basic timing signal. Duty cycle for a periodic digital signal, the ratio of high level time to the period or the ratio of low level time to the period.
A table that shows all of the input output possibilities of a logic circuit is called truth table.

## Slide 13
Clock
A digital circuit having one or more input signals but only one output signal is called a gate.
The most basic gates are -the NOT gate (inverter), the OR gate and the AND gate.
Any logic function/ logic circuit can be implemented using only one kind of gate then such gates are called universal logic gates. NOR gate and NAND gate are called universal logic gates.
The other logic gates are XOR and XNOR gate.

## Slide 14
Basic Logic gates

## Slide 15
Universal Logic gates

## Slide 16
Other Logic gates

## Slide 17
Boolean Rules & Laws

## Slide 18: De Morgan's Theorem The First theorem states that “The complement of the sum of all the terms is equal to the product of the complement of each term”.

## Slide 19: The First theorem states that “The complement of the product of all the terms is equal to the sum of the complement of each term”.

## Slide 20: Minimum Forms of Switching Functions
In a positive logic system, binary 0 stands for low voltage and binary 1 for high voltage.
In a negative logic system, binary 0 stands for high voltage and binary 1 for low voltage.
Combinational Circuits are circuits made up of different types of logic gates

## Slide 21: Minterms and Maxterms for Three Variables
A minterm is a product of “n” literals
A maxterm is a sum of “n” literals
Sum Of Products (SOP): A Boolean equation that is the logical sum of logical products. This type of equation applies to an AND-OR circuit.
Product Of Sums (POS): A Boolean equation that is the logical product of logical sums. This type of equation applies to an OR-AND circuit.

## Slide 22: Steps to get SOP 1) Locate each output 1 in truth table 2) Write the respective minterm 3) Apply OR operation to the minterms

## Slide 24: Steps to get SOP 1) Locate each output 0 in truth table 2) Write the respective maxterm 3) Apply AND operation to the maxterms

## Slide 25: Combinational Circuit with Truth Table is given write SOP and POS expressions.

## Slide 26: Truth Table with Don’t-Cares The X’s in the truth table indicate that we don’t care whether the value of 0 or 1 is assigned to F.
In SOP we use m to denote the required minterms and d to denote the don’t-care minterms.
F(A,B,C) = Σ m(0, 3, 7) + Σ d(1, 6)
In POS we use M to denote the required maxterms and D to denote the don’t-care maxterms.
F(A,B,C) = Π M(2, 4, 5) · Π D(1, 6)

## Slide 27: Write minterm and maxterm expansions for the following truth table.

## Slide 28: The various Boolean expression simplification techniques are 1) Algebraic techniques 2) Karnaugh Map/K-Map Method 3) Quine McCluskey Method 4) Entered Variable Map/ MEV/EMV Method
Karnaugh map/K map is a method simplifying and manipulating switching functions.
K map method is faster and easier to apply than other simplification methods.

## Slide 29: Two Variable K-Map The number of cells in 2 variable K-map is four (2X2), since the number of variables is two. The following figure shows 2 variable K-map and location of minterms on a 2 variable K-map.
Example: Convert following truth table into K map.
Y = F(A, B) = Σ m (2, 3)

## Slide 30: Three Variable K-Map The number of cells in 3 variable K-map is eight (23), since the number of variables is 3. The following figure shows 3 variable K-map and location of minterms on a 3 variable K-map.

## Slide 31: Convert following truth table into K map. Y = F(A, B, C) = Σ m (2,6,7)

## Slide 32: Convert following truth table into K map. Y = F(A, B, C, D) = Σ m(1,6,7,14)

## Slide 33
Truth Table with Don’t-Cares
In SOP we use m to denote the required minterms and d to denote the don’t-care minterms.
F(A,B,C) = Σ m(0, 3, 7) + Σ d(1, 6)
In POS we use M to denote the required maxterms and D to denote the don’t-care maxterms.
F(A,B,C) = Π M(2, 4, 5) · Π D(1, 6)

## Slide 34
Write minterm and maxterm expansions for the following truth table

## Slide 35
Pairs, Quads and Octets
Two adjacent 1’s in the K-map is called a pair and it eliminate one variable.

## Slide 36
A quad is a group of four l’s that are horizontally or vertically adjacent and a quad eliminates two variables and their complements.

## Slide 37
An octet is a group of 8 ls that are horizontally or vertically adjacent and an octet eliminates three variables and their complements.

## Slide 38
Determination of Minimum Expressions using Essential Prime Implicants
Any single 1 or any group of 1’s which can be combined together on a map of the function F represents a product term which is called an implicant of F.
A product term implicant is called a prime implicant if it cannot be combined with another term to eliminate a variable.
The following procedure can then be used to obtain a minimum sum of products from a Karnaugh map
1) Choose a minterm (a 1) which has not yet been covered.
2) Find all 1’s and X’s adjacent to that minterm.
3) If a single term covers the minterm and all of the adjacent 1’s and X’s,
then that term is an essential prime implicant, so select that term
4) Repeat steps 1, 2, and 3 until all essential prime implicants have been chosen.
5) Find a minimum set of prime implicants which cover the remaining 1’s
on the map.

## Slide 40: Implementation of basic gates using NAND gates

## Slide 41: Implementation of basic gates using NAND gates

## Slide 42: XOR & XNOR gates using NAND gates

## Slide 44: Minimum Forms of Switching Functions
In a positive logic system, binary 0 stands for low voltage and binary 1 for high voltage.
In a negative logic system, binary 0 stands for high voltage and binary 1 for low voltage.
Combinational Circuits are circuits made up of different types of logic gates