## Slide 1
ACADEMIC YEAR -2023-24( ODD SEM) SUBJECT:DIGITAL DESIGN & COMPUTER ORGANIZATION SUBJECT CODE: BCS302 MODULE -2 PART - 1
Prepared By,
Prof. Yogesh N
Assistant Professor
Dept. of Computer Science & Design
ATMECE, Mysuru

## Slide 2
COMBINATIONAL CIRCUIT DESIGN & SIMULATION USING GATES
Digital Logic Families
The following are the most popular digital logic families
TTL – Transistor Transistor Logic
ECL – Emitter Coupled Logic
MOS – Metal-Oxide Semiconductor
CMOS – Complementary Metal-Oxide Semiconductor
Characteristics of Logic Families
Fan-in
Fan-out
Propagation delay
Noise margin
Power dissipation

## Slide 3
Fan-in: refers to the number of inputs in a digital logic gate family.
Fan-out: specifies the no. of standard loads that the output of typical gate can drive without impairing its normal operation

## Slide 4
Propagation delay: is the average transition time for a signal to propagate from input to output.
Noise margin: is the maximum external noise voltage added to an input signal that does not cause an undesirable change in the output.
Power dissipation: it is the power consumed by the gate that must be available from power supply.

## Slide 5: REVIEW OF COMBINATIONAL CIRCUIT DESIGN
Steps
Set up a truth table which specifies the output(s) as a function of the input variables.
Derive simplified algebraic expressions for the output functions using Karnaugh Maps, or Quine- McCluskey method, or any other similar procedure.
The resulting algebraic expressions are then manipulated into the proper form, depending on the type of gates to be used in realizing the circuit.
Minimum two-level AND-OR, or NAND-NAND circuits can be realized using the minimum sum-of-products. Minimum two-level OR-AND, or NOR-NOR circuits can be realized using the minimum product-of-sums.

## Slide 6
DESIGN OF CIRCUITS WITH LIMITED GATE FAN-IN
In practical logic design problems, the maximum number of inputs on each gate is limited.
Depending on the type of gates used, this limit may be two, three, four, eight etc..
If a two-level realization of a circuit requires more gate inputs than allowed, factoring the logic expression to obtain a multi-level realization is necessary.
Example 1: Realize the following functions using only two-input NAND gates and inverters.
𝑓1 = Σ𝑚 (0,2,3,4,5)
𝑓2 = Σ𝑚 (0,2,3,4,7)
𝑓3 = Σ𝑚(1,2,6,7)

## Slide 7
GATE DELAYS AND TIMING DIAGRAMS
When the input to a logic gate is changed, the output will not change instantaneously.
The gates take a finite time to react to a change in input.
So that the change in the gate output is delayed with respect to the input change.
If the change in output is delayed by time, ε, with respect to the input, we say that, the gate has a propagation delay of ε.
Figure shows possible input and output waveforms for an inverter

## Slide 8
Timing diagram for a circuit with two gates
Each gate has a propagation delay of 20 ns
Gate inputs B and C are held at constant values 1 and 0.
Input A is changed to 1 at t = 40 ns and then changed back to 0 at t = 100 ns.
The output of gate G1 changes 20 ns after A changes, and the output of gate G2 changes 20 ns after G1 changes.

## Slide 9
HAZARDS IN COMBINATIONAL LOGIC
If, in response to any single input change and for some combination of propagation delays, a circuit output may momentarily go to 0 when it should remain a constant 1, we say that the circuit has a static 1-hazard.
Similarly, if the output may momentarily go to 1 when it should remain a 0, we say that the circuit has a static 0-hazard.
If, when the output is supposed to change from 0 to 1 (or 1 to 0), the output may change three or more times, we say that the circuit has a dynamic hazard.
Fig. Hazards

## Slide 10
static 0-hazard.
If A = B = C = 0 and then output F =0.
When B changes from 1 to 0 then output F should remain a constant 0. Now E will go to 1 before D goes to 0, resulting in a momentary 1 (a glitch) appearing at the output F .
So F momentarily goes to 1. This is called Static 0 Hazard.

## Slide 11
static 1-hazard.
If A = C = 1 and B=1 then output F =1.
When B changes from 1 to 0 then output F should remain a constant 1. Now E will go to 0 before D goes to 1, resulting in a momentary 0 (a glitch) appearing at the output F .
So F momentarily goes to 0. This is called Static 1 Hazard.
Detection of Static 1 Hazard
Hazards can be detected using a Karnaugh map.
Write down the sum-of-products expression for the circuit.
Plot each term on the map and loop it.
If any two adjacent 1’s are not covered by the same loop, a 1-hazard exists for the transition between the two 1’s.

## Slide 12
To Eliminate Static 1 Hazard
If we add a loop to the map of above Figure and, then, add the corresponding gate to the circuit (as shown in the following Figure), this eliminates the hazard.
The term AC remains 1 while B is changing, so no glitch can appear in the output.

## Slide 13
SIMULATION AND TESTING OF LOGIC CIRCUITS
In logic design process, Logic circuits may be tested either by building them or by simulating them on a computer.
As logic circuits become more and more complex, it is very important to simulate a design before building it.
Simulation is done for following reasons
Verification that the design is logically correct
(2) Verification that the timing of the logic signals is correct
Simulation of faulty components in the circuit as an aid to finding tests for the
circuits.
A simple simulator for combinational logic works as follows
The circuit inputs are applied to the first set of gates in the circuit, and the outputs of those gates are calculated.
The outputs of the gates which changed in the previous step are fed into the next level of gate inputs. If the input to any gate has changed, then the output of that gate is calculated.

## Slide 14
Four-Valued Logic Simulator:
The two logic values, 0 and 1, are not sufficient for simulating logic circuits.
The value of a gate input or output may be unknown, and we will represent this unknown value by X.
If no logic signal at an input, as in the case of an open circuit we use the logic value Z to represent an open circuit, or high impedance (hi-Z) connection.
The following Figure shows a typical simulation screen on a personal computer.
The following Table shows AND and OR functions for four-valued logic simulation.

## Slide 15
For an AND gate,
If one of the inputs is 0, the output is always 0 regardless of the other input
If one input is 1 and the other input is X then the output is X.
If one input is 1 and the other input is Z then the output is X.
For an OR gate,
If one of the inputs is 1, the output is 1 regardless of the other input
If one input is 0 and the other input is X or Z, the output is unknown.