## Slide 1
ACADEMIC YEAR -2023-24( ODD SEM) SUBJECT:DIGITAL DESIGN & COMPUTER ORGANIZATION SUBJECT CODE: BCS302 MODULE -2-PART - 2
Prepared By,
Prof. Yogesh N
Assistant Professor
Dept. of Computer Science & Design
ATMECE, Mysuru

## Slide 2
MULTIPLEXERS
A multiplexer is a data selector which has a group of data inputs , a group of control inputs and single output.
The control inputs are used to select one of the data inputs and connect it to the output terminal.
2-to-1 multiplexer
When the control input A is 0, the switch is in the upper position and the MUX output is Z = I0.
when A is 1, the switch is in the lower position and the MUX output is Z = I1.
MUX acts like a switch that selects one of the data inputs (I0 or I1) and transmits it to the output .
The logic equation for the 2-to-1 MUX is

## Slide 3
4 to 1 Multiplexer
For 4 to 1 multiplexer, 4 data inputs, 2 selection lines and 1 output is needed. The block diagram and circuit diagram is shown below.
For selection inputs, A= 0, B=0, first AND gate alone is enabled and the output produced is
For selection inputs, A= 0, B=1, second AND gate alone is enabled and the output produced is

## Slide 4
For selection inputs, A= 1, B=0, third AND gate alone is enabled and the output produced is
For selection inputs, A= 1, B=1, forth AND gate alone is enabled and the output produced is
Truth table for 4 to 1 MUX is shown below

## Slide 5
Figure shows diagrams for a 4-to-1 multiplexer, 8-to-1 multiplexer, and
2n-to-1 multiplexer.

## Slide 6
8 to 1 Multiplexer IC 74151

## Slide 7
A decoder is a multiple-input, multiple-output combinational logic circuit. It converts the n bit data inputs into the coded 2n outputs.
Decoder
2 to 4 binary decoder
Block diagram
Logic diagram
The block diagram and Logic diagram is shown above. A and B are the two inputs and the output produced is one of the minterms.
The circuit diagram has two inverters, which will provide the complement of two inputs A and B.
Each AND gates generates one of the minters as an output.

## Slide 8
Truth table
From the above truth table, the operation can be understood.
When both the inputs A and B are 0, Y0 will be at active HIGH or logic 1 and the remaining output pins are active LOW or logic 0.
When A = 0 and B = 1, Y1 is at HIGH.
When A = 1 and B = 0, Y2 is at HIGH.
When A = 1 and B = 1, Y3 is at HIGH.
Logic Expression

## Slide 9
3-to-8-line decoder

## Slide 10: Problem: Show how using a 3-to8 decoder and multi-input OR gates following Boolean expression can be realized simultaneously. F1 (A, B, C) = ∑m (0, 4, 6) F2 (A, B, C) = ∑m (0, 5) F3 (A, B, C) = ∑m (1, 2, 3, 7).
Solution:

## Slide 11
Seven-Segment Display

## Slide 12
Common Anode Seven-Segment Display
Common Cathode Seven-Segment Display

## Slide 13: BCD to 7 Segment Decoder
It converts BCD into 7 segment outputs

## Slide 14: Truth Table

## Slide 15
Seven-Segment Decoder IC 7446 with Seven –Segment Display

## Slide 16: ENCODERS An encoder (converts an active input signal to a coded output signal) performs the inverse function of a decoder.
4 to 2 Encoder

## Slide 17
8 to 3 Encoder

## Slide 18
THREE STATE BUFFERS
A gate output can only be connected to a limited number of other device inputs without degrading the performance of a digital system.
A simple buffer may be used to increase the driving capability of a gate output.
The following Figure shows a three-statebuffer and its logical equivalent
Fig: Three state buffer
When the enable input B is 1, the output C equals A.
when B is 0, the output C acts like an open circuit. This is called as high-impedance ( Hi-Z ) state.
Three-state buffers are also called tri-state buffers

## Slide 19
Types of three-state buffers.
In Figures (a) and (b) the buffer output is enabled when B = 1 and disabled when B = 0.
In Figures (c) and (d) the buffer output is enabled when B = 0 and disabled when B = 1.

## Slide 20
  PROGRAMMABLE LOGIC DEVICES (PLDs)
A programmable logic device (PLD) is a digital integrated circuit capable of being programmed to provide different logic functions.
Classification
Programmable Read Only Memory (PROM)
Programmable Array Logic (PAL)
Programmable Logic Array (PLA)

## Slide 21
An example of PLA circuit of a combinational circuit is shown below. As you can observe from the circuit diagram, AND array consists of fuses, to program according to the user requirements.

## Slide 22: Example 1 Realize the Boolean expression W = AB + AB’C’ + BC’ and X = BC + A’BC’ + ABC using Programmable Logic Array.
Solution:
There are three inputs(A, B, C) and two outputs(W, X). The complement of three inputs are obtained through NOT gates.
The given expression has six product terms.
Two OR gate arrays are used at the output to realize the the two functions.

## Slide 23
Example 2
Realize a boolean functions
F1(A, B, C) = ∑ m(1, 3, 6, 7) and
F2(A, B, C) = ∑ m(0, 2, 4, 5) using PLA.
Solution
To obtain the expression, the given function is implemented using Karnaugh map.

## Slide 24
Thus for the two obtained expressions, the PLA circuit is realized. There are three inputs(A, B, C) and two outputs(F1, F2). In the obtained expressions, there are four product terms and so four AND gate array is used. Two OR gates are used to generate the two boolean fuctions.
The realization of the given Boolean function is drawn below.

## Slide 25
Programmable Logic Arrays (PLA)
In PLA the product terms of the input variables is realized by an AND array and the OR array to form the output functions.
Hence, a PLA implements a sum-of-products expression.
PLA has “n” input lines and “m” output lines.
Fig: PLA Structure

## Slide 26
Example: Realize the following functions using PLA
F0 = ∑m (0, 1, 4, 6) = A’B’ + AC’ F1 = ∑m (2, 3, 4, 6, 7) = B + AC’
F2 = ∑m (0, 1, 2, 6) = A’B’ + BC’ F3 = ∑m (2, 3, 5, 6, 7) = AC + B
Solution

## Slide 27
Programmable Array Logic (PAL)
A PAL is a programmable logic array (PLA) in which the AND array is programmable and the OR array is fixed.
Consider the PAL segment of the following Figure (a), used to realize the function 𝐼1𝐼′2 + 𝐼′1𝐼2. The X’s in the following Figure (b) indicate that 𝐼1 𝑎𝑛𝑑 𝐼′2 lines are connected to the first AND gate, and The 𝐼′1𝑎𝑛𝑑 𝐼2 lines are connected to the other gate.