## Slide 1
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
1
Computer Networks – 21CS52
                Course Coordinator:
                Prof. Yogesh N
                Assistant Professor
                Dept. of CSD
                ATMECE, Mysuru

## Slide 2
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
2
Module 1
Introduction to networks
Network Hardware
Network Software
Reference models
Physical Layer
Guided transmission media
Wireless transmission

## Slide 3
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
3
Session 2
Introduction to networks
Network Hardware

## Slide 4
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
4
Network Hardware
There is no generally accepted taxonomy into which all computer networks fit, but two dimensions stand out as important: transmission technology and scale.
There are two types of transmission technology that are in widespread use:
Broadcast links
Point-to-point links
Distance is important as a classification metric because different technologies are used at different
scales
Local area networks (LANs)
Metropolitan area networks (MANs)
Wide area networks (WANs)
Inter-networks ( internet vs. Internet)

## Slide 5
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
5
Network Hardware – Transmission Technology
Point-to-point links
Point-to-point links connect individual pairs of machines.
To go from the source to the destination on a network made up of point-to-point links, short messages, called packets in certain contexts, may have to first visit one or more intermediate machines.
Often multiple routes, of different lengths, are possible, so finding good ones is important in point-to-point networks.
Point-to-point transmission with exactly one sender and exactly one receiver is sometimes called unicasting.

## Slide 6
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
6
Network Hardware – Transmission Technology
Point-to-point links

## Slide 7
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
7
Network Hardware – Transmission Technology
Broadcast network
The communication channel is shared by all the machines on the network; packets sent by any machine are received by all the others.
An address field within each packet specifies the intended recipient.
Upon receiving a packet, a machine checks the address field. If the packet is intended for the receiving machine, that machine processes the packet; if the packet is intended for some other machine, it is just ignored.
A wireless network is a common example of a broadcast link, with communication shared over a coverage region that depends on the wireless channel and the transmitting machine.
Broadcast systems usually also allow the possibility of addressing a packet to all destinations by using a special code in the address field. When a packet with this code is transmitted, it is received and processed by every machine on the network. This mode of operation is called broadcasting.
Some broadcast systems also support transmission to a subset of the machines, which known as multicasting.

## Slide 8
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
8
Network Hardware – Transmission Technology
Broadcast network

## Slide 9
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
9
Network Hardware – Scale
An alternative criterion for classifying networks is by scale. Distance is important as a classification metric because different technologies are used at different scales.
In Fig. below, we classify multiple processor systems by their rough physical size.
Fig. Classification of interconnected processors by scale

## Slide 10
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
10
Network Hardware – Personal Area Network (PAN)
PANs (Personal Area Networks) let devices communicate over the range of a person.
A common example is a wireless network that connects a computer with its peripherals.
Almost every computer has an attached monitor, keyboard, mouse, and printer. Without using wireless, this connection must be done with cables. So many new users have a hard time finding the right cables and plugging them into the right place.
To help these users, some companies got together to design a short-range wireless network called Bluetooth to connect these components without wires. The idea is that if your devices have Bluetooth, then you need no cables.
In the simplest form, Bluetooth networks use the master-slave paradigm of Fig. (next slide). The system unit (the PC) is normally the master, talking to the mouse, keyboard, etc., as slaves.

## Slide 11
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
11
Network Hardware – Personal Area Network (PAN)
The master tells the slaves what addresses to use, when they can broadcast, how long they can transmit, what frequencies they can use, and so on.
Fig. Bluetooth PAN configuration
A completely different kind of PAN is formed when an embedded medical device such as a pacemaker, insulin pump, or hearing aid talks to a user-operated remote control.
PANs can also be built with other technologies that communicate over short ranges, such as RFID on smartcards and library books.

## Slide 12
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
12
Network Hardware – Local Area Network (LAN)
A LAN (Local Area Network) is a privately owned network that operates within and nearby a single building like a home, office or factory.
LANs are widely used to connect personal computers and consumer electronics to let them share resources (e.g., printers) and exchange information.
When LANs are used by companies, they are called enterprise networks.
Wireless LANs are very popular these days, especially in homes, older office buildings, cafeterias, and other places where it is too much trouble to install cables.
In these systems, every computer has a radio modem and an antenna that it uses to communicate with other computers. In most cases, each computer talks to a device in the ceiling as shown in Fig. (next slide). This device, called an AP (Access Point), wireless router, or base station, relays packets between the wireless computers and also between them and the Internet.

## Slide 13
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
13
Network Hardware – Local Area Network (LAN)
There is a standard for wireless LANs called IEEE 802.11, popularly known as WiFi, which has become very widespread. It runs at speeds anywhere from 11 to hundreds of Mbps.
Fig. Wireless and wired LANs. (a) 802.11. (b) Switched Ethernet

## Slide 14
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
14
Network Hardware – Local Area Network (LAN)
Wired LANs use a range of different transmission technologies. Most of them use copper wires, but some use optical fiber.
Typically, wired LANs run at speeds of 100 Mbps to 1 Gbps, have low delay (microseconds or nanoseconds), and make very few errors. Newer LANs can operate at up to 10 Gbps.
Compared to wireless networks, wired LANs exceed them in all dimensions of performance. It is just easier to send signals over a wire or through a fiber than through the air.
Both wireless and wired broadcast networks can be divided into static and dynamic designs, depending on how the channel is allocated.
A typical static allocation would be to divide time into discrete intervals and use a round-robin algorithm, allowing each machine to broadcast only when its time slot comes up.

## Slide 15
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
15
Network Hardware – Local Area Network (LAN)
Static allocation wastes channel capacity when a machine has nothing to say during its allocated slot, so most systems attempt to allocate the channel dynamically (i.e., on demand).
Dynamic allocation methods for a common channel are either centralized or decentralized.
In the centralized channel allocation method, there is a single entity, for example, the base station in cellular networks, which determines who goes next. It might do this by accepting multiple packets and prioritizing them according to some internal algorithm.
In the decentralized channel allocation method, there is no central entity; each machine must decide for itself whether to transmit.

## Slide 16
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
16
Network Hardware – Local Area Network (LAN)
Many home devices are capable of being networked:
Computers (desktop PC, PDA, shared peripherals)
Entertainment (TV, DVD, VCR, camera, stereo, MP3)
Telecommunications (telephone, cell phone, intercom, fax)
Appliances (microwave, fridge, clock, furnace, airco)
Telemetry (utility meter, burglar alarm, babycam).
Requirements: easy to install, foolproof in operation, low price, sufficient capacity, to be expandable, secure and reliable.

## Slide 17
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
17
Network Hardware – Metropolitan Area Network (MAN)
A MAN (Metropolitan Area Network) covers a city.
The best-known examples of MANs are the cable television networks available in many cities. These systems grew from earlier community antenna systems used in areas with poor over-the-air television reception.
In those early systems, a large antenna was placed on top of a nearby hill and a signal was then piped to the subscribers’ houses.
When the Internet began attracting a mass audience, the cable TV network operators began to realize that with some changes to the system, they could provide two-way Internet service in unused parts of the spectrum.
At that point, the cable TV system began to morph from simply a way to distribute television to a metropolitan area network.

## Slide 18
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
18
Network Hardware – Metropolitan Area Network (MAN)
To a first approximation, a MAN might look something like the system shown in Fig. below. In this figure we see both television signals and Internet being fed into the centralized cable headend for subsequent distribution to people’s homes.
Fig. A metropolitan area network based on cable TV
Cable television is not the only MAN, though.
Recent developments in highspeed wireless Internet access have resulted in another MAN, which has been standardized as IEEE 802.16 and is popularly known as WiMAX.

## Slide 19
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
19
Network Hardware - Wide Area Network (WAN)
WAN (Wide Area Network) spans a large geographical area, often a country or continent. We will begin our discussion with wired WANs, using the example of a company with branch offices in different cities.
The WAN in Fig. below is a network that connects offices in Perth, Melbourne, and Brisbane. Each of these offices contains computers intended for running user (i.e., application) programs.
Fig. WAN that connects three branch offices in Australia

## Slide 20
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
20
Network Hardware - Wide Area Network (WAN)
A WAN consists of a collection of machines intended for running user programs (hosts, end systems) and a pure communication subnet(subnet).
The subnet consists of two distinct components:
Transmission lines (also called circuits, channels, or trunks) move bits between machines.
Switching elements (packet switching nodes, intermediate system, data switching exchanges, routers) are specialized computers used to connect three or more transmission lines.
When data arrive on an incoming line, the switching element must choose an outgoing line to forward them on.

## Slide 21
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
21
Network Hardware - Wide Area Network (WAN)
There are two other varieties of WANs. First, rather than lease dedicated transmission lines, a company might connect its offices to the Internet. This allows connections to be made between the offices as virtual links that use the underlying capacity of the Internet.
Fig. WAN using a virtual private network
This arrangement, shown in Fig. (right side), is called a VPN (Virtual Private Network).
Compared to the dedicated arrangement, a VPN has the usual advantage of virtualization, which is that it provides flexible reuse of a resource (Internet connectivity).
A VPN also has the usual disadvantage of virtualization, which is a lack of control over the underlying resources. With a dedicated line, the capacity is clear.

## Slide 22
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
22
Network Hardware - Wide Area Network (WAN)
The second variation is that the subnet may be run by a different company. The subnet operator is known as a network service provider and the offices are its customers. This structure is shown in Fig. below.
The subnet operator will connect to other customers too, as long as they can pay and it can provide service.
Since it would be a disappointing network service if the customers could only send packets to each other, the subnet operator will also connect to other networks that are part of the Internet. Such a subnet operator is called an ISP (Internet Service Provider) and the subnet is an ISP network. Its customers who connect to the ISP receive Internet service.
Fig. WAN using a virtual private network

## Slide 23
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
23
Network Hardware - Internetwork
Many networks exist in the world, often with different hardware and software. People connected to one network often want to communicate with people attached to a different one. The fulfillment of this desire requires that different, and frequently incompatible, networks be connected.
A collection of interconnected networks is called an internetwork or internet. A common form of internet is a collection of LANs connected by a WAN.
Differences among WANs, subnets, networks, and internetworks.
– WAN = subnet + hosts
– Subnet + hosts ------ WAN ----- network
– Cable + hosts ----- LAN ----- network
– Many interconnected networks ---- internetworks
Different owners
Different technologies

## Slide 24
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
24
Summary
In today’s session, you all have gone through the following topics
Network Hardware

## Slide 25
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
25
Discussion and Interaction

## Slide 26
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
26
Topics for Next Session
Module 1
Network Software

## Slide 27
Prof. Yogesh N, Dept. of CSD, ATMECE
YN
27