## Slide 1
M.K.Shashidhar
Assistant Professor
Mechanical Engineering
ATMECE
CAD/CAM
18ME72
CAD/CAM 18ME72
CAD/CAM 18ME72

## Slide 2: CAD/CAM 18ME72
Module .1
Introduction to CIM and Automation: Automation in Production Systems, automated manufacturing systems
Types of automation, reasons for automating, Computer Integrated Manufacturing, computerized elements of a CIM system
CAD/CAM and CIM. Mathematical models and matrices: production rate,
production capacity, utilization and availability, manufacturing lead time, work-in- process, numerical problems
Automated Production Lines and Assembly Systems: Fundamentals, system configurations, applications. automated flow lines, buffer storage, control of production line, analysis of transfer lines, analysis of flow lines without storage.
partial automation, analysis of automated flow lines with storage buffer,
fundamentals of automated assembly systems, numerical.

## Slide 3
Module 2
CAD and Computer Graphics Software: The design process, applications of computers in design, software configuration, functions of graphics package, constructing the geometry.
Transformations: 2D transformations, translation, rotation and scaling homogeneous transformation matrix, concatenation, numerical problems on transformations.
Computerized Manufacture Planning and Control System: Computer Aided Process Planning, Retrieval and Generative Systems, benefits of CAPP.
Production Planning and Control Systems, typical activities of PPC system
computer integrated production management system, Material Requirement Planning, inputs to MRP system
Working of MRP, outputs and benefits, Capacity Planning, Computer Aided Quality Control, Shop floor control.

## Slide 4
Module 3.
Flexible Manufacturing Systems: Fundamentals of Group Technology and Flexible Manufacturing Systems, types of FMS, FMS components, Material handling and storage system, applications, benefits, computer control systems, FMS planning and design issues, Automated Storage and Retrieval Systems, AS/RS andAutomatic parts identification systems and data capture. Line Balancing: Line balancing algorithms, methods of line balancing, numerical problems on largest candidate rule, Kilbridge and Waster method, and Ranked Positional Weights method, Mixed Model line Updated on 16.04.2020/28092020 balancing, computerized line balancing methods.

## Slide 5
Module. 4
Computer Numerical Control: Introduction, components of CNC, CNC programming, manual part programming, G Codes, M Codes, programming of simple components in turning, drilling and milling systems, programming with canned cycles. Cutter radius compensations.
Robot Technology: Robot anatomy, joints and links, common robot configurations, robot control systems, accuracy and repeatability, end effectors, sensors in robotics. Robot programming methods: on-line and offline. methods. Robot industrial applications: material handling, processing and assembly and inspection.

## Slide 6
Module 5
Additive Manufacturing Systems: Basic principles of additive manufacturing, slicing CAD models for AM, advantages and limitations of AM technologies, Additive manufacturing processes: Photo polymerization, material jetting, binder jetting, material extrusion, Powder bed sintering techniques, sheet lamination, direct Energy deposition techniques, applications of AM.Future of Automated Factory: Industry 4.0, functions, applications and benefits. Components of Industry 4.0, Internet of Things (IOT), IOT applications in manufacturing, Big-Data and Cloud Computing for IOT, IOT for smart manufacturing, influence of IOT on predictive maintenance, industrial automation, supply chain optimization, supply-chain & logistics, cyber-physical manufacturing systems

## Slide 7: Course outcomes
CO1: Define Automation, CIM, CAD, CAM and explain the differences between these
concepts , solve simple problems of transformations of entities
CO2: Explain the basics of automated manufacturing industries through mathematical
model and analyze different types of automated flow lines.
CO3:Analyse the automated flow lines to reduce time and enhance productivity.
CO4: Explain the use of different computer applications in manufacturing, and able to
Prepare part programs for simple jobs on machine tools and robot programming
CO5: Visualize and appreciate the modern trends in Manufacturing like additive
manufacturing like additive manufacturing, Industry 4.0 and applications of Internet
of things lead to manufacturing

## Slide 8: Production system
A production system is the collection of people, equipment and procedures organized to accomplish manufacturing operations of a company
Production Machines
Material handling systems
Computer control Systems
Human resources

## Slide 9: Types of Production Machines
Manually operated systems
Worker –Machine system
Semi – automated Machines
Fully automated Machines

## Slide 10: A . Manually operated Machines
.
starting Finishing
point point
Hand held Tools
Worker
Process

## Slide 11: B.Worker Machine system
Starting Finishing
Point Point
Machine
(Power Tools)
Process
Operator

## Slide 12: C . Semi automated machines
Starting Finishing
point Point
Machine
(Power Tools)
Process
Operator

## Slide 13: D . Fully automated machines
Starting finishing
point point
Periodic Worker
attention
Automated
Machine
Process

## Slide 14
Material Handling System
Loading and unloading the work Units
Positioning the work unit at each station
Transporting the work units between stations
Providing temporary storage
Computer control system
Control Material handling system
Production Scheduling
Failure analysis
Quality control
Operation Management
Feedback control
Human Resources

## Slide 15
Classification of Production System
Job Shop Production
Batch Production
Mass Production
Job Shop Production
Custom products are made in small batches , Machines are grouped based on functions,small and medium scale industries
Advantages :
1.High Flexibility of Production
2.Complex parts can be Manufactured
3.Expansion Flexibility

## Slide 16
Dis advantages
1. Skilled manpower is required
2. Production Volume is low
3. Scheduling the process is difficult
Batch Production
Components are created stage by stage,different
Batches of products
Food processing Industries ,Manufacture of sports equipment ,Pharmaceutical Companies
Mass Production
Creating interchangeable parts at low cost,large numbers of similar products

## Slide 17
Benefits:
Lower cost per unit
Reduced manufacturing lead time
Increased output

## Slide 18: Plant Layout
Fixed position Layout
Process Layout
Product-flow layout

## Slide 19: Fixed position Layout
Advanages
1.Material movement is reduced
2.Capital investment is minimized
3.Task is usually done by group of operators,hence continuity of
operation
4.Production centers are independent of each other, hence
effective planning and loading
5.It offers great flexibility in equipment and allow change in
product design
Limitations
1.High skilled Manpower is required
2.Movement of machines and equipment to production centers
maybe time consuming
3.Compilcated fixtures are required for positioning of jobs

## Slide 20
Process Layout
Advantages
1.Less duplication of Machines
2.It offers better and more efficient supervision through
specialization
3.There is greater flexibility in equipment and manpower
4.Better utilization5 of equipment
5. Better control of Process
Disadvantages
1.Long material flow line hence process is time consuming
2.More floor area is required
3.Scheduling is more tedious
4.Specialisation creates monotony

## Slide 21
Product layout
Advantages:
1.Less material handling cost
2.Better utilization of men and machines
3.Less floor space
4.Easy to control production
5.Total production time is minimized
Disadvantages :
1.Very limited flexibility in the process
2.Manufacturing cost increases with fall in volume
3.Single machine breakdown may shut down whole
production line.
4.Strict supervision is essential

## Slide 22: Automation
Automation is the use of control system such as Computers or robots and information technologies for handling different process and machineries in an industry to replace a human being
Automation is defined as “ technology concerned with the
Application of mechanical , electronics , and computer based system to operate an control production”

## Slide 23: Reason for Automation
Advantages :
1.Increased productivity
2.High cost of Labour
3.Labour shortages
4.Safety
5.High cost of raw materials
6.Improved product quality
7.Reduced manufacturing lead time
8.Reduction of in-process inventory

## Slide 24
Disadvantages:
1.Technology limits
2.Economic limits
3.Maintenance
4.Increase in unemployment
Automation systems
Information technology
Computer aided manufacturing
Computer aided process planning
Group Technology
Numerically controlled Machines
Robot
Flexible Manufacturing system
Computer integrated Manufacturing

## Slide 25: Types of automation
1.Fixed automation or Rigid Automation
2.Programmable Automation
3.Flexible Automation
Fixed automation
Designed to produce particular product , Volume of production is high, product variety is low,suitable for mass production.e.g, oil refineries,chemical processing
Programmable automation
Sequence of operations are controlled by program of instruction,product volume is low,suitable for batch production,

## Slide 26
Flexible Automation :
Capable of producing large variety of parts , production rate is medium

## Slide 27: Automation Principles and strategies
U S A Principle :
U: understand the existing process
S: Simplify the process
A: Automatic the process

## Slide 28: Automation Strategies
1.Specialization of the process.
2.Combined operations
3.Simultaneous operations
4. Integration of operations
5.Increased flexibility
6.Improved material handling and storage
7.Online Inspection
8.Process control and optimization
9.Plant operations control
10.Computer integrated manufacturing

## Slide 29: Computer integrated Manufacturing
Functional areas of CIM system :
Part and product design
Tool and fixture design
Process planning
Programming of numerically controlled machines
Control of Material handling system
Material requirement planning
Machine loading and scheduling
Machining
Assembly
Maintenance
Quality control
Inspection
Storage and retrieval

## Slide 30: Computerized elements of CIM System

## Slide 31: Automated production lines and assembly system
The objectives of the use of flow line automation are:
To reduce labour costs;
To increase production rates;
To reduce work-in-process;
To minimize distances moved between operations;
To achieve specialization of operations;
To achieve integration of operations

## Slide 32: Automated production lines
Type 1. Single station
Work flow IN OUT
Type 2. Multiple station with variable Routing
Aut Aut
Work in Work out
Aut Aut
Automated
Work Station

## Slide 33
Type3.Multiple station with fixed Routing :
Work in Work out
Automated flow lines
Defn. Automated production line is a fixed rating manufacturing system
that consists of multiple work stations linked together by material handling system that transfer parts from one station to next station
machines capable of performing this production are called transfer lines or transfer machines.

## Slide 34: Automated flow lines
Raw material Finished Parts
station 1 station 2 station 3 station 4
1.Automated flow lines consist of multiple work station with work handling system
2.Work station can be manual or Automated
3.Unprocessed part enters the starting point of production, get processed
and leaves the production line at end
4.Parts are transferred between the station using mechanized transport system
5.Consists of manual work stations and inspection station to perform online inspection
PROC
AUTO
PROC
AUTO
PROC
AUTO
PROC
AUTO

## Slide 35
6. Each station perform different operations
7 No. of parts on the line equal to number of work stations
8.Automated production lines may accommodates buffer storages
9. Some of flow lines use pallet fixtures

## Slide 36: Symbols and notations used in automated flow lines

## Slide 37: Types of flow line configurations
Types of Automated flow lines
Linear or In-line configuration
Segmented In-line configuration
L-Type configuration
U-Type configuration
Rectangular configuration
c) Rotary configuration

## Slide 38: Linear or In-line configuration
Raw material Finished Parts
PROC PROC PROC PROC
AUTO AUTO AUTO AUTO
station 1 station 2 station 3 station 4

## Slide 39: L- Type Configuration

## Slide 40: U-Type Configuration

## Slide 41: Rectangular Type Configuration

## Slide 42: Rotary Configuration

## Slide 43: Work part transport Methods
Main objective of work part transport is to move the part between the station in production line
It should orient and locate the parts in the correct position for processing at each station
(a)Manual method of work transport
(b)Mechanized work transport
There are three types of work transport system.
1.Continuous Transport system
2.Synchronous Transport system
3.Asynchronous Transport system

## Slide 44: Continuous transport system
Sailent features :
Conveyors are are used to transfer parts at constant velocity
The work parts will moving continously
This method is common in case of Manual production lines
This type of transport system cannot be adopted for automated production lines.
This system requires minimum investment
Easy to design
Cannot handle large parts
Has very high production rates
System can be implimented in two ways
(a)Work units are fixed to conveyor:- e.g., Packaging operations,two wheel assembly
(b)Work units are removable :- e.g., Spray painting,four wheel assembly

## Slide 45: 2.Synchronous transport systems or Intermittent transport system
Salient feature:
Parts move simultaneously between the stations with quick discontinuous motion
Parts will move on the conveyors till it reaches the work stations
This system is continuously used in Automated Production lines
Such a system requires the processing operations to be completed in certain time limits
e.g., Press work-in operation , Machining operations

## Slide 46: Asynchronous transport system
Salient features :
Part will move to the work station only when the work stations are free
Each part will move independent of other parts. e.g.,Cart-on-tracks, AGV etc.,
Such a system can accommodate storage buffers.
Initial investment is high
These system can handle large parts and can change the sequence of operations
Production rates are very less in such system@1045

## Slide 47: Factors to be considered to select work transport system
Type of operation to be performed
No. of station on the line
Factory floor space available
Size ,weight , geometry & Material of the work part
Production rate
Buffer storage capacity
Number of components
Sequence of operations

## Slide 48: Work beam transfer mechanism
Operation of the walking beam transfer mechanism

## Slide 49: Buffer Storage
Defn. A storage can be used as buffer storage between two process whose production rates are significantly different , where parts can be collected and temporarily stored before proceeding to subsequent work stations
Automated flow lines either manually operated or automated
Automated versions consists of mechanism for capturing and releasing parts to the
Production line and structure buffer storage for holding the parts

## Slide 50
Advantages of buffer storage :
1.When a particular work station breakdown in a transferline,the entire production
get disturbed.
2.When particular workstation completes processing operation,the storage buffer
supplies workpart,reducing idle time.
3.Storage buffers can provide suffecient time for curing that may be required for
some operation (paint to dry,adhesive to bond)
4.Delay time can be minimized that reduces manufacturing lead time
Control Functions
1.Sequence control
2.Safety monitoring
3.Quality control

## Slide 51
Sequence control :
Purpose of sequence control is to co-ordinate the sequence of activities
Ensures the various activities on the transfer lines must be performed with accuracy and proper time distribution for each activity
Basic function required in an automated transfer line
Safety monitoring :
Production line does not operate under unsafe conditions
Protect human workers and to protect equipment
Various sensors are incorporated in the system to ensure safety operation
Various sensors used are- Interlocks ,Limit switches , photoelectric sensors, Temperature sensors, smoke detectors, pressure sensitive floor pads, Machine vision systems

## Slide 52: Quality Control
Quality control is used to monitor quality of work parts
Detect and Eliminate defective work pieces from production line
To accomplish this function ,inspection devices are placed at the work station
once defect is encountered during quality control, controlling actions- Instantenous control, memory control
Instantaneous control :
Once defect is encountered on the production line,stop production line immediately
Most reliable and easy to implement
Production time will be lost, to reduce loss , repair must be made minimum possible time
Memory control :
Doesn't stop the operation of the production
Defective part is found, it prevent subsequent operation
Parts reaches the last station defective part must be seperated from the rest of goods

## Slide 53: Introduction
A flow line is multi-station manufacturing system with fixed routing,
Production line consists of series of workstation so that product moves from one station to next
Conditions favour the use of production line are :
The quantity of products to be made is very high
The work units are identical or similar
Similar operations on all the work units and in the same sequence
Total work can be divided into separate task
Production lines are either processing or assembly
Production lines are either manually operated or automated
Manual production lines usually perform assembly operation
Automated production lines either perform processing or assembly operation

## Slide 54: Analysis of automated flow lines without internal storage
1.Process Technology:
Deals with concept like metallurgy and machinability of work parts
Proper application of cutting tools, chip control ,machining economics,machine tool vibrations
2.System Technology :
Design of flow lines and overall flow line operation
System technology also refers to the manufacturing process
Problems relate to design of flow line is called “Reliability problems”
It refers that failure of any one component in flow line stop entire system
Proper design of automated flow lines
Line balancing problems
Line balancing refers to total machining work must be accomplished on automated flow line

## Slide 55
Thank you