## Slide 1
Total
Quality
Management
18ME734
Tools and Techniques
Prof. Niranjan Kumar V S Assistant Professor,
Dept. of Mechanical Engineering,
ATMECE, Mysuru

## Slide 2
Module 5
Total Productive Maintenance (TPM):
Definition, Types of Maintenance, Steps in introduction of TPM in an organization, Pillars of TPM – 5S, Jishu Hozen, Quality Maintenance, Planned Maintenance.
Quality by Design (QbD):
Definition, Key components of QbD, Role of QbD in Pharmaceutical Industry, Benefits and Challenges of QbD.
Environmental Management Systems (EMS):
Definition, Basic EMS, EMS under ISO 14001, Costs and Benefits of EMS

## Slide 3
Total Productive Maintenance (TPM)
Definition
TPM (Total Productive Maintenance) is a maintenance philosophy designed to integrate equipment maintenance into the manufacturing process. The goal of any TPM program is to eliminate losses tied to equipment maintenance or, in other words, keep equipment producing only good product, as fast as possible with no unplanned downtime.
Total - All encompassing by maintenance and production individuals working together.
Productive - Production of goods and services that meet or exceed customers expectations
Maintenance - Keeping equipment and plant in as good as or better than the original condition at all times.

## Slide 4
Objectives of TPM

## Slide 5
Types of Maintenance

## Slide 6
Types
Of
Maintenance
01
02
03
04
05
Preventive
Maintenance
Predective
Maintenance
Predetermined
Maintenance
Condition based
Maintenance
Corrective
Maintenance

## Slide 7
Preventive maintenance is defined as taking precautionary steps or actions to prevent equipment failures before they actually occur.
Preventive maintenance typically involves routine inspections, upgrades, proper lubrication (where applicable), adjustments, and replacement of outdated equipment or parts.
Preventive maintenance can be implemented in many areas of your business, and includes any preventive action, such as changing water filters, regularly cleaning essential equipment, inspecting business vehicles (i.e. delivery vans), and checking grout and caulking to protect a property against water damage.
1. Preventive Maintenance

## Slide 8
Minimized downtime and business closures due to unexpected equipment failures – This will help you avoid financial loss, and protect your bottom line.
Increased life expectancy of essential equipment and assets – Inspecting, updating, and caring for your business’s assets will result in less money spent on new equipment in the long run.
Decreased energy consumption for your business’s assets – When equipment runs optimally, less energy is required, which means lower utility bills for your business.
Benefits of Preventive Maintenance

## Slide 9
Relevant Industries For Preventive Maintenance
Preventive maintenance is pretty universal, and should be considered in any industry, including but not limited to manufacturing, food production, oil & gas, restaurants, gyms, retail, education, and healthcare.
Preventive Maintenance
Case Study (example) for Preventive Maintenance
An unexpected refrigerator breakdown can leave a restaurant reeling, resulting in considerable food loss, closing for the rest of the day (or the time it takes to schedule and make repairs), and high repair costs. Performing regular inspections and cleaning of the condenser coils will help prevent such a costly incident from occurring, and will mean less risk to your business in the long run.and checking grout and caulking to protect a property against water damage.

## Slide 10
Predictive maintenance tracks the normal operation of an appliance or machine to detect possible defects before they pose a problem. This type of maintenance uses condition-monitoring technology to measure the performance of equipment, typically by way of IoT (the Internet of Things).
IoT is more or less a system that connects electronic devices to mechanical and digital machines, and is equipped with the ability to detect and transfer data without requiring human interaction or interference.
Predictive maintenance will alert to possible machine deficiencies without any prompting till end
2. Predictive Maintenance

## Slide 11
Predictive maintenance is so valuable is because it allows for maintenance to be performed only when absolutely necessary—that is, just before equipment failure is likely to occur.
Predictive maintenance will enable to save money until the very last minute, when maintenance or repairs are actually required but before any real system damage occurs.
Fewer production hours lost as a result of equipment failure.
Predictive maintenance is shown to contribute to a phenomenal tenfold increase in return on investment, as well as a 70-75% decrease in equipment crashes and a 35%-45% reduction in downtime
Benefits of Predictive Maintenance

## Slide 12
Relevant Industries For Predictive Maintenance
The industries that rely on predictive maintenance usually have equipment that are critical to their operations and have failure modes that can be predicted with regularly monitoring. Industries that can fit this criteria includes food production, oil and gas, manufacturing, power and energy plants, IT, etc.
Predictive Maintenance
Case Study (example) for Predictive Maintenance
A food production plant may rely on predictive maintenance for their valuable industrial ovens, which may be running 24/7 to stay competitive. A sensor would be installed to the oven that would evaluate and produce data regarding temperature and vibration that would alert staff to make adjustments or tweaks to poor performing machines in real-time, reducing the need to shut down production completely.

## Slide 13
Planned maintenance covers any maintenance that is planned, scheduled, and documented. It is specifically defined as, preventive maintenance that is carried out according to a set plan.
Preventive maintenance is one type of planned maintenance, and will account for and prevent machine breakdowns before they occur.
There is also planned, unscheduled maintenance, which is the process of correcting or fixing a system that has already broken, and anticipating such business hindrances ahead of time.
3. Predetermined/ Planned Maintenance

## Slide 14
Preparedness in the event of equipment failure, or preventing such failure altogether
Planned maintenance is often as simple as a regular, planned inspection, seasonal maintenance, etc
Significant cost savings in the long run – The cost of regular, routine maintenance often costs less in the long run than dealing with a major problem after it has occurred.
Benefits of Planned Maintenance

## Slide 15
Relevant Industries For Planned Maintenance
Planned maintenance is universal for all industries, and should be considered in manufacturing, restaurant (food & beverage), hospitality, gym and wellness centers, retail, and schools.
Planned Maintenance
Case Study (example) for Planned Maintenance
It’s generally recommended that a restaurant checks and empties its grease traps every 1-3 months, depending on the size and volume of business. Doing so prevents sewer lines from becoming clogged with waste.

## Slide 16
Condition-based maintenance refers to the process of taking quick action on a machine that is in the early stages of equipment failure.
Many machines produce some sort of alert that the system is beginning to malfunction before total breakdown occurs.
Condition-based maintenance allows for a last-minute response to a system or machine crashing.
4. Condition-Based Maintenance

## Slide 17
Reduced number of total machine breakdowns – Condition-based maintenance may help to avoid a total machine failure
Successful condition-based maintenance means that, It is managed to prevent equipment from totally failing, enabling it to function until it can be troubleshooted more thoroughly.
Advance warning of breakdown – A warning that a machine or system needs attention is preferable to losing its functionality all at once. If such notifications are standard for the machine, Enough time will be there to call a mechanic, rather than attempting to fix equipment by self.
Benefits of Condition-Based Maintenance

## Slide 18
Relevant Industries For Condition-Based Maintenance
Industries that typically have high cost equipment and are critical to operations. Most typically common in manufacturing, oil & gas, power and energy plants, and food production with heavy machinery.
Condition-Based Maintenance
Case Study (example) for Condition-Based Maintenance
A sensor that measures vibrations of a rotating equipment can warn you when the moving piece starts to fall out of alignment and increase in vibration. This will cause the sensor to alert you when the vibration is out of the interval you set.

## Slide 19
Corrective maintenance is best described as any action that targets and fixes a system malfunction so that the equipment can be restored to proper working order.
Additionally, the defect may be caught or noticed before it causes a significant problem, or total equipment breakdown.
It improves equipment and its components so that preventive maintenance can be carried out reliably. Equipment with design weakness must be redesigned to improve reliability or improving maintainability
5. Corrective Maintenance

## Slide 20
Reduced duration of planned and unplanned downtime
Reduced cost and time of running a reactive maintenance strategy
Reduced cost of maintenance operations/reduced emergency maintenance orders
Benefits of Corrective Maintenance

## Slide 21
Relevant Industries For Corrective Maintenance
Any industry may use corrective maintenance, including restaurants, gyms, retail stores, schools, and corporate offices.
Corrective Maintenance
Case Study (example) for Corrective Maintenance
If frost or ice builds up in a walk-in freezer, this can escalate into a costly consequence for a restaurant. Ice accumulation can interfere with optimal refrigeration, causing compressors to use more energy and run less efficiently. If ice has already built up in a commercial freezer, it should be thawed either by turning the system off temporarily, or by using a tool such as a hair dryer to expedite the process.

## Slide 22
Step A - PREPARATORY STAGE
STEP 1 - Announcement by Management to all about TPM introduction in the organization :
Proper understanding, commitment and active involvement of the top management in needed for this step. Senior management should have awareness programmes, after which announcement is made to all. Publish it in the house magazine and put it in the notice board. Send a letter to all concerned individuals if required.
STEP 2 - Initial education and propaganda for TPM :
Training is to be done based on the need. Some need intensive training and some just an awareness. Take people who matters to places where TPM already successfully implemented.
:
Steps in introduction of TPM in a organization

## Slide 23
STEP 3 - Setting up TPM and departmental committees :
TPM includes improvement, autonomous maintenance, quality maintenance etc., as part of it. When committees are set up it should take care of all those needs.
STEP 4 - Establishing the TPM working system and target :
Now each area is benchmarked and fix up a target for achievement.
STEP 5 - A master plan for institutionalizing :
Next step is implementation leading to institutionalizing wherein TPM becomes an organizational culture. Achieving PM award is the proof of reaching a satisfactory level.
Steps in introduction of TPM in a organization

## Slide 24
STEP B - INTRODUCTION STAGE
Suppliers as they should know that we want quality supply from them. Related companies and affiliated companies who can be our customers, etc. Some may learn from us and some can help us and customers will get the communication from us that we care for quality output.
STAGE C – IMPLEMENTATION
In this stage eight activities are carried which are called eight pillars in the development of TPM activity. Of these four activities are for establishing the system for production efficiency, one for initial control system of new products and equipment, one for improving the efficiency of administration and are for control of safety, sanitation as working environment.
STAGE D - INSTITUTIONALISING STAGE :-By all there activities one would has reached maturity stage. Now is the time for applying for PM award. Also think of challenging level to which you can take this movement.
Steps in introduction of TPM in a organization

## Slide 25
Pillars of TPM

## Slide 26
5 S {The foundation of TPM}

## Slide 27
SEIRI - Sort out
This means sorting and organizing the items as critical, important, frequently used items, useless, or items that are not need as of now. Unwanted items can be salvaged. Critical items should be kept for use nearby and items that are not be used in near future, should be stored in some place. For this step, the worth of the item should be decided based on utility and not cost. As a result of this step, the search time is reduced
SEITON – Organise
The concept here is that "Each items has a place, and only one place". The items should be placed back after usage at the same place. To identify items easily, name plates and colored tags has to be used. Vertical racks can be used for this purpose, and heavy items occupy the bottom position in the racks.
5 S {The foundation of TPM}

## Slide 28
SEISO - Shine the workplace
This involves cleaning the work place free of burrs, grease, oil, waste, scrap etc. No loosely hanging wires or oil leakage from machines.
SEIKETSU – Standardization
Employees has to discuss together and decide on standards for keeping the work place / Machines / pathways neat and clean. This standards are implemented for whole organization and are tested / Inspected randomly.
SHITSUKE - Self discipline
Considering 5S as a way of life and bring about self-discipline among the employees of the organization. This includes wearing badges, following work procedures, punctuality, dedication to the organization etc.
5 S {The foundation of TPM}

## Slide 29
It is geared towards developing operators to be able to take care of small maintenance tasks, thus freeing up the skilled maintenance people to spend time on more value added activity and technical repairs.
JISHU HOZEN ( Autonomous maintenance )
Policy :
Uninterrupted operation of equipments.
Flexible operators to operate and maintain other equipments.
Eliminating the defects at source through active employee participation.
Stepwise implementation of JH activities.
Target :
Reduce oil consumption by 50%
Reduce process time by 50%
Increase use of JH by 50%

## Slide 30
Preparation of employees.
Initial cleanup of machines.
Take counter measures
Fix tentative JH standards
General inspection
Autonomous inspection
Standardization and
Autonomous management.
Steps in JISHU HOZEN

## Slide 31
It is aimed to have trouble free machines and equipment's producing defect free products for total customer satisfaction. This breaks maintenance down into groups
PLANNED MAINTENANCE
Policy :
Achieve and sustain availability of machines
Optimum maintenance cost.
Reduces spares inventory.
Improve reliability and maintainability of machines
Target :
Zero equipment failure and break down.
Improve reliability and maintainability by 50 %
Reduce maintenance cost by 20 %
Ensure availability of spares all the time.

## Slide 32
Six steps in Planned maintenance :
Equipment evaluation and recoding present status.
Restore deterioration and improve weakness.
Building up information management system.
Prepare time based information system, select equipment, parts and members and map out plan.
Prepare predictive maintenance system by introducing equipment diagnostic techniques and
Evaluation of planned maintenance.
PLANNED MAINTENANCE

## Slide 33
It is aimed towards customer delight through highest quality through defect free manufacturing.
Focus is on eliminating non-conformances in a systematic manner, much like Focused Improvement.
QM activities is to set equipment conditions that preclude quality defects, based on the basic concept of maintaining perfect equipment to maintain perfect quality of products.
The condition are checked and measured in time series to very that measure values are within standard values to prevent defects.
The transition of measured values is watched to predict possibilities of defects occurring and to take counter measures before hand.
QUALITY MAINTENANCE

## Slide 34
QUALITY MAINTENANCE
Policy :
Defect free conditions and control of equipments.
QM activities to support quality assurance.
Focus of prevention of defects at source
Focus on poka-yoke. ( fool proof system )
In-line detection and segregation of defects.
Effective implementation of operator quality assurance.
Target :
Achieve and sustain customer complaints at zero
Reduce in-process defects by 50 %
Reduce cost of quality by 50 %.

## Slide 35: Quality by Design

## Slide 36: Quality by Design

## Slide 37: Quality by Design

## Slide 38: Quality by Design

## Slide 39: Quality by Design

## Slide 41
What is an Environmental Management System (EMS)?
“The part of the overall management system that includes organizational structure, planning activities, responsibilities, practices, procedures, processes and resources for developing, implementing achieving and reviewing the environmental policy.” ISO14001

## Slide 42
An EMS therefore generally follows the adoption of an environmental policy. The environmental policy formally outlines a company commitments to environmental management and commonly includes commitments to reduce waste, pollution, energy and resource use, sets objectives and targets and reviews the company environmental performance.
Once the policy and EMS are in place a company will consider the publication of an environmental report to document the company progress against its policy and performance targets set within the EMS.
Companies may adopt a certified EMS, such as ISO 14001 or Eco-management and audit scheme (EMAS), or they may develop their own in-house systems.
The certified schemes, ISO 14001 is the most commonly adopted because of its international status and the success of its predecessor, the quality standard ISO 9000. ISO 14001 was written as a consensus standard with nearly 50 countries participating. It can be applied to an entire organization
DEFINITION

## Slide 43
"Total Quality Management* (TQM) and the concept of continual improvement based on Dr.Charles
Deming's "Plan-Do-Check-Act"(PDCA) cycle of continual improvement have been used as management tools for managing environmental performance

## Slide 44
Basic Implementation(process) of EMS

## Slide 45
Environment Policy -This section of the standard stipulates that the top management of the organization shall define the environmental policy such that :
1. It is appropriate to the nature, scale and environmental impacts of its activities, products and services;
2. It includes a commitment to continual improvement and prevention of pollution;
3. it includes a commitment to comply with relevant environmental legislation and regulations, and with other requirements to which the organization subscribes;
4. Provides the framework for setting and reviewing environmental objectives and targets;
5. It is documented, implemented and maintained and communicated to all employees;
6. It is available to the public

## Slide 46
Environmental aspects
Legal and other requirements
Objectives and targets
Environmental management programme
Planning

## Slide 47
Implementation and operation
Structure and responsibility
Training, awareness and competence
Communication
Environmental management system documentation
Checking and corrective action
Monitoring and measurement
Environmental management system audit
Non conformance and corrective and preventive action
Records

## Slide 48
Management Review
This requirement of the standard stipulates that the organization's top management shall, periodically review.
The environment management system to ensure its continuing suitability, adequacy and effectiveness. This review shall be based on necessary information md shall be documented.
Management review shall consider changes to 'environmental policy, objectives and targets and other elements of the EMS in the light of audit results, changing circumstances and commitment to continual improvement.
Annexure A of ISO-14001 provides guidance on the use of the specification
Annexure B provides the links between IS0 14001 and IS0 9001

## Slide 50
https://www.iso.org/iso-14001-environmental-management.html

## Slide 51
Benefits of Implementing EMS

## Slide 52
Costs and Benefits of an EMS
Internal
Staff/manager time (represents the bulk of EMS resources expended by most organizations)
Other employee time
External
Potential consulting assistance
Outside training of personnel
Potential Benefits
Improved environmental performance
Enhanced compliance
Pollution prevention
Resource conservation
New customers/markets
Increased efficiency/reduced costs
Enhanced employee morale
Enhanced image with public, regulators, lenders, investors
Employee awareness of environmental issues and responsibilities