## Slide 1
Material Science and Engg
BME303
Module-2
Physical Metallurgy
Prof. Devaraj M R
Associate professor,
Dept. of Mechanical Engineering,
ATMECE, Mysuru

## Slide 2
A phase diagram is essentially a graphical representation of an alloy system.
Phase diagrams are also called as equilibrium diagrams or constructional diagrams.
Phase diagrams are classified as:
          Unary Phase diagram
          Binary Phase diagram
          Ternary Phase diagram
  Unary Phase diagram is nothing but the Pressure-Temperature diagram of a pure metal.
Phase diagrams

## Slide 3
The Nature and occurrences of these phases in turn is a function of different independent variables such as temperature, pressure and composition.
So in order to predict the properties of materials,
it is important to know the following:
The conditions under which different phases exist.
The conditions under which a change of phase will occur.
Therefore phase diagrams are constructed to provide the following information.

## Slide 4
Therefore phase diagrams are constructed to provide the following information.
The different phases existing in the alloy for any combination of temperature and composition.
(Pressure is assumed to be constant at atmospheric value.)
Temperature at which different compositions begin and end solidification.
To study and control process such as solidification and heat treatment of metals and alloys.
A phase diagram is essentially a graphical representation of an alloy system.
Phase diagrams are also called as equilibrium diagrams or constructional diagrams.

## Slide 5: Classification of Binary Phase Diagrams All binary phase diagrams can be classified according to the appearance of the following reactions or Transformations in them. These include:
Solid solution or Isomorphous phase diagram
Eutectic system(Eutectic type phase diagram)
Eutectoid transformation
Peritectic reaction
Peritectoid transformation

## Slide 6: Solid solution or Isomorphous phase diagram
Solid solution is a combination of two metals which are completely soluble in both the solid and liquid states. It is also known as Isomorphous system. [Iso-means Same & Morphous- means Structure

## Slide 7
Construction of Binary Solid solution Phase diagram using cooling curves.
General steps involved in the construction of a binary equilibrium Diagram between any two metals.
The example taken is the Ni-Cu system which forms a continuous Solid solution.
Cooling curves of pure nickel and pure copper are drawn on two parallel vertical axis which represent temperatures.
A series of cooling curves of different compositions of Nickel and copper are drawn at appropriate places between the cooling curves of the two pure metals.
The cooling curves of all the alloys are that of a solid solution, that is, there is liquid-liquid, liquid-solid and solid-solid transformations which make up each cooling curve.

## Slide 8
Now, a curve is drawn which joins the beginning of solidification points of all the cooling curves of the alloy.
A curve is also drawn which joins the end of solidifications of all the cooling curves.
In the cooling curves of pure metals Ni and Cu the mid points are chosen for both beginning and ending of solidification to join to the two curves since they are at constant temperatures.
Therefore an equilibrium diagram is obtained which is normally shown without the series of cooling curves which helped its construction.

## Slide 9: Determination of phase(s) present
Rule 1: If we know T and Co, then we know:
--how many phases and which phases are present.
Examples:
A(1100, 60):
  phase: α(S)
B(1250, 35):
  phases: L + α (S)
wt% Ni
100 0
0 20 40 60 80 100
110 0
130 0
120 0
150 0
140 0
T(°C)
160 0
L (liquid)
α (FCC solid solution)
L + s
liquidus
solidus
A(1100,60)
B(1250,35)
Cu-Ni phase diagram
Melting points: Cu = 1085°C, Ni = 1453 °C
Solidus - Temperature where alloy is completely solid. Above this line, liquefaction begins. Liquidus - Temperature where alloy is completely liquid. Below this line, solidification begins.

## Slide 10: Phase Diagrams: composition of phases
Rule 2: If we know T and Co, then we know:
--the composition of each phase.
Examples:
20
1200
1300
T(°C)
L (liquid)
S
(solid)
L + S
liquidus
D
TD
TB
B
TA A tie line
L + S
solidus
4043 50
3032 35
CLCo
Cs wt% Ni
Cu-Ni system
At T
A
= 1320°C:
Only Liquid (L) present
CL = C0
( = 35 wt% Ni)
At TB
= 1250°C:
Both α (S) and L present
At TD
= 1190°C:
Only Solid (s) present Cs = C0 ( = 35 wt% Ni)
= Cliquidus ( = 32 wt% Ni)
CL
Cs
= Csolidus
( = 43 wt% Ni)

## Slide 11
Lever rule to find weight fraction or amount of Phases present:

## Slide 13
Solid Solution Phase diagram showing transformation upon cooling at a composition 40%Ni and 60%Cu

## Slide 14
Solid Solution Phase diagram showing cooling curve at a composition 40%Ni and 60%Cu:
Solidification takes place over a range of temperature (from 1280º C to 1240º C)

## Slide 15
Importance of Phase Diagrams
There is a strong correlation between microstructure and mechanical properties, and the development of alloy microstructure is related to the characteristics of its phase diagram.
• Phase diagrams provide valuable information about melting, casting, crystallization and other phenomena.
Microstructure
In metal alloys, microstructure is characterized by the number of phases, their proportions, and the way they are arranged.
The microstructure depends on: – Alloying elements – Concentration – Heat treatment (temperature, time, rate of cooling)

## Slide 16
Eutectic System
A eutectic or eutectic mixture is a mixture of two or more phases at a composition that has the lowest melting point.
It is where the phases simultaneously crystallize from molten solution.
The proper ratios of phases to obtain a eutectic is identified by the eutectic point on a binary phase diagram.
The term comes from the Greek 'eutektos', meaning 'easily melted’.
An eutectic system is the one where two components which are completely
Soluble in the liquid state are either:
      Completely insoluble in the solid state OR
      Partially soluble in the solid state.

## Slide 17
Example of the eutectic system where two components which are completely
Soluble in the liquid state and are : Completely insoluble in the solid state.

## Slide 20
Another Example of the eutectic system where two components which are completely
Soluble in the liquid state and are : Completely insoluble in the solid state.
Example: Cd-Bi alloy system

## Slide 21
A eutectic reaction is defined as the one which generates two solids from the liquid at a given temperature and composition, L → α + β
Three phases (L+α+β) coexist at point E. This point is called eutectic point or composition. Left of E is called hypoeutectic whereas right of E is called hypereutectic.
A eutectic composition solidifies as a eutectic mixture of αand β phases. The microstructure at room temperature (RT) may consist of alternate layers or lamellae of α andβ.
An Example of eutectic system where two components which are completely
Soluble in the liquid state and are: Partially soluble in the solid state.
Eutectic Phase diagram

## Slide 22
In hypoeutectic alloys the α phase solidifies first and the microstructure at RT consists of this α phase (called pro eutecticα) and the eutectic (α+β) mixture.
Similarly, hypereutectic alloys consist of pro- eutectic and the eutectic mixture. The melting point at the eutectic point is minimum. That’s why Pb-Sn eutectic alloys are used as solders. Other eutectic systems are Ag-Cu, Al-Si, Al-Cu.
An Example of eutectic system where two components which are completely
Soluble in the liquid state and are: Partially soluble in the solid state.
Eutectic Phase diagram

## Slide 23
An Example of eutectic system where two components which are completely
Soluble in the liquid state and are: Partially soluble in the solid state.

## Slide 24
The phase diagram displays a simple binary system composed of two components, A and B, which has a eutectic point.
The phase diagram plots relative concentrations of A and B along the X-axis, and temperature along the Y-axis. The eutectic point is the point where the liquid phase borders directly on the solid α + β phase; it represents the minimum melting temperature of any possible A B alloy.
The temperature that corresponds to this point is known as the eutectic temperature.
Eutectic Phase diagram

## Slide 25
Not all binary system alloys have a eutectic point: those that form a solid solution at all concentrations, such as the gold-silver system, have no eutectic. An alloy system that has a eutectic is often referred to as a eutectic system, or eutectic alloy.
Solid products of a eutectic transformation can often be identified by their lamellar structure, as opposed to the dendritic structures commonly seen in non-eutectic solidification.

## Slide 27: Example: Pb-Sn alloy system
Another Example of eutectic system where two components which are completely
Soluble in the liquid state and are: Partially soluble in the solid state.

## Slide 28: Liquid is transformed into solid upon cooling produces a Lamellar Eutectic Structure of Lead (Pb) and Tin (Sn) solid phases
A 2-phase microstructure resulting from the solidification of a liquid having the eutectic composition where the phases exist as a lamellae that alternate with one another.
Formation of eutectic layered microstructure in the Pb-Sn system during solidification at the eutectic composition. Compositions of α and β phases are very different. Solidification involves redistribution of Pb and Sn atoms by atomic diffusion.

## Slide 29
Pb-Sn Microstructures
The dark layers are Pb-rich α phase, the light layers are the Sn- rich β phase

## Slide 30
Eutectoid Transformation/ Reaction
Where one solid transformed into two solids

## Slide 32
Thank You