## Slide 1
Material Science and Engg.-BME303
Crystal Structure

## Slide 2
Structure of Materials
Introduction: Classification of materials, crystalline and non-crystalline solids, atomic bonding: Ionic Bonding and Metallic Bonding.
Crystal Structure: Crystal Lattice, Unit Cell, Planes and directions in a lattice, Planar Atomic Density, Coordination number, atomic Packing Factor of all the Cubic structures and Hexagonal Close Packed structure. Classification and Coordination of voids, Bragg’s Law.
Imperfections in Solids: Types of imperfections, Point defects: vacancies, interstitials, line defects, 2-D and 3D-defects, Concept of free volume in amorphous solids. Slip, Twinning.
Module-1

## Slide 3
Material Science is primarily concerned with the search for basic knowledge about processing of materials.
Materials engineering is mainly concerned with the use of fundamental and applied knowledge of materials so that the materials can be converted into products necessary or desired by the Society.

## Slide 4
There are several ways of classifying engineering materials. One way of classifying them is into five groups.
1.Metallic materials. Example: steels, Cast irons, Al, copper, silver gold, brass Bronzes etc.
2.Polymeric materials. Examples: Plastics, Polyethylene, PVC, Nylon etc.
3.Ceramic materials. Examples: MgO, ZnO, SiC, Silica, Nitrides, etc.
4.Composite materials. Examples: PMC, MMC and CMC etc.,
5.Electronic materials. Examples: Semiconductors

## Slide 5
Materials science restricts itself to solid materials, which help engineers to build machines, structures, automobiles, electronic gadgets and a wide variety of other products useful to mankind.
Solid materials may be broadly classified into two groups based on the regularity with which atoms or molecules are arranged with respect to one another.
Crystalline solids
Amorphous solids
These two types of solids are based on their structural units which make up their building blocks.

## Slide 6
Crystalline solids
The basic structural unit is a crystal and a number of crystals come together to form a crystalline solid. Each of these crystals contain a number of repetitive blocks called unit cells which are arranged neatly in an order.
Density of crystalline solids are generally high since unit cells can be packed in an orderly manner in a given unit space.
Their structure is stable and materials are stronger. They also have higher melting point and strength.
Examples: metals, alloys, some salts like NaCl, KCl, many oxides, ceramics etc.

## Slide 7
Amorphous Solids
In amorphous solids- the basic structural unit here is a molecule and chains of these molecules come together to form an amorphous solid. These chains of molecules are random within the solid and occur in no particular order.
They are irregular and lack of symmetry unlike crystalline solids. Density of amorphous solids is low and their structure is unstable.
Examples: Glass, polymers, elastomers (Rubber).
Although all materials can be classified as either crystalline or non-crystalline, there are certain materials which can occur as both.
Example: Silicate can occur as crystalline solid (quartz) or as a non-crystalline solid as (silicate glass).

## Slide 8
Unit Cell:
Unit cell is a smallest repeatable unit of a crystalline solid.
In other words, every unit cell in a crystalline solid consists of a group of atoms arranged in a definite order. The shape of the unit cell and the atomic arrangements within them can themselves be of different types.
Crystal Structure

## Slide 9
Fig.(a) This cell is known as unit cell (Fig. b) which when repeated in the three dimensions generates the crystal structure.

## Slide 10
Space lattice
A space lattice can be defined as a three-dimensional array of points, each of which has identical surroundings.
There are 14 possible types of space lattices are called “Bravias” space lattices they fall under 7 crystal systems.

## Slide 14
Example of the materials:
Cubic unit cell: Mn, Polonium (Po) Nacl.
Body Centred Cubic: Na, V, Cr, Mo, W, Fe, alfa-iron, delta-iron
FCC: Ni, Cu, Ag, Pb, Au, Pt (platinum)
Tetragonal: (a) ST (b) BCT
ST-Pa (protactinum) and for BCT—Martensite and tin (Sn)
Orthorhombic: (a) SO (b) ECO (c) BCO (d) FCO Examples: Ar (Arsenic) Bi (Bismuth) Sb (Antimony)
BCO-_example:Cementite
FCO- example: S (sulpher), Ga (Gallium)
Rhombohedral: Example:B (Boron), CaCO3, SiO2
Hexxagonal: Example: Mg, Ti, Zr, CO, Zn Be (Beryllium)
Monoclinic: (1) SM and (2) ECM Example: CaSO4, NaSO4
Triclinic: (1) ST Example: CuSO4

## Slide 15
Unit cells of the some of the common space lattices of crystalline solids are:
Simple cubic
Face centred cubic
Body centred cubic
Hexagonal close packed

## Slide 16
Coordination number is the number of nearest neighbour to a particular atom in the crystal.
The coordination number (CN) of a crystal structure is defined as the number of nearest and equidistant neighbouring atoms that the each atom has in a space lattice.
The coordination number (CN) of a few types of crystal structure are:
Simple cubic: 6
BCC: 8
FCC: 12 (4+4+4)
HCP: 12 (3+6+3)

## Slide 22
Atomic packing factor (APF) or packing efficiency indicates how closely atoms are packed in a unit cell and is given by the ratio of volume of atoms in the unit cell and volume of the unit cell

## Slide 23
Atomic Packing Factor: FCC lattice
In the FCC unit cell effective number of atoms = 8 corner atoms x (1/8) (each atom is shared by 8 unit cells) + 6 face centred atoms x1/2 (each shared by two unit cells) = 4.
Considering the atoms as hard spheres of radius R
The relation between R and the FCC cell side a as shown in the figure below is √2a = 4R

## Slide 24
For BCC crystals effective number of atoms per unit cell is 8 x 1/8 + 1 = 2 and the relation between R and a is
√3a = 4R

## Slide 25
Hexagonal lattice
In the Hexagonal unit cell, number of atoms = 12 corner atoms x 1/6 (shared by six unit cells) + Two face atoms x 1/2+ 3 interior = 6.
2R = a
Unit cell volume = (6 x ½ x a x h) x c = (3 x a x a sin600) x c = 3a2 c sin600

## Slide 26
Atomic Bonding:
It is useful to classify the bonds that hold atoms to one another in chemical compounds and crystals into three types.
There are three primary types of bonding:
Ionic bonding,
Covalent bonding and
Metallic bonding.
As the name implies, ionic bonding is due to the attractions between positively and negatively charged ions.

## Slide 27
Under these conditions they lose a few electrons forming cations, ions with a positive charge; the electron greedy atoms gain electrons to become anions, ions with a negative charge.
Oppositely charged ions attract one another forming ionic bonds. The optimum arrangement is one which surrounds each charged ion with several charged ions with the opposite charge.

## Slide 28
Ionic bonding: Definition: An ionic bond is formed when valence electrons are transferred from one atom to the other to complete the outer electron shell. Example: A typical ionically bonded material is NaCl (Salt):

## Slide 31
Covalent bonding :
When the different atoms are almost equal competitors for electrons, neither can take an extra away from the other, and so such atoms bond together by sharing electrons.
This kind of bonding is called covalent bonding. It holds two partners together in a very precise geometrical arrangement. The two bonded atoms can be thought of as an ellipsoid with nuclei at the two foci.

## Slide 32
A covalent bond is formed by equal sharing of electrons from both the participating atoms. The pair of electrons participating in this type of bonding is called shared pair or bonding pair.
The covalent bonds are also termed as molecular bonds. Sharing of bonding pairs will ensure that the atoms achieve stability in their outer shell.

## Slide 33
Elements having very high ionisation energies are incapable of transferring electrons and elements having very low electron affinity cannot take up electrons.
The atoms of such elements tend to share their electrons with the atoms of other elements or with other atoms of the same element in a way that both the atoms obtain octet configuration in their respective valence shell and thus achieve stability.
Such association through sharing of electron pairs among different or same kinds is known as Covalent Bond.

## Slide 35
Difference Between Covalent and Ionic Bonds
Covalent bonds and ionic bonds are types of atomic bonds. These bonds are different in their properties and structure. The covalent bonds include pairs of electrons by two atoms binding them in a fixed orientation. While a bond between two ions is called ionic bonds.

## Slide 36
Covalent vs Ionic Bonds
Covalent bonding occurs between two non-metallic atoms characterized by the sharing of electron pairs between the atoms and other covalent bonds with electronegativity difference is greater than 2.0 (<2.0).
In the case of covalent bond formation, polyatomic ions are formed. Whereas, the ionic bond is formed as a result of electrostatic attraction between the oppositely charged ions.

## Slide 37
Covalent bonds
The outer electron levels of atoms, which are close to each other, can interact. The interaction leads to a sharing of electrons between the atoms.
One pair of electrons shared => single covalent bond
Two pairs of electrons shared => double covalent bond and so on
The shared electrons are said to be delocalized i.e. they do not belong to any particular atom
Generally, between non-metallic atoms
Examples:
H2 , CO2 , C6H12O6 (Glucose) and other molecules

## Slide 39
Covalent Bonding can be Achieved in two Ways:
Sharing of electrons between atoms of the same kind E.g. Formation of H2, Cl2, O2, etc.
Sharing of electrons between atoms of different kind E.g. Formation of CH4, H2O, NH3, etc.

## Slide 40
Difference Between Ionic and Covalent Bond | 
Covalent Bonds | Ionic Bonds
A covalent bond is formed between two similar electronegative non-metals | This type of bond is formed between a metal and non-metal
Bonds formed from covalent bonding have a Definite shape | Ionic Bonds have No definite shape
Low Melting Point and Boiling Point | High Melting Point and Boiling Point
Low Polarity and more Flammable | High Polarity and less Flammable
Covalent Bonds are in Liquid or gaseous State at room temperature | At room temperature, Ionic Bonds have Solid-state.
Examples: Methane, Hydrochloric acid | Example: Sodium chloride, Sulfuric Acid

## Slide 41
Metallic bonds
A metal is defined as any element that tends to lose electrons from the outer shells of its atoms. The resulting positive ions are held together in a crystalline structure by the cloud of these free electrons in what is known as the metallic bond.
The metallic bond yields three physical characteristics typical of solid metals:
• Metals are good conductors of electricity,
• Metals are good conductors of heat, and
• Metals have a lustrous (shiny) appearance.

## Slide 42
Metallic bonds
Atoms come together, electrons from outer shell of atoms share space with neighboring atoms.
The electrons can move freely within the atom orbitals.
Sharing of ‘free’ electrons among a lattice of positively charged ions (An array of positive ions in a sea of electrons)
Electrostatic attractive forces between delocalized electrons and positively charged metal ions.
The chemical bonding that results from the attraction between metal cations and the surrounding sea of electrons, Valence electrons do not belong to any one atom.
Between metallic atoms
Examples: Ni, Fe and other metals

## Slide 44
The electron swarm is all those loose outer electrons. In technical terms, they've been delocalized because their 'parent' atoms can't hold onto them. So instead of hanging around the outskirts of one atom, the outer electrons are shared across the entire metal.
What are delocalised electrons
Delocalized electrons are spread across more than one atom. Usually electrons in materials are bound to one atom, and atoms are held together by the interactions of the charges on different atoms.
In some cases, electrons can be shared between atoms, and are then called delocalized. In the case of hydrocarbons, delocalization occurs in Benzene rings, where a hexagon of six carbon atoms has delocalised electrons spread over the whole ring.
In metals, electrons are delocalized over the whole crystal structure, and carry currents - the outer electrons of the metal atoms are shared in an electron sea, and are not confined to particular atoms.

## Slide 45
In metallic bonding, each atom in the metal contributes its valence electrons to the formation of an electron cloud that surrounds the positively charged metal ions, as illustrated in the diagram. Hence, the valence electrons are shared by all of the atoms.
The positively charged ions repel each other uniformly, so they arrange themselves into a regular pattern that is held together by the negatively charged electron cloud.
Since the negative electron cloud surrounds each of the positive ions that make up the orderly three dimensional crystal structure, strong electronic attraction holds the metal together.

## Slide 46
Geometrical Crystallography
Crystal Symmetry

## Slide 47
Geometrical Crystallography
Crystal Symmetry
The concept of symmetry describes the repetition of structural features. Crystals therefore possess symmetry, and much of the discipline of crystallography is concerned with describing and cataloging different types of symmetry.

## Slide 48
Two general types of symmetry exist:
Internal or Translational symmetry : describes the periodic repetition of a structural feature across a length or through an area or volume.
External or Point symmetry : describes the periodic repetition of a structural feature around a point. Reflection, rotation, and inversion are all point symmetries.
Symmetries are most frequently used to classify the different crystal structures.

## Slide 49
CRYSTAL SYMMETRY
Imagine a small 2 dimensional crystal composed of atoms in an ordered internal arrangement as shown below. Although all of the atoms in this lattice are the same, one of them is coloured red so we can keep track of its position.

## Slide 50
If we rotate the simple crystals by 90o notice that the lattice and crystal look exactly the same as what we started with. Rotate it another 90o and again its the same.
Another 90o rotation again results in an identical crystal, and another 90o rotation returns the crystal to its original orientation.
Thus, in 1 rotation of 360o , the crystal has repeated itself, or looks identical 4 times. We thus say that this object has 4-fold rotational symmetry.

## Slide 51
Symmetry Operations and Elements
External or Point symmetry :
A Symmetry operation is an operation that can be performed either physically or imaginatively and results in no change in the appearance of an object.
External or Point symmetry is describes the periodic repetition of a structural feature around a point. Reflection, rotation, and inversion are all point symmetries. Symmetries are most frequently used to classify the different crystal structures.
Note: It is emphasized that in crystals, the symmetry is internal due to an ordered geometrical arrangement of atoms and molecules in the crystal lattice. Since the internal symmetry is reflected in the external form of perfect crystals, we are going to concentrate on external symmetry, using wooden models of crystals.
There are 3 types of symmetry operations:
Rotation, Reflection, and inversion.

## Slide 52
Symmetry Operations and Elements:
A Symmetry operation is an operation that can be performed either physically or imaginatively that results in no change in the appearance of an object.
Again it is emphasized that in crystals, the symmetry is internal, that is it is an ordered geometrical arrangement of atoms and molecules on the crystal lattice.
But, since the internal symmetry is reflected in the external form of perfect crystals, we are going to concentrate on external symmetry, since this can be observed.
There are 3 types of symmetry operations: Rotation, Reflection, and inversion. We will look at each of these in turn.

## Slide 53
Rotational Symmetry
As illustrated above, if an object can be rotated about an axis and repeats itself every 90o of rotation then it is said to have an axis of 4-fold rotational symmetry.
The axis along which the rotation is performed is an element of symmetry referred to as a rotation axis. The following types of rotational symmetry axes are possible in crystals.
1-Fold Rotation Axis
2-fold Rotation Axis-
3-Fold Rotation Axis
4-Fold Rotation Axis
6-Fold Rotation Axis

## Slide 54
Rotational Symmetry
The imaginary axis along which the rotation is performed is an element of symmetry referred to as a rotation axis. Rotational symmetry axes possible in crystals are 1,2,3,4,6.
1-Fold Rotation Axis - An object that requires rotation of a full 360o in order to restore it to its original appearance has no rotational symmetry. Since it repeats itself 1 time every 360o it is said to have a 1-fold axis of rotational symmetry.

## Slide 55
2-fold Rotation Axis- imagine rotation axis perpendicular to the page If an object appears identical after a rotation of 180o , that is twice in a 360o rotation, then it is said to have a 2-fold rotation axis (360/180 = 2).
Note: A filled oval shape represents the point where the 2-fold rotation axis intersects the page.

## Slide 56
2-fold Rotation Axis - If an object appears identical after a rotation of 180o, that is twice in a 360o rotation, then it is said to have a 2- fold rotation axis (360/180 = 2).
Note that in these examples the axes we are referring to are imaginary lines that extend toward you perpendicular to the page or blackboard. A filled oval shape represents the point where the 2-fold rotation axis intersects the page. This symbolism will be used for a 2-fold rotation axis.

## Slide 57
3-Fold Rotation Axis – An object that repeats itself after a rotation of 120o is said to have a 3-fold axis of rotational symmetry, thus repeating itself 3 times in a 360o rotation (360/120 =3).
Note: A filled triangle is used to symbolize the location of 3-fold rotation axis.

## Slide 58
4-Fold Rotation Axis - If an object repeats itself after 90o of rotation, it will repeat 4 times in a 360o rotation, as illustrated. Note: A filled square is used to symbolize the location of 4-fold axis of rotational symmetry.
Note: A filled square is used to symbolize the location of 4-fold axis of rotational symmetry.

## Slide 59
6-Fold Rotation Axis - If rotation of 60o about an axis causes the object to repeat itself, then it has 6-fold axis of rotational symmetry (360/60=6). Note: A filled hexagon is used as the symbol for a 6-fold rotation axis.
Note: A filled hexagon is used as the symbol for a 6-fold rotation axis.

## Slide 62
Although objects themselves may appear to have 5-fold, 7-fold, 8-fold, or higher-fold rotation axes, these are not possible in crystals. The reason is that the external shape of a crystal is based on a geometric arrangement of atoms.
Note that if we try to combine objects with 5-fold and 8-fold apparent symmetry, that we cannot combine them in such a way that they completely fill space, as illustrated below

## Slide 64
Mirror Symmetry
A mirror symmetry operation is an imaginary operation that can be performed to reproduce an object. The operation is done by imagining that you cut the object in half, then place a mirror next to one of the halves of the object along the cut. If the reflection in the mirror reproduces the other half of the object, then the object is said to have mirror symmetry.
The plane of the mirror is an element of symmetry referred to as a mirror plane, and is symbolized with the letter m. As an example, the human body is an object that approximates mirror symmetry, with the mirror plane cutting through the center of the head, the center of nose and split throughout.

## Slide 65
The rectangles shown below have two planes of mirror symmetry. The rectangle on the left has a mirror plane that runs vertically on the page and is perpendicular to the page. The rectangle on the right has a mirror plane that runs horizontally and is perpendicular to the page. The dashed parts of the rectangles below show the part the rectangles that would be seen as a reflection in the mirror.

## Slide 66
The rectangles shown above have two planes of mirror symmetry. Three dimensional and more complex objects could have more. For example, the hexagon shown above, not only has a 6-fold rotation axis, but has 6 mirror planes.

## Slide 67
Note that a rectangle does not have mirror symmetry along the diagonal lines. If we cut the rectangle along a diagonal such as that labeled "m ???", as shown in the upper diagram, reflected the lower half in the mirror, then we would see what is shown by the dashed lines in lower diagram. Since this does not reproduce the original rectangle, the line "m???" does not represent a mirror plane.

## Slide 68
Thank you