## Slide 1: Waste Collection

## Slide 2: Lesson Objectives
Understand problems and concerns associated with MSW collection.
Compare and contrast privately and publicly operated systems.
Understand the types of collection systems
Identify the benefits associated with the use of transfer stations
Prepare an economic analysis of transfer stations
Understand the design issues associated with transfer stations

## Slide 3
Collection accounts for
70% of a SW budget!

## Slide 4: Types of Waste Collection Systems
Refuse Collection Systems (residential)
Commercial Waste Collection
Recyclable Material Collection
179,000 trucks in the US (most diesel powered)

## Slide 5: Refuse Collection (Residential)
Stationary container emptied into truck
  Manually
    High injury rates (heavy containers, broken glass/sharp objects)
    Temporary containers that fall apart
  Automatic

## Slide 6: Rear Loading Compactor

## Slide 7: Side Loader

## Slide 8: Automatic Collection
Usually only one driver required
Works best
  without on-street parking, low hanging wires, narrow streets
  Where commitment to preventative maintenance
  Where commitment to educating public
  60-90 gal containers

## Slide 9: Automated Collection
Notes: <number>
32, 64, 96 gal cars

## Slide 10: Residential Collection Unit (RCU) Data
Source: O’Brien, J. K. “The Benchmarking of Residential Solid Waste Collection Services, MSW Management, Sept/Oct 2007, pp 12 – 24.
Collection Method* | RCUs/Crew/On-Route Hour
Automated | 139
Semi-Automated | 119
Manual | 136
All Methods | 134
*Once-per-week curbside waste collection

## Slide 11: Maintenance Costs
Collection Method | Annual Maintenance Cost, $
Automated | 35,000
Semi-automated | 15,000
Manual | 8,000
Source: O’Brien, J. K. “The Benchmarking of Residential Solid Waste Collection Services, MSW Management, Sept/Oct 2007, pp 12 – 24.

## Slide 12: Commercial Waste Collection
Mechanically front loaded
Hoist trucks
Trash Trailers

## Slide 13: Front Loading Compactor

## Slide 15: Collection with Recycling
Collection of mixed MSW with sorting at MRF (single stream)
Collection of separated recyclables and MSW(dual stream)
  Hand sorting of recyclables at MRF
  Hand sorting at point of collection (multi-compartment trucks)
  Collection of separate yard waste
    Bags, bins, or carts (require automation)
    Vacuum collection
    Dual compartment collection vehicle
Curbside collection costs are $15/ton lower for single-stream than for separated

## Slide 16: Recycling Hauler

## Slide 17: Split Body Rear Loader

## Slide 18: Vacuum Collection

## Slide 19: Collection Options
Public Collection
Private Collection
  Non-Exclusive Franchise
  Exclusive Franchises

## Slide 20: Labor
Labor intensive
Labor unskilled
High turn-over rates
Few prospects for mechanical replacement of manual labor
Injuries and poor working conditions
Limited career opportunities

## Slide 21: Customer Service
Frequency of service
Container and storage issues particularly for commercial and industrial
Location of pickup
Special wastes

## Slide 22: Management and Financing Issues
Low priority
Resistance to change and new technologies
Lack of quality management
Inflation
Changing with new regulations

## Slide 23: Technological Issues
Collection of recyclables, yard waste, special wastes
Yard waste containers - bagged material must be debagged prior to composting
Automated collection
Development of efficient routes
Vehicle weight restrictions
Vehicle turning radius and clearance

## Slide 24: Reasons for declining collection frequency include
Proportion of putrescible waste declined (food grinders)
Better design of collection vehicles controls odors and flies
Service costs increased
Time between collection and disposal decreased
Better management
Set out for 1/wk = 97%, 2/wk = 60%

## Slide 25: Safety
Third most dangerous job behind fishing and timber cutting
  Falls off trucks
  Hit by cars
  Inappropriate disposal of wastes
  Lifting injuries

## Slide 26: Fixed Factors Affecting Design and Cost
Fixed Factors
Climate
Topography
Layout - container access (alley, curbside, rear of house)
Available transportation systems, traffic, roads (Venice uses boats)
Types of wastes collected
Population density

## Slide 27: Variable Factors Affecting Design and Cost
Storage techniques employed
Recycling
Collection frequency
Crew size
Equipment

## Slide 28: Collection Cost Calculations
Y = a + b + c(d) + e + f + g
Where:
Y = total collection time/day or week
a = garage to route time/day or week
b = actual time collecting waste/day or week
c = number of trips to disposal site/day or week
d = time to drive fully loaded truck to disposal facility,
unload and return to collection area/trip
e = time to drive to garage at the end of the trip/day or week
f + g = off route time, can be expressed as a fraction of Y/day or week

## Slide 29: Collection Cost Calculations - Cont’d
N = SF/XW
Where:
N = number of vehicles required
S = total number of customers served per week
F = collection frequency
X = number of customers truck can serve per day
W = number of work days per week

## Slide 30: Hauled Container System
1
2
3
4
5
Disposal Site
Number of Containers = n
Example below: n=5
The number of
drive between
containers =
n-1
Example: dbc = 4

## Slide 31: Return to Home page