## Slide 1: SOLID WASTE MANAGEMENT THE 3 RS
DR. SUNEETH KUMAR S M
Professor, Department of Civil Engineering
Notes: <number>

## Slide 2: 1. FUNDAMENTALS AND STATISTICS (EPA Version) 2. The 3Rs and its importance

## Slide 3: According to EPA regulations, SOLID WASTE is
Any garbage or refuse (Municipal Solid Waste)
Sludge from a wastewater treatment plant, water supply treatment plant, or air pollution control facility
Other discarded material
Solid, liquid, semi-solid, or contained gaseous material from industrial, commercial, mining, and agricultural operations, and from community activities
http://www.epa.gov/epaoswer/osw/basifact.htm#solidwaste

## Slide 4: Trash or garbage is called Municipal Solid Waste (MSW)
Product packaging, grass clippings, furniture, clothing, bottles, food scraps, newspapers, appliances, paint, batteries…
“In 2010, Americans generated about 250 million tons of trash and recycled and composted over 85 million tons of this material, equivalent to a 34.1 percent recycling rate . On average, we recycled and composted 1.51 pounds of our individual waste generation of 4.43 pounds per person per day.”
http://www.epa.gov/wastes/nonhaz/municipal/index.htm

## Slide 5
http://www.epa.gov/epaoswer/non-hw/muncpl/pubs/msw06.pdf

## Slide 6
http://www.epa.gov/wastes/nonhaz/municipal/

## Slide 7
“By recycling almost 8 million tons of metals (which includes aluminum, steel, and mixed metals), US has eliminated greenhouse gas (GHG) emissions totaling more than 26 million metric tons of carbon dioxide equivalent (MMTCO2E). This is equivalent to removing more than 5 million cars from the road for one year.”

## Slide 8
About 136 million tons of MSW (54.2 percent) were discarded in landfills in 2010

## Slide 9
INDIAN SCENARIO
23.9 M.TONNES IN 1991 to 39 M.TONNES in 2001. (NEERI, NAGPUR)
Domestic Wastes
- all thrown around the bins or overflowing the bins
Industrial Wastes or Construction and Demolition wastes as well as Hazardous Wastes
- Deposited in an open space unauthorised
Biomedical Wastes containing infectious and toxic wastes
- Totally neglected – many times mixed up with domestic wastes or open dumped in the hospital premises unattended for a long time-few with low tempr Incinerators
Absence of a system of storage of wastes and no regular collection of wastes
NIMBY Syndrome still prevails

## Slide 10: CATEGORIES OF WASTE DISPOSAL
DILUTE AND DISPERSE
(ATTENUATION)
Throw it in the river / lake / sea
Burn it
Basically this involves spreading trash thinly over a large area to minimize its impact
Works for sewage, some waste chemicals, when land-disposal is not available
Plastic in Pacific

## Slide 11
CONCENTRATE AND CONTAIN
(ISOLATION)
Waste dumps, landfills
Historically, that’s how most of the solid waste gets treated

## Slide 12: MUNICIPAL WASTE DISPOSAL METHODS
They are “open”
Minimum effort and expense
Unsanitary and smelly
Vermin and pests
Contaminate soil, water and air
Fire hazard
OPEN DUMPS (rarely used in the USA anymore):

## Slide 13: Sanitary Landfill (AKA Municipal Solid Waste Landfill)

## Slide 15: SANITARY LANDFILLS (accommodate 57% of total municipal solid waste):
Each day trash is spread in thin layers
Compacted down
Covered with a soil layer
Graded for drainage
Sanitary landfills have largely replaced open dumps.

## Slide 17
The amount of garbage received by the Dane County Landfill, 7102 Highway 12, each day is enough to cover the surface of the playing field at Camp Randall Stadium to a depth of six inches, said Gerald Mandli, director of public works for the county.

## Slide 18: Site selection criteria for a landfill (page 16 of the DMG)
Is it too close to airports? (bird hazard to aircrafts)
Is it on a flood plain/wetland?
Is it too close to a fault (200 feet or less)?
Is it within seismic zones?
Is it located on unstable areas, such as landslide-prone areas, areas with sinkholes etc.?

## Slide 19: Properly designed Sanitary landfills:
Prevent water infiltration and leaching of toxic fluids
(LEACHATE = a liquid that has passed through or emerged from solid waste and contains soluble, suspended, or miscible materials removed from such waste)
Prevent water pollution
Reduce Vermin and pests
Reduce smell, toxic gases and fire hazard

## Slide 21: Problems with landfills…
Landfills require space
Produce methane gas (can be used for energy, or can cause climate change)
Leachate must be collected and treated
Potential for water pollution
NOT a long-term remedy

## Slide 22: If not landfill, then…?
INCINERATION (burning):
Significantly reduces the volume of garbage
Produces heat energy for generating electricity
Materials such as batteries, glass etc. are NOT suitable for incineration
Causes air pollution
Creates toxic ash and other solid waste

## Slide 23
The three R's - reduce, reuse and recycle –
All help to cut down on the amount of waste we throw away.
They conserve natural resources, landfill space and energy.
Plus, the three R's save land and money communities would use to dispose of waste in landfills.
Locating a new landfill has become difficult and more expensive due to environmental regulations and public opposition.
All the Governmental agencies have a goal of reducing the amount of waste going into landfills by 40 percent.
Everyone can help meet this goal and save natural resources, energy, and money by following the three R's.

## Slide 24
REDUCE
The best way to manage waste is to not produce it.
This can be done by shopping carefully and being aware of a few guidelines:
Buy products in bulk.
Larger, economy-size products or ones in concentrated form use less packaging and usually cost less per unit.
Avoid over-packaged goods, especially ones packed with several materials such as foil, paper, and plastic.
They are difficult to recycle, plus you pay more for the package.
Avoid disposable goods, such as paper plates, cups, napkins, razors, and lighters.
Throwaways contribute to the problem, and cost more because they must be replaced again and again.

## Slide 25
Buy durable goods - ones that are well-built or that carry good warranties.
They will last longer, save money in the long run and save landfill space.
At work, make two-sided copies whenever possible.
Maintain central files rather than using several files for individuals.
Use electronic mail or main bulletin board.
Remove your name from the mailing lists of materials you no longer want to receive.
Use cloth napkins instead of paper napkins.
Use a dish cloth instead of paper towels.

## Slide 26
REUSE It makes economic and environmental sense to reuse products. Sometimes it takes creativity:
Reuse products for the same purpose. Save paper and plastic bags, and repair broken appliances, furniture and toys.
Reuse products in different ways. Use a coffee can to pack a lunch; use plastic microwave dinner trays as picnic dishes.
Sell old clothes, appliances, toys, and furniture in garage sales or ads, or donate them to charities.
Use resealable containers rather than plastic wrap.
Use a ceramic coffee mug instead of paper cups.
Reuse grocery bags or bring your own cloth bags to the store.
Do not take a bag from the store unless you need one.

## Slide 27
RECYCLE Recycling is a series of steps that takes a used material and processes, remanufactures, and sells it as a new product. Begin recycling at home and at work:
Buy products made from recycled material.
Look for the recycling symbol or ask store managers or salesmen.
The recycling symbol means one of two things - either the product is made of recycled material, or the item can be recycled.
For instance, many plastic containers have a recycling symbol with a numbered code that identifies what type of plastic resin it is made from.
However, just because the container has this code does not mean it can be easily recycled locally.

## Slide 28
Check collection centers and curbside pickup services to see what they accept, and begin collecting those materials.
These can include metal cans, newspapers, paper products, glass, plastics and oil.
Consider purchasing recycled materials at work when purchasing material for office supply, office equipment or manufacturing.
Speak to store managers and ask for products and packaging that help cut down on waste, such as recycled products and products that are not over packaged.
Buy products made from material that is collected for recycling in your community.
Use recycled paper for letterhead, copier paper and newsletters.

## Slide 29
4th R – Refuse/Rebuy
Refuse to buy new items though you may think they are prettier than the ones you already have.
Buy and encourage the products made out of recycled materials.

## Slide 30
Reducing and Reusing Basics
The most effective way to reduce waste is to not create it in the first place.
Making a new product requires a lot of materials and energy:
Raw materials must be extracted from the earth, and the product must be fabricated and then transported to wherever it will be sold.
Reduction and reuse are the most effective ways you can save natural resources, protect the environment, and save money.

## Slide 31
Benefits of Reducing and Reusing
Prevents pollution caused by reducing the need to harvest new raw materials;
Saves energy;
Reduces greenhouse gas emissions that contribute to global climate change;
Helps sustain the environment for future generations;
Saves money;
Reduces the amount of waste that will need to be recycled or sent to landfills and incinerators
Allows products to be used to their fullest extent

## Slide 32
Ideas on How to Reduce and Reuse
Buy used things
Everything from clothes to building materials can be traced at specialized reuse centers and consignment shops. Often, used items are less expensive and just as good as new.
Look for products that use less packaging which reduces waste and costs.
Buying in bulk, can reduce packaging and save money.
Buy reusable over disposable items. Look for items that can be reused; the little things can add up. (For example, you can bring your own silverware and cup to work, rather than using disposable items.)
Maintain and repair products, like clothing, tires, and appliances, so that they won't have to be thrown out and replaced as frequently.
Borrow, rent, or share items that are used infrequently, like party decorations, tools, or furniture.

## Slide 33
Donation
One person's trash is another person's treasure.
Instead of discarding unwanted appliances, tools, or clothes, try selling or donating them.
Not only will you be reducing waste, you'll be helping others.
Local churches, community centers, thrift stores, schools, and nonprofit organizations may accept a variety of donated items, including used books, working electronics, and unneeded furniture.
Benefits of Donation
Prevents usable goods from going into landfills
Helps your community and those in need
Tax benefits may be available

## Slide 34
Resources for Donating Specific Goods and Materials:
Households and Personal Items
Goodwill
Salvation Army
Clothing Donations organisations
Lions Club International eyeglass donation
Rotary Club
Donate your used electronics

## Slide 35
Building Materials
Habitat for Humanity
Building Materials Reuse Association

## Slide 36
Recycling Basics
Recycling is the process of collecting and processing materials that would otherwise be thrown away as trash and turning them into new products.
Recycling can benefit your community and the environment.

## Slide 37
Benefits of Recycling
Reduces the amount of waste sent to landfills and incinerators;
Conserves natural resources such as timber, water, and minerals;
Prevents pollution by reducing the need to collect new raw materials;
Saves energy;
Reduces greenhouse gas emissions that contribute to global climate change;
Helps sustain the environment for future generations;
Helps create new well-paying jobs in the recycling and manufacturing industries

## Slide 38
Steps to Recycling Materials
Recycling includes the three steps below, which create a continuous loop
Step 1: Collection and Processing
Step 2: Manufacturing
Step 3: Purchasing New Products Made from Recycled Materials

## Slide 39
What Public Can Do
Learn what you can do to reduce, reuse and recycle Food and Household Hazaradous Waste (HHW):
At home
At school
At work
On the go
In the community

## Slide 40
1. AT HOME
Reducing Wasted Food -
Most people don't realize how much food they throw away every day — from uneaten leftovers to spoiled produce.
More than 96 percent of the food we throw away ends up in landfills.
In 2011, we landfilled more than 36 million tons of food waste. Once in landfills, food breaks down to produce methane, a potent greenhouse gas which contributes to climate change.

## Slide 41
Benefits of Reducing Wasted Food
Saves money from buying less food.
Reduces methane emissions from landfills and lowers your carbon footprint.
Conserves energy and resources, preventing pollution involved in the growing, manufacturing, transporting, and selling food (not to mention hauling the food waste and then landfilling it).
Supports your community by providing donated untouched food that would have otherwise gone to waste to those who might not have a steady food supply.

## Slide 42
Ways to Reduce Wasted Food
Shop your refrigerator first! Cook or eat what you already have at home before buying more.
Plan your menu before you go shopping and buy only those things on your menu.
Buy only what you realistically need and will use. Buying in bulk only saves money if you are able to use the food before it spoils.
Be creative! If safe and healthy, use the edible parts of food that you normally do not eat. For example, stale bread can be used to make croutons and beet tops can be sautèed for a delicious side dish.
Nutritious, safe, and untouched food can be donated to food banks to help those in need.
Freeze, preserve, or can surplus fruits and vegetables - especially abundant seasonal produce.
At restaurants, order only what you can finish by asking about portion sizes and be aware of side dishes included with entrees. Take home the leftovers and keep them for your next meal.
At all-you-can-eat buffets, take only what you can eat.
Compost food scraps rather than throwing them away.

## Slide 43
Food Donation Resources
Orphonages
Beggar’s Colonies
Charity Houses
Old age homes

## Slide 44
Composting at Home
Compost is organic material that can be added to soil to help plants grow.
Food scraps and yard waste currently make up 20 to 30 percent of what we throw away, and should be composted instead.
Making compost keeps these materials out of landfills where they take up space and release methane, a potent greenhouse gas.
All composting requires three basic ingredients:
Browns - This includes materials such as dead leaves, branches, and twigs.
Greens - This includes materials such as grass clippings, vegetable waste, fruit scraps, and coffee grounds.
Water - Having the right amount of water, greens, and browns is important for compost development.

## Slide 45
Your compost pile should have an equal amount of browns to greens.
You should also alternate layers of organic materials of different-sized particles.
The brown materials provide carbon for your compost, the green materials provide nitrogen, and the water provides moisture to help break down the organic matter.

## Slide 46
What to Compost
Fruits and vegetables Eggshells
Coffee grounds and filters Tea bags
Nut shells Shredded newspaper
Cardboard Paper
Yard trimmings Grass clippings
Houseplants Hay and straw
Leaves Sawdust
Wood chips Cotton and Wool Rags
Dryer and vacuum cleaner lint Hair and fur
Fireplace ashes

## Slide 47
What Not to Compost and Why
Black walnut tree leaves or twigs - Releases substances that might be harmful to plants
Coal or charcoal ash - Might contain substances harmful to plants
Dairy products (e.g., butter, milk, sour cream, yogurt) and eggs* - Create odor problems and attract pests such as rodents and flies
Diseased or insect-ridden plants - Diseases or insects might survive and be transferred back to other plants
Fats, grease, lard, or oils* - Create odor problems and attract pests such as rodents and flies
Meat or fish bones and scraps* - Create odor problems and attract pests such as rodents and flies
Pet wastes (e.g., dog or cat feces, soiled cat litter)* - Might contain parasites, bacteria, germs, pathogens, and viruses harmful to humans
Yard trimmings treated with chemical pesticides - Might kill beneficial composting organisms

## Slide 48
Benefits of Composting
Enriches soil, helping retain moisture and suppress plant diseases and pests.
Reduces the need for chemical fertilizers.
Encourages the production of beneficial bacteria and fungi that break down organic matter to create humus, a rich nutrient-filled material.
Reduces methane emissions from landfills and lowers your carbon footprint.
How to Compost at Home
There are many different ways to make a compost pile; A general reference provided the following for general reference. Helpful tools include pitchforks, square-point shovels or machetes, and water hoses with a spray head. Regular mixing or turning of the compost and some water will help maintain the compost.

## Slide 49
HHW Reduction, Reuse, Recycling, and Disposal Options
Leftover household products that contain corrosive, toxic, ignitable, or reactive ingredients are considered to be Household Hazardous Waste (HHW).
Products, such as paints, cleaners, oils, batteries, and pesticides that contain potentially hazardous ingredients require special care when you dispose of them.
Improper disposal of HHW can include pouring them down the drain, on the ground, into storm sewers, or in some cases putting them out with the trash.
The dangers of such disposal methods might not be immediately obvious, but improper disposal of these wastes can pollute the environment and pose a threat to human health. Many communities in the United States offer a variety of options for conveniently and safely managing HHW.

## Slide 50
HHW Reduction, Reuse, Recycling, and Disposal Options
The options of reduction, reuse, recycling, and disposal-listed in order of EPA’s preferred waste management hierarchy-are all important tools to safely manage HHW.
Benefits of Proper HHW Management
Reduction and recycling of HHW conserves resources and energy that would be expended in the production of more products.
Reuse of hazardous household products can save money and reduce the need for generating hazardous substances.
Proper disposal prevents pollution that could endanger human health and the environment.

## Slide 51
Reduction at Home
Consider reducing your purchase of products that contain hazardous ingredients.
Learn about the use of alternative methods or products—without hazardous ingredients—for some common household needs.
To avoid the potential risks associated with household hazardous wastes, it is important that people always monitor the use, storage, and disposal of products with potentially hazardous substances in their homes.

## Slide 52
Some tips for individuals to follow in their own homes:
Use and store products containing hazardous substances carefully to prevent any accidents at home.
Never store hazardous products in food containers; keep them in their original containers and never remove labels.
Corroding containers, however, require special handling for which call your local hazardous materials official or fire department for instructions.
When leftovers remain, never mix HHW with other products.
Incompatible products might react, ignite, or explode, and contaminated HHW might become unrecyclable.
Remember to follow any instructions for use and disposal provided on product labels.
Call your local environmental, health, or solid waste agency for instructions on proper use and disposal and to learn about local HHW drop off programs and upcoming collection days.

## Slide 53
Collection Options—Municipalities and Local Governments Facilitating Reuse, Recycling, and Proper Disposal
Permanent collection or exchange.
See if your community has a facility that collects HHW year-round.
Some of these facilities have exchange areas for unused or leftover paints, solvents, pesticides, cleaning and automotive products, and other materials. By taking advantage of these facilities, materials can be used by someone else, rather than being thrown away.
Special collection days. If your community doesn’t have a year-round collection system for HHW, see if there are any designated days in your area for collecting solid waste at a central location to ensure safe management and disposal.
Local business collection sites. If your community has neither a permanent collection site nor a special collection day, you might be able to drop off certain products at local businesses for recycling or proper disposal. Some local garages, for example, may accept used motor oil for recycling.

## Slide 54
2. AT SCHOOL
For Students:
Waste Reduction and Recycling
Before starting a new school year, sort through the school supplies on-hand.
Many supplies, like notebooks or pens and pencils, can be reused or recycled.
You can share your used books and other school supplies with friends, relatives, or younger schoolchildren.
For school dances or other events, decorations and other supplies can be borrowed or rented.
If you buy these supplies, try adopting a theme that can be used from year-to-year, so that you can reuse them.

## Slide 55
Many schools reuse text books to save money and reduce waste.
Covering your textbooks with cut-up grocery or shopping bags helps reduce waste and keeps your books in good condition.
If you buy lunch, take and use only what you need: one napkin, one ketchup packet, one salt packet, one pepper packet, one set of flatware.
Remember to recycle your cans and bottles, and separate your waste if your school has separation bins.
To reduce packaging waste, use school supplies wrapped with minimal packaging, use compact or concentrated products, or buy products in bulk.

## Slide 56
Community Service and Volunteering
Volunteer for, or start, an environmental club or recycling project in your school.
Work with your teachers and friends to find ways to encourage everyone in your community to make waste reduction a part of their everyday lives, such as starting a school composting project or ask for a day in art class where you can use things that would have normally been thrown away.
Tell your teachers you want to have a time dedicated to learning more about what you and your fellow classmates can do for the environment.
If you are a college student, you can organize an On Campus Eco Ambassadors Program to help green your campus and promote environmental awareness.

## Slide 57
For Staff
Waste Reduction and Recycling
Before starting a new school year, sort through your materials. Many supplies can be reused or recycled.
Notebooks, folders, and binders can be reused.
To reduce packaging waste, use school supplies wrapped with minimal packaging, use compact or concentrated products, or buy products in bulk.
Borrow or rent your decorations and supplies for parties and events.
If you buy these supplies, try adopting a theme that can be used from year-to-year, so that you can reuse your decorations and supplies.

## Slide 58
Setting up Programs
Form a team with committees to take charge of specific tasks.
Set an agenda or goals for the program, and engage parents and volunteers in the process.
Secure materials, donations, and other resources from your community.
Chemical Management
Take note of – but do not touch – chemicals in classrooms, janitorial closets and facility management sheds that do not have proper labels, are old and dusty or look unsafe (for example, have crystals growing around cap). Immediately report the location and description of the chemicals to the principal and the science department chair.
Promote responsible chemical management so that students and staff are protected from chemical accidents or exposures.

## Slide 59
Incorporate green chemistry and sustainability lesson plans in the chemistry curriculum.
Contact your local household hazardous waste collection facility for instructions on safely disposing of harmful waste products and materials, such as empty aerosol paint cans, leftover paint and thinners, used solvents and paint chips, unused garden products like fertilizers and pesticides, and household chemicals.
Properly store unused paint for future use, donate to neighbors or charities, or turn in to a waste collection facility for recycling.

## Slide 60
3. AT WORK
Waste Reduction and Recycling
Recycle office paper, newspapers, beverage containers, electronic equipment andbatteries. Check with your local recycling facility to see what materials they accept.
Consider using safer alternatives to common and potentially hazardous chemicals used in products and processes.
For businesses, there may be federal and/or state regulations on the disposal of electronics and mercury-containing lamps.
To help reduce waste, use two-sided printing and copying, buy supplies made with recycled content, and recycle used printer cartridges.
Before replacing a computer that no longer fits your needs, investigate enhancing the computer's capacity by installing a hard disk drive, chip, or memory-expansion card. Such modifications can be made with little know-how using the help of the manufacturer or a do-it-yourself guide.
When purchasing new electronics, consider a leasing program that includes proper reuse and recycling.
After office festivities, put leftovers in recyclable containers, and share them with family, friends, or others. Donate whole, untouched leftovers from parties to a local food bank or homeless shelter.

## Slide 61
Buying Green
Buy office supplies in bulk or multi-packs to reduce packaging waste.
You can also buy items with packaging that can be reused or recycled.
Buy energy-efficient items in the office with the ENERGY STAR® logo or items that are EPEAT-registered when buying electronics such as computers.
Consider the durability of a product before you buy it. Cheaper, less durable items often wear out quickly, creating waste and costing you money.
Look for items that embody the concept of reuse.

## Slide 62
4. ON THE GO
Whether you're going on vacation or out shopping, there are a number of ways you can reduce waste and conserve resources!
If staying in a hotel, check the bedding and linen policy with housekeeping.
Some hotels ask that the customer request the bedding or linen be laundered by putting a specific note card on the bed and leaving the towels on the floor. This practice conserves water resources.
If your hotel does not follow this practice, use a comment card to ask them to adopt it.

## Slide 63
When you're at the mall, don't get a new shopping bag for every item-combine bags or put them in your backpack. (And be sure to hold onto the receipt!)
When you leave your hotel room, switch off the air conditioning, lights, and TV to reduce energy use.
Before you leave home, adjust the air conditioning and water heater thermostats to conserve energy.
While on your trip, remember to take only the amount of products that you need from restaurants or lodgings.
Take only napkins, condiment packets, free brochures, maps, or coupons that you will actually use.

## Slide 64
5. IN THE COMMUNITY
EPA is challenging everyone—from citizens to community leaders—to do their part to conserve resources. These pages help identify opportunities to get involved in your community, where you can play a significant role in material management and waste reduction.
Volunteering
Find out how to volunteer by reading case studies of other people's projects.
Promote the 3Rs (Reduce, Reuse, Recycle) in your community by organizing community outreach activities and events, promoting sustainable community practices, and sharing knowledge and information on solid waste management.

## Slide 65
Setting up Programs
To set up a program, you should do the following:
Know your community
Name a leader and build an action team
Establish working committees
Develop an action plan
Identify and secure partners
Implement your plan
Evaluate results
Ref: http://www2.epa.gov/recycle
www.dnr.mo.gov/env/swmp/pubs-reports/threers.htm

## Slide 66
THANK YOU
FOR A PATIENT HEARING