## Slide 1
Power Electronics_BEE503
Module-2
Power Transistor
Topic: Power mosfet

## Slide 2
Metal Oxide Semiconductor Field Effect Transistors (MOSFET)
MOSFET are majority carrier devices.
Two types of power MOSFETs :
n-channel MOSFET and p-channel MOSFET.
The MOSËT has three terminals
Gate (G), Drain (D) and Source (S).
MOSFET is turned 'on' the current flows from drain to source
The voltage is applied between gate-source to turn 'on' the MOSFET
POWER MOSFET
Very small current flows from gate to source
Only voltage is to be applied to turn on the MOSFET

## Slide 3
The MOSFET can be turned off by removing the gate to source voltage
The MOSFET can be turned off by removing the gate to source voltage
Operate at very high frequencies
Applications such as choppers and inverters
MOSFETs are mainly used for low power applications

## Slide 4
Structure of MOSFETs
Depletion type MOSFET and Enhancement type MOSFET.
There are two types of MOSFETs
In both of these types the MOSFETs can be n - channel or p-channel
Fig. shows the structure of n-channel Enhancement type MOSFET.
Advantages of vertical structure
On-state resistance Of MOSFET is reduced.
Width of the gate is maximized. Hence, Gain Of the device is increased.

## Slide 5
Steady State Characteristics of MOSFETs
Fig. shows the V-I characteristics of n-channel power MOSFET
The drain current ID is plotted with respect to drain to source voltage VDS
Characteristics are plotted for various values of gate source voltages (VGS).
There are three regions in the characteristics :
Ohmic Region,
Active Region
Cut-off Region.
In cut-off region, the drain current is negligible and the MOSFET is said to be in 'OFF' state.

## Slide 6
When gate to source voltage is less than threshold gate source voltage, MOSFET is off, i.e. in cut-off region
The MOSFET is driven into ohmic region when VGS>> VGS(th).
In the ohmic region, the MOSFET conducts heavily. Hence it is said to be 'on' in the ohmic region
By applying heavy gate to source voltage, MOSFET can be turned on.
MOSFET is never operated in the active region. In active region it acts as an amplifier
For switching applications, MOSFET is operated only in ohmic and cut-off regions.

## Slide 7
Merits, Demerits and Applications of MOSFETs
Merits of MOSFETs
MOSFETs are majority carrier devices.
MOSFETs have positive temperature coefficient, hence their paralleling is easy.
MOSFETs have very simple drive circuits.
MOSFETs have short turn on and turn Off times, hence they operate at high frequencies.
MOSFETs do not require commutation circuits.
Gate has full control over the operation of MOSFET.

## Slide 8
Demerits Of MOSFET
On-state losses in MOSFETs are high.
MOSFETs are used only for IOW power applications.
iii) MOSFETs suffer from static charge.
Applications of MOSFETs
High frequency and low power inverters.
High frequency SMPS.
High frequency inverters and choppers,
iv) Low power AC and DC drives.

## Slide 10
A Bipolar Junction Transistor (also known as a BJT or BJT Transistor) is a three-terminal semiconductor device consisting of two p-n junctions which are able to amplify or magnify a signal.
It is a current controlled device.
The three terminals of the BJT are the base, the collector and the emitter.
There are two types of bipolar junction transistors – NPN transistors and PNP transistors.

## Slide 12
NPN Bipolar Junction Transistor
In an n-p-n bipolar transistor (or npn transistor) one p-type semiconductor resides between two n-type semiconductors the diagram below an n-p-n transistor is shown
IE, IC is emitter current and collect current respectively and VEB and VCB are emitter-base voltage and collector-base voltage respectively.
According to the convention if for the emitter, base and collector current IE, IB and IC current goes into the transistor the sign of the current is taken as positive and if current goes out from the transistor then the sign is taken as negative.

## Slide 13
PNP Bipolar Junction Transistor
For p-n-p transistors, current enters into the transistor through the emitter terminal.
Like any bipolar junction transistor, the emitter-base junction is forward biased and the collector-base junction is reverse biased.
Similarly for p-n-p bipolar junction transistor (or pnp transistor), an n-type semiconductor is sandwiched between two p-type semiconductors. The diagram of a p-n-p transistor is shown below

## Slide 14
Bipolar Junction Transistors Characteristics
The three parts of a BJT are collector, emitter and base. Before knowing about the bipolar junction transistor characteristics, we have to know about the modes of operation for this type of transistors. The modes are
Common Base (CB) mode
Common Emitter (CE) mode
Common Collector (CC) mode
All three types of modes are shown below
Common Base (CB) mode
Common Emitter (CE) mode
Common Collector (CC) mode

## Slide 15
The characteristics for p-n-p transistors are given for different modes and different parameters.
Common Base Characteristics
Input Characteristics
For p-n-p transistor, the input current is the emitter current (IE) and the input voltage is the collector base voltage (VCB).
As the emitter-base junction is forward biased, therefore the graph of IE Vs VEB is similar to the forward characteristics of a p-n diode. IE increases for fixed VEB when VCB increases.

## Slide 16
Common Base (CB) Configuration

## Slide 17
Output Characteristics
The output characteristics show the relation between the output voltage and output current IC is the output current and collector-base voltage and the emitter current IE is the input current and works as the parameters. The figure below shows the output characteristics for a p-n-p transistor in CB mode.

## Slide 18
Common Emitter Characteristics
Input characteristics
IB (Base Current) is the input current, VBE (Base – Emitter Voltage) is the input voltage for CE (Common Emitter) mode. So, the input characteristics for CE mode will be the relation between IB and VBE with VCE as a parameter. The characteristics are shown below

## Slide 19
Common Emitter (CE) Configuration

## Slide 20
Output Characteristics
Output characteristics for CE mode is the curve or graph between collector current (IC) and collector-emitter voltage (VCE) when the base current IB is the parameter. The characteristics is shown below in the figure.

## Slide 21
Common Collector (CC) Configuration

## Slide 35
Switching Limits
Second Breakdown
Forward Biased Safe Operating Area FBSOA
Reverse Biased Safe Operating Area RBSOA
Power Derating
Breakdown Voltages

## Slide 36
Switching Limits
Second Breakdown
It is a destructive phenomenon that results from the current flow to a small portion of the base, producing localized hot spots.
If the energy in these hot spots is sufficient the excessive localized heating may damage the transistor.
Thus secondary breakdown is caused by a localized thermal runaway.
The SB occurs at certain combinations of voltage, current and time.
Time is involved, the secondary breakdown is basically an energy dependent phenomenon.
Forward Biased Safe Operating Area FBSOA
During turn-on and on-state conditions, the average junction temperature and second breakdown limit the power handling capability of a transistor.
The manufacturer usually provides the FBSOA curves under specified test conditions.

## Slide 37
FBSOA indicates the limits of the transistor and for reliable operation the transistor must not be subjected to greater power dissipation than that shown by the FBSOA curve.
The dc FBSOA is shown as shaded area and the expansion of the area for pulsed operation of the BJT with shorter switching times which leads to larger FBSOA.
Reverse Biased Safe Operating Area RBSOA
During turn-off, a high current and high voltage must be sustained by the transistor, in most cases with the base-emitter junction reverse biased. The collector emitter voltage must be held to a safe level at or below a specified value of collector current.

## Slide 38
The manufacturer provide Ic VCE− limits during reverse-biased turn off as reverse biased safe area (RBSOA).
The area encompassed by the RBSOA is somewhat larger than FBSOA because of the extension of the area of higher voltages than BVCEO up to BVCBO at low collector currents.
This operation of the transistor up to higher voltage is possible because the combination of low collector current and reverse base current has made the beta so small that break down voltage rises towards BVCBO .

## Slide 39
A break down voltage is defined as the absolute maximum voltage between two terminals with the third terminal open, shorted or biased in either forward or reverse direction.
BVSUS : The maximum voltage between the collector and emitter that can be sustained across the transistor when it is carrying substantial collector current.
BVCEO : The maximum voltage between the collector and emitter terminal with base open circuited. BVCBO : This is the collector to base break down voltage when emitter is open circuited.
Breakdown Voltages

## Slide 55
Base Drive Control
Following points are to be remembered when designing the base drive circuit for transistor.
BJT is a current controlled device.
Power BJT is used as on/off switch in power converters.
Power BJT operates in saturation and cut-off when used as a switch.
Sufficient base current is required to drive BJT in saturation.
Storage time determines turn on and turn off times Of BJT

## Slide 56
Figure. shows the base drive circuit for turn on of a transistor
when base drive VB is applied
Capacitor C1 acts as a short.
R2 is virtually bypassed
Initial value of base current is only limited by R1 and it is given as,

## Slide 57
The capacitor Cl starts charging and base current starts falling
Then the current reduces to,

## Slide 58
To turn-off the transistor, base voltage is made zero
Capacitor voltage appears as negative voltage across base-emitter
Suddenly base current is reversed as shown in Figure.
Capacitor Cl then discharges through R2
Discharge time constant is
The charging time constant of the capacitor is

## Slide 62
Gate Drive
The gate drive circuit for MOSFET should satisfy the following requirements
The gate-source input capacitance should be charged quickly.
MOSFET turns on when gate-source input capacitance is charged to sufficient level.
To turn off MOSFET quickly, the negative gate current should be sufficiently high to discharge gate-source input capacitance.
Figure shows the gate drive as per above requirements

## Slide 63
The gate drive is applied across the terminals a-b.
Initially the resistance R1 is bypassed by Cl and full voltage is applied through the gate
Required gate current is very small
When MOSFET is to be turned off, the voltage made zero
Capacitor voltage across gate-source in negative direction
is made zero.

## Slide 64
di/dt and dv/dt Limitation
When base drive is applied
VCE starts falling and ic starts increasing
The rate of change of collector current during turn-on is called di/dt

## Slide 65
The fast rate of rise of collector current causes local heating of the BJT and it can be damaged
Hence rating of the transistor should not be exceeded di/dt
We can observe that ic changes from 0 to Ic(max) during times tr.

## Slide 66
BJT is on-state
Voltage across collector emitter will be zero
Full load current will be flowing when the base drive is removed, then collector current starts reducing and collector Emitter voltage starts rising
The rate Of change Of voltage across the device during turn Off is called dv/dt

## Slide 67
A fast rate Of rise of collector-emitter voltage may damage the BJT. Hence it should not be exceeded
We observe that the collector-emitter voltage changes from zero to Vs during time 'tf'

## Slide 68
The series inductance (Ls) reduces the fast rise in collector current. It protects the device against di/dt
The value of this inductance can be obtained as,

## Slide 69
When the BJT turns off the fast rise across collector-emitter is reduced by Cs
When BJT turns on, the capacitor discharges through BJT and Rs
Rs is used to limit the discharge current of Cs

## Slide 74
Isolation of Gate and Base Drives
Necessity of Isolation
Driver circuits operate at very low power levels (3 to 12 volts)
Digital circuits and microprocessors are also used in the triggering circuits
The gate and base drives are connected to power devices which operate at high power levels
Collector of BJT can have voltages of 200 V
Base is connected to trigger circuit that have voltages of 5 V

## Slide 75
If BJT is damaged and collector-base gets shorted, then high voltage will get connected to trigger circuit, This will damage the trigger circuit
This means trigger circuit is damage ----- Control / power levels due to device damage.
Electric isolation between control and power circuit

## Slide 76
Consider that the trigger circuit is deriving the two devices as shown in Fig.
T2 is given the drive between c-d
The trigger circuit must isolate the two drives
The points ‘b’ and ‘d’ may be shorted due to common ground of the trigger circuit.
Isolation can be obtained with the help of Pulse Transformers and Optocouplers.
T1 is given the drive between a-b

## Slide 80
Isolation using Pulse Transformer
Pulse transformer has one primary and one or more secondary windings.
It is normally used for pulsed mode of triggering. Figure shows the isolation using pulse transformer
Triggering circuit is electrically isolated from BJT.
If there is any electric damage to BJT, there will be no effect on triggering circuit.

## Slide 81
Advantages
Pulse transformer does not need external power for its operation.
It is very simple to use,
Disadvantages
Pulse transformer saturates at low frequencies hence it can be used only for high frequencies.
Due to magnetic coupling, the signal is distorted.

## Slide 82
Isolation using Optocouplers
Optocoupler consists of a pair of infrared LED and phototransistor.
When the signal is applied to the infrared LED, it turns-on.
It's light falls on phototransistor. Phototransistor also starts conducting.
There is no electric connection between LED and phototransistor.

## Slide 83
Figure shows the triggering circuit that uses optocoupler
In this circuit the triggering pulses are given to the input (LED) of optocoupler.
When 'Vg' is positive, LED turns-on. It's light falls on phototransistor, it turns-on.
Base Of T1 is connected to zero volts through phototransistor.
Due to this, Tl turns-on.Voltage Vcc is applied to gate of the MOSFET.
Hence MOSFET turns-on.
When the LED turns-off, phototransistor also turn-off. Therefore base drive of Tl goes to Vcc and it turn-off.
When Tl turns-off, MOSFET gate voltage becomes zero. Therefore MOSFET turns-off. Thus gate drive circuit using Optocoupler works.

## Slide 84
Advantages
Very good response at low frequencies
Compact and cheaper optocoupler devices are available
Disadvantages
Optocoupler need, external biasing voltage for their operation.
High frequency response is poor
Applications
Inverters, SMPS, Choppers, AC motor drives use optocouplers.