## Slide 6
PERIPHERAL EFFECTS
The power converter operations are based mainly on the switching of power semiconductor devices.
Due to the continuous & periodic repetitive turn-on and turn-off process of the switching devices used, the power converters introduce current and voltage harmonics into the supply system and on the output of the converters.
These induced harmonics can cause problems of distortion of the output voltage, harmonic generation into the supply system, and interference with the communication and signaling circuits.
It is normally necessary to introduce filters on the input side and output side of a power converter system so as to reduce the harmonic level to an acceptable magnitude

## Slide 7
The figure shows the block diagram of a generalized power converter with filters added.
The application of power electronics to supply the sensitive electronic loads poses a challenge on the power quality issues and raises the problems and concerns to be resolved by the researchers
The input and output quantities of power converters could be either AC or DC

## Slide 8
Factors such as
Total harmonic distortion (THD)
Displacement factor or harmonic factor (HF)
Input power factor
are measures of the quality of the waveforms
To determine these factors it is required to find the harmonic content of the waveforms.
To evaluate the performance of a converter, the input and output voltages/currents of a converter are expressed in Fourier series.
The quality of a power converter is judged by the quality of its voltage and current waveforms.