## Slide 1: WATERSHED MANAGEMENT

## Slide 2: WATERSHED MANEGEMENT

## Slide 3: Introduction
The world has now recognized the importance of watershed planning and established conservation authorities whose functions were to promote water management on a watershed basis. Although flooding and erosion issues had dominated water management for many decades in the world, we have now recognized that water management has many other objectives such as water quality, ecological health, terrestrial and aquatic resources, etc. In order to manage our water resources effectively, we should apply an ecosystem approach in water management.
The logical sequence of water management planning should be watershed plans,
subwatershed plans,
and site plans and these plans should be integrated with municipal land use planning process.
Ecosystem approach in water management

## Slide 4: What is Watershed
Watershed: A watershed is defined as the land area drained by a river and its tributaries. It is used to define the surface water drainage boundary, or A watershed refers to the entire catchment area, both land and water, drained by a watercourse and its tributaries. A subwatershed refers to the catchment area drained by an individual tributary to the main watercourse. The concept of watershed originates from surface hydrology where a river is assumed to be affected primarily by its surface drainage area. In fact, both surface and subsurface hydrology define a river and the importance of subsurface hydrology should not be overlooked.

## Slide 5: River Basin, Drainage Area
River Basin is a larger land area unit that, although comprised of numerous sub watersheds and tributaries still drains the entire basin past a single point. Land use, management and planning is often diverse and complex. River basins, Ogun-Oshun may drain an ocean or inland sea.

## Slide 6: WaterShed Hydrology
The main process in a watershed is the hydrologic cycle which summarizes the movement of water among surface water, air, land, and ground water. This process governs the physical, chemical, and biological characteristics of water ecosystems in a watershed.

## Slide 7: Diagram for Watershed, River basin and Watershed Hydrology cycle

## Slide 8: Define Watershed Management
Watershed management is the process of creating and implementing plans, programs, and projects to sustain and enhance watershed functions that affect the plant, animal, and human communities within a watershed boundary.

## Slide 9: WHAT WSM Manage?
Features of a watershed that agencies seek to manage include water supply, water quality, drainage, stormwater, runoff, water rights, and the overall planning and utilization of watersheds.

## Slide 10: Watershed management is a tool to assist land and water use decision makers
There are four phases:
1) issue identification and data gathering;
2) analysis and planning;
3) implementation; and,
4) monitoring.
NOTE: It should be emphasized that monitoring does not conclude the process, but rather initiates the beginning of understanding of the subwatershed, for which the plans should be updated over time.

## Slide 11: Contemporary Practice of WSM
In the world, the practice of watershed management has evolved over the last decade to become more comprehensive by integrating and addressing a broader range of resource and environmental protection issues and to more thoroughly evaluate the important linkages
between land and water,
between surface and groundwater and
between water quality and water quantity.

## Slide 12: THE NEED/IMPORTANCE FOR WATERSHED MANAGEMENT
Watershed management is necessary for the sustainable protection of natural resources and environmental health.
Watershed management, which recognizes the hydrologic (water) cycle as the pathway that integrates
physical,
chemical and
biological processes, is an important approach to achieving the goal of a sustainable environment, and is the tool to implement an ecosystem-based management strategy.

## Slide 13: Voluntary rather than Compulsory Mandate of WSM
Generally, stakeholders and participants supported the voluntary initiation of watershed management studies by conservation authorities or municipalities rather than provincially mandated watershed management except in the following circumstances:
when development pressure was likely to degrade water quality/quantity or aquatic life;
when there was an urgent threat to water resource sustainability; and,
when there was existing environmental degradation and a pressing need for rehabilitation or restoration.

## Slide 14: WHY IS WATERSHED MANAGEMENT INITIATED AND BY WHOM
Watershed management projects are usually initiated in response to issues and concerns around
existing environmental health,
proposed land use practices,
land use management or
redevelopment/restoration demands.

## Slide 15: WSM INITIATED AND BY WHOM
The evaluation concluded that projects are usually initiated in one or any combination of the following six ways:
by a conservation authority as input to official plans and resource management programs, or to protect particularly sensitive environments;
by a municipality or adjacent municipalities to address environmental protection components in official plans related to or because of proposed land use change;
by a developer landowner, or group of developers as a precursor to the subdivision approval process, commonly at the request of a commenting or approval agency;
by a provincial agency in fulfilling its mandate to protect resources and preserve the environment;
by a federal program for the designation of heritage rivers; and, in the future,
through locally initiated, community driven activities.

## Slide 16: WSM and SubWSM are Driven by
The watershed and sub watershed Management were generally driven by any or all of the following:
environmental resources - a larger scale strategy emphasizing environmental protection and management, eg.
land use changes - input to designate new land uses or input to alternatives for management of already designated, but not yet developed, land uses, eg.
land use management - input to new management applications and practices of already present land use types, eg.
redevelopment/restoration - input to habitat restoration, pollution abatement or environmental enhancement options eg.

## Slide 17: OBJECTIVES OF WATERSHED MANAGEMENT
The overall objectives for the process are divided into two types: Planning Objectives and Implementation Objectives.
Planning Objectives are distinct, specific, measurable statements that reflect and define each goal. They are designed to direct, track and measure progress over the next several years of preparing the Watershed Plan, but they do not necessarily guide implementing “on the ground” actions in the watershed. By definition, Planning Objectives will be one or several Implementation Objectives.
Implementation Objectives are also distinct, measurable statements that reflect the goals, but are meant to guide ongoing implementation actions in the watershed. The Implementation Objectives will become part of the Watershed Plan and can be used to measure long-term progress.

## Slide 18: Objectives of WSM
1) Ensure that the Watershed Management Initiative is a broad, consensus-based process.
2. Ensure that necessary resources are provided for the implementation of the Watershed Management Initiative.
3. Simplify compliance with regulatory requirements without compromising environmental protection.
4. Balance the objectives of water supply management, habitat protection, flood management and land use to protect and enhance water quality.
5. Protect and/or restore streams, reservoirs, wetlands and the bay for the benefit of fish, wildlife and human uses.
6. Develop an implementable Watershed Management Plan that incorporates science and is continuously improved.

## Slide 19
WATERSHED HYDROLOGY (WATERSHED MANAGEMENT AND HYDROLOGY)

## Slide 20: Watershed Hydrology
Physical Hydrology
Watershed Processes
Human Impacts on Water Resources

## Slide 21: Basic Definition
HYDROLOGY is the science of water that is concerned with the origin, circulation, distribution and properties of water of the earth.

## Slide 22: Basic Definition
FOREST HYDROLOGY, RANGE HYDROLOGY, WILDLAND HYDROLOGY is the branch of hydrology which deals with the effects of land management and vegetation on the quantity, quality and timing of water yields, including floods, erosion and sedimentation

## Slide 23: Basic Definition
WATERSHED, or CATCHMENT, is a topographic area that is drained by a stream, that is, the total land area above some point on a stream or river that drains past that point.
The watershed is often used as a planning or management unit. Natural environment unit.

## Slide 24: Basic Definition
RIVER BASIN is a larger land area unit that, although comprised of numerous sub watersheds and tributaries still drains the entire basin past a single point. Land use, management and planning is often diverse and complex. River basins, like Ogun-Oshun may drain an ocean or inland sea.

## Slide 25: Basic Definition
WATERSHED MANAGEMENT is the process of guiding and organizing land and other resource use on a watershed to provide desired goods and services without affecting adversely soil and water resources.

## Slide 26: Oahu’s Watersheds

## Slide 27: Ala Wai Canal Watershed

## Slide 28: Mississippi River Basin

## Slide 29: Why Watershed Approach?
Watersheds are among the most basic units of natural organization in landscapes.
The limits of watersheds are defined by topography and the resulting runoff patterns of rainwater.
The entire area of any watershed is therefore physically linked by the flow of rainwater runoff.
Consequently, processes or activities occurring in one portion of the watershed will directly impact downstream areas (land or water).

## Slide 30: Why Watershed Approach?
When detrimental activities like clear-cut deforestation occur, negative impacts are carried downstream in the form of eroded sediments or flooding.
Poor agricultural land management activities like excess fertilizer application convey negative impacts to downstream areas in the form of eutrophication and possible fish kills.
Notes: <number>

## Slide 31: Why Watershed Approach?

## Slide 32: Why Watershed Approach?

## Slide 33
Water is the fundamental agent that links all components (living and non-living) in watersheds, and watershed management generally revolves around water as a central theme.
A significant portion of the course will be devoted to examining the pathways and mechanisms by which water moves from the atmosphere, to the watershed surface and subsurface, into and out of biological communities, and ultimately downstream to the ocean or subsequent river reach.

## Slide 34
Recognizing that enhanced interactions between seemingly separate systems and organisms occur within watershed areas, both scientists and progressive-thinking resource managers have, in recent years, called for management programs to be organized at the watershed level.
By working in concert with nature in this way, we might manage resources in an integrative fashion that avoids some of the many past failures that were brought by not recognizing or considering the larger-scale impacts of any one management decision.

## Slide 35
Watershed Interactions
Cover crops, vegetation
Waterways, channels
Riparian buffer zones

## Slide 36: WS Management Strategies & Responses to Problems
Watershed management involves:
  Nonstructural (vegetation management) practices
  Structural (engineering) practices
Tools of WS management
  Soil conservation practices
  Land use planning
  Building dams
  Agroforestry practices
  Protected reserves
  Timber harvesting
  Construction regulation
The common denominator or integrating factor is water

## Slide 39: WATERSHED MANAGEMENT PRACTICES

## Slide 40: WATERSHED MANAGEMENT PRACTICES

## Slide 41: Integrated WS Management

## Slide 42: Integrated WS Management

## Slide 43: Integrated WS Management

## Slide 46: Watershed Water Cycle

## Slide 47: Impacts of Management

## Slide 48: WSM: a global perspective
Practices of resource use & management do not depend solely on the physical & biological characteristics of WS
Economical, social, cultural & political factors need to be fully integrated into viable solutions.
How these factors are inter-related can best be illustrated ?

## Slide 49: WSM: a global perspective
Land & water scarcity: is the major environmental issue facing the 21st century
Demands > supplies (17%)
Next 25yrs  2/3 pop. water shortage
Land scarcity  forest cut
Desertification
Hydrometeorological extremes, role of WSM

## Slide 50: Why Watershed Approach?

## Slide 51
Are these disasters preventable ?
Different approaches may be needed:
  Modifying Nat. Sys.
  Modifying Hum. Sys.
  A combination
Bio-engineering & vegetative measures along with structures to have some control over extreme hydro-meteorological events

## Slide 53: Components of hydrologic cycle
Location % of total
Oceans (salt water) 97.5
Fresh water 2.5
Icecaps and glaciers 1.85
Groundwater 0.64
Lakes, rivers, soil, atmosphere 0.01

## Slide 54: Components of hydrologic cycle
Precipitation
- rain, snow, fog interception
Runoff
- surface, subsurface
Storage
Evaporation
- soil, plants, water surface

## Slide 55: Uses of the hydrologic cycle (HC)
One of the uses of the HC is in the estimation of surface storage.
Storing and transferring a sufficient quantity of water has been one of the major problems.
  What volume of water is stored in a surface reservoir/soil and how does the volume change over time? What causes the water supply to be depleted or increased?
  How are the storage and releases managed?

## Slide 56: Watershed Water Cycle
Based on the conservation of mass:
Input – output = change in storage
P + R + B - F - E - T = ΔS
volumes are measured in units m3, L, ac-ft, f3, gal,
or in & cm over the watershed area

## Slide 57: What to do about units?
Rainfall is expressed in mm, in
Stream flow is expressed in cubic feet/cubic meter per second/minute
Evapotranspiration is expressed in mm, in
Soil water storage?
How can we make a mass balance with different units?
Conversion

## Slide 58: Water Depth
We have to use the same units; thus we have to remove the area from our calculation
We need to convert volume into unit depth; thus what’s water depth:
Water depth (d) = Volume of water (V) / Surface of the field (A)

## Slide 59: Conversion
1 acre-foot = 1317.25 m3

## Slide 60: Problem 1
Suppose there is a reservoir, filled with water, with a length of 5 m, a width of 10 m and a depth of 2 m. All the water from the reservoir is spread over a field of 1 hectare. Calculate the water depth (which is the thickness of the water layer) on the field.

## Slide 61: Answer 1
Surface of the field = 10 000 m2 Volume of water = 100 m3
Formula:
d = v/a =100 / 10,000 = 0.01 m = 10 mm

## Slide 62: Problem 2
A water layer 1 mm thick is spread over a field of 1 ha. Calculate the volume of the water (in m3),

## Slide 63: Answer 2
Given
Surface of the field = 10 000 m2 Water depth = 1 mm =1/1 000 = 0.001 m
Formula: Volume (m³) = surface of the field (m²) x water depth (m)
Answer V = 10 000 m2 x 0.001 m V = 10 m3 or 10 000 liters

## Slide 64: PRINCIPLES OF WATERSHED MANAGEMENT
1. Watersheds are natural systems that we can work with.
Delineating the Watershed
Natural Processes at Work in the Watershed
Human Factors at Work
Understanding Your Watershed
2. Watershed management is continuous and needs a multi disciplinary approach.
3. A watershed management framework supports partnering, using sound science, taking well-planned actions and achieving results.
4. A flexible approach is always needed.

## Slide 65: PRINCIPLES OF WATERSHED MANAGEMENT
1. Watersheds are natural systems that we can work with.
Delineating the Watershed
Natural Processes at Work in the Watershed
Human Factors at Work
Understanding Your Watershed

## Slide 66: PRINCIPLES OF WATERSHED MANAGEMENT (Cont)
2. Watershed management is continuous and needs a multi disciplinary approach.
3. A watershed management framework supports partnering, using sound science, taking well-planned actions and achieving results.
4. A flexible approach is always needed.

## Slide 67: Benefits of a Watershed Approach
-It provides a context for integration using practical, tangible management units that people understand
-It provides a better understanding and appreciation of nature
-It yields better management

## Slide 68: SOIL MOISTURE AND ITS MEASUREMENT
Soil Moisture Concepts and Terms
Soil moisture levels can be expressed in terms of soil water content or soil water potential (tension).
Soil water content most commonly is expressed as percent water by weight, percent water by volume, or inches of water per foot of soil. Other units such as inches of water per inch of soil also are used.
Water content by weight is determined by dividing the weight of water in the soil by the dry weight of the soil. It can be converted to percent by multiplying by 100%.
Water content by volume is obtained by multiplying the water content by weight by the bulk density of the soil. Bulk density of the soil is the relative weight of the dry soil to the weight of an equal volume of water. Bulk density for typical soils usually varies between 1.5 and 1.6.

## Slide 69: SOIL MOISTURE AND ITS MEASUREMENT (Cont)
Inches of water per foot of soil is obtained by multiplying the water content by volume by 12 inches per foot. It also can be expressed as inches of water per inch of soil which is equivalent to the water content by volume. By determining this value for each layer of soil, the total water in the soil profile can be estimated.
Soil water potential describes how tightly the water is held in the soil. Soil tension is another term used to describe soil water potential. It is an indicator of how hard a plant must work to get water from the soil The drier the soil, the greater the soil water potential and the harder it is to extract water from the soil. To convert from soil water content to soil water potential requires information on soil water versus soil tension that is available for many soils.
Water in the soil is classed as available or unavailable water.
Available water is defined as the water held in the soil between field capacity and wilting point (Figure 1).

## Slide 70: SOIL MOISTURE AND ITS MEASUREMENT (Cont)
Field capacity is the point at which the gravitational or easily drained water has drained from the soil. Traditionally, it has been considered as 1/3 bar tension. However, field capacity for many irrigated soils is approximately 1/10 bar tension.
Wilting point is the soil moisture content where most plants would experience permanent wilting and is considered to occur at 15 bars tension. Table 1 gives common ranges of available water for soil types.
Readily available water is that portion of the available water that is relatively easy for a plant to use. It is common to consider about 50% of the available water as readily available water.
Even though all of the available water can be used by the plant, the closer the soil is to the wilting point, the harder it is for the plant to use the water. Plant stress and yield loss are possible after the readily available water has been depleted.

## Slide 71: SOIL MOISTURE AND ITS MEASUREMENT (Cont)
Soil Water: Water in the soil resides within soil pores in close association with soil particles. The largest pores transport water to fill smaller pores. After irrigation, the larges pores drain due to gravity and water is held by the attraction of small pores and soil particles. Soil with small pores (clayey soil) will hold more water per unit volume than soil with large pores (sandy soil). After complete wetting and time is allowed for the soil to dewater, the larger pores, a typical soil will hold about 50% of the pore space as water and 50% as air. This is a condition generally called field capacity or the full point.
Methods of Measuring Soil Moisture
Electrical Resistance Blocks
Tensiometers