## Slide 1: GEOMORPHOLOGICAL PRINCIPLES Drainage Basin Morphometry. (Morphometric Variables interrelationships)

## Slide 2
Drainage Basin – Area of land that gathers water from precipitation and deliver it into a large stream or lakes.
Morphometry – Measurement and mathematical analysis of the configuration of the Earth's surface, shape and dimensions of its landforms (Clarke, 1966).
Basin Morphometry- Measurement of 3 dimensional properties of the land of a fluvial erosion system.

## Slide 3: Various variables
Stream order.
Stream length.
Bifurcation ratio.
Stream length ratio.
Basin length.
Valley side slope.
Basin area.
Stream frequency.
Drainage density.
Elongation ratio.
Circularity ratio,
Form factor.
Relief ratio.

## Slide 4: The Morphometric features can be divided into three:
Linear properties – one dimensional.
Aerial properties – two dimensional.
Relief properties – three dimensional.
Streams
Watershed
(drainage area)
Drainage Basin of River Ikiwe, Machakos, Kenya

## Slide 5: 1. Linear properties.
Stream order. (u)
Hierarchical ranking of streams (Strahler 1964)
Order changes at the confluence of streams.
First order stream are ones that do not possess a tributary.
When two first order streams meet, a second order begins.
They include:
Stream order.
Stream number.
Stream length.
Length ratio
Bifurcation ratio.

## Slide 6: Strahler and Shreve ordering
Strahler order method (1957)
Designated 1st order stream as those lacking a tributary.
2nd order at the confluence of 1st order as so on.
Shreve magnitude method (1966)
Streams lacking a tributary are 1st magnitude.
At junction, magnitudes are summed up.

## Slide 7: Stream Number
Example; in Strahler system
Order 1 - 7 streams
Order 2 - 5 streams.
Order 3 – 1 stream
The total number of Stream Segments present in each order.

## Slide 8: Stream length (Lu)
Total length of streams in a particular order.
Reveals surface run off characteristics.
Total length of stream segments is maximum in 1st order streams and decreases as stream order increases.

## Slide 9: Mean stream length
Calculated by dividing the total stream length of order 'u' and a number of stream segments of order 'u‘. (Strahler 1964)
Lsm = Nu
Lsm = Mean Stream Length
= Total stream length of order u
Nu = Total number of stream segments of order u

## Slide 10: Length ratio (Rl)
Ratio of mean length of one order to the next lower order of the stream segment.
Variation of Ri in sub-basins may result from change of slope and topography.
RL = Lu/Lu-1
Where RL = Stream Length Ratio
Lu = Total stream length of the order “u”
Lu-1 = Total stream length of its next lower order

## Slide 11: Bifurcation Ratio (Rb)
A ratio between number of streams in one order to the next higher order (Schumn, 1956)
Not same from one order to its next order as it is dependent upon the geological features of the drainage basin (Strahler, 1964).
Rb = Nu/Nu + 1
Rb = Bifurcation ratio
Nu = Total number of stream segments of order u
Nu + 1 = Number of segments of the next higher order

## Slide 12: Example
Rb = Nu/Nu + 1
1st order to 2nd
Rb= = 1.4
2nd order to 3rd
Rb= = 5
Mean Bifurcation Ratio
Rbm =
= 3.2
Calculate the Rb using Strahler method.

## Slide 13: AERIAL PROPERTIES a) Drainage Area(Au).
Entire area drained by a stream or system of streams such that all stream flow originating in an area is discharged though a single outlet.
b) Drainage Density (Dd)
Expression of closeness of spacing of channels.
Provides a quantitative measure of the average length of stream channel of the whole basin.
Drainage density =

## Slide 14: c) Stream Frequency/Drainage frequency
The number of stream segments per unit area (Horton 1945).
Fs = Nu /A
Where Fs = Stream Frequency
Nu = Total number of streams of all orders
A = Area of the basin (Sq.km)
A higher drainage density may imply an increased stream frequency.

## Slide 15: d) Drainage Texture.
Total number of stream segments of all orders per perimeter of that area.
Influenced primarily by infiltration capacity, and soil type.
Rt = Nu/P
Where Rt = Drainage texture
Nu = Total number of streams of all orders
P = Perimeter (Km)

## Slide 16: Circulatory and Elongation Ratio
Circulatory Ratio
A quantitative measure for visualizing the shape of the basin ; expressed as the ratio of basin area „A‟ to the area of a circle (Ac) having the same perimeter as the basin.
Influenced by length, frequency and gradient of streams.
Elongation ratio
A ratio of the diameter of a circle of the same area as the basin to the maximum basin length.
A circular basin displays better efficiency in the discharge of run-off than the elongated basin.

## Slide 17: Basin Shape (Rf)
The measure of elongation of a basin.
As elongation increases, basin shape decreases.
Length of basin - is a measure of linear distance between the mouth of the basin and the most distant point from the mouth.

## Slide 18: Length of overland flow
Its the distance from the crest-line at which the concentration of flow occurs.
Downslope the runoff concentrates to form rills and gullies after precipitation.
The length of overland flow (Lg) approximately equals half the reciprocal of drainage density.
Lg = of

## Slide 19: RELIEF ASPECT a) Basin Relief
Elevation difference of the highest and lowest point of the valley.
Subtract elevation of the mouth of a basin from highest point within the basin.

## Slide 20: b) Relief ratio
Ratio between total relief of a basin.
Elevation difference of lowest and highest points of a basin and longest dimension of a basin principal to the drainage line.
Relative relief =

## Slide 21: Conclusion
Morphometry is essentially quantitative, involving numerical variables whose values may be recovered from topographic maps.
Relevance of morphometric variables is their usefulness for comparison and statistical analysis.