## Slide 1
Technologies of Renewable Energy Sources
BEE654B
Dr. Sathish K R
Assistant Professor
Dept., of EEE
ATMECE

## Slide 2: Technologies of Renewable Energy Sources BEE654B
Module-1 –Introduction and Energy from Sun
Module-2 -Solar Thermal Energy Collectors and Solar Cells
Module-3 -Hydrogen Energy, Wind Energy, Geothermal & Solid
waste and Agricultural Refuse
Module-4 –Biomass ,Biogas and Tidal Power
Module-5 – Sea Wave and Ocean Thermal Energy
Text Books:
1. Nonconventional Energy sources, Shobh Nath Singh, Pearson Publication, First Edition 2015
2. Energy Technology, S.Rao and Dr. B.B. Parulekar, Khanna Publication, 2nd Edition, 1996.

## Slide 3: Module-2 Solar Thermal Energy Collectors and Solar Cells
Types of Solar Collectors
Configurations of Certain Practical Solar Thermal Collectors
Material Aspects of Solar Collectors
Concentrating Collectors
Parabolic Dish – Stirling Engine System
Working of Stirling or Brayton Heat Engine
Solar Collector Systems into Building Services
Solar Water Heating

## Slide 4
Systems, Passive Solar Water Heating Systems
Applications of Solar Water Heating Systems
Active Solar Space Cooling
Solar Air Heating, Solar Dryers, Crop Drying, Space Cooling,
Solar Cookers, Solar pond

## Slide 5: Types of Solar Collectors

## Slide 6
Solar Collector Type | Advantages | Disadvantages | Applications
Flat-plate collectors | Affordable and versatile | Lower efficiency than other types | Domestic hot water, space heating
Evacuated-tube collectors | High efficiency and good performance in cold temperatures | More expensive than flat-plate collectors | Domestic hot water, space heating
Concentrating collectors: Parabolic trough | High efficiency and ability to generate electricity | Expensive and complex | Large-scale power generation
Concentrating collectors: Dish collector | High efficiency and ability to generate electricity | Expensive and complex | Large-scale power generation
Concentrating collectors: Solar power tower | High efficiency and ability to generate electricity | Expensive and complex | Large-scale power generation

## Slide 11: Causes of Energy Scarcity
Energy scarcity can be caused by several factors:
Population growth: The world's population continues to grow, and with it, the demand for energy increases. This increase in energy demand can lead to energy scarcity, especially in developing countries with inadequate infrastructure to meet the energy demand.
Limited fossil fuel resources: Fossil fuels like coal, oil, and gas are finite resources and will eventually be depleted. As these resources become scarcer, the cost of extracting them increases, making them less affordable and leading to energy scarcity.
Political instability: Political instability and conflicts in regions that produce or transport energy resources can disrupt the supply of energy, leading to energy scarcity. This is especially true for countries heavily reliant on imports of energy resources.

## Slide 12: Causes of Energy Scarcity
Natural disasters: Natural disasters such as hurricanes, earthquakes, and floods can damage energy infrastructure, leading to energy scarcity. This was evident during Hurricane Katrina in the United States, where a significant portion of the country's oil and gas production was affected.
Inadequate infrastructure: Inadequate infrastructure, such as outdated power grids, can lead to energy scarcity. Power outages and brownouts can occur when the power grid is unable to meet the energy demand, leading to energy scarcity.
Climate change: Climate change can also contribute to energy scarcity, especially in regions that rely heavily on hydropower. Changes in precipitation patterns and temperatures can affect water availability, reducing the amount of energy that can be generated from hydropower.

## Slide 13: Solution to Energy Scarcity
There are several solutions to address energy scarcity:
Increase the use of renewable energy sources: Renewable energy sources such as solar, wind, hydro, geothermal, and biomass can play a significant role in reducing energy scarcity. Governments and private sector organizations can invest in the development of renewable energy infrastructure, making it a more accessible and cost-effective alternative to traditional fossil fuels.
Implement energy efficiency measures: Energy efficiency measures, such as improving building insulation and upgrading to energy-efficient appliances, can reduce the demand for energy and decrease the strain on energy infrastructure, ultimately reducing energy scarcity.

## Slide 14: Solution to Energy Scarcity
Develop energy storage technologies: Advances in energy storage technologies can allow renewable energy sources to be stored more efficiently and effectively, reducing energy scarcity during periods of high demand.
Implement demand-side management: Demand-side management involves managing energy consumption during peak periods to reduce the strain on the energy grid. This can be achieved through the use of smart grids and the implementation of pricing policies that encourage consumers to reduce energy consumption during peak periods.
Improve energy infrastructure: Upgrading energy infrastructure, such as power grids and transmission lines, can increase the capacity of the energy system and reduce the risk of energy scarcity.

## Slide 15: Factors Affecting Energy Resource Development
Factors affecting energy resource development include:
Resource Availability: The availability of energy resources is a crucial factor that affects energy resource development. Regions with abundant energy resources are more likely to have developed energy industries. For example, countries with significant oil reserves are more likely to have developed oil industries.
Infrastructure: Adequate infrastructure is essential for energy resource development. Infrastructure includes transportation, communication, and energy infrastructure. For example, the development of pipelines, transmission lines, and roads are essential for the transportation of energy resources.

## Slide 16: Factors Affecting Energy Resource Development
3. Technological Advancements: Advancements in technology can significantly impact energy resource development. New technologies can improve the efficiency and effectiveness of energy production, making it more accessible and cost-effective. For example, advancements in solar panel technology have made solar energy more accessible and cost-effective.
4. Government Policies: Government policies can impact energy resource development. Policies that provide incentives for renewable energy production and limit the use of fossil fuels can promote sustainable energy development. For example, government policies that provide tax incentives for the production of renewable energy can encourage investment in renewable energy.

## Slide 17: Factors Affecting Energy Resource Development
Economic Factors: Economic factors such as investment capital and energy prices can impact energy resource development. For example, high energy prices can encourage investment in renewable energy, while low energy prices can discourage investment.
Environmental Concerns: Environmental concerns such as air and water pollution and climate change can impact energy resource development. The production and use of fossil fuels can result in air and water pollution, while the use of renewable energy can reduce greenhouse gas emissions and promote environmental sustainability.

## Slide 18: Classification of Renewable Energy
Renewable energy can be classified into several types based on the source of energy. The main types of renewable energy include:
Solar Energy: Solar energy is obtained from the sun and can be harnessed using solar panels or concentrated solar power (CSP) systems.
Wind Energy: Wind energy is obtained from the kinetic energy of wind and can be harnessed using wind turbines.
Hydro Energy: Hydro energy is obtained from the kinetic energy of water and can be harnessed using hydropower plants.
Geothermal Energy: Geothermal energy is obtained from the heat generated within the Earth and can be harnessed using geothermal power plants

## Slide 19: Classification of Renewable Energy
Biomass Energy: Biomass energy is obtained from organic matter such as wood, crops, and waste materials, and can be harnessed using various technologies such as combustion, gasification, and anaerobic digestion.
Ocean Energy: Ocean energy is obtained from the kinetic energy of waves, tides, and currents, and can be harnessed using various technologies such as tidal turbines and wave energy converters.
Each type of renewable energy has its unique advantages and challenges, and their suitability varies depending on factors such as location, availability of resources, and technology.

## Slide 20: Worldwide Renewable Energy Availability
Renewable energy sources are available all around the world, although their availability and potential vary depending on several factors such as geographical location, climate conditions, and natural resources. Here are some general facts about renewable energy availability worldwide:

## Slide 21
Solar Energy: The sun is a source of abundant and free energy, and solar power is one of the fastest-growing sources of renewable energy worldwide. The areas with the highest solar energy potential are deserts and other arid regions, as they receive more sunlight and have less cloud cover.
Wind Energy: Wind power is another rapidly growing source of renewable energy, and its potential is highest in areas with consistent and strong winds. Coastal regions, high-altitude areas, and plains are some of the places where wind energy potential is high
Hydropower: Hydropower is generated by the force of falling water, and its potential depends on factors such as the height of the waterfalls and the volume of the water flow. Areas with high rainfall and mountainous terrain tend to have high hydropower potential.

## Slide 22
Geothermal Energy: Geothermal energy is generated by the heat from the Earth's core, and its potential is highest in areas with active tectonic activity or hotspots. Some of the areas with high geothermal energy potential include Iceland, the western United States, and parts of East Africa.
Overall, renewable energy sources have the potential to meet a significant portion of the world's energy demand and reduce our reliance on fossil fuels. However, the deployment and adoption of renewable energy technologies require significant investments and policy support to overcome technical and economic barriers.

## Slide 23: Renewable Energy in India
India has set ambitious targets for renewable energy deployment as part of its efforts to address energy security, climate change, and sustainable development. Here are some facts about renewable energy in India:
Solar Energy: India is one of the largest solar power markets in the world, with a total installed capacity of over 40 GW as of 2021. The Indian government has launched several programs and policies to promote solar energy deployment, including the Jawaharlal Nehru National Solar Mission and the Kisan Urja Suraksha evam Utthaan Mahabhiyan (KUSUM) scheme.

## Slide 24
Wind Energy: India has a total installed wind power capacity of over 39 GW as of 2021, making it the fourth-largest wind power market in the world. The Indian government has implemented several policies and incentives to support wind energy deployment, such as the National Wind-Solar Hybrid Policy and the Generation-Based Incentive (GBI) scheme.
Hydropower: India has significant hydropower potential, with an estimated total potential of over 145 GW. However, the development of hydropower projects in India faces several challenges, including environmental concerns and social issues.
Other renewable energy sources: India has also been exploring other renewable energy sources such as biomass, biogas, and small hydropower projects. The Indian government has launched several programs and initiatives to promote these sources, such as the National Bio-Energy Mission and the Small Hydro Power Programme.

## Slide 25
Overall, renewable energy is a key component of India's energy strategy, and the country has set a target of achieving 450 GW of renewable energy capacity by 2030. The deployment of renewable energy technologies in India is expected to provide significant economic, social, and environmental benefits, including job creation, rural development, and greenhouse gas emissions reduction.

## Slide 26: Sun- earth Geometric Relationship
The Sun-Earth geometric relationship refers to the way that the Earth and the Sun are positioned relative to each other
Some key facts about the Sun-Earth geometric relationship:
Earth's orbit
Rotation and revolution
Seasons
Solstices and equinoxes

## Slide 27: Sun- earth Geometric Relationship
Earth's orbit:
Earth orbits around the Sun in an elliptical path
365.24 days
Tilted at an angle of about 23.5 degrees
Rotation and revolution
Earth rotates on its own axis once every 24 hours
Earth revolves around the Sun, which gives rise to the different seasons that occur throughout the year.

## Slide 28: Sun- earth Geometric Relationship
Seasons
The tilt of the Earth's axis means that different parts of the planet receive different amounts of sunlight throughout the year, which causes the seasons
When the northern hemisphere is tilted towards the Sun, it receives more direct sunlight and experiences summer, while the southern hemisphere experiences winter
This effect is reversed when the northern hemisphere is tilted away from the Sun.
Solstices and equinoxes
The summer solstice occurs around June 21st in the northern hemisphere
The winter solstice occurs around December 21st in the northern hemisphere

## Slide 29: Sun- earth Geometric Relationship
The equinoxes occur around March 20th and September 22nd, when the Sun is directly overhead at the equator, and day and night are of equal length all over the planet

## Slide 30: Layers of Sun
Layers of the Sun, starting from the center and moving outwards:
Core: The core is the central region of the Sun where nuclear fusion takes place. This is where hydrogen atoms are fused together to form helium, releasing a huge amount of energy in the process.
Radiative zone: Surrounding the core is the radiative zone, which is a thick layer of plasma where energy is transferred by radiation. This is where the energy generated in the core gradually moves outward, in the form of electromagnetic radiation.

## Slide 31: Layers of Sun
Convection zone: Beyond the radiative zone is the convection zone, which is a layer of hot plasma where energy is transferred by convection. This is where the hot plasma rises, cools off, and sinks back down, creating a circulation pattern that helps to transport energy to the Sun's surface.
Photosphere: The photosphere is the visible surface of the Sun, where most of the light and heat that we receive on Earth originates.
Chromosphere: The chromosphere is a thin layer of hot plasma that lies just above the photosphere.
Corona: The corona is the outermost layer of the Sun, extending millions of kilometers into space.

## Slide 32: Earth – Sun Angles and their Relationships
Solar altitude angle (h): The solar altitude angle is the angle between the Sun's rays and the Earth's horizon.
It varies throughout the day as the Sun rises and sets.
At solar noon, when the Sun is directly overhead, the solar altitude angle is 90 degrees minus the latitude of the observer.
The solar altitude angle can be calculated using the following equation:
h = sin^-1(sin(δ)sin(φ) + cos(δ)cos(φ)cos(ha))
where δ is the declination angle of the Sun,
φ is the latitude of the observer, and
ha is the hour angle of the Sun.

## Slide 33: Earth – Sun Angles and their Relationships
Solar azimuth angle (A): The solar azimuth angle is the angle between the Sun's rays and due south.
It varies throughout the day as the Sun moves across the sky.
The solar azimuth angle can be calculated using the following equation:
cos(A) = sin(δ)cos(φ) - cos(δ)sin(φ)cos(ha) / cos(h)
where δ is the declination angle of the Sun,
φ is the latitude of the observer, and
ha is the hour angle of the Sun.

## Slide 34: Earth – Sun Angles and their Relationships
Solar declination angle (δ): The solar declination angle is the angle between the plane of the Earth's equator and the line connecting the Earth to the Sun.
It varies throughout the year as the Earth orbits the Sun.
The solar declination angle can be calculated using the following equation:
δ = 23.45°sin(360/365(d-81))
where d is the day of the year, with January 1st being day 1.

## Slide 35: Earth – Sun Angles and their Relationships
Hour angle is the angular distance measured westward along the celestial equator from the observer's meridian to the hour circle of a celestial body. It is usually denoted by the symbol "H".
The formula for calculating the hour angle of a celestial body is:
H = LST - RA
Where:
LST - Local Sidereal Time (the hour angle of the vernal equinox measured from the observer's meridian)
RA - Right Ascension (the celestial equivalent of longitude, measured in hours, minutes, and seconds)

## Slide 36
Parabolic Trough Reflector
It is a type of solar concentrator that is commonly used in solar thermal power plants to generate electricity
It consists of a parabolic-shaped mirror that reflects and concentrates sunlight onto a receiver tube located at the focal point of the parabola
The receiver tube is typically filled with a heat transfer fluid such as thermal oil or molten salt, which absorbs the concentrated sunlight and heats up to high temperatures
Parabolic trough reflectors are highly efficient at concentrating sunlight and are able to achieve temperatures of over 400°C.
They are also relatively easy to manufacture and maintain, making them a popular choice for large-scale solar power plants.

## Slide 37: Mirror-Strip Reflector
A series of flat, parallel mirrors are arranged in a trough shape to reflect and concentrate sunlight onto a central receiver tube
The mirrors are tilted at a specific angle to reflect sunlight onto the receiver throughout the day as the sun moves across the sky
It use a heat transfer fluid to absorb the concentrated sunlight and generate steam to drive a turbine and produce electricity.

## Slide 38
Linear Fresnel
Parabolic Dish.

## Slide 39: Heliostat Field Solar Collector
A heliostat field is a large array of movable mirrors, called heliostats, that track the sun and reflect sunlight onto a central receiver to generate electricity in a solar thermal power plant
The mirrors are usually arranged in a circular or rectangular pattern around the central receiver
Heliostat fields can generate very high temperatures, up to 1000°C, making them very efficient for generating electricity from solar energy

## Slide 40
Advantages and Disadvantages of Concentrating Collectors over Flat Plate Type Collectors
Criteria | Concentrating Collectors | Flat Plate Type Collectors
Efficiency | High efficiency due to concentration of sunlight onto a small area, can achieve high temperatures | Lower efficiency due to smaller surface area and less concentration of sunlight
Cost | Higher cost due to complex design and manufacturing, requires more maintenance | Lower cost due to simpler design and manufacturing, requires less maintenance
Space | Requires more space due to larger size and need for tracking systems | Requires less space due to smaller size and stationary mounting
Direct Sunlight | Requires direct sunlight to function properly, may be affected by weather conditions | Can still function in indirect sunlight or cloudy conditions

## Slide 41
Advantages and Disadvantages of Concentrating Collectors over Flat Plate Type Collectors
Criteria | Concentrating Collectors | Flat Plate Type Collectors
Application | Suitable for large-scale power generation in areas with high solar radiation | Suitable for smaller-scale applications or where space is limited
Durability | May be more susceptible to damage from weather or other external factors | More durable and can withstand a variety of environmental conditions

## Slide 42: WORKING OF PARABOLIC DISH STRILING OR BRAYTON ENGINE SYSTEM
A parabolic dish Stirling or Brayton engine system is a type of concentrated solar power technology that uses a parabolic dish reflector to concentrate sunlight onto a receiver at the focal point of the dish
The receiver contains a Stirling or Brayton engine, which converts the concentrated solar energy into mechanical power that can be used to generate electricity

## Slide 43: WORKING OF PARABOLIC DISH STRILING OR BRAYTON ENGINE SYSTEM
The parabolic dish reflector is pointed at the sun and tracks its movement throughout the day to maintain optimal alignment
Sunlight is concentrated onto a receiver at the focal point of the dish. The receiver contains a Stirling or Brayton engine
In a Stirling engine, the concentrated solar energy heats up a gas, typically helium, inside the engine, causing it to expand and push a piston. The piston is connected to a crankshaft, which converts the linear motion into rotational motion to drive an electrical generator.

## Slide 44: WORKING OF PARABOLIC DISH STRILING OR BRAYTON ENGINE SYSTEM
In a Brayton engine, the concentrated solar energy heats up a gas, typically air, which expands and drives a turbine. The turbine is connected to a generator, which converts the rotational motion into electrical power
The mechanical power produced by the Stirling or Brayton engine is used to generate electricity, which can be fed into the electrical grid or used to power local equipment.

## Slide 45
Thank you