## Slide 1
Technologies of Renewable Energy Sources
BEE654B
Dr. Sathish K R
Assistant Professor
Dept., of EEE
ATMECE

## Slide 2: Technologies of Renewable Energy Sources BEE654B
Module-1 –Introduction and Energy from Sun
Module-2 -Solar Thermal Energy Collectors and Solar Cells
Module-3 -Hydrogen Energy, Wind Energy, Geothermal & Solid
waste and Agricultural Refuse
Module-4 –Biomass ,Biogas and Tidal Power
Module-5 – Sea Wave and Ocean Thermal Energy
Text Books:
1. Nonconventional Energy sources, Shobh Nath Singh, Pearson Publication, First Edition 2015
2. Energy Technology, S.Rao and Dr. B.B. Parulekar, Khanna Publication, 2nd Edition, 1996.

## Slide 3: Updraft Gasifier
An updraft gasifier is a type of gasifier that uses a counter-current flow of fuel and gas
The fuel is fed into the top of the gasifier and the gas is drawn out of the bottom
The hot gas flows up through the fuel bed, causing it to pyrolyze and gasify
Updraft gasifiers are the simplest type of gasifier and are easy to build and operate

## Slide 4: Updraft Gasifier
Fuel bed: The fuel bed is where the fuel is burned. It is typically made of a porous material, such as sand or gravel, to allow for good airflow.
Gasifier: The gasifier is where the fuel is converted into gas. It is typically made of a refractory material, such as a firebrick, to withstand the high temperatures of the gasification process.
Heat exchanger: The heat exchanger is used to cool the gas before it is used. It is typically made of a metal, such as steel, that can withstand the high temperatures of the gas.
Burner: The burner is used to ignite the fuel in the gasifier. It is typically made of a metal, such as steel, that can withstand the high temperatures of the gasification process.

## Slide 5: Updraft Gasifier
Updraft gasifiers are typically used for small-scale applications, such as cooking and heating. They can also be used for larger-scale applications, such as power generation and industrial processes
Overall, updraft gasifiers are a versatile and efficient way to convert biomass and other fuels into gas. They are a good option for small-scale applications where simplicity and cost are important factors.

## Slide 6: Downdraft gasifier
A downdraft gasifier is a type of gasifier that uses a downward flow of gas and air through a bed of fuel. The fuel is typically biomass, such as wood, agricultural waste, or municipal solid waste
Downdraft gasifiers have several advantages over other types of gasifiers
They are relatively simple to operate and maintain. They can be used with a wide variety of fuels. And they produce syngas with a high heating value

## Slide 7: Downdraft gasifier
Downdraft gasifiers also have some disadvantages. They can produce a high concentration of tar, which can be harmful to the environment. They can also be difficult to start and stop.
Components
Feedstock: The feedstock is the material that is being gasified. It can be biomass, coal, or other organic materials.
Gasification agent: The gasification agent is the gas that is used to convert the feedstock into syngas. Air is the most common gasification agent, but other gases such as oxygen or steam can also be used.

## Slide 8: Downdraft gasifier
Reactor: The reactor is the chamber where the gasification reaction takes place. It is typically made of a refractory material such as firebrick or ceramic.
Heat exchanger: The heat exchanger is used to recover heat from the syngas. The heat can be used to preheat the feedstock or to generate steam.
Cooler: The cooler is used to cool the syngas before it is used. The cooling helps to condense water vapor and other impurities in the syngas.
Gas cleaning system: The gas cleaning system is used to remove impurities from the syngas. The impurities can include tar, dust, and other contaminants.

## Slide 9: Cross Draft Gasifier
The fuel is fed into the top of the gasifier and the air is blown in from the side
The fuel burns in the combustion zone and the heat from the combustion zone is used to heat the unburnt fuel in the reduction zone
The unburnt fuel in the reduction zone reacts with the hot gasses from the combustion zone to produce syngas
The syngas is then drawn out of the gasifier at the bottom.

## Slide 10: Main components of a cross draft gasifier
Feedstock hopper: This is where the biomass fuel is stored.
Feedstock feeder: This is a mechanism that feeds the biomass fuel into the gasifier.
Gasifier: This is where the biomass fuel is converted into syngas.
Cooler: This is where the syngas is cooled before it is used.
Heat exchanger: This is where the heat from the syngas is used to preheat the biomass fuel.
Blower: This is a fan that provides the air flow needed for combustion.
Combustion chamber: This is where the air and fuel are mixed and burned.
Ash removal system: This is a system that removes the ash from the gasifier.

## Slide 11: Cross Draft Gasifier
Cross draft gasifiers are a good option for applications that require high efficiency and low ash production. However, they are more complex and expensive than other types of gasifiers

## Slide 12: Use of Biomass Gasifier
Power generation: Biomass gasifiers can be used to generate electricity by burning the syngas in a gas turbine or internal combustion engine.
Heat generation: Biomass gasifiers can be used to generate heat for industrial processes, space heating, or water heating.
Fuel for vehicles: Biomass gasifiers can be used to produce syngas that can be used as a fuel for vehicles, such as cars, buses, and trucks.
Production of chemicals: Biomass gasifiers can be used to produce a variety of chemicals, such as methanol, ethanol, and hydrogen.

## Slide 13: Gasifier Biomass Feed Characteristics
Gasification is a thermochemical process that converts biomass feedstock into a mixture of gases known as syngas (synthetic gas)
The biomass feed characteristics play a crucial role in determining the efficiency and performance of a gasifier
Moisture Content: Higher moisture content requires additional energy to evaporate the water, reducing the overall efficiency of the gasification process. Ideally, biomass feedstock should have low moisture content to maximize gas production.

## Slide 14
Particle Size : The particle size influences the rate of heat transfer and gasification reactions. Smaller particle sizes generally result in faster reaction rates and better conversion of biomass into syngas

## Slide 15
Thank you