## Slide 1
Technologies of Renewable Energy Sources
BEE654B
Dr. Sathish K R
Assistant Professor
Dept., of EEE
ATMECE

## Slide 2: Technologies of Renewable Energy Sources BEE654B
Module-1 –Introduction and Energy from Sun
Module-2 -Solar Thermal Energy Collectors and Solar Cells
Module-3 -Hydrogen Energy, Wind Energy, Geothermal & Solid
waste and Agricultural Refuse
Module-4 –Biomass ,Biogas and Tidal Power
Module-5 – Sea Wave and Ocean Thermal Energy
Text Books:
1. Nonconventional Energy sources, Shobh Nath Singh, Pearson Publication, First Edition 2015
2. Energy Technology, S.Rao and Dr. B.B. Parulekar, Khanna Publication, 2nd Edition, 1996.

## Slide 3: Module-3 Hydrogen Energy
Benefits of Hydrogen Energy
Hydrogen Production Technologies
Hydrogen Energy Storage
Use of Hydrogen Energy
Advantages and Disadvantages of Hydrogen Energy
Problems Associated with Hydrogen Energy

## Slide 4: Benefits of Hydrogen Energy
Environmentally friendly: When hydrogen is used as a fuel, it only produces water and heat, making it a very clean source of energy
Versatile:Hydrogen can be used in a wide range of applications, including transportation, power generation, and industrial processes
Abundant:Hydrogen is one of the most abundant elements in the universe, and it can be produced from a variety of sources, including water, biomass, and natural gas

## Slide 5: Benefits of Hydrogen Energy
Efficient: Hydrogen fuel cells are very efficient, with conversion efficiencies of up to 60%. This means that they can convert a high percentage of the energy stored in the hydrogen into electricity.
Economic benefits: Hydrogen can be produced locally, reducing dependence on imported energy sources
Energy storage: Hydrogen can be used as a way to store energy, making it a valuable resource for balancing the electricity grid and managing energy demand.

## Slide 6
Hydrogen Production Technologies
Thermo-chemical production: Thermo-chemical methods of hydrogen production involve the use of chemical reactions to produce hydrogen from various feedstocks
Electrolytic Production: The electrolytic production of hydrogen involves splitting water (H2O) into hydrogen (H2) and oxygen (O2) using an electric current
Photolytic production: Photolytic production of hydrogen involves the use of sunlight to produce hydrogen from water or other sources

## Slide 7: Electrolytic Production of Hydrogen
The electrolytic production of hydrogen involves splitting water (H2O) into hydrogen (H2) and oxygen (O2) using an electric current. This process is called electrolysis, and it involves the use of an electrolyzer.

## Slide 8: Hydrogen Energy Storage
Hydrogen energy storage involves storing hydrogen in various forms so that it can be used later to generate energy
Compressed hydrogen gas
Liquid hydrogen
Hydrogen storage in materials
Power-to-gas
Underground hydrogen storage

## Slide 9
Compressed hydrogen gas
Hydrogen gas can be compressed and stored in high-pressure tanks, typically at pressures of 350-700 bar
Compressed hydrogen gas is a well-established method of hydrogen storage and is commonly used in fuel cell vehicles
Liquid hydrogen:
Hydrogen gas can also be liquefied and stored at very low temperatures (-253°C).
Liquid hydrogen has a much higher energy density than compressed hydrogen gas, but it requires cryogenic temperatures and specialized storage tanks.

## Slide 10
Hydrogen storage in materials
Hydrogen can also be stored in solid materials, such as metal hydrides, chemical hydrides, and carbon-based materials
When these materials are exposed to hydrogen gas, they absorb the hydrogen and store it in a solid form
When the hydrogen is needed, the material is heated or exposed to a catalyst, releasing the stored hydrogen
Underground hydrogen storage
Hydrogen can also be stored underground in geological formations, such as salt caverns or depleted gas fields.
The hydrogen is typically compressed and injected into the geological formation, where it is stored until needed

## Slide 11: Use of Hydrogen Energy
For residential uses
For industrial uses
For as an alternative transport fuel
For as an alternative fuel for aircraft
For electric power generation (utilities).

## Slide 12: ADVANTAGE AND DISADVANTAGE OF HYDROGEN ENERGY
Advantage:
Zero emissions: One of the biggest advantages of hydrogen energy is that it produces no harmful emissions, such as carbon dioxide, when it is used to generate energy.
Versatility: Hydrogen can be used in a variety of applications, including transportation, electricity generation, and industrial processes.
Energy storage: Hydrogen can be stored and used as an energy carrier, providing a way to store excess renewable energy and use it when needed

## Slide 13
High energy density: Hydrogen has a very high energy density, which means that it contains a large amount of energy relative to its weight
Disadvantage:
Cost: Hydrogen production, storage, and transportation can be expensive, making it a less competitive energy source compared to fossil fuels.
Safety concerns: Hydrogen is highly flammable and can be difficult to store and transport safely.
Energy efficiency: The process of producing hydrogen from other energy sources, such as natural gas or electricity

## Slide 14
PROBLEM ASSOCIATED WITH HYDROGEN ENERGY
Hydrogen Storage: it is a major issue. Because container used must withstand high pressure when hydrogen is stored.
High Reactivity of Hydrogen: it is extremely reactive it is combustible and flammable. The filled container may explode.
Cost and methods of hydrogen fuel production: the cost of production is very high and newer and cleaner technology need to be found.
Consumer Demand: gas filling station to be changed to hydrogen filling, it should be free available to consumers and meet their demand.
Cost of Changing Infrastructure: to accommodate hydrogen equipment and appliances.

## Slide 15: Wind Energy
Windmills
Wind Turbines
Wind Resources
Wind Turbine Site Selection
Windmills: Windmills, also known as wind turbines, are machines that generate electricity by harnessing the power of the wind
Wind turbines have blades that rotate when the wind blows, which in turn drives a generator that produces electricity.

## Slide 16: Wind Turbines
Wind turbines, also known as wind generators, are machines that convert the kinetic energy of the wind into mechanical or electrical energy
They are typically composed of a rotor, blades, a tower, a nacelle, and a generator.
Wind turbines can be classified into two main types:
Horizontal axis turbines
Vertical axis turbines.

## Slide 17: Power in the Wind
The amount of power (in Watts) collected by a wind turbine is explained in the following equations:

## Slide 18
Site Selection Considerations
The power available in the wind increases rapidly with the speed, hence wind energy conversion machines should be located preferable in areas where the winds are strong and persistent.
Technical, economic, environmental, social, and other factors are examined before a decision is made to erect a generating plant on a specific site.
Some of the main considerations are discussed below.
Wind resource: The most important factor in site selection is the wind resource. The wind speed and direction at the site will determine the amount of power that can be generated by the wind turbines
Land availability: The site must have sufficient land available to accommodate the wind turbines and associated infrastructure, such as access roads, transmission lines, and substations.

## Slide 19
Environmental impacts: Wind farms can have a range of environmental impacts, including impacts on wildlife, habitats, and visual landscapes
Grid connection: The site must be located near existing electrical infrastructure or have the potential to connect to the grid
Economic considerations: The cost of land, construction, and operation can vary significantly between sites. Site selection should take into account the economics of the project, including the cost of land, construction, and operation, as well as the potential revenue from electricity sales

## Slide 20: Geothermal Energy
Geothermal Systems
Classifications, Geothermal Resource Utilization
Resource Exploration
Geothermal Based Electric Power Generation
Associated Problems
Environmental Effects

## Slide 21: Geothermal Systems
Geothermal energy is a form of renewable energy derived from the heat generated within the Earth's core
Geothermal energy is considered a sustainable and environmentally friendly energy source because it produces very low emissions and has a virtually limitless supply.
Although higher and lower temperatures occur, the average temperature at a depth of 10 km is about 200°C
Hot molten (or partially molten) rock, called "Magma" is commonly present at depths greater than 24 to 40 km.

## Slide 22
Main advantages of geothermal energy are:
It is a reliable and cheap source of energy.
It is available 24 hours per day.
Its availability is independent of weather.
It has inherent storage feature so no extra storage facility required.
Geothermal plants require little land area.
Feasibility of modular approach represents lot of opportunities for development of relatively quick, cost-effective geothermal projects.
Major disadvantages are:
It is site specific there are not many places where you can build a geothermal power station.
Generally, energy is available as low grade heat.
Continuous extraction of heated ground water may leads to subsidence (setting or slumping) of land.

## Slide 23: Types of Geothermal Resources
There are four main types of geothermal resources They are:
Shallow geothermal heat-pump, or geo-exchange resources
Hydrothermal resources
Enhanced/ engineered geothermal systems
Unconventional or advanced geothermal systems
Shallow geothermal heat-pump, or geo-exchange resources
Shallow geothermal energy systems (SGES), which are commonly known as Ground Source Heat Pump systems (GSHP), use the nearly steady temperature of the ground surface layers as an energy source and/or an energy sink in both heating and cooling modes

## Slide 24
Hydrothermal Resources:
They are characterized by the presence of hot fluids circulating in the Earth's crust
These fluids are heated by the geothermal energy stored in the Earth's interior
Hydrothermal systems include natural features such as hot springs, geysers, and hydrothermal vents
Enhanced/Engineered Geothermal Systems
Enhanced or engineered geothermal systems (EGS) involve creating artificial reservoirs in hot
but impermeable rock formations to extract geothermal energy

## Slide 25
Flash Geothermal Power Plants
The term flash steam refers to the process where high-pressure hot water is flashed (vaporized) into steam inside a flash tank by lowering the pressure.
This steam is then used to drive around turbines.
At high pressure below earth’s surface, the water exists as compressed liquid.
Pipeline is installed to tap into the resource.
When the compressed liquid water reaches the surface at atmospheric pressure then, a portion of it immediately flashes to steam.
The steam portion is redirected into a steam turbine, where power is produced.

## Slide 26
The exhaust is then piped to a condenser where it is returned to liquid. This hot liquid water can then be used for further heating applications prior to the reinjection into the rock.
Flash steam plants are the most common type of geothermal power generation plants in operation today.
Fluid at temperatures greater than 182°C is pumped under high pressure into a tank at the surface held at a much low pressure, causing some of the fluid to rapidly vaporize, or ‘flash.’
The vapour then drives a turbine, which drives a generator. If any liquid remains in the tank, it can be flashed again in the second tank to extract more energy.

## Slide 27
Fig. 3.7 Double-flash geothermal steam-electric power plant

## Slide 28
Double-flash geothermal steam-electric power plant
Single-flash geothermal steam-electric power plant

## Slide 29
Fig. 3.8 Binary fluid hydrothermal system
Binary cycle-based geothermal plants are a type of geothermal power plant that utilizes binary cycle technology to generate electricity from geothermal resources. This technology is particularly suited for low-temperature geothermal resources
Resource Extraction: The first step in the process involves extracting the geothermal fluid from the underground reservoir. In binary cycle systems, this fluid typically has a lower temperature (usually below 150°C or 300°F) compared to traditional flash steam or dry steam geothermal systems. The fluid is pumped to the surface using production wells.

## Slide 30
Fig. 3.8 Binary fluid hydrothermal system
Binary Cycle System: The extracted geothermal fluid is not directly used to generate electricity but is instead used in a binary cycle system. In this system, the geothermal fluid is passed through a heat exchanger or a heat exchanger network. It heats a secondary working fluid with a lower boiling point (such as isobutane, pentane, or other organic fluids) that has been selected to match the temperature range of the geothermal fluid.
Heat-to-Electricity Conversion: The heated secondary working fluid vaporizes due to the heat transferred from the geothermal fluid.
The vaporized working fluid then expands and drives a turbine, which is connected to a generator to produce electricity

## Slide 31
Fig. 3.8 Binary fluid hydrothermal system
Condensation and Re-Injection: After the heat exchange process, the cooled geothermal fluid is typically reinjected back into the underground reservoir to maintain the long-term sustainability of the geothermal resource. This reinjection helps to sustain the pressure and thermal equilibrium of the reservoir.

## Slide 32
Solid Wastes and Agricultural Refuse
Solid waste is the unwanted or useless solid materials generated from human activities in residential, industrial or commercial areas.
It may be categorized in three ways, According to its:
Origin (domestic, industrial, commercial, construction or institutional)
Contents (organic material, glass, metal, plastic paper etc.)
Hazard potential (toxic, non-toxin, flammable, radioactive, infectious etc.).

## Slide 33
SOURCES AND TYPES OF WASTES
The following are some of the wastes:
Residential wastes:
These are single family or multifamily dwellings.
They constitute kitchen wastes, paper and cardboards, clothes and leather materials, plastics and rubber materials, glass, wood and metal crockery and furniture, electrical and electronics appliances and gadgets, etc.
Municipal services wastes:
They include general wastes collected from street sweeping, park, recreational places, sludge, landscaping, and tree trimming.
Industrial and commercial wastes:
They are housekeeping and food wastes, packaging and demolition material wastes, scraps, hazardous wastes, wood, cardboard paper, plastics, etc.

## Slide 34: Define and Explain recycling of waste and its benefits
Recycling of waste refers to the process of converting waste materials into reusable materials or products instead of disposing of them as garbage
It involves collecting, sorting, processing, and transforming waste items into new products or raw materials that can be used in the manufacturing of other goods
It plays a vital role in sustainable development

## Slide 35: Benefits
Resource Conservation: Recycling helps conserve natural resources such as timber, water, minerals, and energy
By using recycled materials instead of extracting and processing new raw materials, we reduce the need for resource-intensive activities
Energy Savings: Manufacturing products from recycled materials often requires less energy compared to producing them from scratch
Waste Reduction: Recycling reduces the amount of waste sent to landfills or incinerators
By diverting waste from disposal sites, recycling helps mitigate environmental pollution and the associated health risks.

## Slide 36
Environmental Protection: Recycling reduces the need for extracting, processing, and manufacturing new materials, which often contribute to environmental degradation
For instance, mining for raw materials can lead to habitat destruction and water pollution.
Economic Benefits: Recycling offers economic advantages at various levels. It creates job opportunities in recycling industries, waste management, and associated sectors
Additionally, recycling can lead to cost savings for businesses by reducing the need for purchasing new raw materials

## Slide 37
Overall, recycling waste is an essential practice for sustainable waste management and environmental conservation. It conserves resources, saves energy, reduces waste, protects the environment, stimulates the economy, and promotes a more circular and sustainable approach to production and consumption.

## Slide 38
Thank you