## Slide 1
Wired LANs:
Ethernet
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.
Notes: 13.#
<number>
<number>

## Slide 2
Outline
ETHERNET PROTOCOL – IEEE802
Evolution
STANDARD ETHERNET – Characteristics
Addressing
Access method
Efficiency
Implementation
Notes: 13.#
<number>
13.#

## Slide 3
13.<number>
    ETHERNET PROTOCOL
The data-link layer and the physical layer are the territory of the local and wide area networks.
Notes: 13.#
<number>
13.#

## Slide 4
13.<number>
IEEE Project 802
In 1985, the Computer Society of the IEEE started a project, called Project 802, to set standards to enable intercommunication among equipment from a variety of manufacturers.
Project 802 is a way of specifying functions of the physical layer and the data-link layer of major LAN protocols.
Notes: 13.#
<number>
13.#

## Slide 5
13.<number>
Figure IEEE standard for LANs
Notes: 13.#
<number>
13.#

## Slide 6
13.<number>
Ethernet Evolution
The Ethernet LAN was developed in the 1970s by Robert Metcalfe and David Boggs.
42, 46, 45, 70, 57, 43,29, 32, 35,400,26,10,20,74,07,405,409,411
Notes: 13.#
<number>
13.#

## Slide 7
13.<number>
    STANDARD ETHERNET
We refer to the original Ethernet technology with the data rate of 10 Mbps as the Standard Ethernet.
Notes: 13.#
<number>
13.#

## Slide 8
13.<number>
Characteristics
Characteristics of the Standard Ethernet.
10Mbps
CSMA/CD
Coaxial
Min frame size is 512 bits (64 bytes)
Max frame size is 12144 bits (1518 bytes)
2500 meter distance between the furthest stations.
Provides a connectionless service
Unreliable like IP and UDP
Frame get corrupted during transmission and if receiver finds about it , the Ethernet drops the frame silently
Notes: 13.#
<number>
13.#

## Slide 9
13.<number>
Ethernet frame format
Notes: 13.#
<number>
13.#

## Slide 10
Data transmission.
Bytes are from left to right
The bits in each byte are right to left.
Show how the address 47:20:1B:2E:08:EE is sent out online.
Example 13.1
13.<number>
Notes: 13.#
<number>
<number>

## Slide 11
Show how the address 47:20:1B:2E:08:EE is sent out online.
Solution
Example 13.1
13.<number>
Notes: 13.#
<number>
<number>

## Slide 12
13.<number>
Addressing
Each station on an Ethernet network (such as a PC, workstation, or printer) has its own network interface card (NIC).
The NIC fits inside the station and provides the station with a link layer address.
Is of 6 Byte(48 bits) – in hexadecimal notation with colon between the bytes.
Notes: 13.#
<number>
13.#

## Slide 13
13.<number>
Unicast and multicast addresses
Source Address is always Unicast
Destination address can be unicast, multicast and broadcast
Notes: 13.#
<number>
13.#

## Slide 14
Define the type of the following destination addresses:
4A:30:10:21:10:1A
47:20:1B:2E:08:EE
FF:FF:FF:FF:FF:FF
Example 13.2
13.<number>
Notes: 13.#
<number>
<number>

## Slide 15
Define the type of the following destination addresses:
4A:30:10:21:10:1A
47:20:1B:2E:08:EE
FF:FF:FF:FF:FF:FF
Example 13.2
Solution
To find the type of the address, we need to look at the second hexadecimal digit from the left. If it is even, the address is unicast. If it is odd, the address is multicast. If all digits are Fs, the address is broadcast. Therefore, we have the following:
13.<number>
Notes: 13.#
<number>
<number>

## Slide 16
Example 13.2 (continued)
a. This is a unicast address because A in binary is 1010 (even).
b. This is a multicast address because 7 in binary is 0111 (odd).
c. This is a broadcast address because all digits are Fs in
hexadecimal.
13.<number>
Notes: 13.#
<number>
<number>

## Slide 17
13.<number>
Implementation of standard Ethernet
Notes: 13.#
<number>
13.#

## Slide 18
13.<number>
Access Method
Standard Ethernet protocol is a broadcast network, needing an access method for the shared medium.
The standard Ethernet chose CSMA/CD with 1-persistent method.
Notes: 13.#
<number>
13.#

## Slide 19
13.<number>
Efficiency of Standard Ethernet
The practical efficiency of standard Ethernet has been measured to be
a – Number of frames that can fit on the medium
– {Propagation delay / transmission delay}
- a decreases ; Efficiency increases
Notes: 13.#
<number>
13.#

## Slide 20
The standard Ethernet with the transmission rate of 10Mbps; the length of the medium is 2500 m and the size of the frame is 512 bits. The Propagation speed of a signal in the cable is normally 2x10^8 m/s. Calculate the efficiency.
Example 13.3
13.<number>
a = 0.24
Eff = 0.39
Notes: 13.#
<number>
<number>

## Slide 21
13.<number>
Distinguish between Unicast, Multicast
and Broadcast
UNICAST | MULTICAST | BROADCAST
In this transmission all stations receives the frame; the intended recipient keeps and handles the frame; the rest discards it. | All stations will receive the frames; the stations that are members of the group keep and handle it; the rest discard it. | All stations will receive the frame and all stations keeps and handles it.
Notes: 13.#
<number>
13.#

## Slide 22
13.<number>
Standard Ethernet Implementation
The Standard Ethernet defined several implementations, but only four of them became popular during the 1980s.
Notes: 13.#
<number>
13.#

## Slide 23
Summary of Standard Ethernet implementations
13.<number>
Notes: 13.#
<number>
<number>

## Slide 24
13.<number>
Figure 13.6: Encoding in a Standard Ethernet
Notes: 13.#
<number>
13.#

## Slide 25
13.<number>
Figure 13.7: 10Base5 implementation
Notes: 13.#
<number>
13.#

## Slide 26
13.<number>
Figure 13.8: 10Base2 implementation
Notes: 13.#
<number>
13.#

## Slide 27
13.<number>
Figure 13.9: 10Base-T implementation
Notes: 13.#
<number>
13.#

## Slide 28
13.<number>
Figure 13.10: 10Base-F implementation
Notes: 13.#
<number>
13.#