## Slide 1: Digital Communication
(BEC503)

## Slide 2: Module 3 Information Theory

## Slide 3: Syllabus
Information theory:
Introduction, Entropy,
Source Coding Theorem,
Lossless Data Compression Algorithms,
Discrete Memoryless Channels,
Mutual Information,
Channel capacity,
Channel Coding Theorem,
Information Capacity Law (Statement).

## Slide 4: Introduction

## Slide 5: Information theory
The purpose of a communication system is to facilitate the transmission of signals generated by a source of information over a communication channel.
In basic terms, what do we mean by the term information?
To address this important issue, we need to understand the fundamentals of information theory.
In the context of communications, information theory deals with mathematical modelling and analysis of a communication system rather than with physical sources and physical channels.

## Slide 6: Information theory
The information theory has two fundamental questions:
  What level of infinite complexity prevents a signal from being compressed?
  In a noisy channel, what is the maximum transmission rate required for dependable communication?
The answers to these two questions lie in the entropy of a source and the capacity of a channel, respectively:
  Entropy is defined in terms of the probabilistic behaviour of a source of information; it is so named in deference to the parallel use of this concept in thermodynamics.
  Capacity is defined as the intrinsic ability of a channel to convey information; it is naturally related to the noise characteristics of the channel.

## Slide 7: Entropy

## Slide 8: Entropy
Suppose that a probabilistic experiment involves observation of the output emitted by a discrete source during every signalling interval.
The source output is modelled as stochastic process, a sample of which is denoted by the discrete random variable S. This random variable takes on symbols from the fixed finite alphabet
with probabilities
of course, this set of probabilities must satisfy the normalization property

## Slide 9: Entropy
Consider the event S = sk, describing the emission of symbol sk by the source with probability pk, as defined
Clearly, if the probability pk = 1 and pi = 0 for all , then there is no “surprise” and, therefore, no “information” when symbol sk is emitted, because we know what the message from the source must be.
If, on the other hand, the source symbols occur with different probabilities and the probability pk is low, then there is more surprise and, therefore, information when symbol sk is emitted by the source than when another symbol si, I ≠ j with higher probability is emitted.
Thus, the words uncertainty, surprise, and information are all related.

## Slide 10: Entropy
uncertainty, surprise, and information
Before the event S = sk occurs, there is an amount of uncertainty.
When the event S = sk occurs, there is an amount of surprise.
After the occurrence of the event S = sk, there is gain in the amount of information.
Most importantly, the amount of information is related to
the inverse of the probability of occurrence of the event S = sk.

## Slide 11: Entropy
Definition:
The amount of information gained after observing the event S = sk, which occurs with probability pk, as the logarithmic function.
It is often termed “self-information” of the event S = sk.

## Slide 12: Properties of Information Theory
Property 1
Property 2
Property 3
1
2
3
4
Property 4

## Slide 13: Entropy
The base of the logarithm in the equation specifies the units of information measure
If it is 2  unit is BITS (BInary DigiTS)
If it is e  unit is NAT
If it is 10 unit is DECITS or HARTLEYS
It is standard practice in information theory to use a logarithm to base 2 with binary signalling in mind. The resulting unit of information is called the bit, which is a contraction of the words binary digit. Thus we can write

## Slide 14: Entropy
When pk = 1/2, we have I(sk) = 1 bit. We may,
Therefore, we can state that :
One bit is the amount of information that we gain when one of two possible and equally likely
(i.e., equiprobable) events occurs.
Note: The information I(sk) is positive, because the logarithm of a number less than one, such as a probability, is negative. Note also that if pk is zero, then the self-information I(sk) assumes an unbounded value.

## Slide 15: Entropy
The amount of information I(sk) produced by the source during an arbitrary signaling interval depends on the symbol sk emitted by the source at the time. The self-information I(sk) is a discrete random variable that takes on the values I(s0), I(s1), ……, I(sK – 1) with probabilities p0, p1, ………, pK – 1 respectively.
The expectation of I(sk) over all the probable values taken by the random variable S is given by
The quantity H(S) is called
the entropy

## Slide 16: Entropy
Definition :
The entropy of a discrete random variable, representing the output of a source
of information, is a measure of the average information
content per source symbol.

## Slide 17: Properties of Entropy
We find the entropy of the discrete random variable S is bounded as follows:
where K is the number of symbols in the alphabet S.
Elaborating on the two bounds on entropy, we now make two statements:
  1. H(S) = 0, if, and only if, the probability pk = 1 for some k, and the remaining probabilities in the set are all zero; this lower bound on entropy corresponds to no uncertainty.
  2. H(S) = log K, if, and only if, pk = 1/K for all k (i.e., all the symbols in the source alphabet S. are equiprobable); this upper bound on entropy corresponds to maximum uncertainty.

## Slide 18: Properties of Entropy
  Statement 1: H(S) = 0, if, and only if, the probability pk = 1 for some k, and the remaining probabilities in the set are all zero; this lower bound on entropy corresponds to no uncertainty.
  Proof:
First, since each probability pk is less than or equal to unity, it follows that each term pklog2(1/pk) is always nonnegative, so H(S) > 0.
Next, we note that the product term pk log2(1/pk) is zero if, and only if, pk = 0 or 1.
We therefore deduce that H(S) = 0 if, and only if, pk = 0 or 1 for some k and all the rest are zero.

## Slide 19: Properties of Entropy
  Statement 2: H(S) = log K, if, and only if, pk = 1/K for all k (i.e., all the symbols in the source alphabet S. are equiprobable); this upper bound on entropy corresponds to maximum uncertainty.
  Observation:
First, we use of a property of the natural logarithm:
where loge is another way of describing the natural logarithm,
commonly denoted by ln; both notations are used
interchangeably.
Let plot the functions ln x and (x – 1) versus x, as shown
in Figure below:
Here, we see that the line y = x – 1 always lies above the
curve y = logex.
The equality holds only at the point x = 1, where the line is
tangential to the curve.

## Slide 20
  Proof:
1. Consider first any two different probability distributions denoted by p0, p1, ….., pK – 1 and q0, q1, ….. , qK –1 on the alphabet 𝒮 = {s0, s1, …… , sK – 1) of a discrete source.
2. Then define the relative entropy of these two distributions:
3. Hence, changing to the natural logarithm and using the inequality of logex < x – 1, x>=0.
4. We may express the summation on the right-hand side of relative entropy as follows:
5. The sums over pk and qk are both equal to unity.
Thus have the fundamental
property of probability theory:
In words:
The relative entropy of a pair of different discrete
distributions is always nonnegative; it is zero only
when the two distributions are identical.

## Slide 21
If and corresponding to equiprobable symbols,
yields
Hence, invoking the fundamental inequality, we may finally write
Thus, H(S) is always less than or equal to log2K.
This proved statement 2 .

## Slide 22: Example:
Entropy of Bernoulli Random Variable:
Consider the Bernoulli random variable for which symbol 0 occurs with probability p0 and symbol 1 with probability p1 with probability p1=1 – p0.
The entropy of this random variable is
Observation:
1. When p0 = 0, the entropy H(S) = 0; this follows from the fact that x logex 0 as x0
2. When p0 = 1, the entropy H(S) = 0.
3. The entropy H(S) attains its maximum value Hmax = 1 bit when p1 = p0 = 1/2; that is,
when symbols 1 and 0 are equally probable
In other words, H(S) is symmetric about p0 = 1/2.

## Slide 23: Example: Entropy of Bernoulli Random Variable:
We will assign a special symbol to this function
we define
H(p0) as the entropy function
Note:
The H(S) in (1) gives the entropy of the Bernoulli random variable S.
The H(p0) in (2), is a function of the prior probability p0 defined on the interval [0, 1].
Plot the entropy function H(p0) versus p0, defined on the interval [0, 1], as shown in Figure below:
1
2

## Slide 25: Extension of a Discrete Memoryless Source
Assumpltions:
Let us assume it to be Memoryless in the sense that the symbol emitted by the source at any time is independent of previous and future emissions.
Also it is useful to consider blocks rather than individual symbols, with each block consisting of n successive source symbols.
Let view each such block as being produced by an extended source with a source alphabet described by the Cartesian product of a set Sn that has Kn distinct blocks, where K is the number of distinct symbols in the source alphabet S of the original source.
With the source symbols being statistically independent, it follows that the probability of a source symbol in Sn is equal to the product of the probabilities of the n source symbols in S that constitute a particular source symbol of Sn
H(Sn), the entropy of the extended source, is equal to n times H(S), the entropy of the original source. i.e.

## Slide 26: Example:
Entropy of Extended Source:
Consider a discrete memoryless source with source alphabet 𝒮 = {s0, s1, s2}, whose three distinct symbols have the following probabilities:
WKT
Then the entropy of the discrete random variable S representing the source as
H(s)

## Slide 27: Example:
Entropy of Extended Source:
Next , consider the second-order extension of the source, with the source alphabet 𝒮 consisting of three symbols, it follows that the source alphabet of the extended source S(2) has nine symbols.
Consider the below table,

## Slide 28: Example:
Entropy of Extended Source:
Accordingly,
The entropy of the extended source as
Therefore, H(S (2)) = 2H(S)

## Slide 29: Source-coding Theorem

## Slide 30
Now, let us understand the representation of data generated by a discrete source of information.
The process by which this representation is accomplished is called source encoding. The device that performs the representation is called a source encoder.
In particular, if some source symbols are known to be more probable than others, then we may exploit this feature in the generation of a source code by assigning short codewords to frequent source symbols, and long codewords to rare source symbols.
We refer to such a source code as a variable-length code.
Ex: The Morse code, used in telegraphy in the past, is an example of a variable-length code.

## Slide 31
Our primary interest is in the formulation of a source encoder that
satisfies two requirements:
The codewords produced by the encoder are in binary form.
The source code is uniquely decodable, so that the original source sequence can be reconstructed perfectly from the encoded binary sequence.
The second requirement is particularly important: it constitutes the basis for a perfect source code.

## Slide 32: Source encoding
Consider then the scheme shown in Figure below that depicts a discrete Memoryless source whose output sk is converted by the source encoder into a sequence of 0s and 1s, denoted by bk.
We assume that the source has an alphabet with K different symbols and that the kth symbol sk occurs with probability pk, k = 0, 1, ……, K – 1.

## Slide 33: Source encoding
Let the binary codeword assigned to symbol sk by the encoder have length lk, measured in bits.
We define the average codeword length L of the source encoder as
The parameter L represents the average number of bits per source symbol used in the source encoding process.
Let Lmin denote the minimum possible value of L. We then define the coding efficiency of the source encoder as

## Slide 34: Source encoding
The source encoder is said to be efficient when η approaches unity.
The minimum value Lmin is determined by source-coding theorem stated as:
Given a discrete memoryless source whose output is denoted by the random variable S, the entropy H(S) imposes the following bound on the average codeword length L for any source encoding scheme: L ≥ H(S).
According to this theorem, the entropy H(S) represents a fundamental limit on the average number of bits per source symbol necessary to represent a discrete memoryless source, in that it can be made as small as but no smaller than the entropy H(S).
Thus, setting Lmin = H(S), defining the efficiency of a source encoder in terms of the entropy H(S) as shown by where as before we have η< 1.

## Slide 35: Lossless Data Compression Algorithms

## Slide 36: Lossless Data Compression Algorithms
For efficient signal transmission, the redundant information should, therefore, be removed from the signal prior to transmission. This operation, with no loss of information, is ordinarily performed on a signal in digital form, in which case we refer to the operation as lossless data compression.
The code resulting from such an operation provides a representation of the source output that is not only efficient in terms of the average number of bits per symbol, but also exact in the sense that the original data can be reconstructed with no loss of information.
The entropy of the source establishes the fundamental limit on the removal of redundancy from the data.
Basically, lossless data compression is achieved by assigning short descriptions to the most frequent outcomes of the source output and longer descriptions to the less frequent ones.

## Slide 37: Lossless Data Compression Algorithms
Prefix Coding: It is a type of source code that offers the possibility of realizing an average codeword length that can be made arbitrarily close to the source entropy.
Consider a discrete memoryless source of alphabet {s0, s1,…., sK – 1} and respective probabilities {p0, p1,....., pK – 1}.
For a source code representing the output of this source to be of practical use, the code has to be uniquely decodable. This restriction ensures that, for each finite sequence of symbols emitted by the source, the corresponding sequence of codewords is different from the sequence of codewords corresponding to any other source sequence.
A special class of codes satisfying this restriction is known as the prefix condition

## Slide 38: Lossless Data Compression Algorithms
To define the prefix condition, let the codeword assigned to source symbol sk be denoted by (mk1, mk2,…..mkn ), where the individual elements mk1 , mk2,… mkn are 0s and 1s and n is the codeword length.
The initial part of the codeword is represented by the elements for some mk1 , mk2,… mki for i ≤ n.
Any sequence made up of the initial part of the codeword is called a prefix of the codeword.
Thus a prefix code is defined as a code in which no codeword is the prefix of any other codeword.
Prefix codes are also referred to as instantaneous codes

## Slide 39: Lossless Data Compression Algorithms
Illustrative Example of Prefix Coding:
Consider the three source codes described in Table below:
Code I is not a prefix code because the bit 0, the codeword for s0, is a prefix of 00, the codeword for s2.
Likewise, the bit 1, the codeword for s1, is a prefix of 11, the codeword for s3.
Similarly, we may show that code III is not a prefix code but code II is.

## Slide 40: Decoding of Prefix Code
To decode a sequence of codewords generated from a prefix source code, the source decoder simply starts at the beginning of the sequence and decodes one codeword at a time.
Specifically, it sets up what is equivalent to a decision tree, which is a graphical portrayal of the codewords in the particular source code.

## Slide 41: Kraft Inequality
Consider a discrete memoryless source with source alphabet {s0, s1,..., sK – 1} and source probabilities {p0, p1,……., pK –1}, with the codeword of symbol sk having length lk, k = 0, 1,….., K-1.
Then, according to the Kraft inequality, the codeword lengths always satisfy the following inequality:
where the factor 2 refers to the number of symbols in the binary alphabet. The Kraft inequality is a necessary but not sufficient condition for a source code to be a prefix code.
1

## Slide 42: Kraft Inequality
Given a discrete memoryless source of entropy H(S), a prefix code can be constructed with an average codeword length , which is bounded as follows:
The left-hand bound of above equation-2 is satisfied with equality under the condition that symbol sk is emitted by the source with probability
where lk is the length of the codeword assigned to source symbol sk.
A distribution governed by equation-3 pk is said to be a dyadic distribution. For this distribution, we naturally have
2
3
4

## Slide 43: Kraft Inequality
Under this condition, the Kraft inequality of equation-1 confirms that we can construct a prefix code, such that the length of the codeword assigned to source symbol sk is –log2pk.
For such a code, the average codeword length is
and the corresponding entropy of the source is
Hence, in this special case, we find from equ-4 and
and equ-5 that the prefix code is
matched to the source in that
4
5

## Slide 44: Kraft Inequality
Know let us match the prefix code to an arbitrary discrete memoryless source using an extended code.
Let denote the denote the average codeword length of the extended prefix code. For a uniquely decodable code, is the smallest possible.
From equ-2, we find that
or, equivalently,
In the limit, as n approaches infinity, the lower and upper bounds in (5.28) converge as shown by

## Slide 45: Kraft Inequality
We may, therefore, make the statement:
By making the order n of an extended prefix source encoder large enough, we can make the code faithfully represent the discrete memoryless source S as closely as desired.
In other words, the average codeword length of an extended prefix code can be made as small as the entropy of the source, provided that the extended code has a high enough order in accordance with the source-coding theorem

## Slide 46: Kraft Inequality
Know let us match the prefix code to an arbitrary discrete memoryless source using an extended code.
Let denote the denote the average codeword length of the extended prefix code. For a uniquely decodable code, is the smallest possible.
From equ-2, we find that
or, equivalently,
In the limit, as n approaches infinity, the lower and upper bounds in (5.28) converge as shown by

## Slide 47: Huffman Coding
An important class of prefix codes known as Huffman codes.
The basic idea behind Huffman coding is the construction of a simple algorithm that computes an optimal prefix code for a given distribution, optimal in the sense that the code has the shortest expected length.
The end result is a source code whose average codeword length approaches the fundamental limit set by the entropy of a discrete memoryless source, namely H(S).
The essence of the algorithm used to synthesize the Huffman code is to replace the prescribed set of source statistics of a discrete memoryless source with a simpler one. This reduction process is continued in a step-by-step manner until we are left with a final set of only two source statistics (symbols), for which (0, 1) is an optimal code.
Starting from this trivial code, we then work backward and thereby construct the Huffman code for the given source.

## Slide 48: Huffman Coding
The Huffman encoding algorithm proceeds as follows:
  The source symbols are listed in order of decreasing probability. The two source symbols of lowest probability are assigned 0 and 1. This part of the step is referred to as the splitting stage.
  These two source symbols are then combined into a new source symbol with probability equal to the sum of the two original probabilities. (The list of source symbols, and, therefore, source statistics, is thereby reduced in size by one). The probability of the new symbol is placed in the list in accordance with its value.
  The procedure is repeated until we are left with a final list of source statistics (symbols) of only two for which the symbols 0 and 1 are assigned.
The code for each (original) source is found by working backward and tracing the
sequence of 0s and 1s assigned to that symbol as well as its successors.

## Slide 49: Huffman Coding
Huffman Tree

## Slide 50: Huffman Coding
Huffman Tree

## Slide 51: Huffman Coding
Huffman Tree

## Slide 52: Huffman Coding
Huffman Tree

## Slide 53: Huffman Coding
Huffman Tree

## Slide 54: Huffman Coding
Huffman Tree

## Slide 55: Huffman Coding
Huffman Tree

## Slide 56: Huffman Coding
Huffman Tree

## Slide 57: Huffman Coding
Huffman Tree

## Slide 58: Huffman Coding
Huffman Tree
The average codeword length is
The entropy of the specified discrete memoryless source is calculated
as follows

## Slide 59: Huffman coding problem solved in DC Lab
Symbol | Probability
1 | 0.4
2 | 0.1
3 | 0.07
4 | 0.03
5 | 0.2
6 | 0.2
Encode the given symbol
Find the average length of the code
Find Entropy
Efficiency

## Slide 60: Huffman Coding
As a measure of the variability in codeword lengths of a source code, we define the variance of the average codeword length over the ensemble of source symbols as

## Slide 61: Lempel–Ziv Coding
A drawback of the Huffman code is that it requires knowledge of a probabilistic model of the source; unfortunately, in practice, source statistics are not always known a priori.
Moreover, in the modelling of text we find that storage requirements prevent the Huffman code from capturing the higher-order relationships between words and phrases because the codebook grows exponentially fast in the size of each super-symbol of letters (i.e., grouping of letters); the efficiency of the code is therefore compromised.
To overcome these practical limitations of Huffman codes, we may use the Lempel–Ziv algorithm, which is intrinsically adaptive and simpler to implement than Huffman coding.
Basically, the idea behind encoding in the Lempel–Ziv algorithm is described as follows:
  The source data stream is parsed into segments that are the shortest subsequence's not encountered previously.

## Slide 62: Lempel–Ziv Coding
To illustrate this simple yet elegant idea, consider the example of the binary sequence 000101110010100101

## Slide 63: Lempel–Ziv Coding
Encode the following information using LZ algorithm.“ THIS_IS_HIS_HIT”
Index | Symbol | Encoded output
1 | T | 0T
2 | H | 0H
3 | I | 0I
4 | S | 0S
5 | _ | 0_
6 | IS | 3S
7 | _H | 5H
8 | IS_ | 6_
9 | HI | 2I
10 | T_ | 1_

## Slide 64: Lempel–Ziv Coding
Encode the following information using LZ algorithm.“ 101011011010101010
Index | Symbol | Encoded output
1 | 1 | 01
2 | 0 | 00
3 | 10 | 10
4 | 11 | 11
5 | 01 | 21
6 | 101 | 31
7 | 010 | 50
8 | 1010 | 60

## Slide 65: Lempel–Ziv Coding - assgnment qn-1
Encode the following information using LZ algorithm.“
AAABABBBABAABABBBABBABB

## Slide 66: Discrete Memoryless Channels
A discrete memoryless channel is a statistical model with an input X and an output Y that is a noisy version of X; both X and Y are random variables.
Every unit of time, the channel accepts an input symbol X selected from an alphabet 𝒳and, in response, it emits an output symbol Y from an alphabet 𝒴.
The channel is said to be “discrete” when both of the alphabets 𝒳 and 𝒴 have finite sizes.
It is said to be “memoryless” when the current output symbol depends only on the current input symbol and not any previous or future symbol.

## Slide 67: Discrete Memoryless Channels
The channel is described in terms of an input alphabet
and an output alphabet

## Slide 68: Discrete Memoryless Channels
The cardinality of the alphabets 𝒳 and 𝒴, or any other alphabet for that matter, is defined as the number of elements in the alphabet. Moreover, the channel is characterized by a set of transition probabilities
for which, according to probability theory, we naturally have

## Slide 69: Discrete Memoryless Channels
When the number of input symbols J and the number of output symbols K are not large, we may depict the discrete memoryless channel graphically in another way, as shown in Figure.

## Slide 70: Discrete Memoryless Channels
Also, the input alphabet 𝒳 and output alphabet 𝒴 need not have the same size; hence the use of J for the size of 𝒳 and K for the size of 𝒴.
For example,
  In channel coding, the size K of the output alphabet 𝒴 may be larger than the size J of the input alphabet 𝒳; thus, K ≥ J.
  On the other hand, we may have a situation in which the channel emits the same symbol when either one of two input symbols is sent, in which case we have K ≤ J.

## Slide 71: Discrete Memoryless Channels
A convenient way of describing a discrete memoryless channel is to arrange the various transition probabilities of the channel in the form of a matrix
The J-by-K matrix P is called the channel matrix, or stochastic matrix. Note that each row of the channel matrix P corresponds to a fixed channel input, whereas each column of the matrix corresponds to a fixed channel output

## Slide 72: Discrete Memoryless Channels
Suppose now that the inputs to a discrete memoryless channel are selected according to the probability distribution {p(xj), j = 0, 1, …., J – 1}.
In other words, the event that the channel input X = xj occurs with probability
Having specified the random variable X denoting the channel input, we may now specify the second random variable Y denoting the channel output. The joint probability distribution of the random variables X and Y is given by

## Slide 73: Discrete Memoryless Channels
The marginal probability distribution of the output random variable Y is obtained by averaging out the dependence of p(xj, yk) on xj, obtaining
The probabilities p(xj) for j = 0, 1, ……., J – 1, are known as the prior probabilities of the various input symbols. Above equation states:
If we are given the input prior probabilities p(xj) and the stochastic matrix (i.e., the matrix of transition probabilities p(yk|xj)), then we may calculate the probabilities of the various output symbols, the p(yk).

## Slide 74: Binary Symmetric Channel
The binary symmetric channel is of theoretical interest and practical importance.
It is a special case of the discrete memoryless channel with J = K = 2.
The channel has two input symbols (x0 = 0, x1 = 1) and two output symbols (y0 = 0, y1 = 1).
The channel is symmetric because the probability of receiving 1 if 0 is sent is the same as the probability of receiving 0 if 1 is sent.
This conditional probability of error is denoted by p (i.e., the probability of a bit flipping).
The transition probability diagram of a binary symmetric channel is as shown in Figure.
Correspondingly, we may express the stochastic matrix as

## Slide 75: Mutual Information
Given that we think of the channel output Y (selected from alphabet 𝒴) as a noisy version of the channel input X (selected from alphabet 𝒳) and that the entropy H(X) is a measure of the prior uncertainty about X, how can we measure the uncertainty about X after observing Y?

## Slide 76: Mutual Information
To answer this basic question

## Slide 77: Mutual Information
We define the conditional entropy of X selected from alphabet 𝒳, given Y = yk.
Specifically, we write
This quantity is itself a random variable that takes on the values H(X|Y = y0), …., H(X|Y = yK – 1) with probabilities p(y0), ….., p(yK – 1), respectively.
The expectation of entropy H(X|Y = yk) over the output alphabet 𝒴 is therefore given by

## Slide 78: Mutual Information
Conditional Entropy
Definition: The conditional entropy, H(X|Y), is the average amount of uncertainty remaining about the channel input after the channel output has been observed.
The conditional entropy H(X|Y) relates the channel output Y to the channel input X.
The entropy H(X) defines the entropy of the channel input X by itself.
Given these two entropies, we now introduce the definition
which is called the mutual information of the channel

## Slide 79: Mutual Information
To add meaning to this new concept, we recognize that the entropy H(X) accounts for the uncertainty about the channel input before observing the channel output and the conditional entropy H(X|Y) accounts for the uncertainty about the channel input after observing the channel output.
We may, therefore, go on to make the statement:
The mutual information I(X;Y) is a measure of the uncertainty about the channel input,
which is resolved by observing the channel output.
Rather, we may define it in another way,
The mutual information I(Y;X) is a measure of the uncertainty about the channel output
that is resolved by sending the channel input.

## Slide 80: Mutual Information
Properties of Mutual Information
Property 1: The mutual information of a channel is symmetric in the sense that
Property 2: The mutual information is always nonnegative; that is;
Property 3: The mutual information of a channel is related to the joint entropy of the channel input and channel output by
where the joint entropy H(X, Y) is defined by

## Slide 81: Channel Capacity
To proceed, consider a discrete memoryless channel, The mutual information of the channel defined is reproduced here for convenience:
Putting these three equations into a single equation, we write

## Slide 82: Channel Capacity
Careful examination of the double summation in this equation reveals two different probabilities, on which the essence of mutual information I(X;Y) depends:

## Slide 83: Channel Capacity
These two probability distributions are obviously independent of each other. Thus, given a channel characterized by the transition probability distribution {p(yk|xj}, we may now introduce the channel capacity, which is formally defined in terms of the mutual information between the channel input and output as follows:
subjected to 2 constraints
and

## Slide 84: Channel Capacity
Statement:
The channel capacity of a discrete memoryless channel, commonly denoted by
C, is defined as the maximum mutual information I(X;Y) in any single use of the
channel (i.e., signalling interval), where the maximization is over all possible
input probability distributions {p(xj)} on X.

## Slide 85: Binary Symmetric Channel (Revisited)
Consider again the binary symmetric channel, which is described by the transition probability diagram of Figure shown
This diagram is uniquely defined by the conditional probability of error p.
the entropy H(X) is maximized when the channel input probability p(x0) = p(x1) = 1/2, where x0 and x1 are each 0 or 1.
Then channel capacity is given as

## Slide 86: Binary Symmetric Channel (Revisited)
With J = K = 2 and input probabilities,
p(x0) = p(x1) = 1/2,
find the capacity of the binary symmetric channel

## Slide 87: Binary Symmetric Channel (Revisited)
Variation of channel capacity of a binary symmetric channel with transition probability p.
Using the definition of the entropy function introduced
The channel capacity C varies with the probability of error (i.e., transition probability) p in a convex manner as shown in Figure

## Slide 88: Binary Symmetric Channel (Revisited)
Variation of channel capacity of a binary symmetric channel with transition probability p.
We make two observations:
When the channel is noise free, permitting us to set p = 0, the channel capacity C attains its maximum value of one bit per channel use, which is exactly the information in each channel input. At this value of p, the entropy function H(p) attains its minimum value of zero.
When the conditional probability of error p = 1/2 due to channel noise, the channel capacity C attains its minimum value of zero, whereas the entropy function H(p)

## Slide 89: Channel-coding Theorem
The inevitable presence of noise in a channel causes discrepancies (errors) between the output and input data sequences of a digital communication system.
For a relatively noisy channel (e.g., wireless communication channel), the probability of error may reach a value as high as 10–1, which means that (on the average) only 9 out of 10 transmitted bits are received correctly.
For many applications, this level of reliability is utterly unacceptable. Indeed, a probability of error equal to 10–6 or even lower is often a necessary practical requirement. To achieve such a high level of performance, we resort to the use of channel coding.

## Slide 90: Channel-coding Theorem
The design goal of channel coding is to increase the resistance of a digital communication system to channel noise. Specifically, channel coding consists of mapping the incoming data sequence into a channel input sequence and inverse mapping the channel output sequence into an output data sequence in such a way that the overall effect of channel noise on the system is minimized.
The first mapping operation is performed in the transmitter by a channel encoder, whereas the inverse mapping operation is performed in the receiver by a channel decoder, as shown in the block diagram of Figure

## Slide 91: Channel-coding Theorem
The channel encoder and channel decoder in Figure are both under the designer’s control and should be designed to optimize the overall reliability of the communication system. The approach taken is to introduce redundancy in the channel encoder in a controlled manner, so as to reconstruct the original source sequence as accurately as possible.
the message sequence is subdivided into sequential blocks each k bits long, and each k-bit block is mapped into an n-bit block, where n > k. The number of redundant bits added by the encoder to each transmitted block is n – k bits.
The ratio k/n is called the code rate. Using r to denote the code rate, we write
r is less than unity

## Slide 92: Channel-coding Theorem
Does a channel-coding scheme exist such that the probability that a
message bit will be in error is less than any positive number Ꜫ
(i.e., as small as we want it), and yet the channel-coding
scheme is efficient in that the code rate need not be too small?

## Slide 93: Channel-coding Theorem
The answer to this fundamental question is an emphatic “yes.”

## Slide 94: Channel-coding Theorem
The answer to this fundamental question is an emphatic “yes.”
The answer to the question is provided by Shannon’s second theorem in terms of the channel capacity C

## Slide 95: Channel-coding Theorem
The source emits symbols once every Ts seconds.
Hence, the average information rate of the source is H(S)/Ts bits per second.
The decoder delivers decoded symbols to the destination from the source alphabet S and at the same source rate of one symbol every Ts seconds.
The discrete memoryless channel has a channel capacity equal to C bits per use of the channel.
We assume that the channel is capable of being used once every Tc seconds.
Hence, the channel capacity per unit time is C/Tc bits per second, which represents the maximum rate of information transfer over the channel.

## Slide 96: Channel-coding Theorem
To state Shannon’s second theorem, the channel-coding theorem, in two parts as follows:
Let a discrete memoryless source with an alphabet 𝒮 have entropy H(S) for random variable S and produce symbols once every Ts seconds. Let a discrete memoryless channel have capacity C and be used once every Tc seconds, Then, if
there exists a coding scheme for which the source output can be transmitted over the channel and be reconstructed with an arbitrarily small probability of error. The parameter C/Tc is called the critical rate, when above equation is satisfied with the equality sign, the system is said to be signalling at the critical rate.

## Slide 97: Channel-coding Theorem
To state Shannon’s second theorem, the channel-coding theorem, in two parts as follows:
2. Conversely, if
it is not possible to transmit information over the channel and reconstruct it with an arbitrarily small probability of error.
Note:
The channel-coding theorem is the single most important result of information theory.
The theorem specifies the channel capacity C as a fundamental limit on the rate at which the transmission of reliable error-free messages can take place over a discrete memoryless channel.

## Slide 98: Channel-coding Theorem
However, it is important to note two limitations of the theorem:
The channel-coding theorem does not show us how to construct a good code. Rather, the theorem should be viewed as an existence proof in the sense that it tells us that if the condition of is satisfied, then good codes do exist.
The theorem does not have a precise result for the probability of symbol error after decoding the channel output. Rather, it tells us that the probability of symbol error tends to zero as the length of the code increases, again provided that the condition of
is satisfied.

## Slide 99: Information Capacity Law
The information capacity of a continuous channel of bandwidth B hertz, perturbed by AWGN of power spectral density N02 and limited in bandwidth to B, is given by the formula
where P is the average transmitted power

## Slide 100: Information Capacity Law
Another insightful statement:
It is easier to increase the information capacity of a continuous
Communication channel by expanding its bandwidth than
by increasing the transmitted power for a prescribed noise variance.