## Slide 1
Subject Name:
Microwave Engineering & Antenna Theory
Subject Code: BEC701
Course Coordinator:
Assistant Professor
Dept. of E&C, ATME
Guruprasad K N

## Slide 8
Module 1
Microwave Sources and Microwave Transmission Lines

## Slide 11
Microwaves are defined as electromagnetic radiations with a frequency ranging between 300 MHz to 300 GHz. In contrast, the wavelength ranges from 1 mm to around 30 cm.
Microwave radiation is commonly referred to as microwaves.
They fall between infrared radiation and radio waves in the electromagnetic spectrum.
Microwaves

## Slide 12
A transferred electron device (TED), is a form of diode, a two-terminal semiconductor electronic component, with negative differential resistance, used in high-frequency electronics.
A transferred electron device (TED),
Negative Resistance:
Negative Resistance (NR) is a property of some electrical circuits and devices in which an increase in voltage across the device's terminals results in a decrease in electric current through it.

## Slide 13
Difference between microwave transistor and TED(Transfer Electronic Device).
Microwave Transistor | TED (Transfer Electronic Device)
It consists of junctions or gates. | It is not having any junction or gate, it is a bulk type of device
It is fabricated from elemental semiconductor such as Ge and Si | It is fabricated from compound semiconductor such as Gallium Arsenide (GaAS), Indium Phosphide (Inp), and Cadmium Telluride (CdTe)
It operates with low energy "Warm" electrons | It operates with high energy "hot" electrons.
Advantages: Low cost, low power supply, small size | Advantages: Low noise, high gain, low power, reliable, lighter in weight

## Slide 14
GUNN-EFFECT DIODES - GaAs DIODE
Gunn-effect diodes are named after J. B. Gunn, who discovered it in 1963.
Gunn Effect: A periodic fluctuations of current passing through the n-type gallium arsenide (GaAs) specimen when the applied voltage exceeded a certain critical value.

## Slide 16
Fig: Schematic diagram for n-type GaAs diode.
A schematic diagram of a uniform n-type GaAs diode with ohmic contacts at the end surfaces is shown in Fig.

## Slide 17
Gunn-effect diodes are named after J. B. Gunn, who in 1963 discovered a periodic fluctuations of current passing through the n-type gallium arsenide (GaAs) specimen when the applied voltage exceeded a certain critical value (2000-4000 V/cm).
The frequency of oscillations was determined by specimen and not by the external circuit.
The period and oscillations was usually inversely proportional to specimen length and is closely equal to transit time of electrons between electrodes. The drift velocity is over 105 m/sec

## Slide 18
Fig: Drift velocity of electrons in n-type GaAs versus electric field
The Drift velocity is linearly increased from zero to a maximum when the electric field is varied from zero to a threshold value.
When the electric field is beyond the threshold value of 3000 V/cm for the n-type GaAs, the drift velocity is decreased and the diode exhibits negative resistance.
The threshold electric field Eth is given by

## Slide 19
The current fluctuations are shown in Fig
Fig: Current waveform of n-type GaAs

## Slide 20
Problem:
The electric field distribution within a specimen of n-type GaAs of length L = 210 µm and cross-sectional area 3.5 x 10-3 cm2 with a low-field resistance of 16 Ω. Current instabilities occurred at specimen voltages is above 59 V.
Calculate the threshold electric field Eth

## Slide 22
Module 1: Chapter 2
Microwave Transmission Lines
Microwave Frequencies ✓
Microwave devices
Microwave Systems
Transmission Line equations and solutions
Reflection Coefficient and Transmission Coefficient
Standing Wave and Standing Wave Ratio,
Smith Chart
Single Stub matching

## Slide 23
Microwave Frequencies
The term microwave frequencies is generally used for those wavelengths measured in centimeters, roughly from 1 mm to 30 cm (1 to 300 GHZ)
Microwave really indicates the wavelengths in micron ranges.

## Slide 26
Module 1: Chapter 2
Microwave Transmission Lines
Microwave Frequencies ✓
Microwave devices ✓
Microwave Systems
Transmission Line equations and solutions
Reflection Coefficient and Transmission Coefficient
Standing Wave and Standing Wave Ratio,
Smith Chart
Single Stub matching

## Slide 27
Late 1930s: Vacuum Tubes
In 1935: A. A. Heil and O. Heil - Lumped tuned circuit
In 1939: W. C. Hahn and G. F. Metcalf- Velocity Modulation for microwave tubes
In 1939: R.H. Varian and S. F. Varian – Two Cavity klystron amplifier
In 1944: R. Kompfner – Helix type travelling-wave tube (TWT)
In 1963: J.B. Gunn – “Gunn Effect”
In the past two decades, however, microwave solid-state devices such as Tunnel Diodes, Gunn Diodes, Transferred Electron Devices (TEDs), Avalanche transit Time Devices have been developed.
Microwave Devices:

## Slide 28
Microwave Oven
Microwave Devices

## Slide 29
Module 1: Chapter 2
Microwave Transmission Lines
Microwave Frequencies ✓
Microwave devices ✓
Microwave Systems ✓
Transmission Line equations and solutions
Reflection Coefficient and Transmission Coefficient
Standing Wave and Standing Wave Ratio,
Smith Chart
Single Stub matching

## Slide 30
Microwave Systems
Jan 2020
A Microwave system normally consists of a transmitter subsystem, including a microwave oscillator, waveguides, and a transmitting antenna, and a receiver subsystem that includes a receiving antenna, transmission line or waveguide, a microwave amplifier, and a receiver.
Fig: Microwave System

## Slide 31
Thank You