## Slide 1
AUTOMOTIVE ELECTRONICS
MODULE 2 Sensors and Actuators

## Slide 2
AUTOMOTIVE CONTROL SYSTEM APPLICATIONS OF SENSORS AND ACTUATORS

## Slide 3
Variables to Be Measured
1. Mass air flow (MAF) rate
2. Exhaust gas oxygen concentration (possibly heated)
3. Throttle plate angular position
4. Crankshaft angular position/RPM
5. Coolant temperature
6. Intake air temperature
7. Manifold absolute pressure (MAP)
8. Differential exhaust gas pressure
9. Vehicle speed
10. Transmission gear selector position

## Slide 4
The switches include the following:
1. Air conditioner clutch engaged
2. Brake on/off
3. Wide open throttle
4. Closed throttle

## Slide 5
AIR FLOW RATE SENSOR
The majority of cars produced since the early 1990s use a relatively simple and inexpensive mass air flow rate (MAF) sensor
This is normally mounted as part of the air cleaner assembly, where it measures air flow into the intake manifold.

## Slide 7
The Wheatstone bridge consists of three fixed resistors R1, R2, and R3 and a hot-film element having resistance RHW. With no air flow the resistors R1, R2, and R3 are chosen such that voltage va and vb are equal.
As air flows across the hot film, heat is carried away from the film by the moving air.
The amount of heat carried away varies in proportion to the mass flow rate of the air.

## Slide 8
The heat lost by the film to the air tends to
cause the resistance of the film to vary, which unbalances the bridge circuit, thereby producing an input voltage to the amplifier.
The output of the amplifier is connected to the bridge circuit and provides the power for this circuit.

## Slide 9
Strain Gauge MAP Sensor

## Slide 10
One relatively inexpensive MAP sensor configuration is the silicon diaphragm diffused strain gauge sensor shown in Figure 6.3.
This sensor uses a silicon chip that is approximately 3 millimeters square. Along the outer edges, the chip is approximately 250 micrometers (1 micrometer = 1 millionth of a meter) thick, but the center area is only 25 micrometers thick and forms a diaphragm.

## Slide 11
The edge of the chip is sealed to a Pyrex plate under vacuum, thereby forming a vacuum chamber between the plate and the center area of the silicon chip.
The resistors are formed by diffusing a doping impurity into the silicon. External connections to these resistors are made through wires connected to the metal bonding pads.

## Slide 12
This entire assembly is placed in a sealed housing that is connected to the intake manifold by a small diameter tube.
The resistance of the sensing resistors changes in proportion to the applied manifold pressure by a phenomenon that is known as piezoresistivity.
An electrical signal that is proportional to the manifold pressure is obtained by connecting the resistors in a circuit called a Wheatstone bridge, as shown in the schematic of Figure 6.4a

## Slide 14
The resistors diffused into the diaphragm are denoted R1, R2, R3, and R4 in Figure 6.4a.
When there is no strain on the diaphragm, all four resistances are equal, the bridge is balanced, and the voltage between points A and B is zero.
When manifold pressure changes, it causes these resistances to change in such a way that R1 and R3 increase by an amount that is proportional to pressure; at the same time, R2 and R4 decrease by an identical amount

## Slide 15
This unbalances the bridge and a net difference voltage is present between points A and B. The differential amplifier generates an output voltage proportional to the difference between the two input voltages.

## Slide 16
ENGINE CRANKSHAFT ANGULAR POSITION SENSOR
Crankshaft angular position is an important variable in automotive control systems, particularly for controlling ignition timing and fuel injection timing.
Automotive electronics use magnetic or optical phenomena as the physical basis. Magnetic means of such measurements are generally preferred in engine applications since they are unaffected by oil, dirt, or other contaminants.

## Slide 18
On the rear of the crankshaft is a large, heavy, circular steel disk called the flywheel that is connected to and rotates with the crankshaft.
Let’s mark a point on the flywheel, as shown in Figure 6.5, and draw a line through this point and the axis of rotation. Let’s draw another line through the axis of rotation parallel to the horizontal center line of the engine as a reference line.
The crankshaft angular position is the angle between the reference line and the mark on the flywheel.

## Slide 19
Crankshaft angular position can be sensed directly at the camshaft, since the camshaft rotates at exactly one-half the speed of the crankshaft.

## Slide 20
Magnetic Reluctance Position Sensor

## Slide 21
In the magnetic reluctance position sensor, a coil wrapped around the magnet senses the changing intensity of the magnetic field as the tabs of a ferrous disk pass between the poles
of the magnet.
This sensor consists of a permanent magnet with a coil of wire wound around it.
A steel disk that is mounted on the crankshaft (usually in front of the engine) has tabs that pass between the pole pieces of this magnet.

## Slide 22
This sensor is of the magnetic reluctance type and is based on the concept of a magnetic circuit. A magnetic circuit is a closed path through a magnetic material (e.g., iron, cobalt, nickel, or synthetic magnetic material called ferrite).

## Slide 24
The voltage generated by the magnetic reluctance position sensor is determined by the strength of the magnetic flux. When a tab on the steel disk passes through the gap, the flow of the magnetic flux changes significantly
The voltage induced in the sensing coil varies with the rate of change of the magnetic flux. When the tab is centered between the poles of the magnet, the voltage is zero because the flux is not changing.

## Slide 26
Engine Speed Sensor

## Slide 27
As the camshaft rotates, the notch passes under the sensor once for every two crankshaft revolutions.
The magnetic flux abruptly decreases, then increases as the notch passes the sensor.
This generates a voltage pulse that can be used in electronic control systems for timing purposes.

## Slide 28
Hall-Effect Position Sensor
The Hall element is a thin slab of semiconductor material that is placed between the magnets so it can sense the magnetic flux variations as the tab passes. A constant current is passed through the semiconductor in one direction, and a voltage is generated that varies with the strength of the magnetic flux.

## Slide 30
The Hall Effect
The Hall element is a small, thin, flat slab of semiconductor material. When a current, I, is passed through this slab by means of an external circuit as shown in Figure 6.11a, a voltage is developed across the slab perpendicular to the direction of current flow and perpendicular to the direction of magnetic flux.
This voltage is proportional to both the current and magnetic flux density that flows through the slab.
the generation of a voltage that is dependent on a magnetic field—is called the Hall effect.

## Slide 32
Whenever an electron moves through a magnetic field, a force (called the Lorentz force) that is proportional to the electron velocity and the strength of the magnetic flux is exerted on the electron.
The direction of this force is perpendicular to the direction in which the electron is moving.
the Lorentz force direction is such that the electrons
are deflected toward the lower sense electrode. Thus, this electrode is more negative than the upper electrode and a voltage exists between the electrodes, having the polarity

## Slide 33
Shielded-Field Sensor

## Slide 34
Here the hall element normally exposed to a magnetic field and produces an output voltage.
When one of the tabs passes between the magnet and the sensor element, the low reluctance of the tab and disk provides a path for the magnetic flux that bypasses the Hall-effect sensor element, and the sensor output drops to near zero.

## Slide 35
Optical Crankshaft Position Sensor

## Slide 36
In the optical crankshaft position sensor, a disk coupled to the crankshaft has holes to pass light between the LED and the phototransistor. An output pulse is generated as each hole passes the LED.
The hole in the disk allows transmission of light through the light pipes from the light-emitting diode (LED) source to the phototransistor used as a light sensor.

## Slide 37
Light would not be transmitted from source to sensor when there is no hole because the solid disk blocks the light
the pulse of light is detected by the phototransistor and coupled to an amplifier to obtain a satisfactory signal level.
The output pulse level can very easily be standard transistor logic levels of +2.4 V for the high level and +0.8 V for the low level.

## Slide 38
One of the problems with optical sensors is that they must be protected from dirt and oil; otherwise, they will not work properly.
They have the advantages that they can sense position without the engine running and that the pulse amplitude is constant with variation in speed.

## Slide 39
THROTTLE ANGLE SENSOR

## Slide 40
Most throttle angle sensors are essentially potentiometers. A potentiometer consists of a resistor with a movable contact, as illustrated in Figure 6.15.
A section of resistance material is placed in an arc around the pivot axis for the movable contact.
One end of the resistor is connected to ground, the other to a fixed voltage V (e.g., 5 volts).

## Slide 41
The voltage at the contact point of the movable contact is proportional to the angle (a) from the ground contact to the movable contact. Thus,

## Slide 42
This potentiometer can be used to measure any angular rotation. In particular, it is well suited for measuring throttle angle.
The only disadvantage to the potentiometer for automotive applications is its analog output. For digital engine control, the voltage v(a) must be converted to digital format using an analog-to-digital converter.

## Slide 43
TEMPERATURE SENSORS
Typical Coolant Sensor
One kind of coolant sensor uses at temperature -sensitive semiconductor called a thermistor. The sensor is typically connected as a varying resistance across a fixed reference voltage. As the temperature increases, the output voltage decreases.

## Slide 45
A typical coolant sensor, shown in Figure 6.16, consists of a thermistor mounted in a housing that is designed to be inserted in the coolant stream.
This housing is typically threaded with pipe threads that seal the assembly against coolant leakage.
A thermistor is made of semiconductor material whose resistance varies inversely with temperature. For example, at -40°C a typical coolant sensor has a resistance of 100,000 ohms. The resistance decreases to about 70,000 ohms at 130°C.

## Slide 47
Exhaust Gas Oxygen Sensor
This sensor is often called a lambda sensor from the Greek letter lambda , which is commonly used to denote the equivalence ratio:

## Slide 48
Whenever the air/fuel ratio is atstoichiometry, the value for l is 1. When the air–fuel mixture is too lean, the condition is represented by lambda greater than one (denoted l > 1). Conversely, when the air–fuel mixture is too rich, the condition is represented by an equivalence ratio of lambda less than one (l < 1).