## Slide 1
Introduction to Non-Traditional Machining
BME755A
Introduction to Non-Traditional Machining
Mr. HEMANTH B R
Assistant Professor,
Dept. of Mechanical Engineering,
ATMECE, Mysuru

## Slide 2
COURSE SYLLABUS
Course Code | BME755A | CIE Marks | 50
Number of Lecture Hours/Week | 03 Hours | SEE Marks | 50
RBT Levels | L1, L2, L3 | Exam Hours | 03
Credits – 03 |  |  | 
Course Objectives:
To learn various concepts related to modern machining processes & their applications.
To appreciate the differences between conventional and non-conventional machining processes.
To acquire a functional understanding of non-traditional manufacturing equipment.
To know about various process parameters and their influence on performance and their applications.
To impart knowledge on various types of energy involved in non-traditional machining processes.

## Slide 3
MODULE 1 - INTRODUCTION
Introduction to Non-traditional machining, Need for Non-traditional machining process, Comparison between traditional and non-traditional machining, general classification Non- traditional machining processes, classification based on nature of energy employed in machining, selection of non-traditional machining processes, Specific advantages, limitations and applications of non-traditional machining processes.
Syllabus of Non-Traditional Machining (NTM)
MODULE 2
Ultrasonic Machining (USM): Introduction, Equipment and material process, Effect of process parameters: Effect of amplitude and frequency, Effect of abrasive grain diameter, effect of slurry, tool & work material. Process characteristics: Material removal rate, tool wear, accuracy, surface finish, applications, advantages & limitations of USM.
Abrasive Jet Machining (AJM): Introduction, Equipment and process of material removal, process variables: carrier gas, type of abrasive, work material, stand-off distance (SOD). Process characteristics-Material removal rate, Nozzle wear, accuracy & surface finish. Applications, advantages & limitations of AJM.

## Slide 4
MODULE 3
ELECTROCHEMICAL MACHINING (ECM)
Introduction, Principle of electro chemical machining: ECM equipment, elements of ECM operation, Chemistry of ECM. ECM Process characteristics: Material removal rate, accuracy, surface finish.
Process parameters: Current density, Tool feed rate, Gap between tool & work piece, velocity of electrolyte flow, type of electrolyte, its concentration temperature, and choice of electrolytes. ECM Tooling: ECM tooling technique & example, Tool & insulation materials.
Applications ECM: Electrochemical grinding and electrochemical honing process. Advantages, disadvantages and application of ECG, ECH
CHEMICAL MACHINING (CHM)
Elements of the process: Resists (maskants), Etchants. Types of chemical machining process- chemical blanking process, chemical milling process.
Process characteristics of CHM: material removal rate, accuracy, surface finish, advantages, limitations and applications of chemical machining process
Syllabus of Non-Traditional Machining (NTM)

## Slide 5
MODULE 4
ELECTRICAL DISCHARGE MACHINING (EDM)
Introduction, mechanism of metal removal, EDM equipment: spark erosion generator (relaxation type), dielectric medium-its functions & desirable properties, electrode feed control system. Flushing types; pressure flushing, suction flushing, side flushing, pulsed flushing. EDM process parameters: Spark frequency, current & spark gap, surface finish, Heat Affected Zone. Advantages, limitations & applications of EDM, Electrical discharge grinding, Traveling wire EDM.
PLASMA ARC MACHINING (PAM)
Introduction, non-thermal generation of plasma, equipment mechanism of metal removal, Plasma torch, process parameters, process characteristics. Safety precautions. Safety precautions, applications, advantages and limitations.
Syllabus of Non-Traditional Machining (NTM)

## Slide 6
MODULE 5
LASER BEAM MACHINING (LBM)
Introduction, generation of LASER, Equipment and mechanism of metal removal, LBM parameters and characteristics, Applications, Advantages & limitations.
ELECTRON BEAM MACHINING (EBM)
Introduction, Principle, equipment and mechanism of metal removal, applications, Advantages & limitations.
Syllabus of Non-Traditional Machining (NTM)

## Slide 7
Course Outcomes
Understand and compare traditional and non-traditional machining process and recognize the need for Non-traditional machining process.
Understand the constructional features, performance parameters, process characteristics, applications, advantages and limitations of USM and AJM.
Identify the need of Chemical and electro-chemical machining process along with the constructional features, process parameters, process characteristics, applications, advantages and limitations.
Understand the constructional feature of the equipment, process parameters, process characteristics, applications, advantages and limitations EDM & PAM.
Understand the LBM equipment, LBM parameters, and characteristics. EBM equipment and mechanism of metal removal, applications, advantages and limitations LBM & EBM..

## Slide 8
CO –PO Mapping
Subject Code: | BME755A |  | TITLE: Introduction to Non-Traditional Machining |  |  |  |  |  |  | Faculty Name: |  |  | Mr. Hemanth B R
List of Course Outcomes | Program Outcomes |  |  |  |  |  |  |  |  |  |  |  | Total
 | PO1 | PO2 | PO3 | PO4 | PO5 | PO6 | PO7 | PO8 | PO9 | PO10 | PO11 | PO12 | 
CO-1 | 2 | 3 | - | - | - | - | - | - | - | - | 2 | 2 | 9
CO-2 | 2 | 3 | - | - | - | - | 3 | - | - | - | 2 | 2 | 12
CO-3 | 2 | 3 | - | - | - | - | 3 | - | - | - | 2 | 2 | 12
CO-4 | 2 | 3 | - | - | - | - | 3 | - | - | - | 2 | 2 | 12
CO-5 | 2 | 3 | - | - | - | - | 3 | - | - | - | 2 | 2 | 12
Total | 10 | 15 | - | - | - | - | 12 | - | - | - | 10 | 10 | 57

## Slide 9
Module 1
INTRODUCTION

## Slide 10
Non-traditional Processes Definition
A group of processes that remove excess material by various techniques involving mechanical, thermal, electrical, or chemical energy (or combinations of these energies) but do not use a sharp cutting tool in the conventional sense

## Slide 11
Non-traditional Machining Processes
Manufacturing processes can be broadly divided into two groups:
Primary Manufacturing Processes : Provide basic shape and size
Secondary Manufacturing Processes : Provide final shape and size with tighter control on dimension, surface characteristics

## Slide 12
Material removal processes once again can be divided into two groups
Conventional Machining Processes
Non-Traditional Manufacturing Processes or non-conventional Manufacturing processes
Conventional Machining Processes mostly remove material in the form of chips by applying forces on the work material with a wedge shaped cutting tool that is harder than the work material under machining condition

## Slide 13
Conventional Machining Processes mostly remove material in the form of chips by applying forces on the work material with a wedge shaped cutting tool that is harder than the work material under machining condition
The major characteristics of conventional machining are:
Generally macroscopic chip formation by shear deformation
Material removal takes place due to application of cutting forces – energy domain can be classified as mechanical
Cutting tool is harder than work piece at room temperature as well as under machining conditions

## Slide 14
Major characteristics of Non-conventional machining
Material removal may occur with chip formation or even no chip formation may take place. For example in AJM, chips are of microscopic size and in case of Electrochemical machining material removal occurs due to electrochemical dissolution at atomic level.
In NTM, there may not be a physical tool present. For example in laser jet machining, machining is carried out by laser beam. However in Electrochemical Machining there is a physical tool that is very much required for machining.
In NTM, the tool need not be harder than the work piece material. For example, in EDM, copper is used as the tool material to machine hardened steels.
Mostly NTM processes do not necessarily use mechanical energy to provide material removal. They use different energy domains to provide machining. For example, in USM, AJM, WJM mechanical energy is used to machine material, whereas in ECM electrochemical dissolution constitutes material removal.

## Slide 15
Traditional vs Non Traditional Machining
 | Conventional Process | Non-Conventional Process
1 | The cutting tool and work piece are always in physical contact with relative motion with each other, which results in friction and tool wear. | There is no physical contact between the tool and work piece, In some non-traditional process tool wear exists.
2 | Material removal rate is limited by mechanical properties of work material. | NTM can machine difficult to cut and hard to cut materials like titanium, ceramics, nimonics, SST, Composites materials.
3 | Relative motion between the tool and work is typically rotary or reciprocating. Thus the shape of work is limited to circular or flat shapes. In spite of CNC systems, production of 3D surfaces is still a difficult task. | Many NTM are capable of producing complex 3D shapes and cavities.
4 | Machining of small cavities, slits, blind holes or through holes are difficult | Machining of small cavities, slits and Production of non-circular, micro sized, large aspect ratio, shall entry angle holes are easy using NTM

## Slide 16
Traditional vs Non Traditional Machining
 | Conventional Process | Non-Conventional Process
5 | Use relative simple and inexpensive machinery and readily available cutting tools | Non-traditional processes requires expensive tools and equipment as well as skilled labour, which increase the production cost significantly
6 | Capital cost and maintenance cost is low | Capital cost and maintenance cost is high
7 | Traditional processes are well established and physics of process is well understood | Mechanics of Material removal of Some of NTM process are still under research
8 | Conventional process mostly uses mechanical energy | Most NTM uses energy in direct form For example : laser, Electron beam in its direct forms are used in LBM and EBM respectively
9 | Surface finish and tolerances are limited by machining inaccuracies | High surface finish(up to 0.1 micron) and tolerances (25 Microns) can be achieved
10 | High metal removal rate. | Low material removal rate.

## Slide 17
Classification of unconventional machining process
Mechanical ‑ erosion of work material by a high velocity stream of abrasives or fluid (or both) is the typical form of mechanical action
Electrical ‑ electrochemical energy to remove material (reverse of electroplating)
Thermal – thermal energy usually applied to small portion of work surface, causing that portion to be removed by fusion and/or vaporization
Chemical – chemical etchants selectively remove material from portions of workpart, while other portions are protected by a mask

## Slide 18
Classification of Unconventional Machining Process
1. Mechanical Processes
  Abrasive Jet Machining (AJM)
  Ultrasonic Machining (USM)
  Water Jet Machining (WJM)
  Abrasive Water Jet Machining (AWJM)
2. Electrochemical Processes
  Electrochemical Machining (ECM)
  Electro Chemical Grinding (ECG)
  Electro Jet Drilling (EJD)
3. Electro-Thermal Processes
  Electro-discharge machining (EDM)
  Laser Jet Machining (LJM)
  Electron Beam Machining (EBM)
4. Chemical Processes
  Chemical Milling (CHM)
  Photochemical Milling (PCM)

## Slide 19
Classification of Unconventional Machining Process

## Slide 28
Classification of NTM Process

## Slide 29
Classification of NTM Process

## Slide 30
Classification of Non Traditional Machining Process
Mechanical Metal removal Processes
It is characterized by the fact that the material removal is due to the application of mechanical energy in the form of high frequency vibrations or kinetic energy of an abrasive jet.
Ultra sonic Machining (USM).
Abrasive Jet Machining (AJM).
Water Jet Machining (WJM).

## Slide 31
Electro-Chemical
It is based on electro-chemical dissolution of materials by an electrolyte under the influence of an externally applied electrical potential.
Electro-Chemical Machining (ECM).
Electro-Chemical Grinding (ECG)
Electro-Chemical Drilling (ECD)
Thermal Method
The material is removed due to controlled, localized heating of the work piece. It result into material removal by melting and evaporation. The source of heat generation in such cases can be widely different.
Electric Discharge Machining (EDM).
Plasma Arc Machining (PAM).
Electron Beam Machining (EBM)
Laser Beam Machining (LBM0

## Slide 32
Need for Non Traditional Machining
Extremely hard and brittle materials or Difficult to machine materials are difficult to machine by traditional machining processes.
When the workpiece is too flexible or slender to support the cutting or grinding forces.
When the shape of the part is too complex.
Intricate shaped blind hole – e.g. square hole of 15 mmx15 mm with a depth of 30 mm
Deep hole with small hole diameter – e.g. φ 1.5 mm hole with l/d = 20
Machining of composites.

## Slide 33
SELECTION OF PROCESS
Physical parameters of the process
Shape to be machined
Process capability
Economics of the processes

## Slide 34
Physical parameters of the process

## Slide 35
Physical parameters of the process

## Slide 36
Shape to be machined

## Slide 37
Shape to be machined

## Slide 38
Material Applications

## Slide 39
Material Applications

## Slide 40
Process capability

## Slide 41
Economics of the processes

## Slide 42
Process capability

## Slide 43
Economics of the processes

## Slide 44
Advantages of Non-Traditional Machining (NTM):
Machining Hard and Brittle Materials – Can machine very hard, tough, and brittle materials (tungsten, carbides, ceramics, composites, superalloys) which are difficult/impossible with conventional methods.
Complex Shapes and Intricate Features – Suitable for producing fine holes, slots, contours, and 3D shapes that are difficult to achieve with traditional machining.
No Direct Tool-Work Contact – Processes like EDM, LBM, ECM avoid physical tool-work contact, reducing cutting forces, tool wear, and mechanical stresses.
High Precision and Surface Finish – Capable of achieving close tolerances (few microns) and good surface finish.
Minimal Heat-Affected Zone (HAZ) – Some processes (e.g., AWJM, USM) have negligible thermal effects on the workpiece.
Micro-Machining Capability – Can be used to produce micro-features, thin slots, fine holes, and miniature components for aerospace, electronics, and medical industries.
Ability to Machine Thin/Delicate Parts – No mechanical force allows safe machining of fragile parts without distortion.
Automation Friendly – Easily integrated with CNC and robotics for precise, unmanned operations.

## Slide 45
Limitations of Non-Traditional Machining (NTM):
High Initial and Operating Cost – Equipment is expensive, requires skilled operators, and sometimes costly consumables (electrodes, abrasives, gases).
Low Material Removal Rate (MRR) – Generally slower compared to conventional machining, hence not suitable for bulk material removal.
Limited Workpiece Size – Some processes are restricted to small or thin components (e.g., EDM, ECM, USM).
Specialized Power Requirements – Needs high electrical energy, lasers, or water jet systems.
Tool Wear Issues – In EDM, USM, AWJM, tool or nozzle wear can affect accuracy and cost.
Surface Integrity Problems – Some processes may cause micro-cracks, recast layers, or residual stresses (e.g., EDM, LBM).
Complex Setup and Maintenance – Requires precise control systems, cooling, flushing, and maintenance.
Environmental and Safety Concerns – Use of chemicals (ECM), high-pressure water (AWJM), and lasers can pose hazards.

## Slide 46
Applications of Non-Traditional Machining (NTM):
Aerospace Industry
Machining of superalloys, titanium, and composites used in turbine blades, nozzles, and engine parts.
Drilling of cooling holes in turbine blades (EDM, LBM, ECM).
Automobile Industry
Precision machining of fuel injectors, engine components, gears, and molds.
Surface texturing for improved wear resistance.
Electronics & Microelectronics
Fabrication of micro-circuits, PCBs, and semiconductor components.
Production of micro-holes and fine slots for sensors and connectors.
Energy Sector
Machining of turbine components for power plants.
Processing of nuclear reactor parts requiring high precision.

## Slide 47
Applications of Non-Traditional Machining (NTM):
Medical & Biomedical Applications
Machining of surgical instruments, orthopedic implants, stents, and dental devices.
Micro-machining of delicate, biocompatible materials (titanium, stainless steel).
Tool & Die Making
EDM and ECM are widely used for producing dies, molds, punches, and intricate cavities.
Hard materials (carbides, HSS) can be machined with high accuracy.
Defense & Military Applications
Precision machining of missile components, nozzles, and guidance systems.
Cutting and drilling of hardened materials used in defense hardware.
General Engineering Applications
Cutting of hard/brittle materials (ceramics, glass, quartz).
Engraving, marking, and surface modification using laser machining.
Cleaning and finishing of delicate or heat-sensitive materials.

## Slide 48
Advantages of Non-conventional machining
High accuracy and surface finish
Less/no wear
Tool life is more
Quieter operation
Disadvantages of Non-conventional machining
High cost.
Complex set-up.
Skilled operator required.