## Slide 1
Department of Computer Science and Engineering
SUBJECT TITLE : DIGITAL DESIGN AND COMPUTER ORGANIZATION (BCS302)
SEMESTER : III
MODULE 3
Bhavya Dechamma K S
Assistant Professor
Dept of CS&E, ATME

## Slide 2
2.4 Instruction and Instruction sequencing
Register Transfer Notation
Assembly Language Notation
Basic Instruction Types
Instruction Execution and straight line sequencing
Branching
Condition Codes
Generating memory address
2.5 Addressing Modes
Implementation of variable and constants
Indirection and pointers
Indexing and arrays
Relative addressing
Additional Modes

## Slide 3
2.4 Instruction and Instruction sequencing
Instructions are commands for a computer to perform an operation, while instruction sequencing is the process of executing these instructions in a specific order.
Instruction include an operation code (what to do) and operands (the data to operate on)
Basic Types of operation:
  Data transfer: Move data between memory, registers, and I/O devices.
  Arithmetic/Logic: Perform calculations and logical operations.
  Program control/Sequencing: Change the flow of execution
  I/O control: Handle input and output operations.

## Slide 4
Instruction sequencing
The instruction cycle: process the CPU follows to execute an instruction.
It consists of these phases:
Fetch: The computer provides the memory address to retrieve the next instruction.
Decode: The CPU determines what operation the instruction is asking it to perform.
Execute: The actual operation is performed.

## Slide 5
2.4.1 Register Transfer Notation
The data transfers can be represented by standard notations:
Processor registers are represented by notations R0, R1, R2,... and so on.
The addresses of the memory locations are represented by names such as LOC, PLACE, MEM, etc.
I/O registers are represented by names such as DATAIN, DATAOUT and so on.
The contents of register or memory location are denoted by placing square brackets around the name of the register or memory location.

## Slide 6
Examples:
R2 ← [LOC] ------------contents of memory location LOC are transferred into the processor register R2.
R3 ← [R1] + [R2] --------- contents of registers R1and R2 are added and the result is stored into the register R3.
[LOC] ← [R1] - [R2] ------- contents of the register R2 is subtracted from register R1 and the result is stored into the memory location LOC

## Slide 7
2.4.2 Assembly Language Notations
Assembly language notations are another type of notations used to represent machine instructions and programs.
These notations use assembly language formats. However, register names, names of memory locations are same as that of register notations.

## Slide 8
Examples:
MOVE R2, R1 ------ contents of processor register R2 are transferred to processor register R1
ADD R1, R2, R3 ------ contents of processor registers R1 and R2 are added and the result is stored in the register R3
Note: The assembly language notations has three fields: Operation, source and destination having their positions from left to right.

## Slide 9
2.4.3 Basic Instruction Types
Each instruction of the CPU contain specific information fields, which are required to execute it. These information fields of instructions are called elements of instruction.
These are:
Operation code : The operation code in the instruction specifies the operation to be performed.
Source / Destination operand: The source/destination operand field specifies the source/destination operand for the instruction.
Next instruction address: The next instruction address tells the CPU from where to fetch the next instruction after completion of execution of current instruction.

## Slide 10
Computers may have instructions of several different lengths. According to address reference there are:
Three address instructions
Two address instructions
One address instruction
Zero address instructions

## Slide 11
1. Three address instructions
Ex: ADD A, B, C
The general instruction format for three address instruction is:
Operation Source 1, Source 2, Destination
2. Two address instructions
Ex: ADD A, B
The general instruction format for two address instruction is:
Operation Source, Destination

## Slide 12
3. One address instruction
Ex: ADD B
The general instruction format for one address instruction is
Operation Source
4. Zero address instructions - These instructions do not specify any operands or addresses. Instead, they operate on data stored in registers or memory locations implicitly defined by the instruction.

## Slide 13
Example 1: Write a program to evaluate the arithmetic statement Y = (A+B) * (C+D) using three-address, two-address, one-address and zero-address instructions.
Using three address instructions
ADD A, B,R1 ; R1←M[A] + M[B]
ADD C, D,R2 ; R2←M[C] + M[D]
MUL R1, R2,Y ; M[Y]← R1 * R2
Solution:
Remember:
Always use minimum number of instructions
Registers can be reused

## Slide 14
Using two address instructions
MOV A, R1 ; R1←M[A]
ADD B, R1 ; R1←R1 + M[B]
MOV C, R2 ; R2←M[C]
ADD D, R2 ; R2←R2+ M[D]
MUL R2, R1 ; R1← R1* R2
MOV R1, Y ; [Y]← R1
Y = (A+B) * (C+D)

## Slide 15
Y = (A+B) * (C+D)
Using one address instruction
LOAD A ; AC←M[A]
ADD B ; AC←AC+M[B]
STORE T ; M[T]←AC
LOAD C ; AC←M[C]
ADD D ; AC←AC+M[D]
MUL T ; AC←AC*M[T]
STORE Y ; M[Y]←AC

## Slide 16
Using zero address instructions
PUSH A ; TOS←A
PUSH B ; TOS←B
ADD ; TOS←(A+B)
PUSH C ; TOS←C
PUSH D ; TOS←D
ADD ; TOS←(C+D)
MUL ; TOS←(C+D)*(A+B)
POP Y ; M[Y]←TOS
Postfix: AB + CD + *
Y = (A+B) * (C+D)

## Slide 17
Example 2: X = A×B + C×C
Using three address instructions
MUL A, B, R1 ; R1←M[A]*M[B]
MUL C, C, R2 ; R2←M[C]+M[C]
Add R1, R1, X ; M[X]←R1*R2
Solution:

## Slide 18
Using two address instructions
MOV A, R1 ; R1←M[A]
MUL B, R1 ; R1←R1*M[B]
MOV C, R2 ; R2←M[C]
MUL C, R2 ; R2←R2*M[C]
ADD R2, R1 ; R1←R1+R2
MOV R1, X ; M[X]←R1
X = A×B + C×C

## Slide 19
Using one address instruction
LOAD A ; AC← M[A]
MUL B ; AC←AC* M[B]
STORE T ; M[T] ←AC
LOAD C ; AC← M[C]
MUL C ; AC←AC* M[C]
ADD T ; AC←AC + M[T]
STORE X ; M[X] ← AC
X = A×B + C×C

## Slide 20
Using zero address instruction
Postfix: AB*CC*+
X = A×B + C×C
PUSH A ; TOS ← A
PUSH B ; TOS ← B
MUL ; TOS ← (A*B)
PUSH C ; TOS ← C
PUSH C ; TOS ← C
MUL ; TOS ← (C*C)
ADD ; TOS ← (C*C) + (A*B)
POP X ; M[X] ← TOS

## Slide 21
QP: Mention four types of operations to be performed by instructions in a computer. Explain the basic types of instruction formats to carry out. C ← [A] + [B]
Answer:
  four types of operations: Data transfer, Arithmetic/Logic, Program control/Sequencing and I/O control. Basic types of instruction formats: Three-address, two-address, one-address, and zero-address instruction formats.
Three-address instructions specify two source operands and one destination operand.
The expression C ← [A] + [B] written as
ADD A, B, C.
Two-address instructions typically specify one source and one destination operand. The destination usually overwrites one of the source operands.
MOV B, C (Move B to C)
ADD A, C (Add A to C, result stored in C)

## Slide 22
One-address instructions use an implied accumulator register for one operand and the result.
LOAD A (Load A into the accumulator)
ADD B (Add B to the accumulator)
STORE C (Store the accumulator content in C)
Zero-address instructions use a stack structure, where all operands are implicitly popped from the stack and the result is pushed back onto the stack.
PUSH A
PUSH B
ADD (Pops A and B, pushes result)
POP C

## Slide 23
2.4.4 Instruction Execution and straight line sequencing
Fig: A program for C ← [A] + [B]

## Slide 24
2.4.5 Branching
Every time it is not possible to store a program in the consecutive memory locations.
In such cases we can not use straight-line sequencing. Here, we have to use branch instructions to transfer the program control from one straight-line sequence to another straight-line sequence of instruction

## Slide 25
Fig: A straight-line program to add n numbers

## Slide 26
Fig: Using a loop to add n numbers
Here, the location N stores the value of n
Register R1 is used as a counter to determine the number of times the loop gets executed.
The contents of the location N are moved into R1 at the start of the program execution.
After that, the register R0 is cleared
The address LOOP is reloaded again and again until R1 becomes 0.
Every time a number is added, the R1 value is decremented.
When R1 becomes 0, we come out of the loop and the result which is stored at R0 is copied into memory location SUM.

## Slide 27
2.4.6 Condition Codes
The processor keeps track of information on all the operations. This is accomplished by recording the required information in individual bits called the condition code flags.
The condition code flags are stored in the status registers. The status register is also referred to as flag register.
The condition code flags are set to 1 or cleared to 0, depending on the operation performed.
The commonly used flags are
N (negative) – Set to 1 if the result is negative, otherwise, cleared to 0
Z (zero) – Set to 1 if the result is 0; otherwise, cleared to 0
V (overflow) – Set to 1 if arithmetic overflow occurs; otherwise, cleared to 0
C (carry) – Set to 1 if a carry-out results from the operation; otherwise, cleared to 0

## Slide 28
2.4.7 Generating memory address
The address of the memory can be specified directly within the instruction.
Ex: MOV [2000H], R1
In this instruction the memory address is fix; it can not be dynamically changed in the program itself.
There are some situations where we need to change the memory address dynamically.

## Slide 29
2.5 Addressing Modes
The various formats of representing location of an operand in an instruction or address of an operand is called as “Addressing Mode”.
The different types of Addressing Modes are:
Register Addressing
Direct Addressing
Immediate Addressing
Indirect Addressing
Index Addressing
f) Relative Addressing
g) Auto Increment Addressing
h) Auto Decrement Addressing