## Slide 1
Department of Computer Science and Engineering
SUBJECT TITLE : DIGITAL DESIGN AND COMPUTER ORGANIZATION (BCS302)
SEMESTER : III
MODULE 4: INPUT/OUTPUT ORGANIZATION
Bhavya Dechamma K S
Assistant Professor
Dept of CS&E, ATME

## Slide 2
4.1 ACCESSING I/O-DEVICES
A single bus-structure can be used for connecting I/O-devices to a computer.
The simple arrangement of connecting set of I/O devices to memory and processor by means of system bus is shown in the figure.
Such an arrangement is called as Single Bus Organization.

## Slide 3
The system bus consists of 3 types of buses:
Address bus (Unidirectional)
Data bus (Bidirectional)
Control bus (Bidirectional)
Address bus – carries memory address. Its unidirectional, that’s from the CPU to memory or I/O devices
Data bus – carries the actual data or instructions transferred between the CPU and the memory or the I/O devices. Its bidirectional, data flows to and from the CPU
Control bus – carries control signals to manage the activities of the system. Its bidirectional, control signals flows to and from the CPU

## Slide 4
The system bus enables all the devices connected to it to involve in the data transfer operation.
The system bus establishes data communication between I/O device and processor.
Each I/O device is assigned a unique set of address.
When processor places an address on address-lines, the intended device responds to the command.
The processor requests either a read or write-operation.
The requested data are transferred over the data-lines

## Slide 5
Steps for input operation:
• The address bus of system bus holds the address of the input device.
• The control unit of CPU generates Control signal.
• When this control signal is activated, the processor reads the data from the input device (DATAIN) into the CPU register.
Steps for output operation:
• The address bus of system bus holds the address of the output device.
• The control unit of CPU generates control signal.
• When this control signal is enabled, CPU transfers the data from processor register to output device(DATAOUT)

## Slide 6
I/O INTERFACE

## Slide 7
The hardware arrangement of connecting input device to the system bus is shown in the figure
This hardware arrangement is called as I/O interface.
The I/O interface consists of 3 functional devices namely:
Address Decoder:
Its function is to decode the address, in-order to recognize the input device whose address is available on the unidirectional address bus.
The recognition of input device is done first, and then the control and data registers becomes active.

## Slide 8
2) Control Circuit:
The control bus of system bus is connected to control circuit
The processor sends commands to the I/O system through the control bus.
It controls the read write operations with respect to I/O device.
3) Data Register:
The data bus carries the data from the I/O devices to or from the processor.
The data register stores the data, read from input device or the data, to be written into output device.
There are 2 types:
DATAIN - Input-buffer associated with keyboard.
DATAOUT -Output data buffer of a display/printer.

## Slide 9
Data buffering is an essential task of an I/O interface.
Data transfer rates of processor and memory are high, when compared with the I/O devices, hence the data are buffered at the I/O interface circuit and then forwarded to output device, or forwarded to processor in case of input devices.
Data buffering

## Slide 10
4.2 Interrupt
It is an event which suspends the execution of one program and begins the execution of another program.
It can be avoided by I/O device sending an ‘interrupt’ to the processor, when I/O device is free.
The interrupt invokes a subroutine called Interrupt Service Routine (ISR), which resolves the cause of interrupt.
The occurrence of interrupt causes the processor to transfer the execution control from user program to ISR.

## Slide 11
Fig: Transfer of control through the use of interrupts

## Slide 12
The following steps takes place when the interrupt related instruction is executed:
It suspends the execution of current instruction i.
Transfer the execution control to sub program from main program.
The state of processor is first saved in memory before working on the interrupt.
When ISR is completed, the state of processor is restored, so that the interrupted program may continue.
Interrupt Latency / interrupt response time is the delay between the time taken for receiving an interrupt request and start of the execution of the ISR.

## Slide 13
4.2.1 INTERRUPT HARDWARE

## Slide 14
The external device (I/O device) sends interrupt request to the processor by activating a bus line and called as interrupt request line.
All I/O device uses the same single interrupt-request line.
One end of this interrupt request line is connected to input power supply by means of a register.
Another end of interrupt request line is connected to INTR (Interrupt request) signal of processor.
The I/O device is connected to interrupt request line by means of switch, which is grounded as shown in the fig.

## Slide 15
When all the switches are open the voltage drop on interrupt request line is equal to the VDD and INTR value at process is 0.
This state is called as in-active state of the interrupt request line.
The I/O device interrupts the processor by closing its switch.
When switch is closed the voltage drop on the interrupt request line is found to be zero, as the switch is grounded, hence INTR=0 and INTR=1.
The signal on the interrupt request line is logical OR of requests from the several I/O devices. Therefore, INTR=INTR1 + INTR2 + + INTRn

## Slide 16
4.2.2 ENABLING AND DISABLING THE INTERRUPTS
The arrival of interrupt request from external devices or from within a process, causes the suspension of on-going execution and start the execution of another program.
Interrupt arrives at any time and it alters the sequence of execution. Hence the interrupt to be executed must be selected carefully.
All computers can enable and disable interruptions as desired.
When an interrupt is under execution, other interrupts should not be invoked. This is performed in a system in different ways.

## Slide 17
There are 3 mechanisms to solve problem of infinite loop:
Processor should ignore the interrupts until execution of first instruction of the ISR.
Processor should automatically disable interrupts before starting the execution of the ISR.
Processor has a special INTR line for interrupt-handling circuit. Interrupt-circuit responds only to leading edge of signal. Such line is called edge-triggered.

## Slide 18
Sequence of events involved in handling an interrupt-request:
The device raises an interrupt-request.
The processor interrupts the program currently being executed.
The device is informed that its request has been recognized. And in response, the device deactivates the interrupt-request signal.
The action requested by the interrupt is performed by the interrupt-service routine.
Interrupts are enabled and execution of the interrupted program is resumed.

## Slide 19
4.2.3 HANDLING MULTIPLE DEVICES
While handling multiple devices, the issues concerned are:
• How can the processor recognize the device requesting an interrupt?
• How can the processor obtain the starting address of the appropriate ISR?
• Should a device be allowed to interrupt the processor while another interrupt is being serviced?
• How should 2 or more simultaneous interrupt-requests be handled?

## Slide 20
VECTORED INTERRUPT
A device requesting an interrupt identifies itself by sending a special-code to processor over bus.
Then, the processor starts executing the ISR.
The special-code indicates starting-address of ISR.
The special-code length ranges from 4 to 8 bits.
The staring address to ISR is called the interrupt vector.

## Slide 21
Processor
→ loads interrupt-vector into PC &
→ executes appropriate ISR.
When processor is ready to receive interrupt-vector code, it activates INTA line.
Then, I/O-device responds by sending its interrupt-vector code & turning off the INTR signal.

## Slide 22
INTERRUPT NESTING
A multiple-priority scheme is implemented by using separate INTR & INTA lines for each device
Each INTR line is assigned a different priority-level as shown in Figure.
Fig: Implementation of interrupt priority using individual interrupt request and acknowledge lines

## Slide 23
Each device has a separate interrupt-request and interrupt-acknowledge line.
Each interrupt-request line is assigned a different priority level.
Interrupt requests received over these lines are sent to a priority arbitration circuit in the processor.
If the interrupt request has a higher priority level than the priority of the processor, then the request is accepted.
Priority-level of processor is the priority of program that is currently being executed.
Processor accepts interrupts only from devices that have higher-priority than its own.
At the time of execution of ISR for some device, priority of processor is raised to that of the device.
Thus, interrupts from devices at the same level of priority or lower are disabled.

## Slide 24
Privileged Instruction
Processor's priority is encoded in a few bits and it can be changed by program instructions. These are privileged instruction.
Privileged-instructions can be executed only while processor is running in Supervisor Mode.
Privileged Exception
User program cannot
→ accidently or intentionally change the priority of the processor &
→ disrupt the system-operation.
An attempt to execute a privileged-instruction while in user-mode leads to a Privileged Exception.

## Slide 25
SIMULTANEOUS REQUESTS
DAISY CHAIN

## Slide 26
The daisy chain with multiple priority levels is as shown in the figure.
The interrupt request line INTR is common to all devices.
The interrupt acknowledge line is connected in a daisy fashion as shown in the figure.

## Slide 27
This signal propagates serially from one device to another device.
The several devices raise an interrupt by activating INTR signal. In response to the signal, processor transfers its device by activating INTA signal.
This signal is received by device 1.
The device-1 blocks the propagation of INTA signal to device-2, when it needs processor service.
The device-1 transfers the INTA signal to next device when it does not require the processor service.
In daisy chain arrangement device-1 has the highest priority.

## Slide 28
4.4 Direct Memory Access (DMA)
The process of transferring the block of data at high speed in between main memory and external device (I/O devices) without continuous intervention of CPU is called as DMA.
The DMA operation is performed by one control circuit and is part of the I/O interface.
This control circuit is called DMA controller. Hence DMA transfer operation is performed by DMA controller.
To initiate direct data transfer between main memory and external devices, DMA controller needs parameters from the CPU.

## Slide 29
The 3 Parameters are:
i) Starting address of the memory block
ii) No of words to be transferred
iii) the type of operation (Read or Write).
After receiving these 3 parameters from CPU, DMA controller establishes directed data transfer operation between main memory and external devices without the involvement of CPU.

## Slide 31
The DMA controller connects two external devices namely disk 1 and disk 2 to system bus.
Let us consider direct data transfer operation by means of DMA controller without the involvement of CPU in between main memory and disk 1
To establish direct data transfer operation between main memory and disk 1, DMA controller request the processor to obtain 3 parameters namely:
1) Starting address of the memory block.
2) No of words to be transferred.
3)Type of operation (Read or Write).
• After receiving these 3 parameters from processor, DMA controller directly transfers block of data main memory and external devices (disk 1).

## Slide 32
This information is informed to CPU.
These are 2 types of request with respect to system bus
1). CPU request.
2). DMA request.
Highest priority will be given to DMA request.
An exclusive option will be given for DMA controller to transfer block of data from external devices to main memory and from main memory to external devices. This technique is called as “Burst mode of operation.”

## Slide 33
4.4.1 BUS ARBITRATION
Any device which initiates data transfer operation on bus at any instant of time is called as Bus- Master.
When the bus mastership is transferred from one device to another device, the next device is ready to obtain the bus mastership.
The bus mastership is transferred from one device to another device based on the principle of priority system.
There are two types of bus-arbitration technique:
a) Centralized bus arbitration
b) Distributed bus arbitration

## Slide 34
a) Centralized bus arbitration

## Slide 35
In this technique CPU acts as a bus-master or any control unit connected to bus can be acts as a bus master.
The following steps are necessary to transfer the bus mastership from CPU to one of the DMA controller:
The DMA controller request the processor to obtain the bus mastership by activating BR (Bus request) signal
In response to this signal the CPU transfers the bus mastership to requested devices (DMA controllers) in the form of BG (Bus grant)
When the bus mastership is obtained from CPU the DMA controller1 blocks the propagation of bus grant signal from one device to another device.

## Slide 36
iv. The BG signal is connected to DMA controller 2 from DMA controller 1 in as daisy fashion style
v. When the DMA controller 1 has not sent BR request, it transfers the bus mastership to DMA controller 2 by unblocking bus grant signal.
When the DMA controller 1 receives the bus grant signal, it blocks the signal from passing to DMA controller 2 and enables BBSY signal.
When BBSY(bus busy) signal is set to 1, the set of devices connected to system bus doesn’t have any rights to obtain the bus mastership from the CPU.

## Slide 37
b) Distributed bus arbitration

## Slide 38
In this technique, 2 or more devices trying to access system bus at the same time may participate in bus arbitration process.
The external device requests the processor to obtain bus mastership by enabling start arbitration signal.
In this technique a 4-bit code is assigned to each device to request the CPU in order to obtain bus mastership.
Two or more devices request the bus by placing a 4-bit code over the system bus.
The signals on the bus interpret a 4-bit code and produces winner as a result from the CPU.

## Slide 39
Consider 2 devices namely A & B trying to access bus mastership at the same time.
Let assigned code for devices A & B are 5 (0101) & 6 (0110) respectively.
The device A sends the pattern (0101) and device B sends its pattern (0110) to master. The signals on the system bus interpret the 4-bit code for devices A & B produces device B as a winner.
The device B can obtain the bus mastership to initiate direct data transfer between external devices and main memory.

## Slide 40
5.4 Speed, Size and Cost

## Slide 41
The fastest and first access, is to the data held in registers. Hence registers are part of the memory hierarchy. More speed, small size and cost per bit is also more.
At the next level of hierarchy, small amount of memory can be directly implemented on the processor chip. This memory is called as processor cache. It holds the copy of recently accessed data and instructions.
There are 2 levels of caches i.e., level-1 and level-2. Level-1 cache is part of the processor and level-2 cache is placed in between level-1 cache and main memory.
The next level in the memory hierarchy is called as main memory. It is implemented using dynamic memory components (DRAM). The main memory is larger but slower than cache memory. The access time for main memory is ten times longer than the cache memory
The level next in the memory hierarchy is called as secondary memory. It holds huge amount of data.

## Slide 42
5.5 Cache Memories
It is the fast access memory located in between processor and main memory
The cache memory holds the copy of recently accessed data and instructions.
The processor needs less access time to read the data and instructions from the cache memory as compared to main memory
Hence by incorporating cache memory, in between processor and main memory, it is possible to enhance the performance of the system.

## Slide 43
5.5.1 Mapping functions
There are 3 techniques to map main memory blocks into cache memory –
Direct mapped cache
Associative Mapping
Set-Associative Mapping

## Slide 44
1. DIRECT MAPPING
The simplest way to determine cache locations to store memory blocks is the direct mapping technique.
The contention may arise even when the cache is full.
The contention is resolved by allowing the new blocks to overwrite the currently resident-block.
The main memory block is loaded into cache block by means of memory address.
The main memory address consists of 3 fields as shown in the figure.
Each block consists of 16 words. Hence least significant 4 bits are used to select one of the 16 words.
The 7 bits of memory address are used to specify the position of the cache block location.
The most significant 5 bits of the memory address are stored in the tag bits.

## Slide 45
main memory block has to be placed in particular cache block number by using below formula
Cache block number=main memory block number % number of blocks present in cache memory.
For eg:
Main memory block 129 is placed in cache block number 1
Cache block number=129 % 128 (consider remainder that is 1).
Main memory block 258 is placed in cache block 2
Cache block number=258 % 128 (consider remainder that is 2).

## Slide 46
2. Associative Mapping
It is also called as associative mapped cache. It is much more flexible.
In this technique main memory block can be placed into any cache block position.
In this case , 12 tag bits are required to identify a memory block when it is resident of the cache memory.
12 bits of address generated by the processor are compared with the tag bits of each block of the cache to see if the desired block is present. This is called as associative mapping technique.

## Slide 47
3. Set Associative Mapping
It is the combination of direct and associative mapping techniques.
The blocks of cache are divided into several groups. Such a groups are called as sets.
The main memory address consists of three fields
The lower 4 bits of memory address are used to select a word from a 16 words.
A cache consists of 64 sets. Hence 6 bit set field is used to select a cache set from 64 sets.
The most significant 6 bits of memory address is compared with the tag fields of each set to determine whether memory block is available or not.

## Slide 48
The End of M4