## Slide 1: Mass-Storage Systems

## Slide 2: Chapter 11: Mass-Storage Systems
Overview of Mass Storage Structure
HDD Scheduling
NVM Scheduling
Error Detection and Correction
Storage Device Management

## Slide 3: Objectives
Describe the physical structure of secondary storage devices and the effect of a device’s structure on its uses
Explain the performance characteristics of mass-storage devices
Evaluate I/O scheduling algorithms
Discuss operating-system services provided for mass storage, including RAID

## Slide 4: Overview of Mass Storage Structure
Bulk of secondary storage for modern computers is hard disk drives (HDDs) and nonvolatile memory (NVM) devices
HDDs spin platters of magnetically-coated material under moving read-write heads
  Drives rotate at 60 to 250 times per second
  Transfer rate is rate at which data flow between drive and computer
  Positioning time (random-access time) is time to move disk arm to desired cylinder (seek time) and time for desired sector to rotate under the disk head (rotational latency)
  Head crash results from disk head making contact with the disk surface -- That’s bad
Disks can be removable

## Slide 5: Moving-head Disk Mechanism

## Slide 6: Hard Disk Drives
Platters range from .85” to 14” (historically)
  Commonly 3.5”, 2.5”, and 1.8”
Range from 30GB to 3TB per drive
Performance
  Transfer Rate – theoretical – 6 Gb/sec
  Effective Transfer Rate – real – 1Gb/sec
  Seek time from 3ms to 12ms – 9ms common for desktop drives
  Average seek time measured or calculated based on 1/3 of tracks
  Latency based on spindle speed
    1 / (RPM / 60) = 60 / RPM
  Average latency = ½ latency

## Slide 7: Hard Disk Performance
Access Latency = Average access time = average seek time + average latency
  For fastest disk 3ms + 2ms = 5ms
  For slow disk 9ms + 5.56ms = 14.56ms
Average I/O time = average access time + (amount to transfer / transfer rate) + controller overhead
For example to transfer a 4KB block on a 7200 RPM disk with a 5ms average seek time, 1Gb/sec transfer rate with a .1ms controller overhead =
  5ms + 4.17ms + 0.1ms + transfer time =
  Transfer time = 4KB / 1Gb/s * 8Gb / GB * 1GB / 10242KB = 32 / (10242) = 0.031 ms
  Average I/O time for 4KB block = 9.27ms + .031ms = 9.301ms

## Slide 8: The First Commercial Disk Drive
1956
IBM RAMDAC computer included the IBM Model 350 disk storage system
5M (7 bit) characters
50 x 24” platters
Access time = < 1 second

## Slide 9: Nonvolatile Memory Devices
If disk-drive like, then called solid-state disks (SSDs)
Other forms include USB drives (thumb drive, flash drive), DRAM disk replacements, surface-mounted on motherboards, and main storage in devices like smartphones
Can be more reliable than HDDs
More expensive per MB
Maybe have shorter life span – need careful management
Less capacity
But much faster
Busses can be too slow -> connect directly to PCI for example
No moving parts, so no seek time or rotational latency

## Slide 10: Nonvolatile Memory Devices
Have characteristics that present challenges
Read and written in “page” increments (think sector) but can’t overwrite in place
  Must first be erased, and erases happen in larger ”block” increments
  Can only be erased a limited number of times before worn out – ~ 100,000
  Life span measured in drive writes per day (DWPD)
    A 1TB NAND drive with rating of 5DWPD is expected to have 5TB per day written within warrantee period without failing

## Slide 11: NAND Flash Controller Algorithms
With no overwrite, pages end up with mix of valid and invalid data
To track which logical blocks are valid, controller maintains flash translation layer (FTL) table
Also implements garbage collection to free invalid page space
Allocates overprovisioning to provide working space for GC
Each cell has lifespan, so wear leveling needed to write equally to all cells

## Slide 12: Volatile Memory
DRAM frequently used as mass-storage device
  Not technically secondary storage because volatile, but can have file systems, be used like very fast secondary storage
RAM drives (with many names, including RAM disks) present as raw block devices, commonly file system formatted
Computers have buffering, caching via RAM, so why RAM drives?
  Caches / buffers allocated / managed by programmer, operating system, hardware
  RAM drives under user control
  Found in all major operating systems
    Linux /dev/ram, macOS diskutil to create them, Linux /tmp of file system type tmpfs
Used as high speed temporary storage
  Programs could share bulk date, quickly, by reading/writing to RAM drive

## Slide 13: Disk Structure
Disk drives are addressed as large 1-dimensional arrays of logical blocks, where the logical block is the smallest unit of transfer
  Low-level fomatting creates logical blocks on physical media
The 1-dimensional array of logical blocks is mapped into the sectors of the disk sequentially
  Sector 0 is the first sector of the first track on the outermost cylinder
  Mapping proceeds in order through that track, then the rest of the tracks in that cylinder, and then through the rest of the cylinders from outermost to innermost
  Logical to physical address should be easy
    Except for bad sectors
    Non-constant # of sectors per track via constant angular velocity

## Slide 14: Disk Attachment
Host-attached storage accessed through I/O ports talking to I/O busses
Several busses available, including advanced technology attachment (ATA), serial ATA (SATA), eSATA, serial attached SCSI (SAS), universal serial bus (USB), and fibre channel (FC).
Most common is SATA
Because NVM much faster than HDD, new fast interface for NVM called NVM express (NVMe), connecting directly to PCI bus
Data transfers on a bus carried out by special electronic processors called controllers (or host-bus adapters, HBAs)
  Host controller on the computer end of the bus, device controller on device end
  Computer places command on host controller, using memory-mapped I/O ports
    Host controller sends messages to device controller
    Data transferred via DMA between device and computer DRAM

## Slide 15: Address Mapping
Disk drives are addressed as large 1-dimensional arrays of logical blocks, where the logical block is the smallest unit of transfer
  Low-level formatting creates logical blocks on physical media
The 1-dimensional array of logical blocks is mapped into the sectors of the disk sequentially
  Sector 0 is the first sector of the first track on the outermost cylinder
  Mapping proceeds in order through that track, then the rest of the tracks in that cylinder, and then through the rest of the cylinders from outermost to innermost
  Logical to physical address should be easy
    Except for bad sectors
    Non-constant # of sectors per track via constant angular velocity

## Slide 16: HDD Scheduling
The operating system is responsible for using hardware efficiently — for the disk drives, this means having a fast access time and disk bandwidth
Minimize seek time
Seek time  seek distance
Disk bandwidth is the total number of bytes transferred, divided by the total time between the first request for service and the completion of the last transfer

## Slide 17: Disk Scheduling (Cont.)
There are many sources of disk I/O request
  OS
  System processes
  Users processes
I/O request includes input or output mode, disk address, memory address, number of sectors to transfer
OS maintains queue of requests, per disk or device
Idle disk can immediately work on I/O request, busy disk means work must queue
  Optimization algorithms only make sense when a queue exists
In the past, operating system responsible for queue management, disk drive head scheduling
  Now, built into the storage devices, controllers
  Just provide LBAs, handle sorting of requests
    Some of the algorithms they use described next

## Slide 18: Disk Scheduling (Cont.)
Note that drive controllers have small buffers and can manage a queue of I/O requests (of varying “depth”)
Several algorithms exist to schedule the servicing of disk I/O requests
The analysis is true for one or many platters
We illustrate scheduling algorithms with a request queue (0-199)
98, 183, 37, 122, 14, 124, 65, 67
Head pointer 53

## Slide 19: FCFS
Illustration shows total head movement of 640 cylinders

## Slide 20: SCAN
The disk arm starts at one end of the disk, and moves toward the other end, servicing requests until it gets to the other end of the disk, where the head movement is reversed and servicing continues.
SCAN algorithm Sometimes called the elevator algorithm
Illustration shows total head movement of 208 cylinders
But note that if requests are uniformly dense, largest density at other end of disk and those wait the longest

## Slide 21: SCAN (Cont.)

## Slide 22: C-SCAN
Provides a more uniform wait time than SCAN
The head moves from one end of the disk to the other, servicing requests as it goes
  When it reaches the other end, however, it immediately returns to the beginning of the disk, without servicing any requests on the return trip
Treats the cylinders as a circular list that wraps around from the last cylinder to the first one
Total number of cylinders?

## Slide 23: C-SCAN (Cont.)

## Slide 24: Selecting a Disk-Scheduling Algorithm
SSTF is common and has a natural appeal
SCAN and C-SCAN perform better for systems that place a heavy load on the disk
  Less starvation, but still possible
To avoid starvation Linux implements deadline scheduler
  Maintains separate read and write queues, gives read priority
    Because processes more likely to block on read than write
  Implements four queues: 2 x read and 2 x write
    1 read and 1 write queue sorted in LBA order, essentially implementing C-SCAN
    1 read and 1 write queue sorted in FCFS order
    All I/O requests sent in batch sorted in that queue’s order
    After each batch, checks if any requests in FCFS older than configured age (default 500ms)
      If so, LBA queue containing that request is selected for next batch of I/O
In RHEL 7 also NOOP and completely fair queueing scheduler (CFQ) also available, defaults vary by storage device

## Slide 25: NVM Scheduling
No disk heads or rotational latency but still room for optimization
In RHEL 7 NOOP (no scheduling) is used but adjacent LBA requests are combined
  NVM best at random I/O, HDD at sequential
  Throughput can be similar
  Input/Output operations per second (IOPS) much higher with NVM (hundreds of thousands vs hundreds)
  But write amplification (one write, causing garbage collection and many read/writes) can decrease the performance advantage

## Slide 26: Error Detection and Correction
Fundamental aspect of many parts of computing (memory, networking, storage)
Error detection determines if there a problem has occurred (for example a bit flipping)
  If detected, can halt the operation
  Detection frequently done via parity bit
Parity one form of checksum – uses modular arithmetic to compute, store, compare values of fixed-length words
  Another error-detection method common in networking is cyclic redundancy check (CRC) which uses hash function to detect multiple-bit errors
Error-correction code (ECC) not only detects, but can correct some errors
  Soft errors correctable, hard errors detected but not corrected

## Slide 27: Storage Device Management
Low-level formatting, or physical formatting — Dividing a disk into sectors that the disk controller can read and write
  Each sector can hold header information, plus data, plus error correction code (ECC)
  Usually 512 bytes of data but can be selectable
To use a disk to hold files, the operating system still needs to record its own data structures on the disk
  Partition the disk into one or more groups of cylinders, each treated as a logical disk
  Logical formatting or “making a file system”
  To increase efficiency most file systems group blocks into clusters
    Disk I/O done in blocks
    File I/O done in clusters

## Slide 28: Storage Device Management (cont.)
Root partition contains the OS, other partitions can hold other Oses, other file systems, or be raw
  Mounted at boot time
  Other partitions can mount automatically or manually
At mount time, file system consistency checked
  Is all metadata correct?
    If not, fix it, try again
    If yes, add to mount table, allow access
Boot block can point to boot volume or boot loader set of blocks that contain enough code to know how to load the kernel from the file system
  Or a boot management program for multi-os booting

## Slide 29
Thank you