## Slide 1: Module - 2
Introduction to the ARM Instruction Set

## Slide 2: 3.1 Data Processing Instructions
The data processing instructions manipulate data within registers.
They are move instructions, arithmetic instructions, logical instructions, comparison
instructions, and multiply instructions.
Most data processing instructions can process one of their operands using the
barrel shifter.
If you use the S suffix on a data processing instruction, then it updates the flags in the
cpsr. Move and logical operations update the carry flag C, negative flag N, and zero
flag Z. The N flag is set to bit 31 of the result. The Z flag is set if the result is zero.

## Slide 3: 3.1.1 Move Instructions
Move is the simplest ARM instruction. It copies N into a destination register Rd,
where N is a register or immediate value.
This instruction is useful for setting initial values and transferring data between
registers.

## Slide 4
Example: This example shows a simple move instruction. The MOV instruction takes the contents of register r5 and copies them into register r7, in this case, taking the value 5, and overwriting the value 8 in register r7.
PRE r5 = 5
r7 = 8
MOV r7, r5 ; let r7 = r5
POST r5 = 5
r7 = 5

## Slide 5: 3.1.2 Barrel Shifter
Data processing instructions are processed within the arithmetic logic unit (ALU).
A unique and powerful feature of the ARM processor is the ability to shift the 32-bit binary pattern in one of the source registers left or right by a specific number of positions before it enters the ALU.
Pre-processing or shift occurs within the cycle time of the instruction. This is particularly useful for loading constants into a register and achieving fast multiplies or division by a power of 2.
It shows the data flow between the ALU and the barrel shifter.

## Slide 6
We apply a logical shift left (LSL) to register Rm before moving it to the destination register.
PRE r5 = 5
r7 = 8
MOV r7, r5, LSL #2 ; let r7 = r5*4 = (r5 << 2)
POST r5 = 5
r7 = 20

## Slide 8
This example of a MOVS instruction shifts register r1 left by one bit. This multiplies register r1 by a value 21. As you can see, the C flag is updated in the cpsr because the S suffix is present in the instruction mnemonic.
PRE cpsr = nzcvqiFt_USER
r0 = 0x00000000
r1 = 0x80000004
MOVS r0, r1, LSL #1
POST cpsr = nzCvqiFt_USER
r0 = 0x00000008
r1 = 0x80000004

## Slide 9: 3.1.3 Arithmetic Instructions
The arithmetic instructions implement addition and subtraction of 32-bit signed and
unsigned values.

## Slide 10
Example 3.4
This simple subtract instruction subtracts a value stored in register r2 from a value stored
in register r1. The result is stored in register r0.
PRE r0 = 0x00000000
r1 = 0x00000002
r2 = 0x00000001
SUB r0, r1, r2
POST r0 = 0x00000001
Example 3.5
This reverse subtract instruction (RSB) subtracts r1 from the constant value #0, writing the
result to r0. You can use this instruction to negate numbers.
PRE r0 = 0x00000000
r1 = 0x00000077
RSB r0, r1, #0 ; Rd = 0x0 - r1
POST r0 = -r1 = 0xffffff89

## Slide 11
The SUBS instruction is useful for decrementing loop counters. In this example we subtract the immediate value one from the value one stored in register r1. The result value zero is written to register r1. The cpsr is updated with the ZC flags being set.
PRE cpsr = nzcvqiFt_USER
r1 = 0x00000001
SUBS r1, r1, #1
POST cpsr = nZCvqiFt_USER
r1 = 0x00000000

## Slide 12: 3.1.4 Using the Barrel Shifter with Arithmetic Instructions
Register r1 is first shifted one location to the left to give the value of twice r1. The ADD instruction then adds the result of the barrel shift operation to register r1. The final result transferred into register r0 is equal to three times the value stored in register r1.
PRE r0 = 0x00000000
r1 = 0x00000005
ADD r0, r1, r1, LSL #1
POST r0 = 0x0000000f
r1 = 0x00000005

## Slide 13: 3.1.5 Logical Instructions
Logical instructions perform bitwise logical operations on the two source registers.

## Slide 14
Example 3.8 This example shows a logical OR operation between registers r1 and r2. r0 holds the result.
PRE r0 = 0x00000000
r1 = 0x02040608
r2 = 0x10305070
ORR r0, r1, r2
POST r0 = 0x12345678
Example 3.9 This example shows a more complicated logical instruction called BIC (Bit Clear), which carries out a logical bit clear.
PRE r1 = 0b1111
r2 = 0b0101
BIC r0, r1, r2
POST r0 = 0b1010
This is equivalent to
Rd = Rn AND NOT(N)

## Slide 15: Comparison Instructions
The comparison instructions are used to compare or test a register with a 32-bit value.
They update the cpsr flag bits according to the result, but do not affect other registers.
Example 3.10 This example shows a CMP comparison instruction.
PRE cpsr = nzcvqiFt_USER
r0 = 4
r9 = 4
CMP r0, r9
POST cpsr = nZcvqiFt_USER

## Slide 16: Multiply Instructions
The multiply instructions multiply the contents of a pair of registers and, depending upon the instruction, accumulate the results in with another register.

## Slide 17
Example 3.11 This example shows a simple multiply instruction that multiplies registers r1 and r2 together and places the result into register r0.
PRE r0 = 0x00000000
r1 = 0x00000002
r2 = 0x00000002
MUL r0, r1, r2 ; r0 = r1*r2
POST r0 = 0x00000004
r1 = 0x00000002
r2 = 0x00000002
Example 3.12 The instruction multiplies registers r2 and r3 and places the result into register r0 and r1. Register r0 contains the lower 32 bits, and register r1 contains the higher 32 bits of the 64-bit result.
PRE r0 = 0x00000000
r1 = 0x00000000
r2 = 0xf0000002
r3 = 0x00000002
UMULL r0, r1, r2, r3 ; [r1,r0] = r2*r3
POST r0 = 0xe0000004 ; = RdLo
r1 = 0x00000001 ; = RdHi

## Slide 18: 3.2 Branch Instructions
A branch instruction changes the flow of execution or is used to call a routine.
This type of instruction allows programs to have subroutines, if-then-else structures, and loops.

## Slide 19
Example 3.13 This example shows a forward and backward branch. Because these loops are address specific, we do not include the pre- and post-conditions. The forward branch skips three instructions. The backward branch creates an infinite loop.
B forward
ADD r1, r2, #4
ADD r0, r6, #2
ADD r3, r7, #4
forward
SUB r1, r2, #4
backward
ADD r1, r2, #4
SUB r1, r2, #4
ADD r4, r6, r7
B backward

## Slide 20: 3.3 Load-Store Instructions
Load-store instructions transfer data between memory and processor registers. There are three types of load-store instructions: single-register transfer, multiple-register transfer, and swap.
3.3.1 Single-Register Transfer
These instructions are used for moving a single data item in and out of a register. The data types supported are signed and unsigned words (32-bit), halfwords (16-bit), and bytes.

## Slide 21
3.3.2 Single-Register Load-Store Addressing Modes

## Slide 22
1. LDR r0, [r1, #4]!
Pre-indexing WITH writeback
Add 4 to r1 first
Load from new address
Update r1
2. LDR r0, [r1, #4]
Pre-indexing (NO writeback)
Calculate address = r1 + 4
Load from that address
Do NOT change r1
3. LDR r0, [r1], #4
Post-indexing
Load from r1 first
Then add 4 to r1

## Slide 23
3.16 Preindex with writeback calculates an address from a base register plus address offset and then updates that address base register with the new address.
PRE r0 = 0x00000000
r1 = 0x00090000
mem32[0x00009000] = 0x01010101
mem32[0x00009004] = 0x02020202
LDR r0, [r1, #4]!
Preindexing with writeback:
POST(1) r0 = 0x02020202
r1 = 0x00009004
LDR r0, [r1, #4]
Preindexing:
POST(2) r0 = 0x02020202
r1 = 0x00009000
LDR r0, [r1], #4
Postindexing:
POST(3) r0 = 0x01010101
r1 = 0x00009004

## Slide 24
shows the addressing modes available for load and store of a 32-bit word or an
unsigned byte.
A signed offset or register is denoted by “+/−”, identifying that it is either a positive
or negative offset from the base address register Rn.

## Slide 25: Multiple-Register Transfer
Load-store multiple instructions can transfer multiple registers between memory and the processor in a single instruction
Tables

## Slide 26: Stack Operations
The ARM architecture uses the load-store multiple instructions to carry out stack
operations.
The pop operation (removing data from a stack) uses a load multiple instruction;
similarly, the push operation (placing data onto the stack) uses a store multiple
instruction.
When using a stack you have to decide whether the stack will grow up or down in
memory.
A stack is either ascending (A) or descending (D). Ascending stacks grow towards
higher memory addresses; in contrast, descending stacks grow towards lower
memory addresses.
When you use a full stack (F), the stack pointer sp points to an address that is the
last used or full location (i.e., sp points to the last item on the stack). In contrast, if
you use an empty stack (E) the sp points to an address that is the first unused or
empty location (i.e., it points after the last item on the stack).

## Slide 27: Swap Instruction
It swaps the contents of memory with the contents of a register.
Swap cannot be interrupted by any other instruction or any other bus access.
The swap instruction loads a word from memory into register r0 and overwrites the
memory with register r1.

## Slide 28
The swap instruction loads a word from memory into register r0 and overwrites
the memory with register r1.
PRE mem32[0x9000] = 0x12345678
r0 = 0x00000000
r1 = 0x11112222
r2 = 0x00009000
SWP r0, r1, [r2]
POST mem32[0x9000] = 0x11112222
r0 = 0x12345678
r1 = 0x11112222
r2 = 0x00009000
This instruction is particularly useful when implementing semaphores and mutual
exclusion in an operating system.

## Slide 29
Software Interrupt Instruction
A software interrupt instruction (SWI) causes a software interrupt exception, which provides
a mechanism for applications to call operating system routines.
When the processor executes an SWI instruction, it sets the program counter pc to the
offset 0x8 in the vector table.
Each SWI instruction has an associated SWI number, which is used to represent
a particular function call or feature.
Since SWI instructions are used to call operating system routines, you need some form
of parameter passing. This is achieved using registers.
Code called the SWI handler is required to process the SWI call. The handler obtains the SWI number using the address of
the executed instruction, which is calculated from the
link register lr.

## Slide 30
1. SWI is used by a user program to request services from the Operating System. ..
2. When SWI instruction executes, the processor: ..
Jumps to address 0x00000008 (SWI vector address).
Switches from User Mode to SVC (Supervisor) Mode.
3. SVC mode is a privileged mode, which allows the OS to access hardware and protected resources.
4. Each SWI instruction has a SWI number, which tells the OS which function to execute. ..
5. Parameters are passed to the OS using registers (for example, r0 = 0x12).
6. Return values from the OS are also given back through registers.
7. When SWI executes, the return address is stored in the Link Register (LR).
8. The SWI handler calculates the SWI instruction address using:
SWI address = LR - 4
9. The handler extracts the SWI number from that instruction.
10. The OS executes the requested service and then returns control to the user program. ..

## Slide 31
🎓 Simple Classroom Analogy
User Program = Student OS = Principal
When student needs help:
Student raises request (SWI)
Goes to principal office (PC → 0x08)
Principal saves student details (SPSR)
Notes where student came from (LR)
Processes request
Sends student back
🔥 One-Line Summary
SWI switches the processor to SVC mode, saves the old status, stores the return address, and jumps to the operating system handler.

## Slide 32: 3.5 Program Status Register Instructions
The ARM instruction set provides two instructions to directly control a program status register (psr).
The MRS instruction transfers the contents of either the cpsr or spsr into a register; in the reverse direction, the MSR
instruction transfers the contents of a register into the cpsr or spsr.
Together these instructions are used to read and write the cpsr and spsr.

## Slide 33
The c field controls the interrupt masks, Thumb state, and processor mode.
The MSR first copies the cpsr into register r1. The BIC instruction clears bit 7 of r1. Register
r1 is then copied back into the cpsr, which enables IRQ interrupts. You can see from this
example that this code preserves all the other settings in the cpsr and only modifies the I bit
in the control field.
PRE cpsr = nzcvqIFt_SVC
MRS r1, cpsr
BIC r1, r1, #0x80 ; 0b01000000
MSR cpsr_c, r1
POST cpsr = nzcvqiFt_SVC
(MRS = Move from Status Register
It is an ARM instruction used to read the Program Status Register (PSR).
MSR = Move to Status Register
It is an ARM instruction used to write a value into the Program Status Register (PSR).)

## Slide 34: 3.5.1 Coprocessor Instructions
Coprocessor instructions are used to extend the instruction set.
A coprocessor can either provide additional computation capability or be used to control the memory subsystem
including caches and memory management.
The coprocessor instructions include data processing, register transfer, and memory transfer instructions.
Syntax: CDP{<cond>} cp, opcode1, Cd, Cn {, opcode2}
<MRC|MCR>{<cond>} cp, opcode1, Rd, Cn, Cm {, opcode2}
<LDC|STC>{<cond>} cp, Cd, addressing
In the syntax, the cp field represents the coprocessor number between p0 and p15. The opcode fields describe the
operation to take place on the coprocessor. The Cn, Cm, and Cd fields describe registers within the coprocessor.

## Slide 35: 3.5.1 Coprocessor 15 Instruction Syntax
CP15 is called the system control coprocessor. Both MRC and MCR instructions are used to
read and write to CP15, where register Rd is the core destination register, Cn is the primary
register, Cm is the secondary register, and opcode2 is a secondary register modifier. You
may occasionally hear secondary registers called “extended registers.”
We use a shorthand notation for CP15 reference that makes referring to configuration
registers easier to follow:
The first term, CP15, defines it as coprocessor 15. The second term, after the separating
colon, is the primary register. The primary register X can have a value between 0 and 15.
The third term is the secondary or extended register. The secondary register Y can have
a value between 0 and 15. The last term, opcode2, is an instruction modifier and can have
a value between 0 and 7. Some operations may also use a nonzero value w of opcode1. We
write these as CP15:w:cX:cY:Z.

## Slide 36: 3.6 Loading Constants
To aid programming there are two pseudoinstructions to move a 32-bit value into a register.
Syntax: LDR Rd, =constant
ADR Rd, label
The first pseudoinstruction writes a 32-bit constant to a register using whatever instructions are available.
The second pseudoinstruction writes a relative address into a register, which will be encoded using a pc-
relative expression.

## Slide 37
Example 3.29 Loading the constant 0xff00ffff using an MVN.
PRE none...
MVN r0, #0x00ff0000
POST r0 = 0xff00ffff
The LDR pseudoinstruction either inserts an MOV or MVN instruction to generate a value (if possible) or generates
an LDR instruction with a pc-relative address to read the constant from a literal pool—a data area embedded within
the code.