## Slide 1
Course Coordinator:
Assistant Professor
Dept. of E&C, ATME
Guruprasad K N
Subject Name: Principles of Communication Systems
Subject Code: BEC402

## Slide 2
Module 2
Amplitude Modulation Fundamentals

## Slide 4
Module 2: Chapter 1
Amplitude Modulation Fundamentals
AM Concepts
Modulation index and Percentage of Modulation
Sidebands and the frequency domain
Single Sideband Modulation
AM Power

## Slide 5
Suggested Reading
Text 1: “Principles of Electronic Communication Systems,”
Louis E Frenzel, 3rd Edition, Mc Graw Hill Education (India) Private Limited, 2016. ISBN: 978-0-07-066755-6.
Text 1:
Sections: 3.1, 3.2, 3.3, 3.4, 3.5

## Slide 7
Module 2: Chapter 1
Amplitude Modulation Fundamentals
AM Concepts ✓
Modulation index and Percentage of Modulation
Sidebands and the frequency domain
Single Sideband Modulation
AM Power

## Slide 8
Modulation:
Modulation is the process by which some characteristic of a carrier is varied in accordance with the message signal. The result of the modulation process is referred to as a modulated wave. Modulation is performed at the transmitting end of the communication system:
Introduction:
Modulation techniques are classified according to which parameter of the carrier is changed.
Amplitude Modulation→ Amplitude of the carrier is varied according to the baseband signal, keeping its frequency and phase constant.
Frequency Modulation→ Frequency of the carrier is varied according to the baseband signal.
Phase Modulation→ The phase of the carrier is varied according to the baseband signal.

## Slide 9
AM Concepts :
Amplitude Modulation (AM) Definition:
Amplitude Modulation (AM) is a modulation technique in which the amplitude of a carrier wave is varied in proportion to the instantaneous amplitude of the baseband (message) signal while keeping the frequency and phase constant
An increase in the amplitude of the modulating signal causes the amplitude of the carrier to increase.
Both the positive and the negative peaks of the carrier wave vary with the modulating signal.
An increase or a decrease in the amplitude of the modulating signal causes a corresponding increase or decrease in both the positive and the negative peaks of the carrier amplitude.

## Slide 12
Envelope:
An imaginary line connecting the positive peaks and negative peaks of the carrier waveform (the dashed line in Fig.) gives the exact shape of the modulating information signal.
This imaginary line on the carrier waveform is known as the envelope.
Because complex waveforms such as that shown in Fig. are difficult to draw, they are often simplified by representing the high-frequency carrier wave as many equally spaced vertical lines whose amplitudes vary in accordance with a modulating signal

## Slide 13
A simpliﬁed method of representing an AM high-frequency sine wave:

## Slide 14
Mathematical Expression:
The sine wave carrier is expressed as
Where
vc is Instantaneous carrier voltage at time t
Vc​ = Peak amplitude of the unmodulated carrier wave
fc​ = Frequency of the carrier wave
t = Time

## Slide 15
In amplitude modulation, the peak value of the modulating signal is less than the peak value of the carrier.
i.e.,

## Slide 16
The instantaneous value of either the top or the bottom voltage envelope v1 can be computed by using the equation,
The instantaneous value of the complete AM wave v2 is given by,
Substituting,
Note: The AM wave is the product of the carrier and modulating signals.

## Slide 17
Amplitude modulator:
The circuit used for producing AM is called a modulator.
It has two inputs, the carrier and the modulating signal. The resulting outputs are shown in Fig.

## Slide 18
Note:
Circuits that compute the product of two analog signals are also known as analog multipliers, mixers, converters, product detectors, and phase detectors.
A circuit that changes a lower-frequency baseband signal to a higher-frequency signal is usually called a modulator.
A circuit used to recover the original intelligence signal from an AM wave is known as a detector or demodulator.

## Slide 19
Module 2: Chapter 1
Amplitude Modulation Fundamentals
AM Concepts ✓
Modulation index and Percentage of Modulation✓
Sidebands and the frequency domain
Single Sideband Modulation
AM Power

## Slide 20
Modulation index:
Also called the modulating factor or coefficient, or the degree of modulation
Percentage of Modulation :
Multiplying the modulation index by 100 gives the percentage of modulation.

## Slide 21
Over modulation and distortion:
The modulation index should be a number between 0 and 1.
If the amplitude of the modulating voltage is higher than the carrier voltage, m will be greater than 1, causing distortion of the modulated waveform.
If the modulating voltage is much greater than the carrier voltage, the resulting condition is called overmodulation. Hence the waveform is flattened at the zero line.

## Slide 23
Percentage of Modulation :
When the AM signal is displayed on an oscilloscope, the modulation index can be computed from Vmax and Vmin as shown in Fig.

## Slide 25
The peak value of the modulating signal Vm is given by :
The peak value of the carrier signal Vc is given by :

## Slide 26
Problem 2.2:

## Slide 28
Solution:

## Slide 29
Module 2: Chapter 1
Amplitude Modulation Fundamentals
AM Concepts ✓
Modulation index and Percentage of Modulation✓
Sidebands and the frequency domain ✓
Single Sideband Modulation
AM Power

## Slide 30
Sidebands :
When a carrier is modulated by an information signal, new signals at different frequencies are generated as part of the process . These new frequencies are called side frequencies or sidebands.
Sidebands appear in the frequency spectrum directly above and below the carrier frequency.

## Slide 31
Sideband Calculations :
When only a single-frequency sine wave modulating signal is used, the modulation process generates two sidebands:
  The Upper Sideband fUSB
  The lower Sideband fLSB

## Slide 32
Mathematical Expression:
The existence of sidebands can be demonstrated mathematically,

## Slide 33
Summary: An AM signal is really a composite signal formed from several components:
AM Signal = Carrier sine wave + USB + LSB

## Slide 35
Frequency-Domain Representation of AM:

## Slide 36
The relationship between the time and frequency domains.

## Slide 37
Problem 2.4:

## Slide 38
Solution:

## Slide 40
c) The upper & lower sidebands of a voice modulated AM signal are shown in fig below.

## Slide 41
Problem 2.5:

## Slide 43
Pulse Modulation
When complex signals such as pulses or rectangular waves modulate a carrier, a broad spectrum of sidebands are produced.

## Slide 45
Amplitude-shift keying (ASK)
Amplitude modulation by square waves or rectangular binary pulses is referred to as amplitude-shift keying (ASK).
ASK is used in some types of data communication when binary information is to be transmitted.

## Slide 47
Problem 2.6:
Consider the sine wave of 500 Hz modulating a 1 MHz carrier. Calculate sidebands frequency & BW. Also draw the spectrum.

## Slide 49
Module 2: Chapter 1
Amplitude Modulation Fundamentals
AM Concepts ✓
Modulation index and Percentage of Modulation✓
Sidebands and the frequency domain ✓
Single Sideband Modulation
AM Power ✓

## Slide 50
AM Power
The AM signal is really a composite of several signal voltages, namely, the carrier and the two sidebands, and each of these signals produces power in the antenna.

## Slide 55
Problem :
An antenna has an impedance of 40 ohms. An unmodulated AM signal produces a current of 4.8 A. The modulation is 90 percent. Calculate
The carrier power
The total power
The sideband power

## Slide 57
Problem :
The transmitter in previous example experiences an antenna current change from 4.8 A unmodulated to 5.1 A. What is the percentage of modulation?

## Slide 59
Advantages of Amplitude Modulation
Generation and detection of AM signal is very easy.
AM transmitters and receivers are relatively very cheap since no specialized components are needed.
AM waves can travel a longer distance.
AM waves have low bandwidth.

## Slide 60
Limitations of Amplitude Modulation
Amplitude modulation is wasteful of power. The carrier wave c(t) is completely independent of the information-bearing signal or baseband signal m(t). Therefore, the transmission of the carrier wave represents a waste of power.
Amplitude modulation is wasteful of bandwidth. In AM, both USB and LSB are transmitted. Since USB is symmetrical to LSB, for the transmission of information, only one sideband is necessary.
AM signals are more prone to high levels of noise.

## Slide 61
Module 2: Chapter 1
Amplitude Modulation Fundamentals
AM Concepts ✓
Modulation index and Percentage of Modulation✓
Sidebands and the frequency domain ✓
Single Sideband Modulation ✓
AM Power ✓

## Slide 62
Single Sideband Modulation
In amplitude modulation, two-thirds of the transmitted power is in the carrier, which itself conveys no information.
The real information is contained within the sidebands.
One way to improve the efficiency of amplitude modulation is to suppress the carrier and eliminate one sideband.
The result is a single-sideband (SSB) signal.

## Slide 63
DSBSC Signals or DSB Signals
(Double-sideband suppressed carrier signal)
"In DSB-SC the transmitted wave consists of only the upper and lower sidebands. The carrier component is suppressed and thus the transmitted power is saved. The saved power is distributed to the two sidebands."
The benefit:
No power is wasted on the carrier.
Note: Double-sideband suppressed carrier modulation is simply a special case of AM with no carrier.

## Slide 64
This signal is the algebraic sum of the two sinusoidal sidebands
The envelope of this waveform is not the same as that of the modulating signal.
A unique characteristic of the DSB signal is the phase transitions that occur at the lower-amplitude portions of the wave.
Fig: Time domain representation of DSBSC signal

## Slide 65
Fig: Frequency domain representation of DSBSC signal

## Slide 66
Single- sideband suppressed carrier (SSBSC or SSB) signal
During modulation, due to the symmetry of the DSB signal about the carrier frequency, the same information is transmitted in the upper and lower sidebands. Therefore, to convey the information, only one sideband is sufficient.
The modulation technique in which information is transmitted using only one of the sidebands and the other sideband is suppressed is known as Single Sideband modulation."

## Slide 67
Benefits of SSB Signals:
The space it occupies is only one-half of AM and DSB signals. Hence it allows more signals to be transmitted in the same frequency range.
SSB signal is more stronger than AM and DSB signals.
SSB transmitters are smaller and lighter and hence less circuitry and less power are used.
Since SSB signals occupy a narrower bandwidth, the amount of noise in the signal is reduced.
There is less selective fading of an SSB signal over long distances.

## Slide 68
Fig : Frequency domain representation of SSB signal

## Slide 69
Disadvantages of DSB and SSB
They are harder to recover, or demodulate, at the receiver.
If the carrier is not present, then it must be regenerated at the receiver and reinserted into the signal. The reinserted carrier must have the same phase and frequency as those of the original carrier.

## Slide 70
Peak Envelope Power (PEP):
The maximum power produced on voice amplitude peaks

## Slide 72
Problem 2.10:

## Slide 73
Problem 2.11:

## Slide 76
Module 2: Chapter 2
AM Circuits
Amplitude Modulators:✓
Amplitude Demodulators
Diode Modulator ✓
Transistor Modulator
Collector Modulator
Diode Detector
Balanced Modulators: Lattice Modulators.

## Slide 77
Amplitude Modulators:
Amplitude modulators are generally one of two types:
Low level AM: Low-level modulators generate AM with small signals
  Diode Modulator
  Transistor Modulator
High level AM: High-level modulators produce AM at high power levels
  Collector Modulator

## Slide 78
Module 2: Chapter 2
AM Circuits
Amplitude Modulators:✓
Amplitude Demodulators
Diode Modulator ✓
Transistor Modulator
Collector Modulator
Diode Detector
Balanced Modulators: Lattice Modulators.

## Slide 79
Diode Modulator

## Slide 80
The Diode Modulator circuit consists:
A resistive mixing network
A diode rectifier
An LC tuned circuit

## Slide 81
Working:
The modulating signal and carrier signals are applied to input resistors R1 & R2
The mixed signals appear across R3.
The composite waveform is applied to a diode rectifier
  During positive half cycle – the diode is forward biased – Signal passes
  During negative half cycle – the diode is cutoff – No signal passes

## Slide 82
The current through the diode is a series of positive-going pulses whose amplitude varies in proportion to the amplitude of the modulating signal.
These positive-going pulses are applied to LC circuit which are resonant at the carrier frequency.
The resulting waveform across the tuned circuit is an AM signal

## Slide 83
Module 2: Chapter 2
AM Circuits
Amplitude Modulators:✓
Amplitude Demodulators
Diode Modulator ✓
Transistor Modulator ✓
Collector Modulator
Diode Detector,
Balanced Modulators: Lattice Modulators.

## Slide 84
Transistor Modulator
It uses a transistor instead of the diode.
The circuit has gain.
The base current controls a larger collector current, and therefore the circuit amplifies.
Rectification occurs because of the emitter-base junction.
The tuned circuit oscillates (rings) to generate the missing half-cycle.

## Slide 85
Module 2: Chapter 2
AM Circuits
Amplitude Modulators:✓
Amplitude Demodulators
Diode Modulator ✓
Transistor Modulator ✓
Collector Modulator✓
Diode Detector,
Balanced Modulators: Lattice Modulators.

## Slide 86
Collector Modulator

## Slide 87
The output stage of the transmitter is a high-power class C amplifier.
The modulator is a linear power amplifier that takes the low-level modulating signal and amplifies it to a high-power level.
The modulating output signal is coupled through modulation transformer T1 to the class C amplifier.
The secondary winding of the modulation transformer is connected in series with the collector supply voltage VCC of the class C amplifier.
With a zero-modulation input signal, there is zero-modulation voltage across the secondary of T1, the collector supply voltage is applied directly to the class C amplifier, and the output carrier is a steady sine wave.
When the modulating signal occurs, the ac voltage of the modulating signal across the secondary of the modulation transformer is added to and subtracted from the dc collector supply voltage.

## Slide 88
When the modulation signal goes positive,
  It adds to the collector supply voltage, thereby increasing its value
  Causes higher-amplitude carrier.
  When the modulating signal goes negative,
    It subtracts from the collector supply voltage, decreasing it.
    Causes lower-amplitude carrier

## Slide 89
Problem 2.12:
An AM transmitter uses high-level modulation of the final RF power amplifier, which has a dc supply voltage Vcc of 48 V with a total current I of 3.5 A. The efficiency is 70 percent.
  What is the RF input power to the final stage?
  How much AF power is required for 100 percent modulation? (Hint: For 100 percent modulation, AF modulating power Pm is one-half the input power.)
  What is the carrier output power?
  What is the power in one sideband for 67 percent modulation?
  What is the maximum and minimum dc supply voltage swing with 100 percent modulation?

## Slide 92
Module 2: Chapter 2
AM Circuits
Amplitude Modulators:✓
Amplitude Demodulators ✓
Diode Modulator ✓
Transistor Modulator ✓
Collector Modulator✓
Diode Detector
Balanced Modulators: Lattice Modulators.

## Slide 93
Amplitude Demodulators :
Demodulators, or detectors, are circuits that accept modulated signals and recover the original modulating information.

## Slide 94
Module 2: Chapter 2
AM Circuits
Amplitude Modulators:✓
Amplitude Demodulators ✓
Diode Modulator ✓
Transistor Modulator ✓
Collector Modulator✓
Diode Detector ✓
Balanced Modulators: Lattice Modulators.

## Slide 95
Diode Detector :

## Slide 96
The AM signal is transformer-coupled and applied to a basic half wave rectifier circuit consisting of D1 and R1.
During the positive half-cycles of the AM signal - The diode conducts - current flows
During the negative half-cycles - the diode is reverse-biased - no current flows through it.
As a result, the voltage across R1 is a series of positive pulses whose amplitude varies with the modulating signal.
A capacitor C1 is connected across resistor R1, effectively filtering out the carrier and thus recovering the original modulating signal.
Because the diode detector recovers the envelope of the AM signal, which is the original modulating signal, the circuit is sometimes referred to as an envelope detector.

## Slide 97
Fig: Diode detector waveforms

## Slide 99
Module 2: Chapter 2
AM Circuits
Amplitude Modulators:✓
Amplitude Demodulators ✓
Diode Modulator ✓
Transistor Modulator ✓
Collector Modulator✓
Diode Detector ✓
Balanced Modulators: Lattice Modulators✓

## Slide 100
Balanced Modulators:
A balanced modulator is a circuit that generates a DSB signal, suppressing the carrier and leaving only the sum and difference frequencies at the output.
The output of a balanced modulator can be further processed by filters to eliminate one of the sidebands, resulting in an SSB signal.

## Slide 101
Lattice Modulators or Ring Modulator:
A balanced modulator is used to generate a DSBSC signal.

## Slide 103
Construction:
It consists of
  An input transformer T1
  An output transformer T2 and
  Four diodes connected in a bridge circuit.
The carrier signal is applied to the centre taps of the input and output transformers.
The modulating signal is applied to the input transformer T1
The output appears across the secondary of the output transformer T2
The carrier sine wave is used as a source of forward and reverse bias for the diodes.

## Slide 104
Working:
Assume that the modulating input is zero.
When the polarity of the carrier is positive
  Diodes D1 and D2 are forward-biased
  D3 and D4 are reverse-biased and act as open circuits
  Current divides equally in the upper and lower portions of the primary winding of T2
  Magnetic fields are equal and opposite and cancel each other
  No output is induced in the secondary

## Slide 105
When the polarity of the carrier is negative
  Diodes D1 and D2 are reverse-biased
  D3 and D4 conduct
  Current divides equally in the upper and lower portions of the primary winding of T2
  Magnetic fields are equal and opposite and cancel each other
  No output is induced in the secondary

## Slide 106
Now assume that a low-frequency sine wave is applied to the primary of T1 as the modulating signal.
The modulating signal appears across the secondary of T1.
When the polarity of the carrier is positive
  D1 and D2 are ON
  D3 and D4 are OFF
As a result, the modulating signal at the secondary of T1 is applied to the primary of T2 through D1 and D2.

## Slide 107
When the polarity of the carrier is negative
  D1 and D2 are OFF
  D3 and D4 are ON
As a result, the modulating signal at the secondary of T1 is applied to the primary of T2 through D3 and D4.
The result is a 180° phase reversal
With this connection, if the modulating signal is positive, the output will be negative, and vice versa.

## Slide 108
Waveforms in the lattice-type balanced modulator. (a) Carrier. (b) Modulating signal.
(c) DSB signal—primary T2. (d) DSB output

## Slide 110
Module 2: Chapter 3
Frequency Division Multiplexing
Frequency Division Multiplexing ✓
Receiver- Demultiplexer
Transmitter-Multiplexer

## Slide 111
Frequency Division Multiplexing :
Frequency-division multiplexing (FDM), is a technique in which multiple signals share the bandwidth of a common communication channel.

## Slide 112
Module 2: Chapter 3
Frequency Division Multiplexing
Frequency Division Multiplexing ✓
Receiver- Demultiplexer
Transmitter-Multiplexer ✓

## Slide 113
Transmitter-Multiplexer:

## Slide 115
Signal Inputs (Signal 1, Signal 2, Input 3, ..., Input m)
  These are the original input signals that need to be transmitted.
  Each input contains unique data (e.g., voice, video, or data signals).
2. Modulators
  Each signal is fed into a Modulator along with a carrier frequency (fc1, fc2, ..., fcn).
  The modulator shifts the baseband signal (original signal) to a specific frequency band by combining it with a carrier wave.
3. Carrier Frequencies (fc1, fc2, ..., fcn)
  These are distinct frequencies assigned to each signal.
4. Linear Mixer or Summer
  Combines all the modulated signals into a single composite signal.
  Each signal remains in its own frequency band due to different carrier frequencies.
  No interference occurs as long as the frequency bands don't overlap.

## Slide 116
5. Transmitter (Optional)
  The composite signal is optionally passed through a Transmitter, which could further modulate the composite signal for long-range transmission.
6. To Single Cable or Antenna
  The composite signal is transmitted over a single communication channel, such as:
    A coaxial cable or fiber (for wired communication), or
    An antenna (for wireless communication)
7. Antenna (Optional)
  If the system is wireless, an antenna broadcasts the signal into the air.

## Slide 117
Fig: Spectrum of an FDM signal. The bandwidth of a single channel is divided into smaller channels.

## Slide 118
Module 2: Chapter 2
Frequency Division Multiplexing
Frequency Division Multiplexing ✓
Receiver- Demultiplexer ✓
Transmitter-Multiplexer ✓

## Slide 119
Receiver- Demultiplexer :

## Slide 121
A receiver picks up the signal and demodulates it, recovering the composite signal.
This is sent to a group of band-pass filters, each centered on one of the carrier frequencies.
Each filter passes only its channel and rejects all others.
A channel demodulator then recovers each original input signal.

## Slide 122
Assignment – 2
Sl. No | Questions | COs | RBT
1 | Explain the working principle of a Diode Modulator | CO1, CO2 | L2
2 | Develop a basic amplitude modulation circuit using a transistor and explain its operation. | CO1, CO2 | L3
3 | Illustrate the collector modulator circuit and describe the role of each component | CO1, CO2 | L2
4 | Describe the operation of a diode detector with a neat diagram. Draw and explain the waveform changes at different stages. | CO1, CO2 | L2
5 | Explain the principle and working of a lattice modulator with a block diagram. Analyze how carrier suppression is achieved | CO1, CO2 | L4
6 | Construct an FDM system using three input signals with different carrier frequencies. Show how signals are combined. | CO1, CO2 | L3
7 | Describe the role of the receiver-demultiplexer in an FDM system | CO1, CO2 | L2

## Slide 123
Thank You