## Slide 1
Course Coordinator:
Assistant Professor
Dept. of E&C, ATME
Guruprasad K N
Subject Name: Principles of Communication Systems
Subject Code: BEC402

## Slide 2
Module 3
Fundamentals of Frequency Modulation

## Slide 4
Module 3: Chapter 1
Fundamentals of Frequency Modulation
Basic Principles of Frequency Modulation
Principles of Phase Modulation
Modulation index and sidebands
Noise Suppression Effects of FM
FM versus AM.

## Slide 5
Suggested Reading
Text 1: “Principles of Electronic Communication Systems,”
Louis E Frenzel, 3rd Edition, Mc Graw Hill Education (India) Private Limited, 2016. ISBN: 978-0-07-066755-6.
Text 1:
Sections: 5.1,5.2,5.3,5.4,5.5,6.1,6.3,9.2,9.3

## Slide 7
Module 3: Chapter 1
Fundamentals of Frequency Modulation
Basic Principles of Frequency Modulation ✓
Principles of Phase Modulation
Modulation index and sidebands
Noise Suppression Effects of FM
FM versus AM.

## Slide 8
FM Concepts :
Frequency Modulation (FM) Definition:
Frequency Modulation (FM) is a modulation technique in which the frequency of a carrier wave is varied in proportion to the message signal while keeping the amplitude and phase constant

## Slide 10
If the amplitude of the modulating signal increases the carrier frequency increases
If the amplitude of the modulating signal decreases the carrier frequency decreases
Frequency deviation fd :
The amount of change in carrier frequency produced by the modulating signal is known as the frequency deviation fd.
Maximum frequency deviation occurs at the maximum amplitude of the modulating signal.
The frequency of the modulating signal determines the frequency deviation rate.

## Slide 12
Carrier.
Modulating signal.
FM signal.

## Slide 13
Problem 3.1:
A transmitter operates on a frequency of 915 MHz. The maximum FM deviation is ±12.5 kHz. What are the maximum and minimum frequencies that occur during modulation?
Solution:

## Slide 14
Frequency-modulating of a carrier with binary data produces FSK.

## Slide 15
Module 3: Chapter 1
Fundamentals of Frequency Modulation
Basic Principles of Frequency Modulation ✓
Principles of Phase Modulation ✓
Modulation index and sidebands
Noise Suppression Effects of FM
FM versus AM.

## Slide 16
PM Concepts :
Phase Modulation (PM) Definition:
Phase Modulation (PM) is a type of analog modulation where the phase of the carrier signal is varied proportionally to the instantaneous amplitude of the message (modulating) signal.
In PM, the frequency of the carrier remains constant.
The instantaneous phase of the carrier changes with the message signal.
The waveform looks similar to FM, but the modulation is based on phase, not frequency.

## Slide 17
Carrier
Modulating signal
FM signal
PM signal

## Slide 18
Modulating signal
PM signal

## Slide 19
Modulating signal
FM signal

## Slide 20
Phase modulation of a carrier by binary data produces PSK.

## Slide 21
Converting PM to FM
Q: With a neat block diagram, explain converting a phase modulated signal into a frequency modulated signal.

## Slide 22
It is the Indirect Method of Frequency Modulation (FM) generation using a Phase Modulator.
It is commonly referred to as Armstrong's method of FM generation.

## Slide 23
Microphone:
  Captures the original audio signal (voice or music)
  Audio Amplifier:
    Amplifies the weak signal from the microphone.
  RC Network (Integrator):

## Slide 24
Phase Modulator:
  Takes the integrated signal and applies Phase Modulation.
  Since the input is already an integrated audio signal, the output becomes an FM signal.
Carrier Oscillator
  Generates a stable, high-frequency carrier signal.
Fig: Frequency Response Graph

## Slide 25
Module 3: Chapter 1
Fundamentals of Frequency Modulation
Basic Principles of Frequency Modulation ✓
Principles of Phase Modulation ✓
Modulation index and sidebands ✓
Noise Suppression Effects of FM
FM versus AM.

## Slide 26
Sidebands :
In FM and PM, sum and difference sideband frequencies are produced.
In addition, a large number of pairs of upper and lower sidebands are generated.
As a result, the spectrum of an FM or a PM signal is usually wider than that of an equivalent AM signal
Note: The sidebands are spaced from the carrier fc and from one another by a frequency equal to the modulating frequency fm.

## Slide 27
Fig:
Frequency spectrum of an FM signal

## Slide 28
Modulation Index:

## Slide 29
Problem 3.2:
What is the deviation ratio of TV sound if the maximum deviation is 25 kHz and the maximum modulating frequency is 15 kHz?

## Slide 30
Problem 3.3:
What is the maximum modulating frequency that can be used to achieve a modulation index of 2.2 with a deviation of 7.48 kHz?

## Slide 31
FM Signal Bandwidth:
The bandwidth of FM signal is determined using simple formula:
Where,
fm is modulating frequency
N is the number of significant sidebands in the signal
Another way to determine the bandwidth of an FM signal is to use Carson’s rule

## Slide 32
Problem 3.4:
What is the maximum bandwidth of an FM signal with a deviation of 30 kHz and a maximum modulating signal of 5 kHz.
(a) Using number of sidebands N=9
(b) Using Carson’s rule

## Slide 33
Solution:

## Slide 34
Module 3: Chapter 1
Fundamentals of Frequency Modulation
Basic Principles of Frequency Modulation ✓
Principles of Phase Modulation ✓
Modulation index and sidebands ✓
Noise Suppression Effects of FM ✓
FM versus AM.

## Slide 35
Noise Suppression Effects of FM :
Noise is interference generated by lightning, motors, automotive ignition systems, and any power line switching that produces transient signals.
Such noise is typically narrow spikes of voltage with very high frequencies.
They add to a signal and interfere with it.
If the noise signals were strong enough, they could completely destroy the information signal.

## Slide 37
FM signals have a constant modulated carrier amplitude, and FM receivers contain limiter circuits that restrict the amplitude of the received signal.
Any amplitude variations occurring on the FM signal are effectively clipped off as shown in Fig.
This does not affect the information content of the FM signal, since it is contained solely within the frequency variations of the carrier.
Because of the clipping action of the limiter circuits, noise is almost completely eliminated.
Even if the peaks of the FM signal itself are clipped or flattened and the resulting signal is distorted, no information is lost.
One of the primary benefits of FM over AM is its superior noise immunity.

## Slide 38
Noise and Phase Shift
The noise amplitude added to an FM signal introduces a phase shift which changes the signal.
The phase shift angle can be computed using the following formula
Where,
S = The carrier signal
N = The noise signal
C = The composite signal
Note:
The maximum phase shift occurs when the noise and signal phasors are at a right angle to each other.

## Slide 39
The frequency deviation produced by noise is given by,
The ratio of the shift produced by the noise to the maximum allowed deviation is
The FM Signal-to-Noise Ratio (SNR) is given by,

## Slide 40
Problem 3.5:

## Slide 41
Solution:

## Slide 42
Pre-emphasis and de-emphasis

## Slide 43
Pre-emphasis :
The pre-emphasis circuit commonly used in FM (Frequency Modulation) transmitters to improve the signal-to-noise ratio (SNR) by boosting the high-frequency components of the audio signal before modulation.

## Slide 44
1. Pre-emphasis Circuit

## Slide 45
2. Frequency Modulator
Function: Modulates the frequency of the carrier wave in accordance with the amplitude of the pre-emphasized input signal.
Purpose: Converts the audio signal into a frequency-modulated signal for transmission.
3. Pre-emphasized FM Output
Function:
This is the final output from the FM transmitter.
It contains the frequency-modulated signal with enhanced high-frequency components, making it more robust against noise during transmission.

## Slide 46
Fig: Pre-emphasis curve

## Slide 47
The De-emphasis Circuit is used in FM (Frequency Modulation) receivers.
It's the counterpart of the pre-emphasis circuit used at the transmitter end.
De-emphasis:

## Slide 48
1. FM in
This is the received FM signal from the antenna or receiver.
It contains the frequency-modulated audio signal, which has undergone pre-emphasis at the transmitter.
2. FM Demodulator
Function: Converts the FM signal back into the original audio signal (demodulates it).

## Slide 49
3. De-emphasis Circuit

## Slide 50
Fig: De-emphasis curve

## Slide 51
Fig: Combined frequency response

## Slide 52
Module 3: Chapter 1
Fundamentals of Frequency Modulation
Basic Principles of Frequency Modulation ✓
Principles of Phase Modulation ✓
Modulation index and sidebands ✓
Noise Suppression Effects of FM ✓
FM versus AM✓

## Slide 53
FM versus AM:
Advantages of FM
In general, FM is considered to be superior to AM
Noise Immunity:
  FM signals have superior immunity to noise because of clipper limiter circuits in the receiver.
Capture Effect.
  The capture effect is a phenomenon in FM receivers where, when two signals at similar frequencies are received, the stronger signal is demodulated and the weaker one is suppressed — even if both are present simultaneously.
Transmitter Efficiency.
  FM signals have a constant amplitude, and it is therefore not necessary to use linear amplifiers to increase their power level.

## Slide 54
Disadvantages of FM
Excessive Spectrum Use:
  The bandwidth of an FM signal is wider than that of an AM signal transmitting similar information
Circuit Complexity
  Complex circuits are used for frequency modulation and demodulation, whereas simple circuits used for amplitude modulation and demodulation.

## Slide 56
FM and AM Applications

## Slide 58
Module 3: Chapter 2
FM Circuits
Frequency Modulators:✓
Frequency Demodulators:
Voltage Controlled Oscillators
Slope Detectors
Phase Locked Loop (PLL)

## Slide 59
Frequency Modulators:
A frequency modulator is a device or circuit that performs frequency modulation (FM).
or
A frequency modulator is a circuit that varies carrier frequency in accordance with the modulating signal.
The carrier is generated by either an LC or a crystal oscillator circuit.

## Slide 60
Module 3: Chapter 2
FM Circuits
Frequency Modulators:✓
Frequency Demodulators:
Voltage Controlled Oscillators ✓
Slope Detectors
Phase Locked Loop (PLL)

## Slide 61
Voltage Controlled Oscillators :
Definition:
A Voltage-Controlled Oscillator (VCO) is an electronic oscillator whose oscillation frequency is controlled by an input voltage.
Basic Concept:
The output frequency of the VCO changes in direct proportion to the applied control voltage VC​.
It converts a DC voltage input into an AC signal output (typically sine, square, or triangular wave).

## Slide 62
Fig: Block diagram with an IC VCO.

## Slide 63
Modulation Input (Pin 5, VC)
  This input controls the frequency of the output waveform.
  Applying a voltage here changes the current from the current sources, which in turn adjusts the charge/discharge rate of the capacitor C1​ , thus changing the oscillation frequency.
Current Sources
  Takes the control voltage VC​ and converts it into a current.
  This current is used to charge and discharge the external capacitor C1​ .
  The rate at which C1​ charges/discharges determines the frequency of oscillation.
Capacitor C1​
  Connected between pin 7 and ground.
  It charges and discharges through the current sources.
  The voltage across this capacitor ramps up and down linearly, creating a triangular waveform.

## Slide 64
Schmitt Trigger
  Monitors the voltage across C1​.
  When the voltage reaches a certain upper or lower threshold, it changes state.
  This state change reverses the direction of current, causing C1​ to start charging in the opposite direction.
  Outputs a square wave corresponding to these state changes.
Buffer Amplifier (Pin 3)
  Provides a square wave output.
  This output can be used for digital logic or timing applications.
Buffer Amplifier (Pin 4)
  Provides a triangular wave output.
  This analog waveform is useful for audio signals or modulation.

## Slide 65
External Resistor R1​ (Connected to Pin 6)
  Sets a reference current in conjunction with the supply voltage V+ ​.
  Affects the charging/discharging rate of C1​, and thus impacts the oscillation frequency.

## Slide 66
Basic frequency modulator using the NE566 VCO

## Slide 68
Construction :
R1​ : Timing Resistor
C1​ : Timing Capacitor
C2​: AC coupling capacitor
R2 and R3: Biasing resistors
R2​, R3​, C2​ : Modulating Network

## Slide 69
Working :
The current sources are biased with a voltage divider made up of R2 and R3
The modulating signal is applied through C2 to the voltage divider at pin 5
The 0.001-μF capacitor between pins 5 and 6 is used to prevent unwanted oscillations.
The center carrier frequency of the circuit is set by the values of R1 and C1 (Maximum of 1 MHz)
The modulating signal can vary the carrier frequency over nearly a 10 :1 range, making very large deviations possible.

## Slide 70
Module 3: Chapter 2
FM Circuits
Frequency Modulators:✓
Frequency Demodulators: ✓
Voltage Controlled Oscillators ✓
Slope Detectors
Phase Locked Loop (PLL)

## Slide 71
Frequency Demodulators
Circuits used to recover the original modulating signal from an FM transmission are called demodulators, detectors, or discriminators.

## Slide 72
Module 3: Chapter 2
FM Circuits
Frequency Modulators:✓
Frequency Demodulators: ✓
Voltage Controlled Oscillators ✓
Slope Detectors ✓
Phase Locked Loop (PLL)

## Slide 73
Slope Detectors
A slope detector is a device or circuit used in communication systems to detect frequency-modulated (FM) signals by converting changes in frequency into changes in amplitude.
Fig: Slope detector operation

## Slide 74
Working:
T₁ (Transformer with L₁ and L₂)
Purpose: Acts as a tuned circuit (band-pass filter).
L₁ (Primary coil): Receives the incoming FM signal.
L₂ (Secondary coil): Works with capacitor C₁ to form a resonant circuit that is slightly offset from the carrier frequency.
Function: Converts frequency changes into amplitude changes (this is the “slope” part of the slope detector).

## Slide 75
C₁ (Capacitor)
Forms an LC circuit with L₂ to create a frequency-selective filter.
Function: Filters and shapes the FM signal so that frequency variations result in amplitude variations.
D₁ (Diode)
Function: Acts as a demodulator (detector).
It rectifies the amplitude-modulated signal coming from the LC circuit, converting it into a pulsating DC that carries the original modulating information.

## Slide 76
R₁ (Resistor) and C₂ (Capacitor)
These form an RC low-pass filter.
Function: Removes high-frequency components (carrier and harmonics), leaving the original modulating signal.
Output Capacitor:
Purpose: Coupling capacitor.
Function: Blocks any remaining DC component and passes the recovered modulating signal (audio signal) to the output.

## Slide 77
X-axis: Frequency of the incoming FM signal.
Y-axis: Voltage across capacitor C₁ in the slope detector circuit.
If the frequency goes lower than the carrier frequency, the output voltage across C1 decreases.
If the frequency goes higher, the output across C1 goes higher.
At the resonant frequency fr the voltage across C1 peaks.
At lower or higher frequencies, the voltage falls off.

## Slide 78
Module 3: Chapter 2
FM Circuits
Frequency Modulators:✓
Frequency Demodulators: ✓
Voltage Controlled Oscillators ✓
Slope Detectors ✓
Phase Locked Loop (PLL) ✓

## Slide 79
Phase Locked Loop (PLL)
A phase-locked loop (PLL) is a frequency- or phase-sensitive feedback control circuit used in frequency demodulation.

## Slide 80
All phase-locked loops have the three basic elements, shown in Fig.
A phase detector:
  It is used to compare the FM input, sometimes referred to as the reference signal, to the output of a VCO.
The VCO:
  Frequency is varied by the dc output voltage from a low-pass filter.
The low-pass filter:
  It smoothes the output of the phase detector into a control voltage that varies the frequency of the VCO.

## Slide 81
Working:
The primary job of the phase detector is to compare the two input signals and generate an output signal.
If there is a phase or frequency difference between the FM input and VCO signals, the phase detector output varies in proportion to the difference.
The filtered output (also called the error signal) adjusts the VCO frequency in an attempt to correct for the original frequency or phase difference.

## Slide 82
When no input signal is applied, the phase detector and low-pass filter outputs are zero. The VCO then operates at a frequency called the free-running frequency.
When an input signal is applied, the phase detector compares the VCO free-running frequency to the input frequency and produces an output voltage proportional to the frequency difference.
The output pulses are then filtered into a dc voltage that is applied to the VCO.
This dc voltage forces the VCO frequency to move in a direction that reduces the dc error voltage.
The error voltage forces the VCO frequency to change in the direction that reduces the amount of phase or frequency difference between the VCO and the input.
When VCO frequency = the input frequency the PLL is said to be in a locked condition
Note: Although the input and VCO frequencies are equal, there is a phase difference of exactly 90° between them.

## Slide 83
If the input frequency changes, the phase detector and low-pass filter produce a new value of dc control voltage that forces the VCO output frequency to change until it is equal to the new input frequency.
Lock range:
The range of frequencies over which a PLL can track an input signal and remain locked is known as the lock range.
The lock range is usually a band of frequencies above and below the free-running frequency of the VCO.
If the input signal frequency is out of the lock range, the PLL will not lock

## Slide 84
If an input frequency within the lock range is applied to the PLL, the circuit immediately adjusts itself into a locked condition. This action is referred to as capturing an input signal.
Once the input signal is captured, the PLL remains locked and will track any changes in the input signal as long as the frequency is within the lock range.
The capture range:
The range of frequencies over which a PLL will capture an input signal, known as the capture range

## Slide 85
Capture range, is much narrower than the lock range

## Slide 87
Module 3: Chapter 3
Communication Receiver
Super heterodyne Receiver✓
Frequency Conversion
Mixing Principles
JFET Mixer

## Slide 88
Super heterodyne Receiver:
Q: Draw the block diagram of a super heterodyne receiver and explain the function of each block.

## Slide 89
Super heterodyne Receiver:
Definition :
A super heterodyne receiver is a type of radio receiver that uses frequency mixing to convert a received signal to a fixed intermediate frequency (IF), which can be more easily and efficiently processed than the original radio frequency (RF).
Key Concept:
Instead of amplifying and demodulating the received RF signal directly, a super heterodyne receiver mixes the incoming signal with a locally generated signal from a local oscillator to produce a new signal at a lower, intermediate frequency (IF). This IF signal is then filtered, amplified, and demodulated to extract the original audio or data.

## Slide 91
RF Ampliﬁers:
The antenna picks up the weak radio signal and feeds it to the RF amplifier, also called a low-noise amplifier (LNA). They are sometimes referred to as pre-selectors.
Mixers and Local Oscillators:
The output of the RF amplifier is applied to the input of the mixer.
The mixer also receives an input from a local oscillator or frequency synthesizer.
The mixer output is the sum and difference frequencies of these signals.
The local oscillator is made tunable so that its frequency can be adjusted over a relatively wide range

## Slide 92
IF Ampliﬁers:
The output of the mixer is an IF signal amplified by one or more IF amplifier stages, and most of the receiver gain is obtained in these stages.
Demodulators:
The highly amplified IF signal is finally applied to the demodulator, or detector, which recovers the original modulating information.
Automatic Gain Control:
The recovered signal, which is usually AC, is rectified and filtered into a dc voltage by a circuit known as the automatic gain control (AGC) circuit.
AGC circuits help maintain a constant output voltage level over a wide range of RF input signal levels.

## Slide 93
Why Use Super heterodyne?
  Improved Selectivity: Narrow and precise filtering at a fixed IF is easier than at variable RF.
  Better Sensitivity: Amplifiers at a fixed IF can be highly optimized.
  Tuning Ease: Only the local oscillator needs to change to select different frequencies, while IF stages remain the same.
Applications:
  AM/FM Radios
  TV Receivers
  Communication Systems
  Radar and Satellite Receivers

## Slide 94
Module 3: Chapter 3
Communication Receiver
Super heterodyne Receiver✓
Frequency Conversion ✓
Mixing Principles
JFET Mixer

## Slide 95
Frequency Conversion :
Frequency conversion is the process of translating a modulated signal to a higher or lower frequency while retaining all the originally transmitted information.
In radio receivers, high-frequency radio signals are regularly converted to a lower, intermediate frequency. This is called down conversion.
In satellite communications, the original signal is generated at a lower frequency and then converted to a higher frequency for transmission. This is called up conversion.

## Slide 96
Module 3: Chapter 3
Communication Receiver
Super heterodyne Receiver✓
Frequency Conversion ✓
Mixing Principles ✓
JFET Mixer

## Slide 97
Mixing Principles:
Q: Interpret the concept of a mixer with a neat schematic diagram.

## Slide 98
Mixing Principles:
Frequency conversion is a form of amplitude modulation or analog multiplication carried out by a mixer circuit or converter. The function performed by the mixer is called heterodyning.

## Slide 99
Mixers accept two inputs. The signal fs, which is to be translated to another frequency, is applied to one input, and the sine wave from a local oscillator fo is applied to the other input.
The signal to be translated can be a simple sine wave or any complex modulated signal containing sidebands.
The oscillator is the carrier, and the signal to be translated is the modulating signal.
The output contains not only the carrier signal but also sidebands formed when the local oscillator and input signal are mixed. The output of the mixer, therefore, consists of signals fs , fo , fo+ fs , and fo - fs or fs - fo.
The local oscillator signal fo usually appears in the mixer output. These are not needed in the output and are therefore filtered out.
Either the sum or difference frequency in the output is the desired signal.

## Slide 100
Module 3: Chapter 3
Communication Receiver
Super heterodyne Receiver✓
Frequency Conversion ✓
Mixing Principles ✓
JFET Mixer ✓

## Slide 101
JFET Mixer :

## Slide 102
Working:
FETs make good mixers because they provide gain, have low noise, and offer a nearly perfect square-law response.
The FET mixer is biased so that it operates in the nonlinear portion of its range.
The input signal is applied to the gate, and the local oscillator signal is coupled to the source.
Again, the tuned circuit in the drain selects the difference frequency.

## Slide 103
Class Test:
  Draw the block diagram of a super heterodyne receiver and explain the function of each block.
  Define PLL. Describe the basic block diagram of a PLL along with capture and lock ranges.
  Interpret the concept of a mixer with a neat schematic diagram.
  Outline Pre-emphasis and De-emphasis in detail with suitable block diagram.

## Slide 104
Thank You