## Slide 1
Course Coordinator:
Assistant Professor
Dept. of E&C, ATME
Guruprasad K N
Subject Name: Principles of Communication Systems
Subject Code: BEC402

## Slide 2
Module 4
Digital Representation of Analog Signals

## Slide 4
Introduction:
Why digitize analog sources?
Digital systems are less sensitive to noise than analog.
Digital systems helps in easier integration of different services. For example, video and corresponding soundtrack can be integrated into same transmission scheme.
The transmission scheme is independent of source. For example, a digital transmission scheme that transmits voice at 10kbps could also be used to transmit computer data at 10kbps.

## Slide 5
Why digitize analog sources?
Circuitry for handling digital signals is easier to repeat.
Digital circuits are less sensitive to physical effects such as vibration and temperature.
It is easier to design hardware associated with digital signals.
Various media sharing strategies such as multiplexing techniques can be easily implemented.
There are many techniques available for removing redundancy from a digital transmission.

## Slide 6
Band-limited Signal:
A signal is said to be band-limited if the amplitude of its spectrum goes to zero for all frequencies beyond some threshold called the cut-off frequency.

## Slide 7
Sampling Theorem:

## Slide 10
Time Domain Analysis

## Slide 15
Line Codes :
1. Unipolar Nonreturn-to-Zero (NRZ) Signaling.
In this line code, symbol 1 is represented by transmitting a pulse of amplitude A for the duration of the symbol, and symbol 0 is represented by switching off the pulse.

## Slide 16
Polar Nonreturn-to-Zero (NRZ) Signaling.
In this second line code, symbols 1and 0 are represented by transmitting pulses of amplitudes +A and -A, respectively

## Slide 17
Unipolar Return-to-Zero (RZ) Signaling
In this other line code, symbol 1 is represented by a rectangular pulse of amplitude A and half-symbol width, and symbol 0 is represented by transmitting no pulse, as illustrated in Figure

## Slide 18
Bipolar Return-to-Zero (BRZ) Signaling
This line code uses three amplitude levels as indicated in Figure . Specifically, positive and negative pulses of equal amplitude (i.e., +A and -A) are used alternately for symbol 1, with each pulse having a half-symbol width. No pulse is always used for symbol 0.

## Slide 19
Split-Phase (Manchester Code).
In this method of signaling, illustrated in Figure, symbol 1 is represented by a positive pulse of amplitude A followed by a negative pulse of amplitude -A, with both pulses being a half-symbol wide. For symbol 0, the polarities of these two pulses are reversed.

## Slide 20
Differential Encoding

## Slide 22
Thank You